## Slide 1: On FIRE mode in KSTAR
S.J. Park1, H. Han2, C. Sung3, D. Kim3, J.H. Lee1, C.H.Heo1, S.C. Hong1,2, J. Kang2, Y.H. Lee2, J. Chung2, T.S. Hahm1, B. Kim1,2, J.-K. Park1, J.G. Bak2, M.S. Cha1, G.J. Choi1, M.J. Choi2, J. Gwak1, S.H. Hahn2, J. Jang2, K.C. Lee2, J.H. Kim2, S.K. Kim4,5, W.C. Kim2, J. Ko2,6, W.H. Ko2,6, C.Y. Lee2, J.H. Lee2,6, J.H. Lee2, J.K. Lee2,6, J.P. Lee7, K.D. Lee2, Y.S. Park2,8, J. Seo9, S.M. Yang4, S.W. Yoon2 and KSTAR Team
1Seoul National Univ., Korea, 2KFE, Korea, 3KAIST, Korea, 4PPPL, U.S.A., 5Princeton Univ., U.S.A., 6KAIST, Korea, 7Hanyang Univ., Korea, 8Colmbia Univ., U.S.A., 9Chung-Ang Univ., Korea
Yong-Su Na1*
*ysna@snu.ac.kr

## Slide 2: Contents
Introduction
  Goal of tokamak research, Internal transport barrier, and FIRE mode
Experimental Approach
Characteristics of FIRE Mode
  Core: Ion transport barrier characteristics
  Edge: I-mode like structures
  MHD activities
Origin of Confinement Enhancement
  Correlation between fast ions and ITB foot
  Stabilization effects of fast ions on plasma turbulence
Comparison with Other Hot Ion Plasmas
Predictive Modeling
Conclusions

## Slide 3: Goal of Tokamak Research
High fusion performance (high )
  Figure of merit 1:
Steady-state operation ()
  Figure of merit 2:
Long pulse operation (
  Profile & MHD control, Particle & power handling, Engineering issues
⇒ “Integrated Advanced Scenarios”

## Slide 4: Internal Transport Barrier as an Advanced Scenario
Rationale
  Figure of merit 1:
  Figure of merit 2:

## Slide 5: Internal Transport Barrier as an Advanced Scenario
Demerits of ITB scenarios
Number of papers with titles including “Internal Transport Barrier”
Reduced interest in the community!
Difficulty in sustainment
Severe instabilities
ELMs and heat load
Impurity accumulations
Sophisticated profile control

## Slide 6: Fast Ion Regulated Enhancement (FIRE) mode[1]
[1] H. Han, S.J. Park and Y.-S. Na et al. Nature 609 269 (2022)
βN
ne
Ti
Te
H89X100
Dα
LV
C-III
  KSTAR #25860:
NBI
Notes: Fortunately, we think we could find solutions with so-called Fast Ion Regulated Enhancement mode, FIRE mode.

## Slide 7: Fast Ion Regulated Enhancement (FIRE) mode[1]
A new ITB scenario
[1] H. Han, S.J. Park and Y.-S. Na et al. Nature 609 269 (2022)
Difficulty in sustainment
Severe instabilities
ELMs and heat load
Impurity accumulations
Sophisticated profile control
Notes: (a), (b) time line으로 표시, EC on/off 표시

## Slide 8: Fast Ion Regulated Enhancement (FIRE) mode[1]
A new ITB scenario
  A stationary ITB in channel
  Almost non-inductive current drive ()
[1] H. Han, S.J. Park and Y.-S. Na et al. Nature 609 269 (2022)
Difficulty in sustainment | Stationary up to 50 s
Severe instabilities | No severe instabilities with high
ELMs and heat load | No ELMs and reduced heat load
Impurity accumulations | No clear impurity accumulations
Sophisticated profile control | Self-organized
Difficulty in sustainment | Stationary up to 50 s
Severe instabilities | 
ELMs and heat load | No ELMs and reduced heat load
Impurity accumulations | No clear impurity accumulations
Sophisticated profile control | Self-organized
  High performance (βN,H89L) even comparable to Hybrid mode
  Almost non-inductive current drive ()
Notes: (a), (b) time line으로 표시, EC on/off 표시

## Slide 9: Fast Ion Regulated Enhancement (FIRE) mode[1]
Comparison at 5.35 s
  <Profiles of FIRE mode and Hybrid scenario>
Comparison with hybrid scenario
Almost the same experimental conditions except for the null configuration (USN vs LSN).
Similar performance of βN < 2.6, H89L < 2.4 but with higher neutron rate in FIRE mode.
Clearly different kinetic profiles (ITB vs ETB)
[1] H. Han, S.J. Park and Y.-S. Na et al. Nature 609 269 (2022)
Notes: (a), (b) time line으로 표시, EC on/off 표시

## Slide 10: Fast Ion Regulated Enhancement (FIRE) mode[1]
Reactor relevant condition in FIRE mode
  Some NBI power replaced by ECH
  Still sustained ion ITB & high content of fast ions
  A possible new advanced scenario in reactor-relevant condition of
EC On
[1] H. Han, S.J. Park and Y.-S. Na et al. Nature 609 269 (2022)
Time evolution of 0d parameters
Notes: (a), (b) time line으로 표시, EC on/off 표시

## Slide 11: Fast Ion Regulated Enhancement (FIRE) mode
Notes: (a), (b) time line으로 표시, EC on/off 표시

## Slide 12: Contents
Introduction
  Goal of tokamak research, Internal transport barrier, and FIRE mode
Experimental Approach
Characteristics of FIRE Mode
  Core: Ion transport barrier characteristics
  Edge: I-mode like structures
  MHD activities
Origin of Confinement Enhancement
  Correlation between fast ions and ITB foot
  Stabilization effects of fast ions on plasma turbulence
Comparison with Other Hot Ion Plasmas
Predictive Modeling
Conclusions

## Slide 13: Key Factors to Access FIRE mode[2]
Low target density
Avoiding H-mode transition due to Increase of following U-shaped curve with respect to plasma density[3]
Deep penetration of NBI to produce rich fast ions in the core region
Diverted configuration
Reducing influx of particles from plasma-wall interactions
Moderate Neutral Beam Injection power
Main heat source and generation of fast ions
< required to keep sustainable ITB
[2] H.S. Han, POP 31, 032506 (2024)
[3] J. W. Ahn et al., NF 52 114001 (2012)

## Slide 14: Key Factors to Access FIRE mode
2.5 T
1.8 T

## Slide 15: Further Optimization for FIRE mode
Upper single null (USN) configuration
USN configuration unfavorable to L-H transition, where ion drift is away from X-point[3]
More margin to increase and plasma density
A long sustained FIRE mode was achieved in USN configuration with higher
The optimization between plasma performance and long-sustainability is still being investigated.
[3] L. Chen et al., PoP 25 072504 (2018)

## Slide 16: Further Optimization for FIRE mode
*S. Yang et al., Naure Comm. 15 1275 (2024)
Avoiding H-mode transition
L-H transition avoided with n = 1 ERMP and high performance sustained*

## Slide 17: Operation Window of FIRE mode
LSN
USN
Yong-Su Na | NSTX-U 2024 | Page

## Slide 18: Contents
Introduction
  Goal of tokamak research, Internal transport barrier, and FIRE mode
Experimental Approach
Characteristics of FIRE Mode
  Core: Ion transport barrier characteristics
  Edge: I-mode like structures
  MHD activities
Origin of Confinement Enhancement
  Correlation between fast ions and ITB foot
  Stabilization effects of fast ions on plasma turbulence
Comparison with Other Hot Ion Plasmas
Predictive Modeling
Conclusions

## Slide 19: Core Characteristics in FIRE mode
ITB characteristics in FIRE mode[1]
  : Considerably relaxed “stiffness” depicted in the ITG marginality scenario
[4] C.Y. Lee, et al., NF 61 96020 (2021)
[5] H. Lütjens, et al., CPC 97 219 (1996)
[6] W.A. Houlberg, et al., PoP 4 3230 (1997)
[7] A. Pankin, et al., CPC 159 157 (2004)
[8] G. Pereverzev, et al., IPP (2002)
※ Power balance analysis by TRIASSIC[4] with
CHEASE[5], NCLASS[6],
NUBEAM[7], ASTRA[8]
  decreased over time, but above the neoclassical level,
  correlated with the expansion of the ITB foot in time
ITB foot
[1] H. Han, et al. Nature 609 269 (2022)
Notes: 화질구지

## Slide 20: Core Characteristics in FIRE mode
ITB characteristics in FIRE mode[1]
  Transport bifurcation at
  “S-curve” between ion energy flux vs. ion temperature gradient
  Reduction in fluctuations measured by Electron Cyclotron Emission Imaging system
Ion Energy Flux Landscape
[1] H. Han, S.J. Park and Y.-S. Na et al. Nature 609 269 (2022)

## Slide 21: Edge Characteristics in FIRE mode
I-mode like structures at the edge region in some discharges
  ETB only in the energy channel, not in the particle channel
  Conjectured weekly coherent mode (WCM) around 50 kHz in the BES edge signals, propagating in the ion diamagnetic direction in the laboratory frame
  Higher performance (, ) and lower due to larger with I-mode structure
KSTAR shot 31923 at r/a=0.95
WCM
BES signal
FIRE+I-mode
FIRE+I-mode
FIRE
FIRE
H-mode
H-mode
ITB
ITB

## Slide 22: MHD Activities in FIRE mode
Fast ion driven Alfven Eigenmode
  Neutron deficit appeared after the AEs occurred compared with the NUBEAM calculation.

## Slide 23: MHD Activities in FIRE mode
Other MHD modes
  High and low frequency modes (not TM) observed
  Not significant impact on plasma performance
  Details under investigation

## Slide 24: Contents
Introduction
  Goal of tokamak research, Internal transport barrier, and FIRE mode
Experimental Approach
Characteristics of FIRE Mode
  Core: Ion transport barrier characteristics
  Edge: I-mode like structures
  MHD activities
Origin of Confinement Enhancement
  Correlation between fast ions and ITB foot
  Stabilization effects of fast ions on plasma turbulence
Comparison with Other Hot Ion Plasmas
Predictive Modeling
Conclusions

## Slide 25: Origin of Confinement Enhancement
Correlation between fast ion density fraction and ITB foot[1]
  Strong relation of the energy confinement to the fast ions
  Clearly remaining ITB with condition in presence of the large fast ion density fraction
KSTAR shot 22663
EC On
Significant effect of fast ions on stabilizing turbulence expected
[1] H. Han, S.J. Park and Y.-S. Na et al. Nature 609 269 (2022)

## Slide 26: Examination of Fast Ion Effect on Turbulence
Gyrokinetic simulations with fast ions for FIRE mode
  Fast ions considered as an independent species with effective temperature
  Reduction of the growth rate and thermal energy flux in presence of fast ions
CGYRO[10] non-linear simulation
[10] J. Candy et al., JCP 324 73 (2016)
GKW[9] linear simulation
[9] A. G. Peeters, et al., CPC 180 2650 (2009)
W fast ion
w/o fast ion

## Slide 27: Fast Ions’ Effects on Turbulence
Stabilization effects of Fast ions on plasma turbulence

## Slide 28: Fast Ions’ Effects on Turbulence
Stabilization effects of Fast ions on plasma turbulence
  stabilization effects
effect
[11] D. Kim et al., NF 63 124001 (2023)
CGYRO non-linear simulations[11]

## Slide 29: Fast Ions’ Effects on Turbulence
Stabilization effects of Fast ions on plasma turbulence
  Thermal ion dilution effects
CGYRO non-linear simulations[11]
  Even more reduced as a/Lni is inverted
Reduction of ni
due to fast ion
∆
w fast ion
Reduction of ni
due to fast ion
w fast ion
  Energy flux reduced as ni/ne is reduced
[11] D. Kim et al., NF 63 124001 (2023)
effect
Dilution
effect

## Slide 30: Fast Ions’ Effects on Turbulence
Stabilization effects of Fast ions on plasma turbulence
  Thermal ion dilution effects
  zonal flow enhanced
[12] T.S. Hahm, et al., PoP 30 072501 (2023) [13] G.J. Choi et al NF 64 016029 (2024)
Zonal flow growth rate in presence of fast ions[12]
: fraction of fast ion charge density
Saturated Turbulence level [13]
Zonal flow
threshold
Zonal flow
growth rate
normalized zonal flow growth rate
amplitude of pump wave
radial wavenumber

## Slide 31: Fast Ions’ Effects on Turbulence
Direct interaction between fast ions and turbulence
  Less contribution to turbulence (ITG, TEM) than thermal ion
  Minor changes observed in the linear GKW analysis when utilizing the fast ion distribution similar to the NUBEAM calculated distribution (preliminary)
NUBEAM
Shifted Maxwell.
anisotropy
thermalization
anisotropy
thermalization
Growth Rate
Shot 30239
w/o fast ion
Dilution
Wave-ptl interaction

## Slide 32: Contents
Introduction
  Goal of tokamak research, Internal transport barrier, and FIRE mode
Experimental Approach
Characteristics of FIRE Mode
  Core: Ion transport barrier characteristics
  Edge: I-mode like structures
  MHD activities
Origin of Confinement Enhancement
  Correlation between fast ions and ITB foot
  Stabilization effects of fast ions on plasma turbulence
Comparison with Other Hot Ion Plasmas
Predictive Modeling
Conclusions

## Slide 33: Comparison with Other Hot Ion Plasmas
Operation mode, Tokamak | Core transport | ITB | ETB | Duration | Ti/Te | SOL limiter divertor
Supershot, TFTR[1,2] | Reduced | No | No | Transient | High | Low recycling: lithium conditioning
Hot-ion H-mode, JET[1,2] | Strong reduction | No | Yes no ELMs | Transient | High | Low recycling
Ion ITB with I-mode, HL-2A[3] | Reduced | Yes | ETB in Te | Transient | High | 
Ion ITB by fast ion, ASDEX-Upgrade[4] | Reduced | Yes | No | Transient | High | 
Hot ion mode, ST-40[5] | Reduced | No | No | Transient | High | 
Hot-ion H-mode, Globus-M2[6] | Reduced | Yes | Yes | Transient | High | 
FIRE mode, KSTAR | Reduced | Yes | Possible | CW | Low to high | Low recycling
[1] J. Jacquinot et al 1999 PPCF 41 A13
[2] R.J. Hawryluk et al 1998 RMP 70 2
[3] A.S. Liang et al 2023 NF 63 056017
[4] G. Tardini et al 2007 NF 47 280, [5] S.A.M. McNamara et al 2023 NF 63 054002
[6] G.S. Kurskiev et al 2022 NF 62 104002

## Slide 34: Contents
Introduction
  Goal of tokamak research, Internal transport barrier, and FIRE mode
Experimental Approach
Characteristics of FIRE Mode
  Core: Ion transport barrier characteristics
  Edge: I-mode like structures
  MHD activities
Origin of Confinement Enhancement
  Correlation between fast ions and ITB foot
  Stabilization effects of fast ions on plasma turbulence
Comparison with Other Hot Ion Plasmas
Predictive Modeling
Conclusions

## Slide 35: Predictive Modelling for the Basis of Future Projections
Equilibrium
Anomalous
transport
Neutral
beam
Neutral source
Neo-classical transport
TRIASSIC[4]
ASTRA[8]
CHEASE[5]
NCLASS[6]
TGLF[4]
NUBEAM[7]
FRANTIC[15]
[4] C.Y. Lee, et al., NF 61 96020 (2021)
[5] H. Lütjens, et al., CPC 97 219 (1996)
[6] W.A. Houlberg, et al.,PoP 4 3230 (1997)
[12] G.M. Staebler, et al., PoP 12 102508 (2005)
[7] A. Pankin, et al., CPC 159 157 (2004)
[13] S. Tamor, et al., JoCP 40 104 (1981)
[8] G. Pereverzev, et al., IPP (2002)
A FIRE mode, #26043 @4.3s
Integrated suite of code, TRIASSIC[1] used
Dominant dilution effects evaluated with TGLF[14]

## Slide 36: Predictive Modelling for the Basis of Future Projections
Equilibrium
Anomalous
transport
Neutral
beam
Neutral source
Neo-classical transport
TRIASSIC[4]
ASTRA[8]
CHEASE[5]
NCLASS[6]
TGLF[4]
NUBEAM[7]
FRANTIC[15]
[4] C.Y. Lee, et al., NF 61 96020 (2021)
[5] H. Lütjens, et al., CPC 97 219 (1996)
[6] W.A. Houlberg, et al.,PoP 4 3230 (1997)
[12] G.M. Staebler, et al., PoP 12 102508 (2005)
[7] A. Pankin, et al., CPC 159 157 (2004)
[13] S. Tamor, et al., JoCP 40 104 (1981)
[8] G. Pereverzev, et al., IPP (2002)
A FIRE mode, #26043 @4.3s
Integrated suite of code, TRIASSIC[1] used
Several effects evaluated with TGLF[14]
  Dilution effect, ExB shearing effect, electromagnetic fluctuation
Exp.(fitting) All considered No dilution No No
used to match the growth rate of ion-scale turbulence from GKW

## Slide 37: Contents
Introduction
  Goal of tokamak research, Internal transport barrier, and FIRE mode
Experimental Approach
Characteristics of FIRE Mode
  Core: Ion transport barrier characteristics
  Edge: I-mode like structures
  MHD activities
Origin of Confinement Enhancement
  Correlation between fast ions and ITB foot
  Stabilization effects of fast ions on plasma turbulence
Comparison with Other Hot Ion Plasmas
Predictive Modeling
Conclusions

## Slide 38: Conclusion
A new ITB scenario, “FIRE mode” (Fast Ion Regulated Enhancement mode)
  High performance and low loop voltage with
    Stationary long-pulse up to ~５0 s so far
    No severe instabilities including ELMs
    No impurity accumulation
    No requirement for delicate feedback control
  Recipe: Moderate NBI at low density in diverted configuration by avoiding the L-H transition
Role of fast ions in ITG turbulence stabilization in FIRE mode
  Enhanced effect, most significantly dilution effect (due to reduced and )
  Reproduced by predictive modeling with TGLF
Remaining Issues
  Increase the performance by broadening the ITB and/or strengthening the I-mode like edge
  Increase the bootstrap current fraction (so far ~20%)
  Access the high plasma density regime for higher fusion power
  Extrapolation to future devices

## Slide 39
Post-credits scene

## Slide 40: Operation Window of FIRE mode
LSN
USN
Yong-Su Na | NSTX-U 2024 | Page

## Slide 41: Predictive Modelling for High Density Operation
  Explored numerically using the predictive models with PNB = 7.5 MW, ENB = 100 keV
  The density profile prescribed twice of the experimental value at 4.2 s of shot 26043

## Slide 42: High Density Operation in Experiment
High density while avoiding H mode transition
  Supersonic molecular beam injection (SMBI) or pellet injection for increase of the core density
  Higher Ip, Bt for higher density and better fast ion confinement
  USN or negative triangularity
  ERMP to avoid H-mode transition

## Slide 43
Thank you.

## Slide 44: Prospect
High density regime by avoiding L-H transition
  High beam energy
  Elongated plasmas for deeper penetration of the beam
  Negative triangularity
p-B reaction
  Two-component, Beam-target fusion
Trigger of alpha dominant heating
  NBI would be needed in fusion reactors for load control together with fuelling
  Ignite alpha heating with fast ions

## Slide 45: Comparison between Hot ion mode and FIRE mode
Ref. J Jacquinot and the JET team 1999 Plasma Phys. Control. Fusion 41 A13
Characteristics of tokamak modes
FIRE mode
CW
None (due to ??)
Reduced
YES
Possible
Low recycling

## Slide 46: Supershot/Hot Ion Mode vs FIRE Mode
Similarity
Difference
NBI heating low density 1)
High core Ti 1)
No ELMs 1)
High fraction of fast ions nfast/ne 50% 2)
Stationarity
Impurity issues 3)
Transport property 2)
ExB shearing model effectively works in Supershots 4)
Compatible with I-mode like edge
J.D Strachan, PRL, ’87
S.D. Scott, PRL, ‘89
A.T. Ramsey, ‘91
D.R. Ernst, PLR, ‘98
~ 0.5 - 1.5 x 1019 m-3
PNBI ~ 3 - 4 MW
PNBI ~ 20 – 30 MW
~ 1 - 4 x 1019 m-3
< FIRE >
< Supeprshot >
Ti,0 ~ 10 keV
Ti,0 ~ 20 - 30 keV
< FIRE >
< Supeprshot >
No sign
of impurities
< FIRE >
< Supeprshot >
degradation
due to carbon influx
< FIRE >
< Supeprshot >
< FIRE >
< Supeprshot >

## Slide 47: Hot Ion Mode vs FIRE Mode
[S. Scott et al., PRL (1990)]
[H. Han, et al., Nature (2022)]
ITB in
“Enhancement of with ”
“De-stiffening with Fast Ions”
TFTR
KSTAR
Overall peaking in

## Slide 48: Fast ion amount in hot ion mode
JET Hot ion H-mode #42976
(DTE1, highest global PDT)
[R.V. Budny, NF, ’16]
TFTR Supershot #80539
(highest PDT)
[R.V. Budny, NF, ’94]
[R.V. Budny, NF, ’16]
Usually, low density with high fast ion amount
However, not always large amount of fast ions for hot ion H-mode
TFTR supershot and hot ion mode have large amount of fast ions ()
[R.V. Budny, NF, ’16]
[S.D. Scott, PRL, ’90]
KSTAR FIRE typically

## Slide 49: Appendix
Adjustable parameter in TGLF
  Parameter to adjust which control the resonance and fraction of trapped particle
  Default:
A. TZANIS(TH-C-2293) on P/6 [Oct.19(Thu) 2PM]

## Slide 50: Comparison of growth rate between GKW and TGLF
KSTAR FIRE shot 26043 at t = 4.2 s
  Maximum growth rate of ion-scale turbulence is roughly same with case
  Further verification of TGLF for FIRE mode is needed
A. TZANIS(TH-C-2293) on P/6 [Oct.19(Thu) 2PM]
Linear Growth rate at ρn = 0.4
GKW
Linear Growth rate at ρn = 0.6
GKW

## Slide 51: Appendix
Some FIRE mode shots exhibit I-mode-like edge characteristics
  Weakly Coherent Mode (WCM) are observed around 50kHz.
D.G. Whyte, et al., NF 50 105005 (2010)
WCM
I-mode like BES spectrogram (#31923)
L-mode like BES spectrogram (#31792)

## Slide 52: Appendix
Some FIRE mode shots exhibit I-mode-like edge characteristics
  WCM structure is localized near the pedestal top-inner half of the pedestal.
  WCM in FIRE mode shows even less coherency compared to the WCMs of I-modes from the other tokamaks.
  - spectrum also reveals WCM structure, but with less coherency.
R. Bielajew, et al., PoP 29 052504 (2022)
#31923 BES 2D coherence analysis
Edge profiles measured by CES
● H-mode
● FIRE mode with pedestal
● L-mode
- spectrum comparison[b]
AUG I-mode
#31923

## Slide 53: Appendix
Some FIRE mode shots exhibit I-mode-like edge characteristics
  WCM structure is localized near the pedestal top-inner half of the pedestal.
  WCM in FIRE mode shows even less coherency compared to the WCMs of I-modes from the other tokamaks.
  - spectrum also reveals WCM structure, but with less coherency.
R. Bielajew, et al., PoP 29 052504 (2022)
#31923 BES 2D coherence analysis
Edge profiles measured by CES
● H-mode
● FIRE mode with pedestal
● L-mode
- spectrum comparison[b]
AUG I-mode
#31923

## Slide 54
Fishbones are found to be the main MHD activity observed during the high confinement phase.
Early in the good confinement phase a saturation of both ion and electron temperatures profiles is observed shortly after the onset of fishbones.
During the high confinement phase, fast ions are not sufficiently energetic to have a stabilizing influence on m = 1 modes.
The sawtooth free periods observed in this phase may be due to the combined stabilization of large ion diamagnetic frequencies and ion-ion collisions.
M.F.F. Nave et al 1995 Nucl. Fusion 35 409

## Slide 55: JET Hot-ion H-mode

## Slide 56
TFTR super shot
Distinctive features of the supershot, compared with other operating modes, include a highly peaked density profile, a broad electron temperature profile, and a very high central ion temperature Ti (0) that is several times higher than Te(0). While the pre-injection density must be low, the central density in a supershot is quite high, up to 1020/m3, and the central pressure is as large as 6.5 atm.