## Slide 1: Overview of D-T fuel cycles: the quest for tritium self-sufficiency and the growth of fusion energy
S. Meschini, R. Delaporte-Mathurin, G. Tynan, D. Whyte, S. Ferry
MIT PSFC

## Slide 2: MOTIVATIONS

## Slide 3: TRITIUM SELF-SUFFICIENCY (TSS)
FPP
Startup inventory
Self-sufficient + produce net tritium
Doubling time,
FPP
TBRa > TBRr
Notes: Figure of merit
We link these figure of merit with fuel cycle models

## Slide 4: SYSTEM-LEVEL MODELING APPROACH
FC
Tritium systems
  1D or 0D + time models for each component
Startup inventory and FC dynamics
Inflow from j-th component
Non-radioactive tritium losses
Tritium generation
Mean residence time in the i-th component
Radioactive tritium losses
Residence time method
Abdou, M., et al., Nuclear fusion 61.1 (2020): 013001.
Meschini, S., et al., Nuclear Fusion 63.12 (2023): 126005.

## Slide 5: TSS IS MULTI-SCALE PROBLEM
H – lattice interaction
  Molecular dynamics
  Density Functional theory
Components
FC
Phenomenology,
…
H transport
  McNabb – Foster model (3D diffusion + trapping)
Tritium systems
  1D or 0D models
FPP fleet
Global market
  Tritium reserves
  Fusion energy penetration
Defect evolution, trap energy and density
Startup inventory and FPP dynamics
Material selection, component design
Technology selection, system design, safety
Tritium management strategies, policies
Notes: Add atomic scale the results do not produce very useful data, but allow to understand the phenomenology

## Slide 6: OUTLINE
Macroscopic H transport
  Tritium implantation and trapping
  Impact of neutron irradiation and material damage on tritium self-sufficiency
Fuel cycle
  Fuel cycle dynamics
  Fuel cycle layout
  Main technologies
Global market
  Tritium reserves management
  Fusion energy penetration
Notes: Add atomic scale the results do not produce very useful data, but allow to understand the phenomenology

## Slide 7: OUTLINE
Macroscopic H transport
  Tritium implantation and trapping
  Impact of neutron irradiation and material damage on tritium self-sufficiency
Fuel cycle
  Fuel cycle dynamics
  Fuel cycle layout
  Main technologies
Global market
  Tritium reserves management
  Fusion energy penetration
Notes: Add atomic scale the results do not produce very useful data, but allow to understand the phenomenology

## Slide 8: A BASIC FUEL CYCLE MODEL
PLASMA
IFC
Storage & fueling
OFC
Outer fuel cycle (OFC)
Inner fuel cycle (IFC)
Tritium flow
Neutron flux
Tritium processing
Tritium breeding and extraction
: Tritium burn rate
TBE: Tritium Burn Efficiency

## Slide 9: THE INITIAL TRANSIENT SETS THE STARTUP INVENTORY
TBRa > TBRr
For 24h tritium reserves

## Slide 10: RISK REGIONS – REFERENCE VALUES
Required TBR
Startup inventory (kg)
World reserves of tritium (non-military)
Doubling time (y)
Risk
High
Medium
Low
Medium-low
1.3
1.2
1
1.1
10
7
2
5
40
20
1
5

## Slide 11
PLASMA
Vacuum Pump
Storage and Management
Fueling System
Fuel Cleanup
Isotope Separation System
Detritiation System
First Wall
Blanket
Divertor
Heat exchanger
DIR
Outer fuel cycle (OFC)
Inner fuel cycle (IFC)
Tritium flow
Tritium ion flux
Neutron flux
Path may or may not be present, pending technology choices
Tritium fuel cycle of an ARC-class fusion power plant
TES
T separation membrane
Meschini, S., et al., Nuclear Fusion 63.12 (2023): 126005.

## Slide 12
PLASMA
Vacuum Pump
Storage and Management
Fueling System
Isotope Separation System
Detritiation System
First Wall
Blanket
Divertor
Heat exchanger
DIR
FUEL CLEANUP
TES
T separation membrane
GOAL
Separate fuel (D and T) from other gases
Fuel Cleanup
Different flavors of Pd membranes

## Slide 13
PLASMA
Vacuum Pump
Storage and Management
Fueling System
Fuel Cleanup
Isotope Separation System
Detritiation System
First Wall
Blanket
Divertor
Heat exchanger
DIR
Outer fuel cycle (OFC)
Inner fuel cycle (IFC)
Tritium flow
Tritium ion flux
Neutron flux
Path may or may not be present, pending technology choices
MOST CRITICAL COMPONENTS
TES
T separation membrane
!
!
!
!

## Slide 14: DIRECT INTERNAL RECYCLING
Metal Foil Pumps
GOALS
Provide effective pumping
Sharp H selectivity
Peters, B.J, and Day, C., FED 124 (2017): 696-699.
SUPERPERMEATION
CLASSIC DIFFUSION
x102 – 104

## Slide 15: DIRECT INTERNAL RECYCLING
Metal Foil Pumps
FUNCTIONS:
Effective pumping
Sharp H selectivity
Peters, B.J, and Day, C., FED 124 (2017): 696-699.
SUPERPERMEATION
CLASSIC DIFFUSION
x102 – 104

## Slide 16: TRITIUM BURN EFFICIENCY
Tritium removal is a collateral effect of He ash removal
Whyte, D. G., et al, Nuclear Fusion 63.12 (2023): 126019.
ITER TBE = 0.36%

## Slide 17: TBE and TSS
TSS is virtually impossible at low TBE
Meschini, S., et al., Nuclear Fusion 63.12 (2023): 126005.

## Slide 18: TBE and FUSION POWER
TBE can be improved by:
  Increasing the He fraction in the divertor,
  Selective He pumping,
Improving tritium self-sufficiency
Decreasing power production
Tritium self-sufficiency and power production are competing goals!
Meschini, S., et al., Nuclear Fusion 63.12 (2023): 126005.

## Slide 19: TBE and FUSION POWER
Possible strategies to improve TBE and
  Selective He pumping
  Spin polarized fuels
  Asymmetric transport
Improving tritium self-sufficiency
Decreasing power production
Meschini, S., et al., Nuclear Fusion 63.12 (2023): 126005.

## Slide 20: OUTLINE
H transport
  Tritium implantation and trapping
  Impact of neutron irradiation and material damage on tritium self-sufficiency
Fuel cycle
  Fuel cycle dynamics
  Fuel cycle layout
  Main technologies
Global market
  Tritium reserves management
  Fusion energy penetration

## Slide 21: NEUTRON-INDUCED DAMAGE IN MATERIALS
Implantation
Diffusion
Trapping
Detrapping
Material damage and hydrogen trapping
n
Radiation damage
n
H
PLASMA
Vacuum Pump
Storage and Management
Fueling System
Fuel Cleanup
Isotope Separation System
Detritiation System
First Wall
Blanket
Divertor
Heat exchanger
DIR
TES
T separation membrane
+ COMPONENT REPLACEMENT

## Slide 22: TRAPPING AND COMPONENT REPLACEMENT STRONGLY IMPACT TSS
No traps
As before
Intrinsic traps
Trapping energy negligible at blanket operating temperatures
Negligible (constant) trap density
Damage-induced traps
High trapping energy
Non-negligible, increasing trap density
+ 3% TBRr and + 20% startup inventory
Trapping + component replacement
Periodic tritium sink
Must recover trapped tritium before disposal
Meschini et al., Submitted to NF

## Slide 23: DESIGN CONSIDERATIONS DUE TO TRAPPING
Tritium retention in tritium facing components (structural materials) dominates the reactor tritium inventory
Very high operating temperatures may worsen retention due to trapping

## Slide 24: OUTLINE
Macroscopic H transport
  Tritium implantation and trapping
  Impact of neutron irradiation and material damage on tritium self-sufficiency
Fuel cycle
  Fuel cycle dynamics
  Fuel cycle layout
  Main technologies
Global market
  Tritium reserves management
  Fusion energy penetration
Notes: Add atomic scale the results do not produce very useful data, but allow to understand the phenomenology

## Slide 25: TRITIUM RESOURCES AVAILABLE
Kovari, M., et al. "Tritium resources available for fusion reactors." Nuclear Fusion 58.2 (2017): 026010.
See also: Pearson, R., et al., Fusion Engineering and Design 136 (2018): 1140-1148.
Private companies might deploy FPPs2 even before ITER starts D-T operations (delayed to 20391)
Goal:
375 TWh of electricity production by 2050
with
1 https://www.iter.org/newsline/-/4056
2 The global fusion industry in 2024, Fusion Companies Survey by the Fusion Industry Association

## Slide 26: UNCERTAINTY IN FC DESIGN MAKES THE RESERVES EVOLUTION VERY UNCERTAIN
Multiple factors impact tritium reserve evolution:
TBR
Startup inventory
FPP construction time
FPP availability
…
First FFP operations start
First FPP construction starts
S. Meschini, TOFE 2024

## Slide 27: STARTUP INVENTORY DRIVES FUSION ENERGY GROWTH AND TRITIUM ECONOMY
1
Limit at
1 Kovari, M., et al. "Tritium resources available for fusion reactors." Nuclear Fusion 58.2 (2017): 026010.
Tritium reserves chocked by too high, scattered demand
Assuming a regulated market as for He3
S. Meschini, TOFE 2024

## Slide 28: CONCLUSIONS
Tritium self-sufficiency is a multiscale problem. Lack of coordination and experiments to connect the scales.
Technology development (DIR) and ‘tritium efficient’ plasma operations (TBE) can revolutionize fuel cycle designs
Tritium retention in tritium facing components (structural materials) dominates the reactor tritium inventory
Very high operating temperatures may worsen retention due to trapping

## Slide 29: CONCLUSIONS
Tritium reserves might easily approach 0 for
  Regulated or unregulated market?
If the operations of FPPs start between 2035 and 2040, ITER T consumption will be easily covered by surplus production from FPP
T price is likely to spike, then fall - might be a valuable revenue stream for 1st generation FPPs

## Slide 30: BACKUP SLIDES

## Slide 31: R&D H TRAPPING
Trap energy and density data is scarce and unreliable for structural materials (V alloys, Eurofer, HEA, Nikel superalloys)
Defect production and dynamics need deeper understanding, especially at high fluences and high neutron energies
Tungsten is assumed to be a good proxy for fusion neutrons (demonstrated for fission neutrons only). None of the available facilities can achieve FPP-relevant fluences (or dpa) with 14 MeV neutrons
Computational material science (DFT and MD) might be pivotal to speed up R&D in this field

## Slide 32: RELATION BETWEEN TSS FIGURES OF MERIT
Set by FC design and reserves
Set by FC design and reserves
Informed by global scale constraints (economics, policies, T supply)
Design requirement for blankets
Uninformed approach
From blanket design
Informed approach

## Slide 33: MAJOR DRIVERS ARE IFC RESIDENCE TIME AND TRITIUM BURN EFFICIENCY
Faster T processing time
Better fuel usage
Relative sensitivity index

## Slide 34
PLASMA
Vacuum Pump
Storage and Management
Fueling System
Fuel Cleanup
Isotope Separation System
Detritiation System
First Wall
Divertor
Heat exchanger
DIR
BREEDING BLANKETS
TES
T separation membrane
TECHNOLOGIES
Liquid breeders:
  Molten salts*
  Li
  PbLi
Solid breeders:
  HCPB
GOAL
Breed tritium (+ heat extraction and shielding)
Blanket
*LIBRA experiment at MIT

## Slide 35
PLASMA
Vacuum Pump
Storage and Management
Fueling System
Fuel Cleanup
Isotope Separation System
Detritiation System
First Wall
Divertor
Heat exchanger
DIR
BREEDING BLANKETS
TES
T separation membrane
TECHNOLOGIES
Liquid breeders:
  Molten salts
  Li
  PbLi
Solid breeders:
  HCPB
GOAL
Breed tritium (+ heat extraction and shielding) 1,2
Blanket
1Di Giacomo, M., Master Thesis, PoliTo, 2024.
2Bae, Jin Whan, et al., Nuclear Fusion 64.5 (2024): 056013.
Shimwell, J., https://xsplot.com/

## Slide 36
PLASMA
Vacuum Pump
Storage and Management
Fueling System
Fuel Cleanup
Isotope Separation System
Detritiation System
First Wall
Blanket
Divertor
Heat exchanger
DIR
TRITIUM EXTRACTORS
T separation membrane
TECHNOLOGIES
Permeator against vacuum
Vacuum sieve tray
Gas-liquid contactor
GOAL
Extract tritium from a carrier
TES

## Slide 37
PLASMA
Vacuum Pump
Storage and Management
Fueling System
Fuel Cleanup
Isotope Separation System
Detritiation System
First Wall
Blanket
Divertor
DIR
HEAT EXCHANGERS
TES
T separation membrane
TECHNOLOGIES
Direct coupling with power cycle
  Double wall heat exchanger
Indirect coupling
  Intermediate loop (+storage)
Simultaneous extraction of heat and tritium?
GOAL
Heat transfer
Prevent contamination (if double function coolant/carrier)
Heat exchanger
Colliva, Francesco, et al., FED 201 (2024): 114261.

## Slide 38
PLASMA
Storage and Management
Fueling System
Fuel Cleanup
Isotope Separation System
Detritiation System
First Wall
Blanket
Divertor
Heat exchanger
DIR
VACUUM PUMPS
TES
T separation membrane
TECHNOLOGIES
Kinetic
  Turbomolecular
  Vapor diffusion
Getter
  Cryopump
DIR:
  Metal foil pumps
  Proton conducting pumps
  Multistage cryopumps
GOAL
Remove He ash (plasma operations)
Pump down (dwell time)
Vacuum Pump

## Slide 39: DESIGN CONSIDERATIONS DUE TO TRAPPING
Tritium retention in tritium facing components (structural materials) dominates the reactor tritium inventory
Tritium retention in plasma facing components still important but less relevant (compare an FPP vs experimental device)
Very high operating temperatures may worsen retention due to trapping
Frequent replacement of in-vessel components requires fast and efficient tritium removal techniques
Standard tritium removal techniques are not effective to remove tritium from high energy traps