## Slide 1
“Controlling” MHD During the Plasma Start-Up
S.P. Gerhardt, Alessandro Bortolon, other victims
2011 & 12 NSTX Research Forum
MS TSG Breakout Session
NSTX
Supported by
College W&M
Colorado Sch Mines
Columbia U
CompX
General Atomics
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Nova Photonics
New York U
Old Dominion U
ORNL
PPPL
PSI
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Washington
U Wisconsin
Culham Sci Ctr
U St. Andrews
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Hebrew U
Ioffe Inst
RRC Kurchatov Inst
TRINITI
KBSI
KAIST
POSTECH
ASIPP
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
U Quebec

## Slide 2: Overview
“Low-density startup” should include surviving the entrance of q=4,3, & 2 into the plasma…typically some few hundred msec. after SOFT.
Tearing/mhd associated with those surfaces often locks to the wall, leading to large b collapse or disruption.
I (we?) think that any of the current profile, plasma b, rotation, or rotation shear may impact the amplitude locking of these modes.
  Also all the early EPM/TAE activity.
Propose to optimize the discharge to ride through early modes:
  b: Feed forward or feedback control of NB heating.
  Current profile: heating timing, ramp rate.
  Rotation: H-mode timing.
Early EFC is not a focus of the XP, but will be used as available.

## Slide 3: S. Sabbagh’s Low ne Shots Failed When Rotating Modes Started to Lock
“Good Low
Density Shot”
“Good Low Density Shot”
“Bad Shot”
Fixed the gas.
Good high
density shot.
Chirping?
Chirping?
Mode at q=4 locks to wall

## Slide 4: Appears that EPM May Have Triggered the Mode That Ultimately Locks
q=4 enters the plasma at ~0.19, but mode does not strike till 0.22.
Mode strike coincident with large EMP.
Does some triggering physics explain why previous shots didn’t have large q=4 modes?

## Slide 5: Chirping q=3 Mode Settles With Inversion Radius In the Outer Plasma
Mode chirps down.
Inversion layer develops in the outer plasma.
q=3 island?…need bit more analysis.
Core kink-like component as well?
ME-USXR may be quite useful analyzing this data.

## Slide 6: Not Easy To Find Difference Between Shots Using 0D Parameters
Long-Pulse Lower Density
Disrupting Lower Density
Long Pulse Higher Fuelling

## Slide 7: We Have Evidence That Changing the Heating Profile Can Impact the Evolution of These Modes.
Tried early and late heating.
  Delay of H-mode as well.
  Substantial changes in EP/TAE
Rotating n=1 mode amplitudes are modified.
  Need to look more carefully at m-number identification.
135642: Early Pinj 135647: Late Pinj

## Slide 8: XP Plan: Needs refinement, but basics are…
Reload a scenario such as 141178 (S. Sabbagh’s reduced density target).
Study the space of rotation, b, and ne vs. mode dynamics.
  Test low power early, delayed H-mode.
    Reduced b and density with single source will allow surfaces in quickly, should have strong rotation.
    Elimination of EPMs may be important…lower voltage pre-heating beam?
  Study timing of b (Pinj) ramp.
    When is the earliest time that we can ramp b without EPMs and large modes.
    Can we prevent too-rapid J evolution if we only heat strongly after q=2 enters?
  Vary the ramp rate:
    If we slow the ramp rate, can we prevent some unstable current profiles?
    And eliminate some irreproducibility of the modes?
    Target the q=2 & 3 surfaces entering just after the IOH zero crossings?
  What is the impact of reduced input power?
    Onset of “IREs” will be unacceptable.
    Unsustainably high li will be unacceptable.
    Earlier onset of RWMs or the “late” rotating MHD is OK…
      not in scope of XP
Diagnostic considerations.
  Need source A for important MSE measurements.
    MSE-LIF might be OK…?
  Need USXR measurements, BES (?) for MHD identification.
Typical q and J|| profile during time of q=2 & 3 entering