## Slide 1: The Centrifugal Granule Injector Concept: Can Injected Li Granules Trigger ELMs ?
5.5 inch
8 inch
6 inch
V = 0 - 100 m/s
Freq = 0 - 100 Hz
Independent Control:
Granule Size : 0.5 - 1 mm
(change between shots)
Injection Speed: 0 - 100m/s
(ramp during shots)
Pacing Frequency: 0 - 100 Hz
(ramp during shots)
Dropper
Li Granules
1
1 mm Scale
Li Granules

## Slide 2: Calculated Pedestal Deposition for 1 mm Li Granules with Injection Speeds from 30 m/s to 100 m/s
Paul Parks, Wen Wu
Deposited Li Density vs r/a
Linear Temperature and Density
Profiles Assumed for Pedestal:
Te (r/a = 1) = 0
Te(r/a = 0.94) = 1 keV
ne(r/a = 1 ) = 0
ne(r/a = 0.94) = 5 x 1013 cm-3
Reasonable Approximation
to DIII-D Pedestal R = 1.67 m
a = 0.65 m
Neutral Gas Shielding Ablation
Model for Li Employed
Results Similar to D Pellet Ablation
Which Does Trigger ELMs on DIII-D
Top of Pedestal
7

## Slide 3: The Granule Injector
8 Inches
Existing Laser
& Photodiode
(Particle Counter)
Air Driven
Micromotor
Ferro Tec
Rotary Feed-thru
Flexible
Coupling
Existing Laser
& Photodiode
(Freq. Monitor)
Delivery Tube
from Dropper
19

## Slide 4: Granule Injection Run Plan
Systematic scan of granule size and velocity
  Do granules trigger ELMs?
  What kind of ELMs?
    Is the evaporated Li swept toward the LSN?
Systematic scan of pacing frequency
  Is Prad reduced?
1 day requested

## Slide 5: Serving Double Duty to Inject Li Powder at the Midplane (Li Swept by SOL Flow Toward LSN)
8 Inches
Existing Laser
& Photodiode
(Particle Counter)
Air Driven
Micromotor
Ferro Tec
Rotary Feed-thru
Flexible
Coupling
Existing Laser
& Photodiode
(Freq. Monitor)
Delivery Guide
from Dropper
Li Powder
20

## Slide 6: Midplane Powder Injection Run Plan
Systematic scan of powder size and velocity
  Does midplane injection cause the evaporated Li to be swept toward the LSN?
Systematic scan of powder flux
  Signs of improved plasma performance
  Elms triggering?
1 day requested

## Slide 7: Extra Slides

## Slide 8: The Scheme: Redirecting a Regular Stream of Falling Lithium Granules with a Rotating Impeller
Insertion Velocity
Shaft Rotation Frequency
Depth of Insertion
Rotor Period
  Injection Velocity
Free Fall Distance
Impeller Radius
Pacing Frequency
Granule Reservoir
Pacing Frequency
8

## Slide 9: Demonstration of ELM Pacing by Deuterium Pellets with No Fueling on DIII-D
14 Hz Pellets
No Pellet Comparison
1.5
2.0
2.5
3.0
3.5
Density
Div Da
Div Da
Pellet
3.0
2.0
4.0
1.0
0.0
(1014 cm-2)
4
2
6
0
4
2
6
0
(a.u.)
(a.u.)
Time (s)
ITER shape
bN = 1.8
1.8 mm D2 Pellets
100-150 m/s
Larry Baylor
4

## Slide 10: Lessons Learned from Successful ELM Pacing Experiments on DIII-D using D Pellets
ELM triggered
No ELM triggered
?
Chart: DIII-D Pellet Parameters



Velocity yes | 200 | 100 | 800
no | 3 | 10
? | 40
ELM triggered
No ELM triggered
ELM Triggering
Boundary ?
Li ELM Triggering
Boundary ?
DIII-D results indicate thresholds of D pellet sizes and speeds exist for reliable ELM pacing.
A hypothetical curve is drawn by hand on the right indicating where a threshold boundary may exist. (shown in yellow)
A second hypothetical curve for Li granules is shown (in grey). This curve is meant to indicate that lower speeds and small sizes may be needed with Li granule injection.
The crossed lines indicate the chosen design parameters for the prototype Li.
Larry Baylor
5

## Slide 11: Examples of Edge Perturbations from Low-Velocity (~ 5m/s) Lithium Clumps (~ 2mm) in Four Discharges (2008)
130364@ 272 ms
130364@ 280 ms
130389@ 353 ms
130389@ 356 ms
130387@ 191 ms
130387@ 197 ms
130385@ 393 ms
130385@ 400 ms
ELM
Triggered !
3

## Slide 12: LiD is Another Interesting Candidate for ELM Pacing
 | Mass Density (gm/cm3) | Atomic Density (1022/cm3) | Electron Density (1022/cm3) | Melting Temp (°K) | Boiling Temp (°K)
D | 0.20 | 6.0 | 6.0 | 18.6 | 23.6
Li | 0.52 | 4.5 | 13.5 | 454 | 1615
LiD | 0.82 | 5.5 | 22 | 969 | N/A*
For the same size granule/pellet, Li (LiD) ablates 2.25 (3.66) times as many electrons as D.
* In vacuum, LiD dissociates before it boils
Physical Properties of D, Li and LiD

## Slide 13: Lithium Coating Reduces Deuterium Recycling, Suppresses ELMs & Improves Confinement in NSTX
No lithium (129239); 260mg lithium (129245)
Without ELMs, impurity accumulation increases radiated power and Zeff
H. Kugel, B. LeBlanc, R.E. Bell, M. Bell