## Slide 1: Actuator Sharing and Integrated Control Demonstration for ITER
J A Snipes
ITER Organization
E Kolemen
Princeton University
Notes: <number>

## Slide 2
Motivation: ITER needs to define the Plasma Control System (PCS) architecture for the PCS Preliminary Design by the end of 2016. Demonstrating the feasibility of shared actuator management and integrated control on existing devices would help make design choices for the ITER PCS architecture.
Goals: Demonstrate feasibility of shared actuator control with multiple simultaneous control schemes using the same actuator as well as integrated control of multiple actuators. Can actuator management be performed before each controller in a supervisory way or must actuator management be performed between the controller and the actuator? Experiments designed to test the advantages and disadvantages of these approaches for multiple control schemes would be valuable to determine the best approach for ITER.
Plan of execution: Possible shared actuator and integrated control schemes to be attempted on NSTX-U include: 1) ELM control (3D fields) + divertor detachment control (gas puffing) + core radiation control (central heating); 2) ELM control + EFC with 3D fields + rotation control and real-time kink resonance measurement through q ramp; 3) simultaneous control of βN, the q profile, and plasma rotation with NBI.
Actuator Sharing and Integrated Control Demonstration for ITER
Notes: <number>
<number>

## Slide 3
MHD control and development of integrated control in MST1 on ASDEX Upgrade and TCV – S. Coda, F. Felici, C. Rapson
  Demonstrate integrated control of three or more among NTMs, sawteeth, ELMs, disruption mitigation and divertor detachment, using diagnostic observers + real-time modelling and assessing minimal necessary observer set
  Sawteeth, NTMs: ECRH
  ELMs: pellets, RMP, vertical kicks
  Radiation: impurity injection
Shared actuator and integrated control proposal on DIII-D – D. Humphreys, E. Kolemen, E. Schuster
  combined q-profile control (NBI + ECH/ECCD), beta control (NBI + ECH/ECCD), and NTM suppression (ECCD repurposing, managed sharing, or as disturbance)
Proposed NSTX-U shared actuator and integrated control experiments would provide good diversity with a range of actuators, repurposing, sharing, and integration
IOS ITPA Joint Plasma Control Experiments
Notes: <number>
<number>