## Slide 1
Parallel Correlation of SOL Turbulence
S.J. Zweben, F. Scotti, J.W. Ahn, T. Gray, M. Jaworski,
S. Kubota, R. Maqueda, N. Mandell, D. Smith, V. Soukhanovskii
with D.A. D’Ippolito, J.R. Myra, D.A. Russell (Lodestar)
and C.S. Chang, R. Hager, M. Churchill, S. Ku, D. Stotler
Goal:
Better understand the contribution of SOL turbulence and blobs
to the SOL width, in part through theory and simulation
Method:
Measure the parallel (i.e. 3-D) structure of SOL turbulence and
blobs using all available edge fluctuation diagnostics, and
compare results with SOL widths, theory and simulation
s

## Slide 2
Diagnostics to Cross-Correlate with GPI
GPI (at outer midplane) vs. fast camera on divertor plate (Scotti),
  using LiI filter (like Maqueda NF ‘10), or other lines (Da, maybe C )
  Maybe use divertor gas puffing to do “GPI” at divertor plate, and
  maybe try to align B field to connect GPI and divertor camera.
GPI vs. divertor Langmuir probe Isat or floating potential (Jaworski).
  Maybe sweep OSP over probes to minimize heating. Similar to
  Grulke in C-Mod (NF ‘14), where a ~75% correlation was seen.
GPI vs. lower divertor tangential imaging (Maqueda), maybe with
local gas puff, maybe with B field alignment. Look for X-point
  effects on turbulence structure and motion (like MAST APS ‘14)

## Slide 3
SOL Turbulence Measurements…cont…
GPI vs. wide-angle fast camera view of GPI gas puff from
  across machine, to look for parallel motion of ‘blobs’
GPI vs. BES (Smith), similar to previous study (Sechrest),
  but maybe with improved B field alignment
GPI vs. reflectometer (Kubota), at least for n ≥ 1x1013 cm-3,
  but probably not possible to align along B field line
7) GPI vs. IRTV (Gray) using fastest possible IRTV speed; also
  compare SOL heat flux width to SOL turbulence properties

## Slide 4
Plasma Conditions and Other Diagnostics
• Can do some of these correlations by piggy-backing on other XPs
• Dedicated shots needed for B-field alignment of GPI with divertor
camera, probes, and IRTV, probably with OSP scan for probes
• Density scan -> OSP detachment interesting for SOL turbulence,
also X-point location, snowflake, LII scan, Ip scan, RMP fields, etc.
Additional useful diagnostics for SOL:
• Divertor spectroscopy, bolometry, and neutral density
• Thomson profiles at outer edge (pdf from repeated shots)
• Edge ion temperature, rotation, and USXR measurements
• Fast magnetics for separatrix magnetic fluctuations

## Slide 5
Data Analysis and Interpretation Questions
• Is SOL turbulence highly correlated along B field line from outer
midplane to divertor plate, or disconnected by shear, collisions…?
• How well does SOL turbulence correlate with SOL heat flux width ?
Might be correlated through turbulence level, size, or radial speed.
• Can we use fluctuation levels to estimate turbulent vs. neoclassical transport? Does ñ/n ~ 1 imply that neoclassical transport is small ?
Theory/simulation tools:
• Analytic blob models for parallel correlation estimates
• 2-D SOLT simulations for turbulence vs. estimated SOL width
• XGC-a simulations for estimation of neoclassical transport
• XGC-1 simulations for SOL turbulence and transport