## Slide 1: ​AE damping rates in 3D perturbed equilibria
A. Bortolon, E.D.Fredrickson, G.J. Kramer, M. Podestà (PPPL), D.A. Spong (ORNL)
NSTX-U Research Forum 2015
Notes: Good afternoon, I’d like to thank the organizing committee for the opportunity of presenting my work here.
acknowledge the valuable contributions of many collaborators from various institutions.

## Slide 2: 3D Magnetic Perturbations can modify continuum gaps
AE develop in frequency gaps between classes of (strongly damped) continuum modes
Interaction of AE with continuum results in increased damping
3D magnetic perturbations break axisymmetry
  Eigen mode have mixed toroidicity
  Continuum structure computation has to include toroidal coupling
VMEC+STELLGAP computation for NSTX H-mode, with static n=3 perturbations
  Continuum gaps strongly reduced near the edge
  Might explain observed reduction of TAE amplitude with n=3
TAE gap
EAE gap
TAE gap
EAE gap
n=2
n=5
TAE gap
EAE gap

## Slide 3: XP proposal
Goal: demonstrate TAE mitigation by enhanced damping with 3D fields
Strategy: physics basis + demonstration
  Use TAE antenna to measure TAE damping rates in axisymmetric and (increasingly) perturbed magnetic configuration (n=2,3) [0.5 days]
  Use TAE antenna to drive TAE to measurable amplitude and subsequently apply 3D fields to modulate it [0.5 days, if A works]
Scenario: L-mode, Ohmic or low NBI (diagnostic blips)
  no fast-ion drive, no rotation, no steep gradients: accurate modeling
  core fluctuation measurements with reflectometer
Requirements: TAE antenna, RWM coils (n=2, n=3), background profiles for modeling, MSE, reflectometer for mode structure
Combinability: Part A is a natural extension of TAE check out. But…
  Extra discharge optimization might be required to get field penetration