## Slide 1
Columbia U. Group – NSTX-U Macrostability TSG XPs
S. A. Sabbagh, J.W. Berkery, J.M Bialek
Y.S. Park, (et al…)
Department of Applied Physics, Columbia University, New York, NY
NSTX-U
Supported by
Culham Sci Ctr
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Inst for Nucl Res, Kiev
Ioffe Inst
TRINITI
Chonbuk Natl U
NFRI
KAIST
POSTECH
Seoul Natl U
ASIPP
CIEMAT
FOM Inst DIFFER
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
NSTX-U Research Forum
February 25th, 2015
PPPL
V1.2
Coll of Wm & Mary
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Lehigh U
Nova Photonics
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Tennessee
U Tulsa
U Washington
U Wisconsin
X Science LLC

## Slide 2: Columbia U. Group 2015 Macrostability TSG XPs (Short Summary)
XPs (related XPs assigned numbers for “2011 run”)
  RWM stabilization dependence on neutral beam deposition angle (~XP1149) (Berkery)
  RWM stabilization physics at reduced collisionality (~XP1148) (Berkery)
  RWM state space active control physics (independent coil control) (~XP1145) (Sabbagh)
  RWM control physics with partial control coil coverage (JT-60SA) (~XP1147) (Y-S Park)
  RWM PID control optimization based on theory and experiment (~XP1111) (Sabbagh)
  RWM state space active control at low plasma rotation (~XP1146) (Y-S Park)
  Neoclassical toroidal viscosity - reduced n (independent coil control) (~XP1150) (Sabbagh)
  NTV steady-state rotation at reduced torque (HHFW) (~XP1062) (Sabbagh)
  Multi-mode error field correction using the RWMSC (to follow initial EFC XP)
  NTM Entrainment in NSTX-U (Y.S. Park)
Piggyback XPs
  Disruption PAM characterization, measurements, and criteria (Sabbagh, for DPAM WG)
NOTE: - some shot plans already scoped out in web submissions (not repeated here)
- run day requests mostly assume leveraging “2nd NBI XP”, “Ip/Bt scaling XP”

## Slide 3: XP: RWM state space active control physics (independent coil control) – Sabbagh, et al.
Motivation
  RWM state space controller (RWMSC) allowing influence of conducting structures, plasma mode shape / response expected to improve control performance, allows greater shielding of control coils needed in future devices
  Improve capability of present NSTX-U RWMSC by using new 2nd SPA, more plasma modes, etc.
Goals / Approach
  Examine control aspects of different high performance target plasmas
    Key step to prepare the RWMSC for general use in the future
  Determine control physics advantages of including influence of wall, choice of input eigenfunction set, inclusion of n > 1 eigenfunctions
  Determine effect of control with 6 independent RWM coils
  Determine influence of reducing effect of conducting structure
  Examine influence of adding n = 1 RWM PID control using Br sensors
Addresses
  NSTX Research Milestones R(15-3),JRT-16
  ITPA joint experiments MDC-17, MDC-21

## Slide 4: Increased number of states in RWM state space controller improves match to sensors over entire mode evolution
RWM Upper Bp Sensor Differences (G) – 2 States
Sensor not functioning
137722
180 degree
differences
180 degree
differences
90 degree
differences
90 degree
differences
RWM
Black: experiment Red: offline RWM state space controller
Sensor not functioning
137722
180 degree
differences
180 degree
differences
90 degree
differences
90 degree
differences
RWM
Some 90 degree differences not as well matched
  Indicates potential need for an n = 2 eigenfunction state
  Attempt n = 2 control in 2015
0.56
0.58
0.60
0.62
0.56
0.58
0.60
0.62
t (s)
t (s)
RWM Upper Bp Sensor Differences (G) – 7 States
100
200
0
-100
100
-50
0
50
150
100
150
50
0
-50
50
0
-100
-50
-100
100
0.56
0.58
0.60
0.62
0.56
0.58
0.60
0.62
0.56
0.58
0.60
0.62
0.56
0.58
0.60
0.62
100
-50
0
50
150
100
200
0
-100
100
150
50
0
-50
50
0
-100
-50
-100
100
0.56
0.58
0.60
0.62
0.56
0.58
0.60
0.62
t (s)
t (s)
Reasonable match to all Bp sensors during RWM onset, large differences later in evolution

## Slide 5: Upgrades of new RWM state space controller will leverage new 2nd SPA power supply to study physics effects
n = 1 multi-mode RWM spectrum (mmVALEN)
2nd SPA power supply allows independent control of the 6 RWM coils
  We need new phase and gain scans (test new control matrices) – this was not performed in 2011
New RWM state space controller physics studies
  Addition of n > 1 eigenfunction will then yield n = 1, 2 feedback, and higher n based on observer match to wall states
  Test controller on various high performance targets
    E.g. (i) fiducial, (ii) low li, (iii) snowflake divertor
    Eigenfunction variations: e.g. does snowflake divertor configuration reduce divertor mode?
  Compare controller with influence of wall vs. without influence of wall
XP needs
  Request: 1.5 run days
n = 1 ideal eigenfunctions for fiducial plasma
NSTX 133775
t = 0.495 [s]
RWM BR and Bp sensor locations
Z(m)
R(m)

## Slide 6: XP: RWM control physics with partial control coil coverage – Y.S. Park, et al.
Motivation
  Effect of partial coil coverage (e.g. JT-60SA)*, and impact of internal coil loss (e.g. ITER) may lead to “mode non-rigidity” during RWM feedback – the effect on mode control needs to be understood
  NSTX active RWM control failed with 2 coils missing
Goals / Approach
  RWM control in NSTX will be attempted with partial coverage of the RWM coils to test the physics of RWM mode rigidity
  Leverage new independent control of the RWM coils
  Determine the change in the computed multi-mode RWM spectrum and compare to experiment
  Compare attempted control with both the RWM PID controller, and RWM state space controller
Addresses
  *Collaborative RWM stabilization research with JAEA (for JT-60SA) – IEA joint research task
  ITPA joint research MDC-17, MDC-21
JT-60SA passive plates and RWM control coils
Request:
1 run day

## Slide 7: XP: RWM PID control optimization based on theory and experiment – Sabbagh, et al.
Motivation
  Experiments using n = 1 RWM control in 2010, and subsequent analysis using the VALEN code show that some settings for control using dual BR and Bp sensor feedback were optimal, others could have been improved
  Active RWM PID control settings need to be re-optimized for NSTX-U
  Support general NSTX-U experiments by optimizing RWM PID control
Goals / Approach
  Optimize n = 1 RWM PID control focusing on scans of key parameters
    Vary Bp feedback phase, BR feedback gain – which differ in the most in the analysis from the experimental settings
    Bp sensor gain will also be examined in this experiment (never scanned with r/t AC compensation).
    Perform on high performance target plasmas (fiducial; low li; snowflake)
Addresses
  General support for NSTX-U high beta experiments, R(15-3), JRT-16
  ITPA joint experiment MDC-17
Request: 0.5 – 1.0 run days (depends on desired targets, number of parameter variations/shot)

## Slide 8: RWM Br sensor n = 1 feedback phase variation shows superior settings when combined w/Bp sensors; good agreement w/theory so far
VALEN calculation of Br+Bp feedback follows XP
  stable plasma (negative “s”)
  Now examining plasma response model variation
    impact of “s”, and diff. rotation (“a”) on results
Dt (s)
Radial field n = 1 (G)
Favorable (experimental) Bp feedback settings, varied BR settings
  Positive/negative feedback produced at theoretically expected phase values
180 deg FB phase
90 deg FB phase
0 deg FB phase
Vacuum error field
Vacuum EF + RFA
VALEN calculation of NSTX Br + Bp control
n = 1 BR + Bp feedback
(Bp gain = 1, BR gain = 1.5)
NSTX Experiments: Bp + BR feedback
Feedback on

## Slide 9: XP: RWM state space active control at reduced plasma rotation – Y.S. Park, et al.
Motivation
  Present theory shows ITER advanced scenario plasmas are kinetic RWM unstable just above the n = 1 no wall limit, and alpha particle stabilization is required; Amount of kinetic resonance stabilization at low rotation is uncertain
Goals / Approach
  Demonstrate RWM control over a greater range of plasma rotation using RWM state space control (incl. (i) low wf, (ii) intermediate wf at marginal stability)
  Determine control physics differences of varying input eigenfunction set (including allowance of n > 1 eigenfunctions) at various wf
  Vary key controller parameters to examine influence on stability
  Test compatibility with applied fields for NTV rotation damping
    Ensure controller doesn’t reduce n = 2, n = 3 braking field significantly
  Examine influence of adding n = 1 RWM PID control using Br sensors
Addresses
  NSTX Research Milestones R(15-3)
  ITPA joint experiment MDC-17, MDC-21

## Slide 10: Kinetic stability calculations show reduced stability in low li target plasma as wf is reduced; also at low wf
Can RWM unstable regions be controlled using the RWMSC, including low rotation?
  Ideal stability analysis shows high margin over no-wall limit
    RWM stabilization by kinetic effects large
  MISK: RWM marginal stability at various wf
    Demonstrate control in these regions!
140132, t = 0.704s
unstable
Experiment
(marginal)
RWM stability vs. wf (contours of gtw)
2.0
1.0
wf/wfexp
thermal
w/fast particles
MISK code
Ideal stability
Find RWMSC matrices most effective for control
  Includes n > 1 control, variation of eigenfunctions used in controller, etc.
Request: 1 run day

## Slide 11: XP: Neoclassical toroidal viscosity at reduced collisionality (independent coil control) – Sabbagh, et al.
Motivation
  Experimentally, the dependence of neoclassical toroidal viscosity (NTV) at low collisionality is not well known
  Understanding important for NSTX-U Vf control, other tokamaks, future devices
Goals / Approach
  Examine the dependence of NTV on ion collisionality
    expected to increase with decreasing ni from present experiments, and theory
  Determine if superbanana plateau increase of NTV depends on ni
  Operate with pre-programmed n = 2, 3 applied fields for Vf feedback control testing at reduced ni
Addresses
  NSTX Milestones R(15-3), closed-loop rotation control with 3D fields
  ITPA joint experiment MDC-21
NTV strength varies with plasma collisionality n, dB2, rotation
K.C. Shaing, M.S. Chu, C.T. Hsu, et al., PPCF 54 (2012) 124033
plasma rotation
Ti5/2
K.C. Shaing, et al.,
PPCF 51 (2009) 035004
NTV force in “1/n” collisionality regime
1/aspect ratio (compare to KSTAR)
ni* ~ 1
NSTX
NSTX-U
“offset” rotation

## Slide 12: Measured NTV torque density profiles quantitatively compare well to computed TNTV – NTVTOK code interfaced to NSTX-U
Scale factor ((dL/dt)/TNTV) = 1.7 and 0.6 (for cases shown above) – O(1) agreement
Comparison to full Shaing, et al. theory with NTVTOK code (applicable for all collisionality (as shown above) is possible to compute between shots for NSTX-U
Comparisons will also be made to other NTV codes (e.g. by J-K. Park, K. Kim, Z. Wang)
Experimental
-dL/dt
yN
NSTX
NTVTOK code
n = 2 coil configuration
S.A. Sabbagh, et al., IAEA FEC 2014, paper EX/1-4
n = 3 coil configuration
Experimental
-dL/dt
NTVTOK
yN
NSTX
x0.6
x1.7

## Slide 13: NTV experiment at reduced n is a key step for closed-loop Vf feedback using 3D fields in NSTX-U
Expect stronger NTV torque at higher Ti (-dwf/dt ~ Ti5/2 wf)
  Initially shown in NSTX
  Shown in our recent KSTAR XPs
Present XP
  Operate with larger change in ni
  Attempt to reach quasi-steady-state wf for each ni
  Use braking fields envisioned for Vf FB
Request: 1 run day
S.A. Sabbagh, et al, NF 50 (2010) 025020
S.A. Sabbagh, et al., IAEA FEC 2014, paper EX/1-4
I. Goumiri (PU), S.A. Sabbagh (Columbia U.), D.A. Gates (PPPL)
Y.S. Park, et al, IAEA FEC 2014, paper EX/P8-05

## Slide 14: XP: NTV steady-state offset velocity at reduced torque with HHFW – Sabbagh, et al.
Motivation
  Measure and understand neoclassical toroidal viscosity (NTV) steady-state offset velocity physics to gain confidence in extrapolation of the effect to future devices
    Background: NSTX low wf NTV experiments with co-NBI + non-resonant magnetic braking do not show NTV steady-state offset velocity to be in the counter-Ip direction (e.g., shown in DIII-D (Garofalo, PRL 2008), claimed consistent with theory)
Goals
  Complete XP1062, partially run in 2010 (**but excluded HHFW portion of shot list**)
  Determine NTV offset rotation in plasmas with no, varied NBI torque (HHFW heated)
    Use demonstrated technique to measure wf in RF plasmas
    Use n = 3 applied field, compare to results with n = 2 applied field configuration
  Demonstrate for the first time NTV with strong electron component
  Key code validation in new regime: for the NTVTOK code, and other NTV codes
  Determine if low wf (low wE superbanana plateau (SBP) regime) can be reproduced during the NBI portion of these discharges with non-resonant braking
    Can attempt to measure NTV steady state offset velocity this way as well when varying non-resonant applied field magnitude
Addresses
  NSTX Milestone R(15-3)
  Desire to understand potential sources of momentum input for ITER

## Slide 15: Zero input torque wf profile diagnosed in 2009 RF XPs
Since SBP regime yields maximum NTV
  Entering it by lowering wf yielded an observed increase in NTV without mode locking (2009-10)
  Conversely, attempt to measure decrease in NTV as SBP regime is exited
Request: 0.5 – 1.0 run days (depends on goals, and leveraging RF+NBI development )
J. Hosea, APS DPP 2009
Determine NTV offset rotation – RF approach
  Generate wf with RF at highest Ti, Wtot possible, diagnose similar to Hosea/Podesta 2009
  Repeat for different *initial* values of n = 3 (and/or 2) field, determine if pre-NBI wf changes
  Note that if NTV offset is indeed only in counter-Ip direction, the wf profile will change (it’s presently counter in core, co at the edge
Attempt to maintain near-zero wf during NBI phase
  New way to enter/sustain low wE SBP regime

## Slide 16: XP: Multi-mode error field correction with the RWM state-space controller (RWMSC) – Sabbagh, et al.
Motivation
  Produce multi-mode error field correction for the first time using the inherent capability of the RWMSC to include multiple modes (different n; different poloidal spectra)
  High interest for ITER and other tokamaks
Goals / Approach
  Demonstrate reduction of applied n = 1, 2, 3 error fields
    Test the need for matching n values between applied field and modes
    Test the influence of wall states in the error field reduction effectiveness
  Demonstrate reduction of NSTX-U intrinsic error fields
    Use “best” set of RWMSC control matrices determined from above step (including n > 1, and sufficient number of wall states)
  Demonstrate reduction of dynamic error fields (at higher bN)
    Determine if increase of plasma permeability is required in control model for best performance at increased bN
Addresses
  Milestone R(15-3), JRT-16
  ITPA joint experiment MDC-17, MDC-19, MDC-21

## Slide 17: Multi-mode RWM computation shows 2nd eigenmode component has dominant amplitude at high bN (vs. 1st eigenmode dominant at lower bN)
Multi-mode error field correction experiment differs from RWM active control experiments
  Theoretically, the multi-mode spectrum is simplified away from RWM marginal stabilty points
    Are different control matrices needed for the best error field correction compared to RWM control at marginal stability?
  Compare effect on RWM PID and RWMSC for error field correction
    PID should be more subject to failure by n > 1 mode content, error in tracking toroidal phase
    State space controller with n > 1 eigenfunctions and wall effects is expected to provide greater EFC
Request: 1 run day (should run after PID EFC experiment (by C. Myers))
NSTX dBn RWM multi-mode spectrum
at high bN
ideal eigenmode number
dBn amplitude (arb)
t = 0.655s
mode 1
mode 2
2.0
1.0
0.0
R(m)
1.0
-1.0
Z(m)
2.0
0.0
-2.0
mode 3
q
133775
mode
1
mode
3
mode
2
Unstable
Stabilized by rotation
mmVALEN code
bN = 6.1

## Slide 18: XP: NTM Entrainment on NSTX-U – Y.S. Park, et al.
Motivation
  NTM “entrainment”, in which tearing modes are partially controlled to avoid locking, can be used for disruption avoidance (or at least in conjunction with controlled shutdown)
Goals / Approach
  Attempt entrainment for the first time on NSTX-U with a somewhat novel technique
    Slow NTM (attempt both 3/1, and 2/1 modes) using non-resonant NTV (n = 3) to slow the plasma
    With NTM slowed to near, or below the critical rotation speed for mode locking, apply an n = 1 AC field to attempt to keep the NTM rotating at low frequency ~ 50Hz (far slower speed than the critical mode rotation speed for locking)
    Attempt to use n = 1 “slow” feedback with a phase that sustains the n = 1 mode rotation to avoid mode lock
Addresses
  NSTX-U Milestones R(15-3), JRT-16
  ITPA joint experiment MDC-8, MDC-17, MDC-22

## Slide 19: Present entrainment experiment would be similar (could be compared to) past DIII-D experiments
Will entrainment be different at varied aspect ratio, higher edge q shear?
  DIII-D / NSTX-U comparison
  Also NSTX-U / KSTAR (A = 3.5) comparison (we will propose XP on KSTAR in 2015)
A key motivation for NSTX-U is disruption avoidance by mode locking avoidance
Request: 0.5 – 1.0 run days
M. Okabayashi, et al., ITPA MHD Stability meeting, April, 2013
Tearing mode entrainment with n = 1 feedback in DIII-D

## Slide 20: Piggyback XP: Disruption PAM (DPAM) Characterization, Measurements, and Criteria - Sabbagh, for the DPAM WG
Motivation
  Serve NSTX-U DPAM Working group main goal: Satisfy gaps in understanding prediction, avoidance, and mitigation of disruptions in tokamaks, applying this knowledge to move toward acceptable levels of disruption frequency/severity using quantified metrics
Goals / Approach
  Initial discussion held at first DPAM Working Group meeting
  ( see http://nstx.pppl.gov/DragNDrop/Working_Groups/DPAM/2015 )
  Start early in NSTX-U operation to
    Characterize NSTX-U disruptions (similar to P. deVries, et al. approach taken on JET)
    Quantify results with measurements (similar to S. Gerhardt, et al. pioneering work on NSTX)
    Expand disruption determination/avoidance models - as stated in NSTX-U 5 Year Plan
  Tools are presently being developed for this purpose
  Analysis will be conducted/communicated to/by NSTX-U DPAM WG meetings, planned as a multi-year effort
  This step is expected to be conducted in piggyback – NO RUN TIME request
Addresses
  NSTX-U Milestones: R(15-3), JRT-16, NSTX-U DPAM WG charges
  ITPA joint experiment MDC-21, MDC-22

## Slide 21: Example of disruption physics elements interconnected to describe paths toward disruption
P.C. de Vries et al., Nucl. Fusion 51, 053018 (2011)
Example: Disruption Elements and Connections Diagram (JET)
Elements
  Provide a logical and quantifiable set of components in the disruption chain, with underlying physics
Connections
  Shows interrelations of the elements, arrow thickness showing relative probability of path
  Can have multiple inputs / outputs

## Slide 22: Supporting slides follow

## Slide 23: (Incomplete) List of physics elements tied to disruption prediction, avoidance (individual involvement) – 1/30/15 mtg
Impurity control (NC)
  bolometry-triggered shutdown (SPG); "tailoring” radiation-induced TM onset (LD, DG)
  change plasma operational state / excite ELMs, etc. (TBD – perhaps JC)
Greenwald limit (GWL)
  density/power feedback, etc. (DB)
Locked TM (LTM)
  TM onset and stabilization conditions, locking thresholds (JKP,RLH,ZW)
  TM entrainment (YSP)
Error Field Correction (EFC)
  NSTX-U EF assessment and correction optimization (CM,SPG)
  NSTX-U EF multi-mode correction (SAS, YSP, EK)
Current ramp-up (IPR)
  Active aux. power / CD alteration to change q (MDB, SPG)
Shape control issues (SC)
  Active alteration of squareness, triangularity, elongation – RFA sensor (SPG,MDB)
Transport barrier formation (ITB)
  Active global parameter, Vf, etc. alteration techniques (SAS,JWB,EK)
H-L mode back-transition (HLB)
  Active global parameter, Vf, etc. alteration techniques (SAS,JWB,EK)
Approaching vertical instability (VSC)
  Plasma shape change, etc. (SPG, MDB)
Resistive wall mode (RWM)
  Active global parameter, Vf, etc. alteration techniques (SAS,JWB)
  Active multi-mode control (SAS,YSP,KT)
Ideal wall mode (IWM)
  Active global parameter, Vf, etc. alteration techniques (JEM)
Internal kink/Ballooning mode (IKB)
  Active global parameter, Vf, etc. alteration techniques (SAS,JWB)
  Active multi-mode control (SAS, YSP, KT)
Abbreviations:
JWB: Jack Berkery
AB: Amitava Bhattacharjee
DB: Devon Battaglia
MDB: Dan Boyer
JC: John Canik
LD: Luis Delgado-Aparicio
DG: Dave Gates
SPG: Stefan Gerhardt
MJ: Mike Jaworski
EK: Egemen Kolemen
RLH: Rob La Haye
JEM: Jon Menard
CM: Clayton Myers
JKP: Jong-Kyu Park
YSP: Young-Seok Park
RR: Roger Raman
SAS: Steve Sabbagh
KT: Kevin Tritz
ZW: Zhirui Wang
TBD: (To be decided)
Interest from Theory
  Amitava Bhattacharjee, Allen Boozer, Dylan Brennan, Bill Tang have requested involvement