## Slide 1: Characterizing Type I ELMy H-modes in He plasmas and demonstration of ELM Control
J A Snipes, A Loarte
ITER Organization
F Poli
PPPL
Notes: <number>

## Slide 2
Motivation: The ITER Research Plan assumes H-modes in helium plasmas with large Type I ELMs can be achieved in ITER at 2.65 T because of the lower H-mode threshold observed in helium plasmas in some devices. These H-modes will be used to develop operational requirements and control schemes such as ELM control, W control, core W transport control, radiative divertor operation and access/exit to/from H-mode in the non-active phase in advance of DT operation. ELM control is essential to control divertor heat flux and avoid W accumulation, which could lead to the loss of the H-mode by increased core radiative losses and possibly to increased disruptions.
Goals: Demonstrate feasibility of Type I ELMy H-modes in helium and characterize the pedestal, ELM, and impurity behavior compared to deuterium. Determine if the foreseen ELM control schemes in ITER will be effective in helium plasmas and whether the ELM control requirements are similar to D.
Plan of execution: Obtain Type I ELMy H-modes in helium in NSTX-U with ICRF or NBI (in D or H) if D/H concentration can be kept low (Li coatings ?). Characterize the pedestal and ELM behavior in helium compared to deuterium as a function of density and input power. Apply ELM control techniques using 3D fields and pellet pacing and compare control requirements with those of D plasmas
Characterizing Type I ELMy H-modes in He plasmas and demonstration of ELM Control
Notes: <number>
<number>

## Slide 3
Initial experiments carried out in DIII-D in 2014
  ELM suppression with RMP was only observed at low power
  Core D concentration < 20%, low rotation with balanced NBI + ECH
  Only a few regular Type I ELMy H-modes were obtained at high and low power with high helium concentration and deuterium reference pulses still need to be taken
AUG helium experiments
  Performed at q95 ~3 in ITER baseline scenario
  ELM frequency > 100 Hz in helium without W accumulation, much less in D
Proposed experiments in AUG to reduce ELM frequency
Possible additional helium experiments in C-Mod
Proposed NSTX-U helium H-mode experiments would provide additional low rotation comparison if possible with ICRF heating and comparison of ELM control with 3D fields and pellet pacing
IOS-2.1 Compare helium H-modes in different devices
Notes: <number>
<number>