## Slide 1
Radiative divertor with impurity seeding in NSTX
V. A. Soukhanovskii (LLNL)
Acknowledgements:
NSTX Team
NSTX Results Review
Princeton, NJ
Wednesday, 1 December 2010
NSTX
Supported by
College W&M
Colorado Sch Mines
Columbia U
CompX
General Atomics
INEL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Nova Photonics
New York U
Old Dominion U
ORNL
PPPL
PSI
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Washington
U Wisconsin
Culham Sci Ctr
U St. Andrews
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Hebrew U
Ioffe Inst
RRC Kurchatov Inst
TRINITI
KBSI
KAIST
POSTECH
ASIPP
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
U Quebec

## Slide 2: Use of impurity seeding provided an opportunity to study NSTX-U-relevant radiative divertor
Radiative divertor experiments used D2 injection to demonstrate peak heat flux reduction in NSXT with carbon radiation
A significant divertor peak heat flux reduction will be needed in NSTX-U, probably not possible with low Z impurities
Reduced density LITER operation reduces radiated power due to extrinsic impurity seeding
Control aspects of radiative divertor
  Identify divertor quantities that can be monitored and used as actuators for feeding into PCS to regulate impurity injection

## Slide 3: First demonstration of divertor peak heat flux reduction with impurity seeding in NSTX
Ip=0.9 MA, PNBI = 4 MW
d=0.85, k=2.3, fexp~20
PSOL = 3 MW
Marginal performance degradation

## Slide 4: Divertor peak heat flux reduced by up to 80 %, clear signs of partial detachment observed

## Slide 5: Divertor profiles confirm partial strike point detachment with increased radiation

## Slide 6: Radiative divertor with CD4 seeding appears to reduce divertor heat flux as good as PDD with D2
Radiative CD4 divertor (*): PSOL~3-4 MW, qpeak~0.5-1.0 MW/m2
V. A. Soukhanovskii et. al, PoP 16, 022501 (2009)
*

## Slide 7: Snowflake divertor with CD4 seeding leads to increased divertor carbon radiation
Ip=0.9 MA, PNBI=4 MW, PSOL=3 MW
Snowflake divertor (from 0.6 ms)
  Peak divertor heat flux reduced from 4-6 MW/m2 to 1 MW/m2
Snowflake divertor (from 0.6 ms)
+ CD4
  Peak divertor heat flux reduced from 4-6 MW/m2 to 1-2 MW/m2
  Divertor radiation increased further

## Slide 8: Conclusions and Future plans
First demonstration of impurity-seeded radiative divertor provided very encouraging results
  Marginal core plasma performance degradation
  Significant peak heat flux reduction
Continue with these studies in FY2011-2012
  Optimize CD4 PDD performance for 1.2 MA, 6 MW
  Develop feedback control of radiative divertor
  Combine radiative divertor with snowflake and X-divertor
  Demonstrate and optimize for NSTX-U shape and performance

## Slide 9: Impurity radiation role is to be clarified in radiative divertor experiments
It is marginally possible to radiate the necessary fraction of q|| with intrinsic carbon in NSTX
Lithium and helium can play an important role in divertor power balance
  Helium - energy expensive (first I.P. 24.6 eV), radiates at 1-10 eV
  Lithium – highly radiative at Te < 1-3 eV
In PDD experiments in FY 2006-2008
  Radiated power was due to D, He, Li, C
  He and C were main contributors

## Slide 10: Previous NSTX radiative divertor experiments with neon demonstrated that the divertor was too cold for efficient neon radiation