## Slide 1: M3D-C1-K
Joshua Breslau
NSTX-U Results Review
September 22, 2016

## Slide 2: Background & Motivation
M3D-C1 is a mature nonlinear extended MHD code that has superseded the old M3D code for most tokamak applications because of its
  Efficient, high-accuracy 5th-order-polynomial finite-element field representation with C1 continuity
  Fully implicit time advance scheme
  More accurate model of gyroviscous stress and Hall terms, etc.
  Fast 2D-complex mode of operation for linear problems
  Finite-thickness resistive wall capability and in-mesh coils
  Clean, modern Fortran programming paradigm
A key remaining step to achieving feature parity with M3D-K is the development of a hybrid kinetic capability for energetic ions.

## Slide 3: Particle loading
Physical space initialization: uniform over (R,,z) cube with Jacobian to ensure uniformity over d3x. Particles outside mesh rejected.
Velocity space initialization: use Jacobian to initialize distribution uniformly on d3v, with 0<|v|<sqrt(2Emax/m).
Uniform particle weights.
Sample spatial distribution over four-partition KSTAR mesh:
5840 / 8192 = 32 x 8 x 32 particles deposited.

## Slide 4: Particle push
Particles advance by a specified time increment between fluid steps, using given 2D (real or complex) or 3D fields, subcycling as necessary.
Hierarchical organization of particles by element, element ensemble, OMP thread, and MPI/mesh partition allows good optimization.
4th- and 5th-order Runge-Kutta ODE integration have been implemented; both show good energy, P conservation over many time steps.

## Slide 5: Sample trapped orbit (0 = 3/5)
5000 steps, dt (drift-kinetic)=10-7 s  5 gyroperiods.
Initial KE=9.9995e+03 eV; final=9.9990e+03.
Initial P=-0.476633; final=-0.476630.
Colors indicate advancing time.
R-z plane projection

## Slide 6: Drift-kinetic/full-orbit comparison
Full-orbit: 20,480 steps, dt=10-10 s  0.005 gyroperiods.
Detail
      KE conservation for full-orbit is good, but angular momentum conservation is relatively poor.
      A drift-kinetic step is about twice as fast as a full-orbit step, and can be around 1600x larger for comparable accuracy.

## Slide 7: Pressure deposition
RHS vectors for p||, p computed by integrating over particle delta functions within each element.
LHS vectors computed by mass matrix inversion for each component.
  Very fast (time is independent of particle count).

## Slide 8: Fluid coupling
In progress!
Plan: pressure coupling, i.e.,
where
so that if p  p||-p, then
(1)
(3)
(2)

## Slide 9: Fluid coupling, continued
All terms in (3) are projected to the M3D-C1 velocity representation with appropriate operators integrated by parts:
e.g.

## Slide 10: I/O & Diagnostics
The particle_test() subroutine writes out the entire trajectory of a predetermined subset of particles, tracking KE and P .
Subroutine hdf5_write_particles() uses parallel HDF5 to dump the entire particle distribution at a given time, including positions, velocities, and weights.
  Utilities exist to extract position data from these to a text file, enabling comparisons and plotting with VisIt.
  Utilities to visualize velocity distributions, pressure tensor components are now being developed.
Checkpointing of particle distribution will be based on HDF5.

## Slide 11: Summary
Particle initialization, full-f push, pressure deposition, and I/O now working, tested and optimized for 2D complex version.
Weight evolution, fluid coupling in progress.
First linear validation tests on fishbone mode to be conducted in October.