## Slide 1: Equilibrium, NTV, and Disruption Event Characterization and Forecasting Results Update for NSTX/NSTX-U
NSTX-U Results Review
September 22nd, 2016
PPPL
V1.2
S.A. Sabbagh1, J.W. Berkery1, R.E. Bell2, J.M Bialek1, M.D. Boyer2, D.A. Gates2, S.P. Gerhardt2, I Goumiri3, C. Myers2, Y.S. Park1, J.D. Riquezes4, C. Rowley3
1Department of Applied Physics, Columbia University, New York, NY
2Princeton Plasma Physics Laboratory, Princeton, NJ
3Princeton University, Princeton, NJ
4University of Michigan, Ann Arbor, MI
*This work supported by the US DOE contracts DE-AC02-09CH11466 and DE-FG02-99ER54524

## Slide 2: OUTLINE – Updates on three subjects
Impact of PF1aU on equilibrium reconstruction
Disruption Event Characterization and Forecasting development
Neoclassical Toroidal Viscosity on NSTX-U
  One shot identified in Walter’s L-mode experiments has sufficient data for NTV profile analysis
  More to do, not enough time to show – will send by email

## Slide 3: Equilibrium reconstruction recent conclusion: PF1aU issue has negligible effect on reconstructions since it appeared
Reconstructions use PF coil currents, have small error (~ 0.5%), so PF1aU issue might affect result
However, the balance of the magnetics minimize reconstruction changes
  The fitted PF1aU does deviate from the measured value – becomes worse in time
Near peak stored energy
Stored energy
DRSEP
Near maximum difference
Stored energy

## Slide 4: DECAF is structured to ease parallel development of disruption characterization, event criteria, and forecasting
Initial DECAF analysis goals
  Define physics criteria that define an initial set of disruption “events”
  Characterize time sequences of events in disruptive shots
  Produce initial physics models to define marginal points of key events
  Enable initial disruption forecasting capability for most well-defined events / sequences
VDE
SCL
IPR
RWM
DIS
SCL
 e.g. Loss of shape control

DECAF disruption events and chains
DECAF code schematic

## Slide 5: Recap: DECAF results detect disruption chain events when applied to dedicated 44 shot NSTX RWM disruption database
Several events detected for all shots
  RWM: RWM event warning
  SCL: Loss of shape control
  IPR: Plasma current request not met
  DIS: Disruption occurred
  LOQ: Low edge q warning
  VDE: VDE warning (40 shots)
Others:
  PRP: Pressure peaking warning
  GWL: Greenwald limit
  LON: Low density warning
  LTM: Locked tearing mode
Occur with or after RWM

## Slide 6: DECAF results detect disruption chain events when applied to dedicated 44 shot NSTX RWM disruption database
Most RWM near major disruption
  61% of RWM occur within 20 tw of disruption time (tw = 5 ms)
  Earlier RWM events NOT false positives – cause large decreases in bN with recovery (minor disruptions)
VDE
60
40
20
0
0
2
4
6
BPLn=1 (G)
bN
0.2
0.4
0.6
0.8
1.0
0.0
t(s)

## Slide 7: Initial DECAF analysis finds common disruption event chains (44 shot NSTX disruption database)
Common disruption event chains (52.3%)
  Related chains
    RWM  SCL  VDE  IPR  DIS
    VDE  RWM  SCL  IPR  DIS
    VDE  RWM  IPR  DIS  SCL
    RWM  SCL  VDE  GWL  IPR  DIS
Disruption event chains w/o VDE (11.4%)
New insights being gained
  Chains starting with GWL are found that show rotation and bN rollover before RWM (6.8%)
  Related chains
    GWL  VDE  RWM  SCL  IPR  DIS
    GWL  SCL  RWM  IPR  DIS
Disruption event chains with RWM
VDE
SCL
IPR
RWM
DIS
Event chains with RWM and VDE
(52.3%)
No
VDE
(11.4%)
Other
(29.5%)
GWL start
(6.8%)

## Slide 8: First DECAF results for NSTX-U replicate the triggers found in new real-time state machine shutdown* capability
Important capability of DECAF to compare analysis using offline vs. real-time data
  Simple, initial test
PCS Shut-down conditions are analogous to DECAF events
  PCS loss of vertical control  DECAF
DECAF comparison:VDE event
  Matches PCS when r/t signal used (1 criterion)
  VDE event 13 ms earlier using offline EFIT signals (3 criteria)
VDE
PCS trigger
For VDE
(t = 0.733s)
VDE
Using r/t data (t = 0.733s) Using EFIT (t = 0.720s)
DECAF
EFIT offline reconstruction
of Z position
Zaxis (m)
Ip (MA)
PCS trigger
0
0.4
0.8
0.2
0.4
0.6
0.8
1.0
0.0
t(s)
0
0.4
-0.4
0
2
4
*See S.P. Gerhardt, et al., NSTX-U shutdown handler talk

## Slide 9: Next essential step for DECAF analysis: Identification of rotating MHD (e.g. NTMs)
Initial goals
  Create portable code to identify existence of rotating MHD modes
  Track characteristics that lead to disruption
    e.g. rotation bifurcation, mode lock
Approach
  Apply FFT analysis to determine mode frequency, bandwidth evolution
  Determine bifurcation and mode locking
n = 1 mode frequency vs. time
(new code)
w0 ~ 9 kHz
bifurcation ~ 4 kHz
w/ J. Riquezes (U. Michigan – SULI student)

## Slide 10
      Many shots with rotating MHD (e.g. NTMs) examined for NSTX and NSTX-U – two illustrated here
Magnetic spectrogram of rotating MHD mode locking termination
NSTX 138854
NSTX-U 204202

## Slide 11: Fast Fourier transforms used to find mode peak frequency within a time interval
Reveals potential issues handling multiple frequency peaks
Next step to include toroidal array / n number discrimination
Odd-n
Even-n
FFTs
Signals
J. Riquezes (U. Michigan – SULI student)

## Slide 12: The characterization algorithm shows that the expected bifurcation event can be found
Algorithm written looks for a “quasi-steady state” period, a potential bifurcation, the possible mode locking
shot 204202
odd-n peak frequencies
lock
shot 138854
odd-n peak frequencies
lock
quasi-SS
bifurcates

## Slide 13: Continuing analysis of rotating MHD for DECAF includes accurate analysis of mode “status” (I)
Odd-n magnetic signal / analysis (mode locking / unlocking)
B (G)
t (s)
204202
Frequency vs. time
DECAF mode status
1 = Mode present
-1 = Mode locked
Signal
0 = No mode
mode lock

## Slide 14: Continuing analysis of rotating MHD for DECAF includes accurate analysis of mode “status” (II)
Even-n magnetic signal / analysis (mode present, not locked)
Frequency vs. time
DECAF mode status
1 = Mode present
-1 = Mode locked
Signal
0 = No mode
t (s)
B (G)
204202

## Slide 15: Model for mode rotation evolution / mode lock forecasting derived, will be tested in DECAF in next step
Model derived to allow island drag for both “slip” and a “no slip” condition
Simple “W0” defines steady state
  Best way to define this?
Simple “W0/2” defines bifurcation point
   Next step is to analyze this model using DECAF
Model based on
R. Fitzpatrick et al., Nucl. Fusion 33 (1993) 1049
Bifurcation frequency
“steady-state”
~ W0/2
W0

## Slide 16: DECAF reduced kinetic MHD model implemented: initially tested on database of NSTX discharges with unstable RWMs
84% of shots are predicted unstable
44% predicted unstable < 320 ms (approx. 60tw) before current quench
33% predicted unstable within 100 ms of a minor disruption
Predicted instability statistics (45 shots)
Normalized growth rate vs. time
Chart: 
Stable
(16%)
Instability within 100 ms of minor
disruption
(33%)
Instability < 320 ms
before disruption
(44%)
unstable
stable
(7%) False
positives
See Jack Berkery’s talk (next) for full detail

## Slide 17: Another criterion: what levels of plasma disturbances (dBp; dBp/Bp(a)) are permissible to avoid disruption MHD modes?
ITER high priority need
  Analysis requested by ITER
  Vetted through ITPA
Compare maximum dBp (n = 1 amplitude) causing disruption vs Ip
  Maximum dBp increases with Ip
Further analysis may provide guidance for a disruption predictor in DECAF
NSTX
RWM-induced
Disruptions
(n = 1 global
MHD mode)

## Slide 18: Maximum dBp might follow de Vries-style* empirical scalings
*P.C. de Vries, G. Pautasso, E. Nardon, et al., Nucl. Fusion 56 (2016) 026007
NSTX RWM-induced disruptions (n = 1 global MHD mode)
Will be tested in DECAF as a “tolerable limit” to global mode amplitude

## Slide 19: In contrast, maximum dBp/<Bp(a)> seems independent of scaling on (li) or (Fp) (or (Fp/li))
Fp = ptot(0)/<ptot>vol (from kinetic equilibrium reconstructions)
Dependence on li, Fp expected for RWM marginal stability points
NSTX
RWM-induced
Disruptions
(n = 1 global
MHD mode)
internal inductance
total pressure peaking factor

## Slide 20: Reminder: NSTX-U rotation controller including NTV and NBI torque profiles can compensate for Ti variations in NTV
t (s)
t (s)
3D coil current and NBI power (actuators)
yN
NBI, NTV torque density (N/m2)
Plasma rotation (rad/s)
NTV
torque
104
desired wf
t1
t3
NBI
torque
t1 = 0.59s
t2 = 0.69s
t3 = 0.79s
NTV torque profile model for feedback dependent on ion temperature
Rotation evolution and NBI and NTV torque profiles
K1 = 0, K2 = 2.5
3D Coil Current (kA)
0.5
0.7
0.9
1.0
0.8
1.2
1.4
1.6
1.8
2.0
0.5
0.7
0.9
Ti (keV)
0.6
1.2
1.8
0.0
t (s)
0.5
0.7
0.9
0.8
0.6
0.4
NBI power (MW)
7
1
0
6
5
4
3
2
t2
t1
t3
t2
t1
t2
t3
0
6
8
4
2
10
0.0
0.2
0.4
0.6
0.8
1.0
0.0
0.5
1.0
1.5
2.0
2.5
t1
t3
t2

## Slide 21
Supporting Slides Follow

## Slide 22
JET disruption event characterization provides framework for understanding / quantifying disruption prediction
P.C. de Vries et al., Nucl. Fusion 51 (2011) 053018
JET disruption event chains
Related disruption event statistics
JET disruption event chain analysis performed by hand, desire to automate

## Slide 23
Disruption Event Characterization And Forecasting Code (DECAF) yielding initial results (pressure peaking example)
PRP warnings
PRP
VDE
IPR
SCL
Detected at: 0.4194s
0.4380s
0.4522s
0.4732s
NSTX
142270
Disruption
10 physical events presently defined in code with quantitative warning points
  Builds on manual analysis of de Vries
  Builds on warning algorithm of Gerhardt
  New code written (in Python), easily expandable, portable to other tokamaks (can now read DIII-D data)
Example: Pressure peaking (PRP) disruption event chain identified by code before disruption
  (PRP) Pressure peaking warnings identified first
  (VDE) VDE condition subsequently found 19 ms after last PRP warning
  (IPR) Plasma current request not met
  (SCL) Shape control warning issued
Event chain
P.C. de Vries et al., Nucl. Fusion 51 (2011) 053018
S.P. Gerhardt et al., Nucl. Fusion 53 (2013) 063021
J.W. Berkery, S.A. Sabbagh, Y.S. Park (Columbia U.)
and the NSTX-U Disruption PAM Working Group

## Slide 24: DECAF is structured to ease parallel development of disruption characterization, event criteria, and forecasting
Physical event modules encapsulate disruption chain events
  Development focused on improving these modules
  Structure eases development
    E.g. separate code by C. Myers that improved disruption timing definition was quickly imported
Physical events are objects in physics modules
  e.g. VDE, LOQ, RWM are objects in “Stability”
  Carry metadata, event forecasting criteria, event linkages, etc.
Main data structure
Code control workbooks
Density Limits
Confinement
Stability
Tokamak dynamics
Power/current handling
Technical issues
Physical event modules
Output processing

## Slide 25: The model using a “no slip” condition has no steady state solutions at a large enough island width ()
For steady state
solutions:
= 0 : “red curve”
  No mode present
< : “blue curve”
  Two steady state solution
= : “”orange curve”
  One steady state solution ()
  Bifurcation
  Bifurcation
    At close to half the steady state natural rotation frequency ()