## Slide 1: GTS simulations of NSTX L- and H-Mode Plasmas
Y. Ren1
W. Wang1, W. Guttenfelder1, S.M. Kaye1, J. Ruiz-Ruiz2, S. Ethier1, R.E. Bell1, B.P. LeBlanc1, E. Mazzucato1,
D.R. Smith3, C.W. Domier4, H. Yuh5 and the NSTX-U Team
1. PPPL 2. MIT 3. UW-Madison 4. UC-Davis 5. Nova Photonics
NSTX-U Results Review
September 21st – 22nd, 2016

## Slide 2: Why are Global Effects Important?
Global effects are considered to be important for STs
  Local assumption of flux tube simulations based on ρ*~0
  Large ρ* of STs due to weaker toroidal field compared to conventional tokamaks (ρ* ~ 0.01 for NSTX)
  Global effects, i.e. turbulence spreading, requiring global GK codes
Study of global effects are important for achieving predictive capability for future STs
  Need to validate first principle model for developing reduced transport model with global effects
Serious validation efforts applying global GK codes to ST plasmas are still lacking

## Slide 3
NSTX L-mode plasmas

## Slide 4: GTS Simulations were Carried Out to Assess Thermal Transport before and after RF Cessation
Time of the RF cessation
<15% variation in equilibrium quantities in the high-k measurement region before and right after the RF cessation (over 17 ms)
Equilibrium quantities not expected to change significantly on the time scale on which the turbulence changes (0.5-1 ms)
  Energy confinement time~ 10 ms
High-k measurement region
Shot=140301
RF-heated L-mode plasma with
BT =5.5 kG and Ip=300 kA
Ren et al., PoP 2015

## Slide 5: Similar Energy Fluxes from GTS are Seen before and after the RF cessation
Electron energy flux matches experimental value after the RF cessation but not before
  Experimental values from TRANSP+TORIC analysis
Ion energy flux is over-predicted
Electron thermal transport
Ion thermal transport

## Slide 6
NSTX H-mode plasmas

## Slide 7
Current Ramp-down in NSTX H-mode Plasma Leads to Core Density Gradient Increase
Shot=141767
NBI-heated L-mode plasma with
BT =5.5 kG
Ruiz-Ruiz et al., PoP 2015

## Slide 8: Ion Energy Flux from GTS Is in Agreement with Experiment
Ion energy flux from ion-scale turbulence contributes significantly at R>135 cm
t=332 ms
t=565 ms
Neoclassical ion thermal transport can account for experimental ion thermal transport
Ion-scale turbulence suppression due to ExB shear

## Slide 9: Electron Thermal Transport is Significantly Under-predicted by GTS
Electron energy flux from GTS is only significant at R>135 cm
  Much smaller than experimental electron thermal transport
Contribution from ETG and electromagnetic effects may be important
t=332 ms

## Slide 10: Dissipative-TEM May be Important for NSTX H-mode Plasmas
Dissipative-TEM found due to strong ∇n in an NSTX H-mode right after ELM
  Capable to survive Strong E × B shear
  Drives experimentally relevant transport
  DTEM-transport increases with
  CTEM strongly suppressed by collisions in STs
  C/DTEM-free regime in low collisionality
(possibly relevant to NSTX-U & ST-FNSF)
Roles of DTEM further investigated over broad NSTX discharges