## Slide 1: TRANSP Analysis of NSTX-U L- and H-modes
S. M. Kaye, PPPL
NSTX-U Results Review
Sept. 22, 2016

## Slide 2: New NSTX-U tool: Between and Among Shot TRANSP (BEAST) will aid experiment execution
Typical BEAST run completed in 8 mins
  NSTX-U has 15-20 mins between shots
In preparation for next shot, session leader can gauge:
  Non-inductive fraction
  Beam loss
  Confinement quality
  Any TRANSP quantity…
NSTX-U BEAST TRANSP run

## Slide 3: TRANSP Runs Performed for Many L- and H-mode Discharges
Perform global/thermal confinement analysis
Study local transport (interpretive and predictive)
Hampered by either no CHERS (when second beam on) or poor signal
(at low input power)
  Often use Chang-Hinton neoclassical prediction for Ti
  Flat Zeff=2 profile
  Feedback on AFID for neutron match
L-mode data taken from Beam #1 L-mode scan (W. Guttenfelder)
  Ip = 0.6 to 1.0 MA
  Pinj = 1 to 5 MW
  ne,bar = 2.8 – 6 x 1019 m-3
Compare to 204118 (H-mode)

## Slide 4: Thermal Confinement Trends Difficult to Extract Due to Poor Coverage Across Parameter Space
L-Mode

## Slide 5: H-mode Confinement Enhancement Well Above that of L-mode (and >=1)

## Slide 6: Reduction in χe Going From L- to H-; RLW predicts Te
Caveat: Linear GYRO indicates
microtearing is NOT dominant
μinstability