## Slide 1: NSTX-U Mission Elements:
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
Develop solutions for plasma- material interface (PMI)
Advance ST as Fusion Nuclear Science Facility and Pilot Plant
Liquid metals / Lithium
Snowflake/X
ST-FNSF /
Pilot-Plant
ITER

## Slide 2: NSTX-U will access new physics with 2 major new tools:
Higher T, low collisionality at high 
 Unique regime, study new transport and stability physics
Full non-inductive current drive
 Not demonstrated in ST at high-T
Essential for any future steady-state ST
2. Tangential 2nd Neutral Beam
1. New Central Magnet

## Slide 3: NSTX-U will have major boost in performance
2× toroidal field (0.5  1T)
2× plasma current (1  2MA)
5× longer pulse (1  5s)
2× heating power (5  10MW)
Tangential NBI  2× current drive efficiency
4× divertor heat flux ( ITER levels)
Up to 10× higher nTE (~MJ plasmas)
2. Tangential 2nd Neutral Beam
1. New Central Magnet

## Slide 4: Completed NSTX Upgrade Project
New Central Magnet
New 2nd Neutral Beam
Original Neutral Beam

## Slide 5: Design studies show ST potentially attractive as Fusion Nuclear Science Facility (FNSF) or Pilot Plant
FNSF with copper TF coils
A=1.7, R0 = 1.7m, x = 2.7
Fluence = 6MWy/m2, TBR ~ 1
FNSF / Pilot Plant with HTS TF coils
A=2, R0 = 3m, x = 2.5
6MWy/m2, TBR ~ 1, Qeng ~ 1
FNSF: Provide neutron fluence for material/component R&D + T self-sufficiency
Pilot Plant: Electrical self-sufficiency: Qeng = Pelec / Pconsumed ≥ 1 + FNSF mission

## Slide 6: NSTX-U = National Spherical Torus eXperiment - Upgrade Highly collaborative research program
~400 team members
~350 data users
55 institutions
22 US Universities
April 2016
Domestic (33)
International (22)

## Slide 7: Central magnet construction was complex, multi-stage, multi-year effort
Built 4 toroidal field (TF) quadrants
Combine quadrants (5th VPI)
Install vacuum- tight casing over TF + OH bundle
4 vacuum pressure impregnations (VPI)
Wind ohmic heating (OH) coil over TF, then final 6th VPI

## Slide 8: Fabrication and installation of central magnet ultimately successful
Over shield wall
Over the machine
Inside NSTX-U!

## Slide 9: Tangential neutral beam required major vacuum vessel modifications
JK cap
Interior View of Bay J-K
Exterior View of Bay J-K

## Slide 10: 2nd beam (from TFTR DT campaign) required T decontamination, NSTX test-cell re-arrangement
Beam Box being lifted over NSTX
Beam Box placed in its final location and aligned
Beam Box being populated with components