## Slide 1: 3D Fields: Detection and Application
Stefan Gerhardt, Eric Fredrickson, Clayton Myers, Steve Sabbagh, Weiguo Que
Phys. Ops. Course 2015

## Slide 2: Topics
Motivation for low-frequency 3-D field sensors and coils.
Application of low-frequency 3D fields
Detection of low-frequency 3D fields
Determination of the currents in the RWM coils
High-frequency rotating MHD detection.

## Slide 3: Topics
Motivation for low-frequency 3-D field sensors and coils.
Application of low-frequency 3D fields
Detection of low-frequency 3D fields
Determination of the currents in the RWM coils
High-frequency rotating MHD detection.

## Slide 4: Why Do We Have 3-D Field Detection and Application? (I)
Deliberately apply fields as perturbations:
  Locked mode thresholds vs. density, field,…
  Magnetic braking to study “stuff” as a function of rotation.
  (N)RMP for modifications to pedestal transport & ELM suppression.
    or ELM triggering.
  Strike-point splitting, 3-D effects on divertor loading, “homoclinic tangles”

## Slide 5: Why Do We Have 3-D Field Detection and Application? (II)
Control of Error Fields
  Small non-axisymmetries in machine construction lead to error fields.
  Plasma can amplify the error field (RFA), causing their effect to become stronger….effect is stronger at higher .
  Detect the amplified error field and suppress it with feedback
    Called “dynamic error field correction” (DEFC).

## Slide 6: Why Do We Have 3-D Field Detection and Application? (III)
Suppression of Resistive Wall Modes.
  RWM=external kink instability modified by the resistive wall.
    Both pressure and current driven kinks can become RWMs.
  Grows on the scale of the wall time=L/R time for dominant eddy current patterns. (~2-5 msec).
  Detect and suppress it.
    Call this “fast” n=1 feedback.

## Slide 7: Why Do We Have 3-D Field Detection and Application? (IV)
Kink, Tearing, *AE
  These show up as rapidly rotating/varying 3D perturbations.
    5 kHz -> 1s of MHz
  Can only be detected with sensors inside the vessel
  Tearing modes and kinks can degrade thermal confinement, stop the plasma rotation, modify the fast ion confinement and current drive.
  Bursting TAE modes can eject (or steal energy from) fast ions, changing beam current drive.
  GAE/CAE modes lead to PRLs.

## Slide 8: Topics
Motivation for low-frequency 3-D field sensors and coils.
Application of low-frequency 3D fields
Detection of low-frequency 3D fields
Determination of the currents in the RWM coils
High-frequency rotating MHD detection.

## Slide 9: 3D Fields Are Applied by the RWM Coils
VALEN Model of NSTX (Columbia Univ.)
6 ex-vessel midplane control coils

## Slide 10: RWM Coil Current is Provided by the SPAs
SPAs are H-bridge power Supplies
  Capacitor bank is a constant voltage
  If G1 and G4 conduct, then load voltage is one polarity
  If G2 and G3 conduct, load voltage has the other polarity.
  Rapidly switch which IGBT conduct. This leads to regulation of the current.
We rely on the on-board controller, and only issue a current request to the SPA.
SPA cap bank is charged by “HF Supply”
  If HF supply doesn’t work, then neither will the SPAs

## Slide 11: Previously: Each SPA in Connected To Two RWM Coils
2
3
4
5
6
Bay A
Bay L
SPA 1
SPA 2
SPA 3
RWM/EF coil #
1
IP

## Slide 12: Now: Each SPA in Connected To a Single RWM Coil
2
3
4
5
6
Bay A
Bay L
SPA 1
SPA 2
SPA 3
1
IP
RWM/EF coil #
SPA 4
SPA 5
SPA 6
BT
Positive SPA current makes:
Field flowing CW in the RWM coil as you face the coil.
This makes field pointing into the vessel

## Slide 13: More on Signal Polarities
Positive SPA supply current makes current flowing clockwise when viewed from outside NSTX-U.
  This makes field that points into the vessel.
  Hence, positive supply current makes field pointing into the vessel.
The PCS requests are always supply current.
  So a positive PCS request will make field pointing into the vessel for the associated coil.
  This is a bit different than for the PF/TF coils, where the requests are the coil current.
The SPA currents are recorded multiple ways.
  \pc_spa_SUX_IY, X={1:6} & Y={1:2}, are the 2 DCCTs on the SPAs themselves. They have the polarity of the supply current.
  The \IRWMX, X={1:6} are the subunit currents mapped to the coils and corrected for signs so that positive current corresponds to positive radial field.
  The \RWMX_I, X={1:6}, are current measurements on the coil leads, but with the engineering convention.
    Positive values correspond to clockwise currents and inward pointing field

## Slide 14: Typical Application is to Make n=1 Traveling Waves

## Slide 15: You Will Use the PCS Waveform Generator Function to Produce Traveling Waves
PCS Sine Wave Generator
Determined by Parameters
1: offset,
2: amp,
3: period [seconds],
4: # of periods,
5: start phase [degrees]}
Or
[YDC,Yamp,Tcycle, # of periods, fstart]
ISPA=YDC+YAMPsin(2pt/Tcycle + pfstart/180))
XP authors/forms should know exactly the parameters to get the correct traveling wave

## Slide 16: Topics
Motivation for low-frequency 3-D field sensors and coils.
Application of low-frequency 3D fields
Detection of low-frequency 3D fields
Determination of the currents in the RWM coils
High-frequency rotating MHD detection.

## Slide 17: NSTX-U has Off-Midplane Internal 3D Field Sensors
VALEN Model of NSTX (Columbia Univ.)
6 ex-vessel midplane control coils
SS Vacuum
Vessel
Copper passive
conductor plates
BR
BP sensor
Sontag et al., Physics of Plasmas 12 056112 (2005)
BP Sensor in a Stainless Box
BR sensor is a loop behind the tiles, but in front of the plate.

## Slide 18: We Actually Integrate Sensor Sums and Differences

## Slide 19: PCS Signal Compensation For RWM Coils
Any given sensor detects the field from the plasma perturbation, plus other sources.
  “Other sources” include direct coil pickup, eddy currents.
Subtract non-plasma pickup from each signal.
Many coefficients involved, all in model tree.
Static
Direct pickup between coil and sensor. Pi,j are mutual inductances
AC Compensation For Fluctuating RWM Coil Currents
Eddy currents driven by RWM coils make fields…subtract these out.
504 Coefficients
816 Coefficients
Final Field For Plasma Mode Identification
In ACQ
In the modeID category

## Slide 20: Topics
Motivation for low-frequency 3-D field sensors and coils.
Application of low-frequency 3D fields
Detection of low-frequency 3D fields
Determination of the currents in the RWM coils
High-frequency rotating MHD detection.

## Slide 21: Overall Scheme for Control
Data from 48 RWM Sensors
Comes in on FPDP Stream
Signal Processing To Remove Pickup From All Non-Plasma Field Sources (“Compensation”)
Done in ACQ and ModeID
Combine signals to form an amplitude and phase of the plasma 3-D perturbation
Done in ModeID Algorithms
Form Request For SPA Current From RWM Category
1: Preprogrammed Part
2: RWM Feedback Part
Done in RWM Category
Pre-Programmed Requests for Current in Individual SPA Subunits
Done in RWM Category Algorithms
SPA Request Summer
Done in System Category
Raw Data
Compensated Data
Mode amplitude
and phase
PCS Waveforms
Compensated
Data
6 SPA Current Requests
Other Category Making SPA Request
Vertical Control Category
PSRTC (clamping)
To SPA On-Board Controller Via FPDP
6 SPA Current Requests
6 SPA Current Requests

## Slide 22: Process for Mode Identification
The actual magnetic perturbation has an amplitude (ARWM) and phase (RWM)
  How to determine ARWM & RWM?
We measure the plasma field:
  Above and below the midplane
  With BR and BP sensors
Convert the sensor fields at each time point to amplitude and phase.
  Assemble all the measured fields in a column vector [24x1].
  Construct the mode-ID matrix [2 x 24]
  Multiply these together…resulting [2 x 1] array contains (essentially) ARWM & RWM
Matrix elements are a/the primary input to the algorithm.
  Stored as “parameter data”
  Restored with the shot.
  GUI matrix editor for changing the values.
Contents of matrix generally come from SPG, SAS, CEM, or JEM.

## Slide 23: What is the mode-ID matrix?
The mode has an amplitude (ARWM) and phase (RWM)
At the ith sensor, the measured amplitude is:
Many sensors…build a matrix and invert it!
  Matrix elements are a/the primary input to the algorithm.
Many more details in reality, but this is the idea.
Big gotcha: Sometimes sensors fail. The mode-ID matrix must use only the good sensors.
  Beware reloading! Consult CEM and SPG if in doubt.

## Slide 24: Algorithms for Mode Identification: mid
mid=“Mode Identification” (modeid Category)
Uses static compensation only.
Inputs:
  Rezeroing time (time at end of Ip flat top where sensor values are reset to zero).
  The mode-ID matrix (2x24): see previous slide.
Outputs passed within PCS to RWM feedback algorithms.
  Amplitude and phase of mode as detected by BP sensors.
  Amplitude and phase of mode as detected by BR sensors.
  Amplitude and phase of mode as detected by BR + BP sensors.

## Slide 25: Algorithms for Mode Identification: miu
miu=“Mode Identification Upgrade” (modeid Category)
Applies AC compensation (with an on/off switches).
Inputs:
  Rezeroing time (time at end of Ip flat top where sensor values are reset to zero).
  Switches to turn off various compensations
  The Matrix (2x24): see previous slides.
Outputs passed within PCS to RWM feedback algorithms.
  Amplitude and phase of mode as detected by BP sensors.
  Amplitude and phase of mode as detected by BR sensors.
  Amplitude and phase of mode as detected by BR + BP sensors.
  Compensated sensor data for the “advanced controller”.

## Slide 26: RWM/DEFC Feedback Methodology in the “tmf” Algorithm
We know the amplitude B1(t) and phase 1(t) of the detected 3D field, from both BR and BP sensors.
Apply an n=1 field with:
  Amplitude proportional to the detected 3-D field
  Fixed phase shift from the detected 3-D field.

## Slide 27: RWM/DEFC Feedback Methodology in the “tmf” Algorithm
We know the amplitude B1(t) and phase 1(t) of the detected 3D field, from both BR and BP sensors.
Apply an n=1 field with:
  Amplitude proportional to the detected 3-D field
  Fixed phase shift from the detected 3-D field.
Detected Mode Amplitude
(From Mode ID)
Feedback Gain (PCS Waveform)

## Slide 28: RWM/DEFC Feedback Methodology in the “tmf” Algorithm
We know the amplitude B1(t) and phase 1(t) of the detected 3D field, from both BR and BP sensors.
Apply an n=1 field with:
  Amplitude proportional to the detected 3-D field
  Fixed phase shift from the detected 3-D field.
Coil Toroidal Angle
(Hard Coded)
Detected Mode Phase
(From Mode-ID)
Feedback Phase Shift
(PCS Waveform)
Detected Mode Amplitude
(From Mode ID)
Feedback Gain (PCS Waveform)

## Slide 29: RWM/DEFC Feedback Methodology in the “tmf” Algorithm
We know the amplitude B1(t) and phase 1(t) of the detected 3D field, from both BR and BP sensors.
Apply an n=1 field with:
  Amplitude proportional to the detected 3-D field
  Fixed phase shift from the detected 3-D field.

## Slide 30: RWM/DEFC Feedback Methodology in the “tmf” Algorithm
We know the amplitude B1(t) and phase 1(t) of the detected 3D field, from both BR and BP sensors.
Apply an n=1 field with:
  Amplitude proportional to the detected 3-D field
  Fixed phase shift from the detected 3-D field.

## Slide 31: RWM/DEFC Feedback Methodology in the “tmf” Algorithm
We know the amplitude B1(t) and phase 1(t) of the detected 3D field, from both BR and BP sensors.
Apply an n=1 field with:
  Amplitude proportional to the detected 3-D field
  Fixed phase shift from the detected 3-D field.

## Slide 32: There Are Other Algorithms in the RWM Category
“ssp”=“six subunit control”
  Pre-programmed EFC coil currents only.
  No real reason for you to use this.
“LQG” = “Linear Quadratic Gaussian”
  State-Space feedback
  Next slide.
Old defunct algorithms that have vanished
  “spa”: pre-programmed control of 3 sub-units
  “fec”: Field Error Correction
  “imf”=Initial Mode Feedback
  “smf”=Second Mode Feedback

## Slide 33: Advanced RWM Controller
Effort lead by Columbia University collaborators
State-Space implementation of RWM feedback.
  “State” is a mathematic representation of the system status
    Plasma surface currents to represent the RWM.
    Vessel and plate currents (VALEN EM model).
    Coil currents.
  Solve a linearized version of the dynamical system equations to determine optimal correction currents.
    A simple model of the RWM is built into the controller.
    No PID…”Gains” are numbers in a bunch of matrices.
  Will generate requests for currents:
Add the optimal controller request to other requests.
  Preprogrammed, Proportional feedback,…
Tested in 2010 run, will be used again in 2016 run.

## Slide 34: About Reloading
All plasma shots ever taken were in the 3 subunit configuration.
  A few engineering test shots taken with 6 subunits.
Therefore, you should never reload the entire RWM category from ShotNumber<200000.
  OK to reload specific waveforms after consideration.
Due to changes in the RWM sensor availability, you should never reload the ModeID category from ShotNumber<200000
  Again, OK to reload specific waveforms after consideration.
No use of these categories until they have been qualified by XMPs (Gerhardt, et al)

## Slide 35: Topics
Motivation for low-frequency 3-D field sensors and coils.
Application of low-frequency 3D fields
Detection of low-frequency 3D fields
Determination of the currents in the RWM coils
High-frequency rotating MHD detection.

## Slide 36: High-Frequency 3D Fields Detected by In-Vessel Sensors (NSTX, not NSTX-U, but Conceptually Identical)
High-f BP Sensors
High-f BT Sensor
RWM BP Sensor
High-n BP Sensors
RWM BP Sensors

## Slide 37: Analysis Methods For High-Frequency Perturbations
Pick 2 sensors 180º apart
  Add the signals: Even-n magnetic signature.
  Subtract the signals: Odd-n magnetic signature.
  These signals written to the tree on every shot.
Or, do a full decomposition in n-number….type in idl:
  @/u/sgerhard/NSTX/idl/startup
  Mirnovgui
Or Eric Fredrickson has lots of routines.

## Slide 38: Who’s Who For 3D Fields
SPAs: Weiguo Que, Bob Mozulay, Raki Ramakrishnan
RWM Coils: George Labik, Steve Raftopoulos
RWM Sensors: Stefan, Clayton
Mode-ID Software: Stefan, Clayton
RWM Control Codes: Stefan, Steve Sabbagh, Clayton
High-n array: Eric Fredrickson and Stefan Gerhardt
High-f array: Eric Fredrickson
Magnetic Braking: S. Sabbagh, J.-K. Park