## Slide 1
College W&M
Colorado Sch Mines
Columbia U
CompX
General Atomics
INEL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Nova Photonics
New York U
Old Dominion U
ORNL
PPPL
PSI
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Washington
U Wisconsin
NSTX
Supported by
Culham Sci Ctr
U St. Andrews
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Hebrew U
Ioffe Inst
RRC Kurchatov Inst
TRINITI
KBSI
KAIST
POSTECH
ASIPP
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
U Quebec
COE and Machine Operations
Ray Camp
* Responsibilities
* Daily Startup Activities
* Typical Shot Sequence
* Machine/Vacuum Tech Operations
* COE Operations
NSTX Physics Operations Course July 2015

## Slide 2: COE Responsibilities
Safe operation of NSTX-U
  Personnel Safety
  Equipment Operation within established limits
Coordinating the various groups to achieve the above
  Machine Technicians
  Health Physics
  Physics Operator/Session Leader
  Diagnostics
  ESU
  Engineering (PCEIC, Grounding, OIT)

## Slide 3: Machine/Vacuum Techs - Daily Startup
* Hi-pot the inner and outer vessel
* Configure the gas injection system and check pumping systems
* Configure diagnostics as required
* Kirk keys at appropriate stations for operations
* Ensures the experimental areas (TC, TCB gaged area and VCR/CSR) clear of personnel (search and secure) and set the loops
* Informs the COE that the machine and test cell are ready for operations
* Runs typically 30 minutes of helium GDC prior to fiducial plasma
NSTX Physics Operations Course Feb. 9-11, 2010

## Slide 4: COE Daily Startup
* Instructs water systems and MG to startup at 7 am
* Starts up various programs:
- EPICS
- Energy monitor
- Scope pages
- Database for shot statistics
* Runs clock cycle to test acquisition and EPICS are OK
* At 7:30 test cell is cleared and closed up and COE requests the Safety Lockout Device (SLD) be pressurized by FCPC
- SLD supplies air to the Safety Disconnect Switches (SDSs) in the FCPC area so that the line and ground switches can be configured
NSTX Physics Operations Course July 29, 2015

## Slide 5: COE Daily Startup (cont)
* Supplies enable and arming permits to NB and RF(ECH)
* FCPC performs a hi-pot of the coils separately and the coils and rectifiers together
* Hi-pot values entered in database and checked for typical values
* PCEIC starts PSRTC/DCPS and Runs two coil only test shots at 50% and 100% current levels
* Runs fiducial plasma discharge and hands over plasma operations to the Physics Operator and Session Leader (usually between 8 and 8:30 am)
NSTX Physics Operations Course July 29, 2015

## Slide 6: Typical Shot Sequence
NSTX Physics Operations Course July 29, 2010

## Slide 7: Vacuum Tech / Between Shot GDC
* Enters:
- Operating mode (lithium and operations or operations only)
- Time period per SL or PO
- Pressure (typically 2.5 mT)
- Gas/injector (typically helium from injector #3 at Bay J mid-plane but may use #1 at the top of Bay K this run)
* Ensures shutter configuration is correct
* GDC runs and shuts down automatically
* PLC cog may assist until interlocks and timing between GDC and LITER are developed
* GDC time usually decreases with increased lithium use
NSTX Physics Operations Course July 29, 2015

## Slide 8: Vacuum Tech Operation
* One of four PLC controlled diagnostic shutter pages
* Can be operated manually or programmed for automatic actions in different modes of operation such as plasma operation, GDC and shutdown
* Diagnostic TIV page which is controlled in a similar manner as the shutters
NSTX Physics Operations Course July 29, 2015

## Slide 9: Vacuum Tech Lithium Operations
* Controls and monitors the operation of the two LITER probes from EPICS pages
- Home, parked and operate
* Co-ordinates GDC and LITER probe operation with lithium operator and COE to get requested between shot lithium and GDC
NSTX Physics Operations Course July 29, 2015

## Slide 10: Vacuum Tech – Gas Injection
* Fills high field side center stack injections systems (and lower dome injector if needed) to requested pressure per PO
* Controls SGI (PLC and EPICS based) and other EPICS gas injection systems at request of cogs and with concurrence of SL
* Monitors vacuum conditions
NSTX Physics Operations Course July 29, 2015

## Slide 11: COE Panels
LHS panel status:
- Test cell status
- Loop status
- E-Stop status
- Permit to pressurize/vent the SLD
- Enable and arm permits to FCPC
for configuring TF/PF/CHI line and ground SDSs
- Reset hardwired faults
RHS panel status:
- Provides final arm for FCPC/NB/RF(ECH) after systems are ready
- E-Stop alarm and acknowledge
- E-Stop button and resets
- Enable and arming permit for NB and RF to configure
NSTX Physics Operations Course July 29, 2015

## Slide 12: COE Operations
* Monitors configuration of the FCPC SDS and ground switches.
* Gives permissive to FCPC to make configuration changes by placing the switch on the COE panel to configure
* Monitors fault conditions and resets faults when systems are satisfactory
NSTX Physics Operations Course July 29, 2015

## Slide 13: COE Operations
* Monitors ACP for faults and resets when satisfactory
* Lower right corner is a summary page of the status of a various systems
* Sets minimum clock cycle, (NB interlock 2.5 minutes) and starts clock when all systems and personnel are ready
NSTX Physics Operations Course July 29, 2015

## Slide 14: DCPS

## Slide 15: Controlled Access and Shutdown
Controlled Access
- FCPC, NB, RF, CHI shutdown and safed
- FCPC then vents the SLD
- Machine tech obtains the SPA kirk key from the transfer station on 2nd floor of FCPC
- Machine techs let personnel into the test cell once all systems are safed (HP may be first)
- Activity is monitored by machine techs and search and secure is performed before exiting the test cell and loop is set
Shutdown
- All systems safed (FCPC, MG, NB, RF and MPTS) and SLD vented
- Cool down LITER probes (couple of hours)
- Kirk keys back at test cell door
- Place test cell in Free Access (typically 10-15 minutes after last shot)
NSTX Physics Operations Course July 29, 2015

## Slide 16: Conduct of Operations
At the Controls Area
Health Physics
Stubborn COE
Communications
Emergencies and Off-normal Events