## Slide 1: Gas Injection System (GIS)
Devon Battaglia,
Keith Erickson, Dennis Mueller, Stefan Gerhardt,
Roger Raman, Vlad Soukhanovskii
NSTX-U Physics Operators Training
September 15, 2015

## Slide 2: Gas Injection Systems on NSTX-U for FY16
Piezoelectric (P10) valves
  Fast on/off using piezoelectric crystal that bends in response to voltage
  PZV: Main LFS injection valves
  SGI: Supersonic gas injector
    Advanced nozzel on moveable probe
  GPI and Impurity: Diagnostic gas
  DIVL: Two valves (Bay I and Bay C)
    Two upper divertor systems (DIVU) in the future
Pneumatic (puff) valves
  Empty plenum into vessel when triggered
  HFS: 2 at midplane, 2 at shoulder
    Each location has 2 varieties of tube diameter
  CHI: 2 systems used for CHI
    See Rogers talk
Massive gas injector (MGI)
  See Roger’s talk
Midplane
Shoulder
PZV1
PZV2
PZV3
SGI
GPI
Imp.
DIVL
CHI

## Slide 3: Piezo valves on NSTX-U
Piezoelectric (P10) valves
  PZV, SGI used for prefill, plasma fueling, GDC
  GPI, DIV, Impurity used for specific experiments
  Each valve supplies gas from a plenum
  Typical maximum flow rates ~ 150 Torr-liters/second
Flow-rate control using pulse-width modulation
  Valves cycle between fully-opened and closed to achieve, on average, the desired flow rate
    Algorithm considers min on/off time, evolving plenum pressure to compute open/close times
  Why not control flow by partially opening valve?
    Drifting voltage response of piezo crystal requires frequent tuning, irreproducible results
PZV1
PZV2
PZV3
SGI
GPI
Imp.
DIVL

## Slide 4: Prefill control for plasma startup
Gas injected prior to breakdown
  Pumped away by turbo (vessel) and cyro (beam) pumps
  Prefill algorithm does active feedback on vessel pressure
Vessel pressure gauges have a slow response
Target
Field pickup
Closed
Open

## Slide 5: Prefill is mostly left alone, except …
Approximate vessel volume must be chosen
  NBI beam line volume similar to NSTX-U volume
  Planned: consistency check with beam TIV status in EPICs
    Until then, be aware of opening and closing NBI TIVs
  Not fatal, but could result in missing prefill target
Gas injection category 
Prefill Subset 
Prefill Data …
25000 liters: No beam TIVs open
50000 liters: One beam TIV open
75000 liters: Both beam TIVs open

## Slide 6: Prefill is mostly left alone, except …
Approximate vessel volume must be chosen
  NBI beam line volume similar to NSTX-U volume
  Planned: consistency check with beam TIV status in EPICs
    Until then, be aware of opening and closing NBI TIVs
  Not fatal, but could result in missing prefill target
All other changes or problems …
  Fail to break down, gas injector or pressure gauge breaks, not getting prefill target, changing prefill gas type …
  Call Devon or Dennis

## Slide 7: If you want gas, you must …
Enable valve in PCS
  Gas Injection  Enable and Status  Injector enable …
Tell the vacuum PLC operator
  They also need to know the plenum pressure
Make sure Piezo gas type is correct in PCS at the start of XP
  Gas Injection  Enable and Status  Gas type …
  Daily checklist would have this in it
  Future: check consistency with EPICS

## Slide 8: Piezo valve control from the PCS
Piezo valve control waveform
  Valve is closed, open or in flow rate (PWM) control
  In the future, could have option for density, div radiation …
Piezo flow rate waveform
  Set target flow rate for when valve control = flow

## Slide 9: Early fueling (t < 100ms) was important on NSTX for avoiding locked-modes
Time (s)
PZV2 Voltage 141182

## Slide 10: HFS gas important for H-mode access
Reliable and lower power H-mode access observed on STs with HFS fueling
  HFS geometry limits injectors to solenoid valves with long tubes
  P.O. sets trigger to open in PCS
Gas “leaks” in after some delay
  Flow rate and gas load set by plenum pressure and tube diameter
  Two poloidal locations: midplane and shoulder
  NSTX-U: two tube diameters at each location to choose from

## Slide 11: Supersonic gas injector (SGI) provides increased fueling efficiency
SGI is a standard piezo valve fitted with a nozzle
  Mounted on a moveable, shielded probe at the midplane
    Probe position request made to vacuum PLC operator
  Gas injected at Mach 4 speeds
NSTX experiments demonstrated SGI can replace HFS fueling for H-mode access
  Also shown to increase fueling efficiency for early LFS gas
Vlad Soukhanovskii SOFE07

## Slide 12: Summary of NSTX-U gas injection system
LFS Piezo valves
  Prefill with vessel pressure feedback
  Early fueling with flow-rate feedback
  Glow-discharge cleaning (GDC)
  Diagnostics (GPI), trace impurities or divertor fueling
Puff valves
  HFS for H-mode access
  CHI startup
Supersonic Gas Injector
  Tool for improving fueling efficiency