## Slide 1
NSTX Upgrade: ST research to
accelerate fusion development
Jon Menard (PPPL)
For the NSTX-U Research Team
FESAC Strategic Planning Panel Meeting
Gaithersburg Marriott - Washingtonian Center
July 8-10, 2014
NSTX-U
Supported by
Culham Sci Ctr
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Inst for Nucl Res, Kiev
Ioffe Inst
TRINITI
Chonbuk Natl U
NFRI
KAIST
POSTECH
Seoul Natl U
ASIPP
CIEMAT
FOM Inst DIFFER
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
Coll of Wm & Mary
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Lehigh U
Nova Photonics
Old Dominion
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Tennessee
U Tulsa
U Washington
U Wisconsin
X Science LLC

## Slide 2: NSTX Upgrade mission elements
Advance ST as candidate for Fusion Nuclear Science Facility (FNSF)
Develop solutions for the plasma-material interface challenge
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
Develop ST as fusion energy system
ITER
Liquid metals/Li
Snowflake/X
ST-FNSF

## Slide 3: NSTX-U provides world-leading research capabilities across all 5 ReNeW Themes
Theme 1: Burning Plasmas in ITER
  Access, understand, control non-linear Alfvénic instabilities
Theme 2: Predictable, High-Performance, Steady-State Plasmas
  Goal: 100% non-inductive operation with high-bT ~15-20%, profile control
Theme 3: Taming the Plasma-Material Interface
  Leader in Li PFCs, integration: core + snowflake + detachment + high-Z + Li
Theme 4: Harnessing Fusion Power
  Leader in physics basis and design of low-A fusion systems
Theme 5: Optimizing the Magnetic Configuration
  NSTX-U most capable ST facility/program in world for assessing ST for FNSF
NSTX-U + DIII-D/U provide world-leading development of ST, AT for FNSF
Present New 2nd
Neutral Beam Injector (NBI)
Previous New
Center-stack
+
BT = 0.5  1T
IP = 1  2MA
Full non-inductive ~1MA
5× longer pulse
5-10× higher nTt
1st plasma Jan/Feb 2015

## Slide 4: 10 year goal: Integrate high-performance core + metal walls
Sustain high bN ~ 6 with profile/mode control
Reduce collisionality: ~10× lower vs. NSTX
Mitigate high qdiv: up/down snowflake/X+radiation
2× field, power, current, 5× pulse-length
100% non-inductive:
Start-up to 0.4MA
Ramp-up 0.4  ~1MA
Sustain at ~1MA
(Density control needed for all phases)
Establish ST physics / scenarios
Inform choice
of FNSF
aspect ratio
and divertor configuration (with divertor data from
MAST-U Super-X + other experiments)
2015-2019
Inform choice
of FNSF/DEMO plasma-facing materials for
divertor and first-wall
10-20s pulses for PFC/LM equilibration
All high-Z PFCs, hot walls, static Li-wall
Liquid Li modules  flowing Li/LM modules  flowing Li divertor
Divertor C  high-Z, Li vapor shielding
High-performance + metal walls
2015-2019
5 year goal: Establish core physics/scenarios for ST-FNSF

## Slide 5: ST is potentially attractive as Fusion Nuclear Science Facility (FNSF)
Projected to access high neutron wall loading at moderate R0, Pfusion
  Wn ~ 1-2 MW/m2 , Pfus ~ 50-200MW, R0 ~ 0.8-1.8m
Modular, simplified maintenance
Tritium breeding ratio (TBR) near 1
  Requires sufficiently large R0, careful design
Challenges/Gaps: (FESAC-TAP, ReNeW)
  Non-inductive start-up, ramp-up, sustainment
    Low-A  minimal inboard shield  no/small transformer
  Confinement scaling (especially electrons)
  Stability and steady-state control
  Divertor solutions for high heat flux
  Radiation-tolerant magnets
Culham (UK)
UT Austin
ORNL
PPPL
Example ST-FNSF concepts

## Slide 6: Gap 1: Start-up/ramp-up with small/no transformer
Helicity injection (HI) start-up: 150-200kA  projects to ~0.4MA on NSTX-U
New 2nd NBI projected to enable non-inductive ramp-up from ~0.4  1MA
HI start-up Te too low for fast-wave or NBI coupling  use ECH to raise Te
  Achievements since Greenwald Report, NSTX-U base-program research, remaining gaps/enhancements needed
0
1.0 ms
1.6 ms
2.7 ms
1
2
0
1
2
0
1
2
R (m)
R (m)
R (m)
0
-2
1
2
-1
Z (m)
CHI startup
TSC Simulations of CHI
  See Raman Whitepaper: “Simplifying ST and AT Concepts”
13
~0.8-1
~0.5
IP [MA]
10-15
P [MW]
~0.3-0.4
CHI, LHI,
EBW,
Fe core
4
Fast wave
Time
NBI
NSTX-U start-up/ramp-up strategy
EC/EBW
1  3MW 28GHz (with 2nd NBI)  world-leading start-up/ramp-up for ST/AT
EBW: efficient off-axis current drive for over-dense ST/RFP/AT plasmas

## Slide 7: Gap 2: Understand/optimize ST energy confinement
Ion thermal transport ~neoclassical, electron transport anomalous
Confinement scaling: BtE ~ n-0.9 b-0.2 differs from ITER-98y,2 ~ n0 b-0.9
High-b  electromagnetic turbulence (m-tearing, Alfvénic, kinetic ballooning)
Doubling IP, BT  2× Te,i, but need improved pumping to sustain lowest ne, n*
  See Guttenfelder/Crocker whitepaper “Validating EM turbulence/transport effects for burning plasmas”, also A. White whitepaper
  Achievements since Greenwald Report, NSTX-U base-program research, remaining gaps/enhancements needed
ITER-like scaling
ST-FNSF
?
constant q, b, r*
NSTX
NSTX Upgrade
ne*  ne / Te2
Typical c values in NBI H-mode
To reliably project to FNSF-ST/AT  need to understand transport vs. b, n
Diagnostics: Beam emission spectroscopy, high-kr,q, polarimetry, Doppler back-/cross-polarization scattering
Leading opportunity to measure, model, understand electron transport
Divertor cryo-pump

## Slide 8: Gap 3: Plasma sustainment, stability, and control
NSTX achieved ~65% non-inductive current drive at FNSF-level bT ~ 15-20%
NSTX-U designed for 100% non-inductive using more tangential 2nd NBI
TAE avalanches can cause redistribution/loss of NBI current drive
High bN ~ 6 sustained w/ active feedback, optimized/broad p, rotation profiles
  Achievements since Greenwald Report, NSTX-U base-program research, remaining gaps/enhancements needed
NSTX Results
NSTX-U projections
via high harmonic FW
Non-inductive fraction
  See Sabbagh whitepaper on Disruption PAM, Podestá whitepaper on energetic particle/*AE control, also Strait, Buttery whitepapers
New 3D coils would greatly aid control, disruption avoidance for ITER, FNSF
Will also test novel disruption warning, mitigation (fast MGI, EM mass injector)
Total assuming
classical JNBI-CD
Reconstruction
Plasma w/ rapid TAE avalanches
Minor radius
Non-axisymmetric Control Coils (NCC)
Existing
6 midplane
Planned 2x12
off-midplane
Simultaneous control of:
rotation, EF, RWM, ELMs, EP/AE

## Slide 9: Gap 4: Mitigating high heat (and particle) flux (+ core/edge integration with high-Z / liquid metal PFCs)
High-flux-expansion snowflake/X-divertor + radiation reduce qpk-div (up to 5×)
NSTX-U: 2× PNBI, IP, 0.5× lq  qpk-div ~4× higher  30-40MW/m2 unmitigated
Will test mitigation of high qpk-div w/ double snowflake/X + partial detachment
  Achievements since Greenwald Report, NSTX-U base-program research, remaining gaps/enhancements needed
C
BN
Li
High-Z
Bakeable cryo-baffle
for liquid Li modules
Cryo-pump
High-Z outboard divertor PFCs
2015
by 2020
Full toroidal flowing Li divertor (closed-loop)
All
high-Z PFCs + high-Twall
by 2025
Static
liquid Li on hot high-Z walls
  See Maingi / Jaworski / Allain whitepapers on liquid metals, Hill whitepaper on FNSF PMI, ADX whitepapers
Steady-state FNSF scenario not demonstrated in any device w/ high-Z walls
 NSTX-U aims to integrate full non-inductive with high-Z + liquid metal PFCs
Standard
Snowflake/X
NSTX results
Standard
Snowflake/X
Snowflake/X + radiation

## Slide 10: Gap 5: Radiation-tolerant magnets (+ advanced magnet / configuration design)
Ex-vessel equilibrium PF coils
  Shielding + MgO insulation  6 FPY
Long-leg divertor: qpk-div < 5MW/m2
TBR = 0.95-1 for R0 = 1.6m
Find tE > 1.5× ITER H-mode needed for compact FNSF, Pilot (ST or AT)
Recommend enhancing AT/ST FNSF design funding, include QAS, SC/HTS
  Endorse Majeski / LTX whitepaper for high confinement, Minervini / Whyte whitepapers on HTS R&D
*Work supported by Tokamak Energy (UK)
High-temp superconductor (HTS) attractive for efficient+compact ST*
Possible missions:
  Steady-state toroidal PMI facility
  ST Pilot Plant (Qeng~ 1), ST DEMO
Key research need: radiation limits

## Slide 11: US STs aim to accelerate fusion development (see LTX and Pegasus presentations later this afternoon)
Advance ST as Fusion Nuclear Science Facility
  Pegasus-U, NSTX-U: non-solenoidal start-up: helicity injection, EBW
  NSTX-U: physics + scenario basis for FNSF-ST (also ST DEMO)
Develop solutions for plasma-material interface
  LTX-U, NSTX-U: liquid Li for very high confinement, liquid metal PFCs
  NSTX-U: novel divertors: snowflake/X, detachment, vapor shielding
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
  Pegasus-U, NSTX-U: high b, toroidicity, MHD / transport validation
  NSTX-U: non-linear Alfvénic modes, electromagnetic turbulence
NSTX-U
LTX
PEGASUS
FNSF
ITER
DEMO

## Slide 12: Backup slides

## Slide 13: Cost estimates for facility enhancements to address Gaps
~$45M
NSTX-U 5YP base / +10% sustained for 10 years  $65M / $95M for enhancements
~$23M
~$8M
~$19M
10 year total:
$65M
$95M

## Slide 14: NSTX-U plan: ST physics/scenarios integrate high-perf core + metal walls (high-Z + Li)  flowing / large area liquid metals
2015-2019 | 2020-2024 | 2025-2029
High-performance + metal walls
Establish ST physics/scenarios
Inform choice
of FNSF/DEMO plasma-facing materials for
divertor and first-wall
Inform choice
of FNSF
aspect ratio
and divertor configuration
Sustain high bN ~ 6 w/ advanced control
Reduce collisionality n* ~ factor of 10
Mitigate high divertor heat flux
2× BT, IP, PNBI, 5× pulse-length
100% non-inductive:
Start-up to 0.4MA
Ramp-up 0.4  ~1MA
Sustain at ~1MA
(Density control needed for all phases)
All high-Z PFCs, hot walls, static Li-wall
Static liquid Li modules  flowing Li modules  flowing Li divertor
Div. C  high-Z, Li vapor shielding
Slow-flow Li wall segment
Test large area
liquid Li for very high energy confinement, flowing LM divertors for PFC resilience to off-normal events: ELMs, disruptions
Flowing LM divertor/wall
Flowing Li / Sn divertor
10-20s pulses for PFC/LM equilibration
LTX-U results

## Slide 15
NSTX-U Test Cell Aerial View (May, 2014)
Upgrade project now ~90% complete
HHFW
System
1st NBI
2nd NBI
NSTX-U

## Slide 16: NSTX has already accessed shaping and stability performance needed for an ST-FNSF
NSTX data points

## Slide 17: NSTX-U is developing a range of profile control actuators for detailed physics studies, scenario optimization for FNSF
Variations in Beam Sources
800 kA Partial Inductive, 87% < fNI < 100%
Variations in Outer Gap
27 22 17 12 7 2
Outer Gap
800 kA and 1 T
[50,60,70,130] cm
[50,60,120,130] cm
[60,70,110,120] cm
[70,110,120,130] cm
q-Profile Actuators
Torque Profiles From 6 Different NB Sources
Neutral
Beams
(TRANSP)
Rotation Profile Actuators
Largest Rtan
Smallest Rtan
Measured and Calculated Torque Profiles from 3D Fields
n=3 Experiment
n=3 POCA

## Slide 18: Rotation profile control will be an important tool for accessing and sustaining high b
For these plasmas, high bN was correlated with rotation that maximizes RWM damping
  Stabilization from ion precession drift resonance
  Strong motivation for rotation profile control
5YP: Off-midplane 3D coils enable control of resonant vs. non-resonant torques, vf profile
n=1 MHD spectroscopy: high bN can be more stable  important for advanced scenarios
Resonant Field
Amplification (G/G)
bN / li
E×B rotation frequency
Resonant Field
Amplification (G/G)
1
0
S. Sabbagh, J. Berkery (Columbia)
J-K Park (PPPL), J. Canik (ORNL)
Berkery - APS Invited 2013

## Slide 19: Simulations support non-inductive start-up/ramp-up strategy
TRANSP: NSTX-U more tangential NBI  3-4x higher CD at low IP (0.4MA)
  1.5-2x higher CD efficiency, 3x lower prompt loss
New TRANSP simulations of ramp-up: 0.3MA0.9MA with FW+BSNBI+BS
  1st self-consistent NBI-CD calcs during NI ramp-up
TSC code successfully simulates CHI IP ~200kA achieved in NSTX
TSC + tools included in 5 year plan support CHI IP  400kA in NSTX-U
  2.5 x higher injector flux (scales with IP)
  Higher BT = 1T (increases current multiplication)
  > 2kV CHI voltage (increases flux injection)
  1MW 28GHz ECH (increases Te)
Vsurface = 0 constraint  need to add induction from PF coil swing (future)
FY14: Implemented NSTX-U geometry in TSC
R. Raman (U-Wash)
F. Poli

## Slide 20: NSTX-U internal component staging supports goal to assess compatibility of high tE and b + 100% NICD with metallic PFCs
Cryo +
full lower
outboard high-Z divertor
Lower
OBD
high-Z row of tiles
C
BN
Li
High-Z
Cryo + U+L OBD
high-Z rows of tiles
Nominal 2014-18 5 year plan steps for implementation of cryo-pump + high-Z PFCs + LLD
2015
2016
2017
2018-19
High-Z tile row
Bakeable cryo-baffle for liquid Li
Base budget case (from 5 Year Plan for FY2014-18)
Flowing Li module
All
high-Z FW + divertors
+ flowing LLD module
Cryo + high-Z FW and OBD
+ liquid Li divertor (LLD)
2021
2022-23
Cryo-pump

## Slide 21: NSTX-U internal component staging supports goal to assess compatibility of high tE and b + 100% NICD with metallic PFCs
Flowing liquid Li divertor (LLD) module
Full toroidal flowing Li
Cryo-pump
Upper cryo + all
high-Z & higher-T PFCs
+ full toroidal LLD
All
high-Z FW + divertors
+ flowing LLD module
Lower
OBD
high-Z row of tiles
C
BN
Li
High-Z
Cryo + high-Z FW and OBD
PFCs
Nominal 2014-18 5 year plan steps for implementation of cryo-pump + high-Z PFCs + LLD
2015
2016
2017
2018
High-Z tile row
2021
Bakeable cryo-baffle for liquid Li
Cryo-pump
2019-20
Cryo + high-Z FW and OBD
+ liquid Li divertor (LLD)
Incremental budget case (from 5 Year Plan for FY2014-18)

## Slide 22: NSTX-U will explore advanced divertor operation, and extend scaling and understanding of power exhaust
NSTX-U: 2× higher IP and PNBI  access q|| 4-5× higher than NSTX
Will ~1/BP scaling still hold?
Snowflake Divertor
Standard Divertor
Snowflake high flux expansion = 40-60 lowers incident q, promotes detachment
  See R. Maingi and D. Hill whitepapers

## Slide 23: NSTX-U will explore broad range of fast-ion instability physics and control for ITER and FNSF
Fast-wave heating, 3D fields (NSTX), ECH (DIII-D) also influence AE stability
E. Fredrickson, NF 2014 (submitted)
Mapping of instabilities based on exp’t DATA and TRANSP analysis
ST-FNSF
ITER
NSTX-U
NSTX
blue: stable
red: unstable
M. Podestà, PoP 2013
TAE stability from NOVA-K
  See Podestá whitepaper on fast-ion instability control

## Slide 24: NSTX-U will explore a new high b + low n* transport and turbulence regime
  Will access a variety of drift wave and AE transport mechanisms:
MT
KBM
ITG, TEM, ETG
r/a~0.6-0.7
NSTX-U
Is core ce from stochastic fields, or mid-radius KAW excitation  e-heating?
CAE/GAE
Will tE~1/n* remain valid?
Will microtearing be suppressed?
Will cici,NC & DimpDimp,NC hold?
  See Guttenfelder/Crocker whitepaper on electromagnetic effects in transport

## Slide 25: Self-consistent ST configurations identified for Fusion Nuclear Science Facility (FNSF)
Current drive: bootstrap + NNBI
Neutron wall loading ~1 MW/m2
Tritium breeding ratio (TBR) ~ 1
  Requires breeding blanket near top + bottom of centerstack (CS)
PF coil configuration:
  Strong shaping (k ~ 2.8-3, d ~ 0.5-0.6)
  Flexibility in equilibrium bN and li
  All equilibrium PF coils are ex-vessel
  Long-legged Super-X/snowflake divertor
    qpeak ~ 3-5MW/m2, partially detached
  Breeding in CS end region + vertical maintenance scheme
Exploring plasma start-up options
  Identified locations for electrodes for coaxial helicity injection (CHI) start-up
  Retractable plasma “guns” may be more compatible with FNSF environment
Vertical maintenance
R0 = 1.6m, BT = 3T, IP = 10MA, Pfus = 160MW
Blanket regions

## Slide 26: H98y,2 range of 1.4-2.2 favorable for achieving FNSF-relevant neutron wall loading ≥ 1MW/m2 , fBS < 85% for external control
Power limited for H98y,2 < 1.5
ST-FNSF
A = 1.75
R0 = 1.7m
BT = 2.9T
k, d = 2.8, 0.55
fGreenwald = 0.8
fNICD = 100%
ENNBI = 0.5MeV
PNNBI ≤ 80MW
Stability limited for H98y,2 > 1.6

## Slide 27: NNBI CD efficiency vs. injection tangency radius and energy for R=1.6m using TRANSP
Fixed target parameters in DD
  IP = 7.5MA, bN = 4.5, li = 0.5
  ne / nGreenwald = 0.75, H98y,2 = 1.5
  A=1.75, R=1.7m, BT = 3T, k = 2.8
  Te=5.8keV, Ti=7.4keV
Little current drive benefit from injecting above 0.5MeV
Shine-thru onset for Rtan > 2.4m
Achieve full non-inductive for Rtan > 2m with PNBI = 60MW
  (Note: Pfusion in DT is ~160MW)
0.5MeV NNBI is good choice
(as has been assumed for this configuration)

## Slide 28: Free-boundary TRANSP used to compute 100% non-inductive QDT ~ 2 plasma equilibrium consistent with 0D scalings
TRANSP-ISOLVER (boundary-fit)
Neoclassical ci
Scaled NSTX Te, ne
  Zeff ~ 2-2.5
ne / nGreenwald = 0.65
IP = 9.8MA, BT = 2.9T
H98,y2 = 1.55
bN = 5.9, Wtot = 67MJ
  Wfast / Wtot = 14%
fNICD = 100%, fBS = 65%
ENNBI = 0.5MeV
PNNBI = 80MW
Pfusion = 160MW (50-50 DT)
  ~3% alpha bad orbit loss
Need to further tweak NBI-CD to reduce reversed-shear and maintain qmin > 2

## Slide 29: Ideas to enhance TBR for latest ST-FNSF design
Uniform OB blanket (1 m thick everywhere; no thinning)
Less cooling channels and FCIs within blanket
  Need thermal analysis to confirm
Replace PF coil shield and triangle by blanket (TBD)
Thicker IB VV with internal breeding
Smaller opening to divertor to reduce n leakage
Shield
Triangle
PF Coils

## Slide 30: HTS potentially attractive for making electrically efficient ST* (~10× lower magnet cooling power vs. copper)
Possible missions:
  Steady-state toroidal PMI facility
  ST Pilot Plant (Qeng~1 for weeks/months)
Initial configurations favorable:
  A=1.8 w/ strong shaping: k~2.7, d~0.5
  All equilibrium PF coils outside TF
    No joints needed for HTS TF coils
  Long-legged divertor for qdiv-pk < 5MW/m2
  Vertical port-based maintenance
  WC inboard thermal shield for TF
Many remaining issues:
  HTS lifetime in radiation environment
  Blanket/shield thickness, location, TBR
  Endorse Minervini / Whyte whitepapers for HTS R&D
*This work supported by Tokamak Energy (UK)
R0 = 1.4m, BT = 3.2T, IP = 7-8MA, Pfusion-DT = 100MW