## Slide 1
NSTX-U 5 Year Plan for Macroscopic Stability
J. Berkery (Columbia University)
J.-K. Park, A. Boozer,
S.A. Sabbagh, S. Gerhardt, and R. Raman
for the NSTX Research Team
NSTX-U PAC-33 Meeting
PPPL – B318
February 19-21, 2013
NSTX-U
Supported by
Culham Sci Ctr
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Inst for Nucl Res, Kiev
Ioffe Inst
TRINITI
Chonbuk Natl U
NFRI
KAIST
POSTECH
Seoul Natl U
ASIPP
CIEMAT
FOM Inst DIFFER
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
Coll of Wm & Mary
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Lehigh U
Nova Photonics
Old Dominion
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Tennessee
U Tulsa
U Washington
U Wisconsin
X Science LLC

## Slide 2: Overall objective: establish the physics and control capabilities needed for sustained stability of high performance ST plasmas
Overview of 2014-2018 NSTX-U Five Year Plan
  Thrust 1, Stability:
  Understand and advance passive and active feedback control to sustain macroscopic stability at low collisionality
  Thrust 2, 3D Fields:
  Understand 3D field effects and provide physics basis for optimizing stability through equilibrium profile control by 3D fields
  Thrust 3, Disruptions:
  Understand disruption dynamics and develop techniques for disruption prediction, avoidance, and mitigation in high-performance ST plasmas
MS TSG milestone, FY15 (with ASC):
  Develop physics and operational tools for high-performance discharges
The proposed research is directly coupled to ITER through the ITPA
  Through the experimental outage, the group maintains contributions to five joint experiments and two working groups (see backup slide)
Thrust

## Slide 3: Overall objective: establish the physics and control capabilities needed for sustained stability of high performance ST plasmas
Overview of 2014-2018 NSTX-U Five Year Plan
  Thrust 1, Stability:
  Understand and advance passive and active feedback control to sustain macroscopic stability at low collisionality
    Resistive wall mode (RWM) active control
    New NCC coils and enhanced magnetics
    MHD mode stability physics
  Thrust 2, 3D Fields:
  Understand 3D field effects and provide physics basis for optimizing stability through equilibrium profile control by 3D fields
  Thrust 3, Disruptions:
  Understand disruption dynamics and develop techniques for disruption prediction, avoidance, and mitigation in high-performance ST plasmas
Stability

## Slide 4: Dual-component PID (Br + Bp) and model-based RWM state-space (RWMSC) active control will enable long pulse, high β operation
Year 1 of 5 year plan (FY14):
  Expand/analyze RWMSC for 6 coil control and n>1 physics
Years 4 & 5:
  Utilize model-based active control with the new NCC to demonstrate improved global MHD mode stability and very low plasma disruptivity, producing highest-performance, longest-pulse plasmas
Brn = 1 (G)
Br phase = 0o
Br phase = 90o
Br phase = 180o
t (s)
6
4
2
0
0.0
0.2
0.4
0.6
0.8
1.0
1.2
bN
140124
140125
140126
140127
6
4
2
0
Active n = 1 Bp + BR feedback control
Br phase = 225o
Feedback on
RWMSC
Years 2 & 3:
  Establish Br + Bp active control capability in new operational regime, use with snowflake divertor, compare to theory
  Examine RWMSC with:
    independent actuation of six control coils
    multi-mode control with n up to 3
    rotational stabilization in the controller model
Stability

## Slide 5: NCC will greatly enhance physics studies and control; Enhanced magnetics near divertor will measure multi-modes
Present sensor locations
Multi-mode n = 1 ideal eigenfunction for fiducial plasma
Proposed new sensor locations
mmVALEN
Stability
Years 4 & 5:
  Implement improvements to active feedback of n =1-3 modes via RWMSC control allowed by the partial NCC
  Utilize rotation profile control capabilities allowed by the partial NCC to demonstrate reduced disruptivity by actively avoiding global instability boundaries
Partial NCC
Existing coils
(Next talk by Park will concentrate on NCC)
Mode diagnosis:
  Measure increased amplitude near divertor
  Similar results in ITER simulations
3D analysis shows:
  >2x field increase over present sensors
  Reversal in sign of field perturbation
Significant toroidal phase change would be measured
  Constrain RWMSC, test observer physics

## Slide 6: MHD spectroscopy shows improved stability at high bN/li, and kinetic RWM stability may be enhanced at low n
Years 2 & 3:
  Investigate the dependence of stability on reduced n through MHD spectroscopy; compare to kinetic stabilization theory
Years 4 & 5:
  Utilize rotation control, NCC, and cryo-pump (for reduced n) to change proximity to kinetic resonances for RWM control
Stability
Theory: RWM γ vs. n and wf
Mode stability directly measured in experiment using MHD spectroscopy
  Decreases up to bN/li = 10
  Increases at higher bN/li
  Supports kinetic RWM stability theory
  Decreases with n “on resonance”
  Independent of n “off resonance”
Resonant Field Amplification (RFA) vs. bN/li
unstable
mode
0.0 0.5 1.0 1.5 2.0
Rotation ω/ωexp
0.1
0.0
-0.1
-0.2
-0.3
-0.4
Growth rate gtw
off
resonance
Decreasing
Collisionality
on resonance

## Slide 7: Realizing NSTX-U long-pulse scenarios will require stability of internal MHD modes
Years 2 & 3:
  Use new neutral beam and qmin control to determine increment of qmin above rational values to avoid internal modes
  Measure internal modes non-magnetically with RWMSC and ME-SXR
Years 4 & 5:
  Examine time-evolution of global mode internalization using newly-installed, additional toroidally-displaced ME-SXR diagnostic
  Combine rotation, q, and βN control to demonstrate improved RWM/internal MHD mode stability
Coupled m/n = 1/1+2/1 modes grow when qmin -> 1
NSTX-U: Combinations of NB sources
Stability
(steady-state)
Low frequency mode activity measured with multi-energy soft X-ray

## Slide 8: Overall objective: establish the physics and control capabilities needed for sustained stability of high performance ST plasmas
Overview of 2014-2018 NSTX-U Five Year Plan
  Thrust 1, Stability:
  Understand and advance passive and active feedback control to sustain macroscopic stability at low collisionality
  Thrust 2, 3D Fields:
  Understand 3D field effects and provide physics basis for optimizing stability through equilibrium profile control by 3D fields
    Error field (EF) correction
    Locking and tearing modes with resonant and non-resonant EFs
    Neoclassical toroidal viscosity
  Thrust 3, Disruptions:
  Understand disruption dynamics and develop techniques for disruption prediction, avoidance, and mitigation in high-performance ST plasmas
3D Fields

## Slide 9: Correction of intrinsic error fields (EFs) is critical for performance; Resonant and non-resonant EFs affect locking and tearing stability
Error field threshold vs. locking density (IPEC) for five devices
Year 1:
  Use IPEC to model EFs
Years 2 & 3:
  Assess intrinsic EFs in new machine
  Optimize dynamic EF correction, including n>1 and using 6 SPAs and RWMSC
  Investigate resonant EF effects on tearing mode onset
Years 4 & 5:
  Utilize NCC to understand locking and tearing modes in the presence of resonant and non-resonant EFs
    develop predictability for ITER
3D Fields
Dynamic error field correction in NSTX
Gain

## Slide 10: NSTX-U will investigate neoclassical toroidal viscosity (NTV) at reduced n, which is important for rotation control and ITER
Year 1:
  Analyze existing NSTX NTV data on n dependence and offset rotation
  Develop/benchmark leading theory/codes
    NTVTOK, IPEC, POCA, FORTEC-3D
0.0 0.5 1.0 1.5 2.0
ω/ωexp
1.5
1.0
0.5
n/nexp
9
0
Analytic NTV calculations for n=1 magnetic braking in NSTX
3D Fields
POCA NTV calculations for n=2 and n=3 magnetic braking in NSTX
Years 2 & 3:
  Assess NTV profile and strength at reduced collisionality, and examine the NTV offset rotation at long pulse
  Prepare an initial real-time model of NTV profile for use in initial tests of the plasma rotation control system
Years 4 & 5:
  Utilize NCC, demonstrate low rotation profile operation (ITER-like) in steady-state with closed-loop rotation control

## Slide 11: Overall objective: establish the physics and control capabilities needed for sustained stability of high performance ST plasmas
Overview of 2014-2018 NSTX-U Five Year Plan
  Thrust 1, Stability:
  Understand and advance passive and active feedback control to sustain macroscopic stability at low collisionality
  Thrust 2, 3D Fields:
  Understand 3D field effects and provide physics basis for optimizing stability through equilibrium profile control by 3D fields
  Thrust 3, Disruptions:
  Understand disruption dynamics and develop techniques for disruption prediction, avoidance, and mitigation in high-performance ST plasmas
    Thermal quench, heat loads, and halo currents
    Prediction and avoidance
    Mitigation with MGI
Disruptions

## Slide 12: NSTX-U will provide projections of thermal quench physics, transient heat loads, and halo currents for ITER and FNSF
Year 1:
  Examine thermal loading projections for ITER, including assumptions of axisymmetry
Years 2 & 3:
  Investigate halo current toroidal asymmetry and loading on the center column, using newly installed center column shunt tiles
  Upgrade shunt tile diagnostics for complete coverage of divertor
  Study spatial extent and timing of the heat deposition during VDEs
Years 4 & 5:
  Assess halo current scalings using the full field and current capabilities
  Study 3D and non-axisymmetric effects on the divertor heat loading
Halo current diagnostics
Rapid thermal quench
neutron emission
Soft X-ray
Time [s]
0.410 0.412 0.414
f
300
200
100
0
Halo current rotation
Halo currents: ITER high priority item
Disruptions
= Existing
= Baseline plan
(others incremental)

## Slide 13: Disruption prediction by multiple means will enable avoidance via profile or mode control or mitigation by MGI (1)
Plasma Operations
Avoidance Actuators
PF coils
2nd NBI: q, vf, p control
3D fields (upgraded + NCC):
EF, vf control
n=1-3 feedback
Divertor gas injection
Mitigation
Early shutdown
Massive Gas Injection
EPI (tbp)
Control Algorithms: Steer
Towards Stable Operation
Isoflux and vertical position ctl
LM, NTM avoidance
RWM and dynamic EF control
RWMSC (plasma response)
Divertor radiation control
Disruption Warning
System
Predictors (Measurements)
Shape/position
Eq. properties (b, li, Vloop,…)
Profiles (p(r), j(r), vf(r),…..)
Plasma response (n=0-3, RFA, …)
Divertor heat flux
Loss of Control
General framework & algorithms applicable to ITER
Disruptions

## Slide 14: Disruption prediction by multiple means will enable avoidance via profile or mode control or mitigation by MGI (2)
RWMSC observer
MHD Spectroscopy
Kinetic Physics
Compare mismatch between the RWMSC observer and sensor measurements, and disruption occurence
Evaluate simple physics criteria for global mode marginal stability in real-time
Use real-time MHD spectroscopy while varying rotation, qmin, and βN to predict disruptions
  ITER gas-loading :
  Injection into private flux region with higher assimilation efficiency?
γ contours
Disruptions
Avoidance Actuators
Control Algorithms
Disruption Warning System
Predictors
Mitigation
q, vf , βN control
3D fields, feedback
Resonant Field
Amplification (G/G)
1

## Slide 15: Disruption prediction by multiple means will enable avoidance via profile or mode control or mitigation by MGI (3)
Year 1:
  Evaluate initial simple physics model for marginal stability based on kinetic stability physics
Years 2 & 3:
  Measure plasma stability using MHD spectroscopy vs. key variables and compare to theory
  Compare the mismatch between the RWMSC observer model and sensor measurements, and disruption occurrence
Years 4 & 5:
  Implement real-time evaluations of: kinetic stability model, MHD spectroscopy, and RWMSC observer disruption prediction for input to profile control algorithms
Disruptions
Year 1:
  Model neutral gas penetration of SOL
Years 2 & 3:
  Commission MGI system
  Characterize density assimilation vs. poloidal location
Years 4 & 5:
  Trigger the MGI system based on warning of an impending disruption
Predictors
Mitigation

## Slide 16: Summary of NTSX-U 5 year plan for Macroscopic Stability
MS research is establishing the physics understanding and control capabilities needed for sustained stability of high performance ST plasmas
  In unexplored ST operational regime: low n, high β, low li, long pulse
NSTX-U will make critical contributions in the areas of:
  Advancement of stability physics and control to sustain macroscopic stability at low collisionality
  Understanding 3D field effects and providing the physics basis for profile control by 3D fields
  Understanding disruption dynamics and developing techniques for disruption prediction, avoidance, and mitigation
MS research in NSTX-U will be greatly enriched, and have significantly greater impact on ITER, by having the NCC coils

## Slide 17: Backup

## Slide 18: NSTX-U macroscopic stability research is directly coupled to ITER through the ITPA
Through the experimental outage, our group:
  Maintains contributions to five joint experiments and two working groups
    leads the MDC-2 joint experiment / analysis on RWM physics
    co-leads the Working Group 7 effort on aspects of active mode control
  Communicated NSTX research bi-annually at each ITPA MHD Stability group meeting for many years
  Led two elements of the recent ITPA Integrated Plasma Control Working Group study, led by Dr. Joseph Snipes of ITER
    also contributed with direct calculations for ITER on RWM and error field control associated with this effort.
 | MHD |  | 
MDC-2 | Joint experiments on resistive wall mode physics | MDC-17 | Active disruption avoidance
MDC-8 | Current drive prevention/stabilization of NTMs | MDC-18 | Evaluation of axisymmetric control aspects
MDC-15 | Disruption database development |  | 
NSTX-U stability research plans expand this effort in the coming five year period.

## Slide 19: Dual component (BR, Bp) PID and state space control
t (s)
40
0
80
0.56
0.58
0.60
t (s)
0.56
0.58
0.60
d
B
p
90
Dt (s) (model)
phase = 180o
phase = 90o
phase = 0o
Calculation of Br + Bp control (VALEN)
2.4
2.6
2.8
0.0
0.04
0.08
0.12
Brn = 1 (G)
Br phase = 0o
Br phase = 90o
Br phase = 180o
t (s)
6
4
2
0
0.0
0.2
0.4
0.6
0.8
1.0
1.2
bN
140124
140125
140126
140127
6
4
2
0
Active n = 1 Bp + BR feedback control
Br phase = 225o
Feedback on
RWM State Space Controller
No NBI port
3D wall,
ports,
mode currents
Sensor Differences (G)
Measurement
Controller
Measurement
Controller
With 3D NBI port
Inclusion of 3D mode and wall detail improves control
d
B
p
90
Model validation and predictive capability:
VALEN code feedback predictions
Brn = 1 (G)

## Slide 20: RWM active control capability increases as partial NCC coils are added
Partial 1x12 NCC coil set significantly enhances control
  Present RWM coils: active control to bN/bNno-wall = 1.25
  NCC 1x12 coils: active control to bN/bNno-wall = 1.54
Existing
RWM
coils
NCC upper
1x12 coils
Using present midplane RWM coils
Partial NCC 1x12 (upper), favorable sensors

## Slide 21: RWM active control capability increases further with full NCC
NCC 2x12 with favorable sensors, optimal gain
NCC 2x6 odd parity, with favorable sensors
Full NCC coil set allows control close to ideal wall limit
  NCC 2x6 odd parity coils: active control to bN/bNno-wall = 1.61
  NCC 2x12 coils, optimal sensors: active control to bN/bNno-wall = 1.70
Existing
RWM
coils
NCC full
2x12 coils
NCC partial
2x6 coils

## Slide 22: Multi-mode theory shows high amplitude near divertor, enhanced magnetics proposed
Present sensor locations
Multi-mode n = 1 ideal eigenfunction for fiducial plasma
Proposed new sensor locations
mmVALEN
code
Global mode diagnosis: measure theoretically increased amplitude in the divertor at high βN
3D analysis of candidate sensor positions show >2x increase in signal over present sensors
Significant toroidal phase change would be measured
  Constrain RWM state space controller
toroidal angle
poloidal angle
Present sensor positions
outboard midplane
center
column
new sensors
n = 1 mode
new sensors
Multi-mode physics
  Implement in RWMSC
  Validate theory predictions with measurements
  Found similar results in ITER simulations

## Slide 23: 3D analysis of extended MHD sensors show significant mode amplitude off-midplane, approaching divertor region
New sensor locations (includes
one new location above midplane)
n = 1 ideal eigenfunction for high beta plasma
Present sensor locations
Z(m)
R(m)
BR sensors (nominally normal, Bnorm)
Bp sensors (nominally tangential, Btan)
Bnorm(normalized)
q (deg)
Model characteristics
  New 3D model of divertor plate
  3D sensors with finite toroidal extent; n*A of existing sensors
Results summary
  Field amplitude increases >2x with new sensors
  Perturbed field reversals observed with new sensors
  Signals sufficient with plasma shifted off-midplane
q
Bnorm vs. theta (normalized to present Br sensors)
q (deg)
F = 0 deg
F = 0 deg
Present sensors
Zplasma = -10 cm
= -5 cm
= 0 cm

## Slide 24: Stability control improvements significantly reduce unstable RWMs at low li and high bN; improved stability at high bN/li
Resonant Field Amplification (RFA) vs. bN/li
unstable
mode
Unstable RWM
Stable / controlled RWM
Disruption probability reduced by a factor of 3 on controlled experiments
  Reached 2 times computed n = 1 no-wall limit of bN/li = 6.7
Lower probability of unstable RWMs at high bN/li
Mode stability directly measured in experiments using MHD spectroscopy
  Stability decreases up to bN/li = 10
  Stability increases at higher bN/li
  Presently analysis indicates consistency with kinetic resonance stabilization

## Slide 25: Internal modes may limit long-pulse scenarios; kinetic RWM stability may be enhanced at low n
0.0 0.5 1.0 1.5 2.0
Coupled m/n = 1/1+2/1 modes grow when qmin approaches 1
  EPM or ELM triggers cause modes to onset at larger qmin.
  “triggerless” internal kinks as qmin -> 1
Expectations at lower n:
Mode stability directly measured in experiment using MHD spectroscopy
  Decreases with n “on resonance”
  Independent of n “off resonance”
Experiment: RFA vs n
Theory: RWM γ vs. n and wf
on resonance
off resonance
off
resonance
on resonance
  More stability on resonance almost no effect off-resonance
Experiments measuring global stability vs. n support kinetic RWM stability theory
Model validation and predictive capability:
MISK code RWM stability calculations
Collisionality
Unstable
RWMs
n = 1 RFA (G/G)
1.5
1.0
0
.5
0.0
n
ii
[kHz]
0
1
3
2
ω/ωexp
0.1
0.0
-0.1
-0.2
-0.3
-0.4
gtw
NBCD can determine the required increment of qmin above rational values to avoid internal modes
Various combinations of neutral beam sources

## Slide 26: Internal kink/ballooning modes must be measured via non-magnetic means
Non-magnetic measurement is also important for mode control systems to be used in future devices with high neutron fluence
The RWMSC can determine how incorrect the observer is in reproducing the measured magnetic flux
  Can be used as a criterion as input to a disruption warning system.
Multi-energy soft X-ray can measure low frequency mode activity
  used to determine mode amplitude and in conjunction with the external magnetic sensors to determine the degree to which the mode is internal

## Slide 27: Realizing NSTX-U long-pulse scenarios will require stability of internal and external MHD modes
Years 4 & 5:
  Utilize rotation control, NCC, and cryo-pump (for reduced n) to change proximity to kinetic resonances for RWM control.
  Combine rotation, q, and βN control, and use ME-SXR (non-magnetic) to demonstrate improved RWM/internal MHD mode stability.
Coupled m/n = 1/1+2/1 modes grow when qmin -> 1
NSTX-U: Combinations of NB sources
Years 2 & 3:
  Investigate the dependence of stability on reduced n through MHD spectroscopy; compare to kinetic stabilization theory.
Years 2 & 3:
  Use new neutral beam and qmin control to determine increment of qmin above rational values to avoid internal modes
Stability
0.0 0.5 1.0 1.5 2.0
on resonance
ω/ωexp
0.1
0.0
-0.1
-0.2
-0.3
-0.4
gtw
off
resonance
Decreasing
Collisionality
(steady-state)
Experiments measuring global stability vs. n support kinetic RWM stability theory
Theory: RWM γ vs. n and wf

## Slide 28: Understanding neoclassical toroidal viscosity (NTV) is crucial for rotation control
NTVTOK code:
  Shaing theory NTV computation including ion and electron effects
  Comparison to experiment of NTV in all collisionality regimes
A new δf guiding-center particle code, POCA, was developed to investigate neoclassical transport in perturbed tokamaks.
  solves the Fokker-Planck equation with non-axisymmetric magnetic field perturbations
“Investigate magnetic braking physics to develop toroidal rotation control at low n”
Model validation and predictive capability: NTV calculations with multiple codes, comparison to experiments
R(12-1)
POCA NTV calculations for n=2 and n=3 magnetic braking in NSTX
Analytic NTV calculations for (a) n=1 and (b) n=3 magnetic braking in NSTX, as a function of collisionality and rotation
0.0 0.5 1.0 1.5 2.0
ω/ωexp
0.0 0.5 1.0 1.5 2.0
ω/ωexp
1.5
1.0
0.5
n/nexp
1.5
1.0
0.5
n/nexp
(a) n=1
(b) n=3
9
0
2
0

## Slide 29: Correction of intrinsic error fields is critical for studies of 3D field physics and for performance
The perturbed n=1 field (IPEC) from intrinsic error fields in NSTX
Various successful error field correction schemes in NSTX
Dynamic error field correction (green)
  sustains βN above the no-wall limit
  sustains substantial toroidal rotation
NSTX-U will have a different error field
  Identification of error field in first year of operation
  measure vacuum fields; revise models
  Perform n=1,2 compass scans with 6 independent SPAs.
  RWMSC for dynamic error field correction
Predictive capability:
IPEC model of error fields

## Slide 30: Resonant and non-resonant error fields affect locking and tearing stability
Error field threshold vs. locking density (IPEC) for five devices
Change of the βN threshold of the NTM with rotation
Studies of intrinsic error fields focus on compensation of the resonant component to avoid locking
  Error field threshold at locking will be used to predict the tolerance of error fields in ITER
Tearing mode onset modified by both resonant and non-resonant error fields
  βN threshold will be decreased by non-resonant error field magnetic braking
Goal: Understand locking and tearing modes in the presence of resonant and
non-resonant error fields, and develop predictability for FNSF and ITER

## Slide 31: Disruption mitigation technologies that will benefit the ITER design are being prepared
MGI research will assess gas penetration efficiency by injection at different poloidal locations
NSTX-U can offer new insight by
  Reducing the amount of gas
  Injecting gas into the private flux and lower x-point regions of divertor to determine if these are more desirable locations for MGI.
Predictive capability: Modeling using DEGAS-2 is quantifying the gas penetration past the SOL for NSTX-U
The EPI is capable of delivering:
  A large particle inventory
  All particles at nearly the same time
  Particles tailored to contain multiple elements in different fractions and sizes
  Tailored particles fully ionized only in higher current discharges (to control current quench rates)
Well suited for long stand-by mode operation
A novel mitigation technology, an electromagnetic particle injector (EPI), will be used to terminate plasmas
Rail gun electrodes
Particulate container projectile
Cone for shattering

## Slide 32: Understanding of thermal quench physics and transient heat loads is critical for projections
Examining assumptions:
  How much stored energy?
Typically only 15-20% of the stored energy remains in a late flat top disruption in NSTX
Example of rapid disruption with high stored energy
 | NSTX-U | ITER | ST-Pilot | Power Reactor
Thermal Loading [MJ m2 s-1/2] | 15 | 540 | 768 | 2061
0.408 0.410 0.412 0.414
f
300
200
100
0
Time [s]
  Halo currents are non-axisymmetric, but are heat fluxes?
rapid thermal quench
neutron emission [arb.]
Soft X-ray
Proposed expansion of the NSTX-U shunt tile diagnostic set

## Slide 33: Disruptivity studies and warning analysis of NSTX database are being conducted for disruption avoidance in NSTX-U
Disruption warning algorithm shows high probability of success
  Based on combinations of single threshold based tests
Results
  ~ 98% disruptions flagged with at least 10ms warning, ~ 6% false positives
  False positive count dominated by near-disruptive events
Disruptivity
Physics results
  Low disruptivity at relatively high bN ~ 6; bN / bNno-wall(n=1) ~ 1.3-1.5
    Consistent with specific disruption control experiments, RFA analysis
  Strong disruptivity increase for q* < 2.5
  Strong disruptivity increase for very low rotation
Warning Algorithms
All discharges since 2006
bN
li
q*

## Slide 34
KSTAR: equilibrium operating space 2009 –11
(evolution of > 130 discharges) + new results
New MP2012-04-23-021
session 1 session 2+
Plasmas have passed the predicted “closest approach” to the n = 1 ideal no-wall stability limit: li = 0.7, bN = 2.5
DIII-D: RFA of ~ 20Hz n = 1 increase to very high levels while βN increases and rotation decreases
Rapidly rotating n = 1 appears (TM?), clamps RFA amplitude
MS group continues strong collaborations with other devices such as KSTAR, DIII-D, and ITER team
ITER: RWM passive growth rates by CarMa and VALEN

## Slide 35: Many important computational codes are used for theory-experiment comparison on NSTX-U
Code | Description | Scope | Improvements
VALEN | Models currents in structures with thin shell finite elements | RWM active feedback simulation, growth rate prediction with 3D walls | Multi-mode effects, study extra time delay in plasma model
RWMSC | Resistive wall mode state-space controller computations | Generate control matrices for real-time controller, and offline physics studies | Generalization for partial actuator availability, n > 1 and multi-mode spectrum
NTVTOK | Shaing theory NTV computation including ion and electron effects | Calculation for comparison to experiment of NTV in all collisionality regimes | Continued implementation of NTV models, guided by experiment
DCON | Ideal MHD stability code | Ideal Kink stability analysis with and without the wall up to n=6 | Resistive layer physics across rational surfaces (Resistive DCON)
MISK | Modifications to ideal stability by kinetic effects | Calculation of resistive wall mode stability | Improved model of energetic particle, anisotropy effects
DEGAS-2 | Monte Carlo code to compute transport of neutral atoms | Calculation of neutral gas penetration through SOL | Include multiple gas species Use exact NSTX-U SOL conditions from UEDGE
EFIT | Equilibrium reconstruction code | Between-shots equilibriumreconstruction | Higher resolution, auto best level, new diagnostics
IPEC/GPEC | Ideal and general perturbed equilibrium with 3D fields | Plasma response, locking, and NTV studies with 3D fields | General force balance equation including general jump conditions
MARS-K | Self-consistent kinetic stability calculation | Calculation of RWM stability and plasma response to perturbation | Inclusion of energy dependent collisionality for NTV calculation
M3D-C1 | Implicit resistive and 2-fluid MHD code | Linear and nonlinear MHD stability | Neoclassical terms, resistive wall being added
FORTEC-3D |  |  | 
POCA | δf guiding-center orbit code | Calculation of neoclassical transport, perturbed pressures and NTV | Improved numerical scheme to enhance computation speed

## Slide 36: Many important computational codes are used for theory-experiment comparison on NSTX-U
Code
VALEN
RWMSC
NTVTOK
DCON
MISK
DEGAS-2
EFIT
IPEC/GPEC
MARS-K
M3D-C1
FORTEC-3D
POCA

## Slide 37
FY13
14
15
16
17
18
Physics
Optimize shaping, RWM/TM control (n≥1 using the second SPA), validate internal mode physics and RMW kinetic physics
Optimize error field correction (n≥1), dynamic correction, and understand NTV physics in reduced v* and controlled rotation
5 year plan period
Study halo currents, disruption loads, and precursors, and test MGI or other mitigation techniques
Optimize and combine rotation profile and β-feedback control using NCC, to improve stability and for fully non-inductive operation
Understand non-resonant error field effects using NCC, NTV effects vs. rotation profile on transport, utilize 3D field to improve stability
      Provide FSNF/Pilot projection,
      Integrate MS control to improve RWM/TM/ELM/ internal mode stability, disruption avoidance, with disruption mitigation protection
Tools
Real-time velocity measurement and MSE, toroidally displaced ME-SXR
Utilize 3D field for rotation (profile) and β-feedback control, to improve RWM/TM/internal mode stability
5 year goal
Diagnostics
Theory
Facility
Plasma Control
Integrate and validate 3D equilibrium, stability, and transport codes
5 year plan period
Investigate avoidance scenarios and couple to mitigation techniques
Integrate MS control with disruption avoidance and mitigation
Utilize equilibrium reconstruction, and transport and stability codes
RWM state-space control (n≥1), error field control, snowflake divertor control
Non-axisymmetric Control Coil (NCC), enhanced magnetics, cryopump for low v*
Thrust #1
Thrust #2
Thrust #3
Real-time MPTS, X-ray imaging spectrometer,
Internal dB measurement from MSE,
enhanced magnetic sensors
Expanded shunt tile measurements, disruption load diagnostics
Gas penetration dynamics
Disruption simulation
Second switching power amplifier (SPA),
MGI disruption mitigation system
2014-18 Macroscopic Stability Research Timeline

## Slide 38: Thrust MS-1: Understand and advance passive and active feedback control to sustain macroscopic stability
Vary q (via BT and 2nd NBI), plasma rotation (via 2nd NBI and NTV), beta, collisionality (via Li and cryo) to investigate passive stability thresholds for locked modes, RWM, NTM
Quantify disruption frequency reduction using active mode control (RWM state-space controller) + profile control
  In particular, investigate interplay/compatibility between fast (~ms) mode growth (RWM) and feedback control and slower (~0.05-1s) equilibrium profile evolution and control (rotation, q, beta)
Optimize passive stability and state-space control to minimize control power needs for ITER, next-steps

## Slide 39: Thrust MS-2: Understand 3D field effects to provide basis for optimizing stability thru rotation profile control by 3D fields
Study 3D field effects on rotation as a function of:
  Plasma collisionality as density/collisionality control is improved
  Torque deposition profile using 2nd NBI
  Relative strength of resonant vs. non-resonant rotation damping
    Enabled by off-midplane non-axisymmetric control coils (NCC) to vary poloidal spectrum to vary resonant/non-resonant at fixed n-number
Utilize independent control of n=1,2,3 fields from midplane coils - enabled by 2nd switching power amplifier (SPA)
  Study non-resonant field effects on resonant error field correction
  Develop the physics basis for control of toroidal rotation through magnetic braking while also controlling error fields and RWM
Use combination of 2nd NBI + 2nd SPA + partial-NCC + collisionality to vary, understand, control toroidal rotation

## Slide 40: Thrust MS-3: Understand disruption dynamics, develop disruption detection, avoidance, and mitigation
Explored low-f, n=1 resonant field amplification (RFA) as a means to detect approach to global stability limit
  If effective, real-time RFA detection will be implemented and coupled to control of bN + rotation + q to keep plasma in stable regime
Measure dynamics of NSTX-U disruptions and develop models to improve understanding of:
  Heat loading from disruptions, dynamics of the thermal quench, and the generation of halo currents
Develop and explore disruption mitigation:
  Examine poloidal angle dependence of Massive Gas Injection (MGI) mitigation efficiency/assimilation
    Model/interpret SOL gas penetration with DEGAS-2
  Explore novel electromagnetic particle injector (EPI) (rail-gun)
    Potential to rapidly deliver large quantities of material to the plasma

## Slide 41: Global mode stability at lower collisionality
Years 2 & 3:
  Assess βN and q stability limits at the increased aspect ratio of NSTX-U, with new shaping control and off-axis NBI.
  Utilize off-axis NBI to produce initial investigation determining the effect of pressure, q, and vϕ profile variations on RWM and NTM stability
  Investigate the dependence of stability on reduced n through MHD spectroscopy, and compare to kinetic stabilization theory.
Years 4 & 5:
  Utilize rotation control and NCC to alter rotation shear for improved NTM control and change proximity to kinetic resonances for RWM control.
  Combine rotation, q, and βN control to demonstrate improved RWM/TM/internal MHD mode stability in 100% non-inductive plasmas.

## Slide 42: Dual-field component active RWM control and improved mode discrimination at high normalized beta
Years 2 & 3:
  Establish dual field component n = 1 active control capability in new NSTX-U operational regime with 6 independent SPAs and more standard use of the snowflake divertor.
  Attempt initial control of internal MHD modes that appear at low density during current ramp-up.
Years 4 & 5:
  Characterize n = 1 – 3 global mode activity using enhanced RWM sensor set, and compare to multi-mode spectrum.
  Employ superior multi-mode settings for n = 1 and 2 active control with the partial NCC to demonstrate improved global MHD mode stability in 100% non-inductive plasmas.

## Slide 43: Model-based RWM state-space controller for active RWM control
Year 1:
  Expand RWMSC real-time control software to allow independent actuation of 6 RWM control coils, and a general sensor input scheme.
Years 2 & 3:
  Examine effectiveness of RWM model-based state space control with:
    independent actuation of six control coils
    multi-mode control with n up to 3
    plasma rotation-induced stabilization in the controller
Years 4 & 5:
  Examine superior RWMSC settings and multi-mode active control with n up to 3, enhanced magnetics, and the partial NCC to demonstrate improved global MHD mode stability in 100% non-inductive plasmas.

## Slide 44: Internal kink/ballooning mode control scoping study
Years 2 & 3:
  Determine the degree of global mode internalization by comparing diagnosis by magnetic and SXR means as a function of proximity to the mode marginal stability point.
Years 4 & 5:
  Examine mode internalization with new toroidally-displaced ME-SXR diagnostic

## Slide 45: Use of NCC for mode control and integration of stability control elements
Years 4 & 5:
  Determine improvements to kinetic RWM and NTM stability possible by utilizing expanded capability for non-resonant rotation control by the enhanced 3D field spectrum afforded by the partial NCC
  Implement improvements to active feedback of n > 0 modes via PID and RWMSC control allowed by the partial NCC.
  Utilize rotation profile control capabilities allowed by the partial NCC to demonstrate reduced disruptivity by actively avoiding global instabilities.

## Slide 46: Error field and island dynamics
Years 2 & 3:
  Optimize and combine dynamic error field correction with intrinsic error field correction, including n>1 and using 6 SPAs.
  Investigate resonant error field effects on tearing mode onset
Years 4 & 5:
  Utilize NCC to understand locking and tearing modes in the presence of resonant and non-resonant error fields, and develop the predictability for FNSF, ST-Pilot, ITER.

## Slide 47: Neoclassical toroidal viscosity at reduced collisionality and applicability to an ST-FNSF and ITER
Year 1:
  Analyize existing NSTX data from experiments investigating NTV
  Update all NTV analysis tools for NSTX-U capabilities
Years 2 & 3:
  Assess NTV profile and strength as a function of plasma collisionality, and examine the NTV offset rotation.
  Prepare an initial real-time model of NTV profile for use in initial tests of the plasma rotation control system
Years 4 & 5:
  Demonstrate low rotation profile operation in steady-state with closed-loop rotation control, producing plasma rotation most applicable to ITER and utilizing the partial NCC.

## Slide 48: Understanding neoclassical toroidal viscosity (NTV) physics to control rotation braking
Years 2 & 3:
  Investigate NTV physics with enhanced 3D field spectra and NBI torque profile at increased pulse lengths, and NTV behavior at reduced ν* regime.
Years 4 & 5:
  Study NTV physics in the lowest ν* regimes.
  Optimize vϕ feedback control in regimes of high non-inductive fraction to improve RWM/TM stability.
  Fully explore the rotation control system to maintain the optimized vϕ and its profiles for microscopic and macroscopic instabilities.

## Slide 49: Stability physics for disruption prediction
Year 1:
  Evaluate simple physics criteria for the approach to global mode marginal stability based on kinetic stability physics
Years 2 & 3:
  Construct an MHD spectroscopy database to determine the measured variation of global mode stability as a function of key parameters.
  Compare the mismatch between the RWMSC observer model and sensor measurements, and the occurrence of plasma disruptions
Years 4 & 5:
  Implement a real-time evaluation of a simple global mode marginal stability model including important parameters available in real-time
  Examine real-time MHD spectroscopy in determining global mode stability boundaries for input to stability profile control systems
  Improve disruption prediction using the RWMSC observer by the addition of the newly-installed expanded RWM sensor set.

## Slide 50: Stability control for disruption avoidance
Years 2 & 3:
  Perform experiments using open-loop plasma rotation, current profile, and energetic particle control to demonstrate the ability to avoid stability boundaries based on kinetic RWM stabilization models.
  Implement and test initial disruption avoidance using the RWMSC observer model in real-time.
Years 4 & 5:
  Implement simple global mode marginal stability model, single mode RFA amplitude and RWMSC observer model as input to profile control systems and disruption warning system.
  Combine disruption avoidance control with simultaneous use of n > 0 active feedback and the partial NCC, determining physics implications of this combination and potential control conflicts.

## Slide 51: Rapid shutdown techniques via mass injection for disruption avoidance
Years 2 & 3:
  Commission MGI system and diagnostics, test EPI capsule injection
  Investigate high-Z gas fractions, gas transit times, the amount of gas required, and symmetry of the radiated power profile
Years 4 & 5:
  Assess reduction in divertor heat loads and reduction in divertor halo currents for variations in the gas injection location.
  Trigger the MGI or EPI systems based on sensor provided data on an impending disruption.

## Slide 52: Disruption physics
Years 2 & 3:
  Investigate halo current loading on the center column, using newly installed center column shunt tiles.
  Upgrade shunt tile diagnostics for complete coverage of divertor.
  Assess total halo current fraction, toroidal structure, and poloidal width.
  Study spatial extend and timing of the heat deposition during VDEs
Years 4 & 5:
  Assess halo current scalings using the full field and current capabilities
  Assess disruption power balance for the different disruption types
  Utilize upgraded 3D magnetics for comparison of helical distortions and local halo currents.
  Study 3D and non-axisymmetric effects on the divertor heat loading.