## Slide 1
Progress and Plans for Non-inductive Ramp-up/Sustainment Modeling
Francesca Poli
for the NSTX-U team
NSTX-U PAC-35 Meeting
PPPL – B318
June 11-13, 2013
NSTX-U
Supported by
Culham Sci Ctr
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Inst for Nucl Res, Kiev
Ioffe Inst
TRINITI
Chonbuk Natl U
NFRI
KAIST
POSTECH
Seoul Natl U
ASIPP
CIEMAT
FOM Inst DIFFER
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
Coll of Wm & Mary
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Lehigh U
Nova Photonics
Old Dominion
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Tennessee
U Tulsa
U Washington
U Wisconsin
X Science LLC

## Slide 2: NSTX-U experiments will guide development of ST-FNSF strategies for non-inductive ramp-up and sustainment
Develop and understand non-inductive start-up and ramp-up (overdrive) to project to ST-FNSF with small/no solenoid
  Contributes to the finalization of the EC system design
  Contributes to optimized use and synergy of RF and NBI in ramp-up
Demonstrate 100% non-inductive sustainment at performance that extrapolates to ≥ 1MW/m2 neutron wall loading in FNSF
  Contributes to the optimization of profile evolution and control in the ramp-up to access advanced operation
“the gap in demonstrating non-inductive startup and ramp-up is larger than the gap in demonstrating 100% non-inductive sustainment in the ST” [PAC33]
Also emphasized in FESAC TAP 2008, RENEW 2009

## Slide 3: Detailed modeling of ramp-up phases informs plans for dedicated experiments in FY15-16
3
~0.75-1
~0.3-0.4
~0.5
I [MA]
Time
NBI + bootstrap
NBI + FW + bootstrap
EC heating
FW current
CHI
(R.Raman)
HHFW
ECH
NBI
Challenges in ramp-up modeling/experiments
Heat CHI target plasma to maximize efficiency of external H/CD sources
Combine RF and NBI, aim at best synergy of sources
Minimize beam losses at low current => density control, heat start-up plasma
Optimize NBI source combination for profile control
Tailor kinetic and current profiles to access target flattop plasmas (see Gerhardt)
(and do this while maintaining the discharge in the MHD stable operational space)
Up to 15MW
1MW
4MW
P [MW]

## Slide 4: H/CD sources are evolved self-consistently in TRANSP with free-boundary equilibrium solver (Isolver)
Use NSTX discharges to build-up discharge in NSTX-U geometry
Addressing challenges along the way:
  Self-consistent evolution of equilibrium and pressure evolution during startup with external H/CD
  Confinement level typically H98,y2~1.0-1.2
  Thermal transport => either predictive or scale analytic temperature profiles (use MMM95 in RF phase, analytic Te and ci=ce in NBI phase)
  Particle transport => density profiles are prescribed (0.5-1.0 nGw)
ECRH: ray tracing codes (TORAY-GA)
HHFW: full wave code TORIC with Fokker-Planck treatment for resonant species
NBI: Monte-Carlo orbit NUBEAM

## Slide 5: Time-dependent simulations of EC heating in startup plasma support FY15 facility milestone for ECH system design
~0.75-1
~0.3-0.4
~0.5
Time
NBI + bootstrap
NBI + FW + bootstrap
CHI
(R.Raman)
HHFW
NBI
Up to 15MW
4MW
P [MW]
1MW
EC heating
FW current
ECH
5
Without electron heating, CHI current would decay within 5-10ms
expect it to be difficult to couple FW directly to CHI-only target
Planned EC-EBW system: 1MW power @28GHz, O-mode heating (see Perkins)
The role of EC is to heat CHI plasma to a level where FW and/or NBI can be efficiently absorbed
I [MA]

## Slide 6: Planned ECH system needed to heat CHI targets from 10eV to above 500eV in 30ms
Ref: NSTX CHIOH+NBI H-mode discharge #142140 (Raman, NF2013)
First-pass absorption in low density startup plasma
Simulations confirm that HHFW cannot efficiently heat CHI-only target, but HHFW can heat ECH-heated CHI target (see lower right)
EC accessibility @ t<100-150ms depending on density
#142140
NOTE: preliminary results

## Slide 7: Detailed modeling of ramp-up phases highlights requirements for dedicated experiments in FY15-16
7
Select target scenario (Menard et al, NF 2012, Table I, Gerhardt NF 2012)
100% NICD (1T/1MA) with 10MW of NBI @0.5-1.0nG, bootstrap fraction 0.61-0.85
Use reference discharge #142305, k~2.55, li(1)~0.5, A~1.55 (Gerhardt, NF 2011)
Assume initial target of 300kA and plasma heated at ~400eV (needed for HHFW)
Use 4MW of HHFW and 10MW of NBI at 80keV
HHFW drives L-H transition and current at low density where NBI shine-thru large
NBI second beam-line ramps current to the target plasma
~0.75-1
~0.3-0.4
~0.5
Time
NBI + bootstrap
NBI + FW + bootstrap
CHI
(R.Raman)
HHFW
NBI
Up to 15MW
4MW
P [MW]
1MW
EC heating
FW current
ECH
I [MA]

## Slide 8: 2nd NB line can ramp-up current from HHFW-heated plasma and sustain stationary 900kA
HHFW used @ t<0.5 to ramp to ~400kA
ne,lin = 8x1019 m-2 -> ~900kA non-inductive, ~60% bootstrap
bT~7%, bP~6%, bFAST/bTOT~0.25-0.35, H98~1.2 (t98~70ms)
Isolver equilbrium
t = 3.5s
k~2.50
d~0.75

## Slide 9: Results sensitive to Greenwald fraction, which affects the beam pressure and shape control
Second beam line has high efficiency
Peaked deposition profiles at low density (~50%nG)
=> elongation decreases, li increases
=> q(0) drops below 1 in the flattop
=> q(0) drops below 1 during the HHFW phase
k
Li(1)
q(0)
NBI phase needs optimization: broad deposition
Optimize outer gap
Beam modulation
Early phase needs optimization: elevate q(0)
Use beams early in the discharge (with RF)
t=3.5s
nG
0.5 nG
ci=ce

## Slide 10: Goals FY15: validate simulations for non-inductive startup and ramp-up
Modeling:
ECRH: TSC CHI startup simulations as initial conditions to improve time-dependent predictions using ECRH (with SFSU-TSG)
Simulate EC+NBI and EC+FW combinations for CHI target
HHFW: Explore effect of FW phasing on scenarios (with WEP-TSG)
NBI: scan density and temperature and source energy to optimize deposition
Experiments:
NBI: assess NBI injection and CD profiles in targets with 0.5-1.0MA, 0.75T with density of 0.5-1.0 Greenwald (R15-2)
Use results from R15-1 (H-mode characteristic, pedestal, see Diallo) to improve predictions of H-mode ramp-up plasmas with NBI.
=> experiments, including National Campaign on DIII-D to constrain simulations of NSTX-U overdrive ramp-up discharges at 1T with inductive seeding to guide experiments in FY16.

## Slide 11: Goals FY16: guide ramp-up experiments with inductive seeding
  R16-3: Assess FW coupling to NBI and modeling (with WEP and ASC TSGs)
  Optimize FW phasing to maximize electron heating (at 300-500kA)
  use FY15 simulations to guide experiments and results for model validation.
R16-4: Develop high-non-inductive fraction NBI H-modes for ramp-up and sustainment.
Obtain full non-inductive target in flattop phase with ohmic seeding, then
Clamp OH coil current to constant value progressively earlier in time
Attempt use of FW (phasing for electron heating) and NBI at low current on CHI target with inductive seeding (support for SFSU-TSG)

## Slide 12: Summary
Substantial progress in ramp-up modeling using TRANSP
  Compute RF NBI absorption and CD self-consistently for the first time
  Use experimental discharges from NSTX for projection
  Simulations of the startup phase present computational challenges
  Density control is crucial to the scenario solution and to the evolution in the ramp-up and flattop sustainment.
Future work:
  more physical constraint on surface voltage, use coil currents to drive the simulation and control the discharge (shape, gaps, aspect ratio)
  Specification of Greenwald fraction vs time in TRANSP simulations
  Sensitivity studies on choice of thermal transport models

## Slide 14: MMM95 reproduces average amplitude and peaking of electron temperature profile during the HHFW phase
#138498
#138506
#140353
HHFW only, 300kA
High density
HHFW only, 300kA
low density
HHFW+NB
Profiles averaged over the heating phase
MMM95 reproduces the average amplitude and peaking in HHFW discharges and in discharges with HHFW+NBI.
Ion temperature overestimated in NBI discharges
Electron temperature too peaked in NBI discharges

## Slide 15: Optimal range of 350-400kA for non-inductive current from HHFW in startup plasma conditions
NSTX experiments demonstrated sustainment of 300kA with 1.5MW of HHFW, with 80% bootstrap current
However, we aim at using HHFW at startup
  Density is low
  Coupling might be an issue
Absorption of FW to fast ions is an issue
=> avoid to superpose FW and NBI in simulations

## Slide 16: Large beam shine-thru at low density prevents use of beam on CHI-only target
Shine-thru can be reduced by controlling density at low current
Might be an issue for EC accessibility
Low driven current => need to optimize window before 0.3s for external current drive

## Slide 17: Procedure for non-inductive ramp-up experiments
Start with a fully inductive discharge
Optimize non-inductive fraction (density is critical)
Clamp ohmic at progressively earlier times
Clamp ohmic at progressively earlier times