## Slide 1
Progress and Plans for Fast Wave and Electron Cyclotron Heating Research
NSTX-U
Supported by
Culham Sci Ctr
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Inst for Nucl Res, Kiev
Ioffe Inst
TRINITI
Chonbuk Natl U
NFRI
KAIST
POSTECH
Seoul Natl U
ASIPP
CIEMAT
FOM Inst DIFFER
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
Coll of Wm & Mary
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Lehigh U
Nova Photonics
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Tennessee
U Tulsa
U Washington
U Wisconsin
X Science LLC
Rory Perkins
Gary Taylor, Nicola Bertelli, Mario Podestà, Nikolai Gorelenkov
for the NSTX-U Research Team
NSTX-U PAC-35 Meeting
PPPL – B318
June 11-13, 2014

## Slide 2: Outline
Motivation for Fast Wave (FW) & (future) Electron Cyclotron (EC) and Electron Bernstein Wave (EBW) research
Progress during the past year
Research goals and plans for FY 2015 & 2016
Summary
2

## Slide 3: Outline
Motivation for Fast Wave (FW) & (future) Electron Cyclotron (EC) and Electron Bernstein Wave (EBW) research
Progress during the past year
Research goals and plans for FY 2015 & 2016
Summary
3

## Slide 4: RF research in Five-Year Plan supports non-inductive (NI) operation
30 MHz FW and 28 GHz EC/EBW heating research support two high-level NSTX-U goals:
  Developing and understanding NI plasma current start-up and ramp-up in order to project to a ST-FNSF
  Demonstration of 100% NI operation at performance levels extrapolating to ≥ 1 MW/m2 neutron wall loading in a FNSF
FW, EC and electron Bernstein wave (EBW) heating can facilitate start-up, ramp-up, and sustainment:
  EC heating can increase Te(0) in CHI and gun-initiated plasmas to allow NBI and FW heating
  FW-driven NI Ip ramp-up to a level that can confine fast-ions from neutral beams
  EBW heating can potentially provide CD in NBI H-mode plasmas
4

## Slide 5
FW heating led to record high electron temperatures and support a largely NI 300 kA H-mode plasma on NSTX
Record Te ~ 6.3 keV attained with 2.7 MW of FW power
    L-mode Ohmic target plasmas
    Can potentially be used for physics studies
Sustained >70% NI Ip ~ 300 kA H-mode plasma
  Mostly bootstrap current
  PFW ~ 1.4 MW; limited by antenna arcing (Li flakes or density drops)
5
[G. Taylor et al., Phys. Plasmas 19 (2012) 042501]

## Slide 6: Optimized FW heating requires understanding FW interactions with SOL and with ions
FY16 milestone [R16-3]
Field-aligned FW losses in SOL produced bright hot spiral on NSTX divertors
    Up to 30% of applied FW power might be lost to the SOL in this fashion
    Mechanisms responsible for this power loss have yet to be definitively identified
6
Assess FW absorption on NB and thermal ions in NSTX-U:
    Fast ions accelerated by FW power to loss orbits could significantly reduce heating efficiency
    Can influence/suppress Alfvén eigenmodes [M. Podestà’s talk]

## Slide 7: Continue to develop and validate RF codes for ST parameters to predict future performance
7
AORSA: full-wave code, all-orders in kperpρ
  Compare computations of RF fields in SOL against measurements of RF fields in divertor over a range of SOL and antenna parameters
  Validate partition of FW power absorption between fast ions, thermal ions, and electrons
TORIC: full-wave code (reduced model) with TRANSP interface
  Benchmark ion absorption of FW against AORSA and GENRAY
  Study non-Maxwellian (fast ion) effects on FW propagation
GENRAY (ray-tracing) & CQL3D (Fokker-Planck code)
  Hybrid full-orbit, finite orbit width has potential to accurately describe beam-ion interaction with FW (collaboration with R. Harvey, CompX)

## Slide 8: Outline
Motivation for Fast Wave (FW) & (future) Electron Cyclotron (EC) and Electron Bernstein Wave (EBW) research
Progress during the past year
Research goals and plans for FY 2015 & 2016
Summary
8

## Slide 9: AORSA simulations show low FW losses in SOL depending on location of righthand cutoff
Cutoff layer
Lower SOL density (nant = 1x1012 cm-3)
Antenna
Location
Higher SOL density (nant = 2x1012 cm-3)
kφ = 13 m-1
Heating phasing
NSTX-U at BT(0) = 1.0 T will have wider evanescent region:
  AORSA predicts reduced SOL losses
  Previous experiments showed improved heating in going from 0.45 T to 0.55 T
[N. Bertelli et al., Nucl. Fusion 54 (2014) 083004]
9
Field-amplitude depends on location of righthand cutoff
  Large amplitude when region in front of antenna is propagative
  Low amplitude when region in front of antenna is cutoff
  Transition is sharp
  [J. Hosea et al., Phys. Plasma 15 (2008) 056104]

## Slide 10
Probe analysis suggests RF rectification is an important contributor to FW losses in SOL
Heat flux to Langmuir probes is doubled underneath spiral relative to probe away from spiral (shot 141899)
  qRF = 0.209 MW/m2 qnoRF = 0.103 MW/m2
RF fields produces negative shift in probe floating potential
  Vfl-RF and Vfl-noRF floating potentials relative to tile with and without RF
  RF voltage (VRF) under spiral related to shift in floating potential:
exp[(Vfl-noRF-Vfl-RF)/Te) = I0(VRF/Te)
[A. Boschi and F. Magistrelli, Il Nuovo Cimento 29 (1963) 487]
Sheath transmission factor with RF obtained by adding VRFsin(ωt) to potential drop and averaging  over RF cycle
Enhancement of heat flux probably larger at more intense portion of spiral
Coaxial Langmuir probes on NSTX-U will permit direct measurement of VRF
qsurface = ×j+sat×Te

## Slide 11: Using upgrade outage period to identify and implement improvements to FW antenna for NSTX-U
11
Utilizing RF test-stand previously used for TFTR
Arcing observed between straps near low-voltage point
  Resolved with additional grounding to vessel wall
  Being implemented on NSTX-U
Additional grounding implemented
Location of arc
Good agreement between measured and predicted antenna heating (see backup)
Face-on View of Two Antenna Straps
Poloidal Cut of Antenna Strap

## Slide 12: Modeling for EC/EBW heating and current drive performed for long-term NSTX-U goals
ECH simulations suggest favorable performance in start-up
  BT(0) = 1 T CHI start-up plasma (F. Poli’s presentation)
  First-pass EC absorption rising to ~ 50% from initial < 5 %
  Te(0) increasing from 10 eV to ~ 1 keV in < 30 ms
  73 kA NI CD with 80 kW of EBW power during MAST EBW startup experiment last year (V. Shevchenko, G. Taylor in collaboration)
12
[G. Taylor, et al., Proc. 18th Joint Workshop on ECE and ECRH, Nara, Japan (2014)]
EBWCD profiles
EBW modeling for NBI H-modes predicts CD efficiencies ≤ 40 kA/MW:
  100% NI plasmas
  Peak EBWCD density around 1 MA/m2/MW

## Slide 13: Outline
Motivation for Fast Wave (FW) & (future) Electron Cyclotron (EC) and Electron Bernstein Wave (EBW) research
Progress during the past year
Research goals and plans for FY 2015 & 2016
Summary
13

## Slide 14: FY2015 Goal: Assess antenna performance and characterize field-aligned FW losses in SOL
Assess performance of FW antenna in NBI H-mode BT(0) ≤ 0.8 T discharges:
    Assess double-feed performance in both boronized and lithiated conditions
    Assess interactions of beam-ions with antenna limiters
      New dedicated IR camera will monitor antenna heat loads
Optimize FW heating by varying the position of the righthand cutoff for BT(0) ≤ 0.8 T:
  Vary the toroidal field strength (expect higher heating efficiency)
  Modify edge density (gas puffing and Li conditioning)
  Vary antenna phasing
  Monitor SOL losses with wide-angle IR camera, dedicated Langmuir probe array, and poloidal bolometric array for SOL
14

## Slide 15: FY2015 Goal: Assess FW heating and current drive with NBI fast-ions in BT(0) ≤ 0.8 T discharges
AORSA simulations predict greater deuterium heating when Ti > Te
  Ion heating increases and electron heating decreases as kf decreases
  Results sensitive to Ti/Te (= 2.5 in figure)
  Current drive is mostly bootstrap
Will vary the beam tangency radius, beam injection voltage, kφ and Ti/Te (varying density & heating source timing) in experiments
  Continue validation of CQL3D with fast ion diagnostic (FIDA) data
15
Current Drive
Phasing
[Collaboration with R. Harvey & CompX]
  [N. Bertelli, AIP Conf. Proc. 1580, 310 (2014)]

## Slide 16: FY2015 Goal: Sustain fully NI Ip ~ 300 kA H-mode plasmas with only FW power
Previously generated >70% NI Ip = 300 kA H-mode
  Rapidly heated plasma to Te ~ 3 keV
  PRF ~ 1.4 MW; previously limited by antenna arcing
This goal will be aided by:
  Improved Li conditioning & high-voltage standoff of antenna
  Improved FW coupling (increased BT)
  new MSE-LIF q(r) diagnostic
    does not require heating beam
    available end of FY2015
16
[G. Taylor et al., Phys. Plasmas 19 (2012) 042501]

## Slide 17: FY2015 Goal: Synthetic aperture microwave imaging (SAMI) diagnostic to image EBW emission
  Assess O-X-B coupling efficiency versus poloidal and toroidal angle
    Important for EBW heating design (mirror aiming)
17
    [Collaboration with University of York and CCFE]
  Image Doppler reflectometry to measure edge plasma flows
  Can observe density fluctuation on millisecond timescale
  Will measure magnetic pitch near edge region

## Slide 18: Research goals and plans for FY2016
Optimize FW heating at highest field values BT(0) ≤ 1.0 T
    Field-aligned SOL losses expected to diminish with increased field
    Study FW interaction with fast-ions at higher fields
Assess need for FW limiter upgrade that is compatible with higher Pnbi available on NSTX-U:
    If necessary, upgrade FW limiter during FY16-17 vacuum opening
Test impact of FW on NBI Ip ramp-up from 400 kA to ~ 1 MA
Demonstrate NI ramp-up of an FW-only H-mode to higher currents (~ 400 - 500 kA)
18

## Slide 19: Summary: NSTX-U FW and EC/EBW research supports non-inductive start-up / ramp-up necessary for ST-based FNSF
Aim to deliver efficient and reliable coupling of 4 MW of FW power into low-current H-mode plasmas
    Establish whether combining FW and NBI is operationally viable
    Establish if upgraded FW limiter is needed to be compatible with NBI
Demonstrate that FW heating and CD can (with future ECH assist) bridge the gap between CHI start-up and NBI ramp-up
Establish physics design basis for 28 GHz heating system and complete engineering design:
  Measure O-X-B coupling efficiency for a wide range of plasma scenarios to determine viability of EBW heating and CD
19

## Slide 20
Backup Slides
20

## Slide 21: Develop FW and EC heating for fully NI discharges
NBI and Bootstrap current sustainment
IP Target [kA]
Time
EC/EBW heating
(to 400 eV)
FW
(to 1 keV)
NBI and FW
Bootstrap current ramp-up
CHI
Plasma guns
~300
~500
~750
Non-Inductive Strategy
H-mode
Experiments in NSTX-U will initially develop NI start-up, ramp-up and plasma sustainment separately
Reduced RF edge losses and fast-ion interactions with the FW antenna may yield improved RF coupling and heating efficiency
21

## Slide 22: AORSA predicts RF field amplitude in SOL increases when FW cut-off is “open” in front of antenna
22
[N. Bertelli, et al., accepted for publication in Nuclear Fusion (June 2014)]
Etot for nf = -21, Df = -150o (for NSTX Shot# 130608)

## Slide 23: Total pressure rise in test stand as a function of applied RF power
Rise and fall in pressure with increased RF power suggests multipacting
BN stands of the boron nitride septum pieces, which could be removed from test stand
  Rise and fall is present both with and without boron nitride

## Slide 24
Probe analysis suggests RF rectification is an important contributor to FW losses in SOL
Heat flux to Langmuir probes is double for Probe 4 (under spiral) relative to Probe 2 (away from spiral)
  qP4 = 0.209 MW/m2
  qP2 = 0.103 MW/m2
Results obtained by:
  Negative shift in floating potential Vf for P4 to P2
  Gives RF voltage via the equation:
exp(DVf/Te) = I0(VRF/Te)
[A. Boschi and F. Magistrelli, Il Nuovo Cimento 29 (1963) 487.]
  Average γ over an RF cycle of amplitude VRF
  Assumes same Te and Isat for both probes
VRF = 43.7 V
For Ti = Te
gP4 = 14.43
gP2 = 7.12
141899 - t = 0.451 sec
Enhancement of heat flux probably larger at more intense portion of spiral
Coaxial Langmuir probes on NSTX-U will permit direct measurement of VRF
= qsurface/(j+sat *Te)

## Slide 25: Return RF currents in antenna visualized with infrared camera and show agreement with simulations
IR camera image after RF pulse
Microwave Studio calculations of RF currents

## Slide 26: RF research will also benefit from upgraded fast-ion, current profile and edge density diagnostics
Several diagnostics will provide information on fast-ion interactions with FW power in NSTX-U:
  Vertical and tangential FIDA systems will provide time (Dt ~ 10 ms), space (Dr ~ 5 cm) and energy (DE ~ 10 keV) measurements of the fast-ion distribution
  FIDA data will be complemented by an upgraded solid-state Neutral Particle Analyzer with 5 radial channels and ~ 1 MHz data rate
  Also there will be a new charged fusion product profile diagnostic and a scintillator-based lost fast-ion probe
New MSE diagnostic using laser-induced fluorescence will measure CD profile without needing high-power NBI blip:
  Important for CD measurements in FW-only H-modes
Upgraded 10-40 GHz refectometer and additional laser Thomson scattering channels will provide improved SOL density data
26

## Slide 27: 28 GHz EBW heating will be used for plasma start-up using a technique used successfully in MAST*
O-mode EC waves launched from low field side are weakly absorbed (< 2%) below the cut off electron density of ~ 1 x 1019 m-3
Grooved reflecting polarizer on the center column converts O-mode to X-Mode that then ~ 100% converts to EBWs
* V. F. Shevchenko et al. Nucl. Fusion 50 (2010) 022004
Grooved reflecting polarizer machined into center column in MAST
27

## Slide 28: Simulations of EC heated NSTX-U start-up plasma predict rapid core electron heating
TRANSP-TORAY simulations of 28 GHz O-mode were recently run for a BT(0) = 1 T start-up plasma :
  Various transport models were used resulting in variations in time evolution of the EC absorption and Te(0)
  All cases had first-pass EC absorption reaching ~ 50% and Te(0) increasing from 10 eV to > 1 keV within 30 ms
TRANSP-TORAY Simulation Results
    Model #1: Analytic ne(r) that reproduce NSTX L-mode profiles.
    Model #2: ne(r) from NSTX CHI discharge (shot #142140)
    Model #1 and #2: Analytic Ip waveform starting at 100 kA and ramping to 300 kA in 50 ms.
    Model #3: ne(r) and Ip evolution from shot #142140
28
[G. Taylor, et al., Proc. 18th Joint Workshop on ECE and ECRH, Nara, Japan (2014)]
F. Poli
Plasma
Overdense

## Slide 29: NSTX-U scenario used for computing FW power absorbed by ions and electrons
H-mode scenario planned for NSTX-U, obtained by TRANSP simulations [S. P. Gerhardt, Nucl. Fusion 52, 083020 (2012)]
B(R0) = 1 T, Ip= 1.1 MA, and PNBI = 6.3 MW
ne(0) = 1.1 x 1020 m-3, Te(0) = 1.22 keV, and TD(0) = 2.86 keV
Density, temperature profiles used in the simulations:

## Slide 30: Large ion absorption of FW power decreases as when Te >= Ti
Te(0) = 1.22 keV and Ti(0)/2 = 1.43 keV
2Te(0) = 2.44 keV and Ti(0)/2 = 1.43 keV
Electron and ion absorption is strongly sensitive to the ratio Te/Ti
Electron absorption increases when Te/Ti increases
Stronger effect for |kf| ≥ 8 m-1
|kf| ≥ 8 m-1 favorable for heating electrons
Thermal D and beam ions absorption decreases for Te much larger than Ti
Te > Ti in ramp-up phase

## Slide 31: FY16 Milestone R16-3: Assess fast-wave SOL losses and core thermal and fast ion interactions at increased field and current
Use of high-harmonic fast wave (HHFW) injection for heating and current drive in NSTX-U is important to develop non-inductive start-up/ramp-up schemes, to achieve higher plasma performance, and to validate RF codes in support of the ITER FW program. The successful exploitation of HHFW depends on how much power can be coupled to the core plasma through the scrape-off layer (SOL) and how the coupled power is partitioned between different species in the core. For NSTX-U H-mode plasmas, the latter typically include thermal electrons/ions and fast ions from Neutral Beam (NB) injection. Mechanisms responsible for RF power losses in the SOL will first be addressed to optimize FW coupling to the core as a function of excited wave spectrum, toroidal field and plasma current (BT and IP). For instance, full-wave simulations with the AORSA code suggest a local enhancement of RF fields for propagating (rather than evanescent) fast waves in the SOL, which results in increased losses through damping. Losses are predicted to decrease at lower SOL density and/or at higher BT. AORSA predictions will be tested against improved measurements of RF fields through dedicated probe arrays. The amount of lost power will be quantified through infrared cameras. The improved understanding of SOL loss mechanisms will provide more accurate estimations of the fraction of injected HHFW power reaching the core. The synergy between NB and FW injection in H-mode plasmas will be evaluated for the higher BT and IP of NSTX-U. In particular, the efficiency of thermal ions heating at higher BT, predicted to increase by full-wave simulations, will be investigated. Similarly, modifications of the fast ion distribution, previously observed on NSTX, will be assessed with the enhanced fast ion diagnostics set of NSTX-U as a function of plasma parameters, FW spectrum and NB injection geometry, including the new (more tangential) NB lines. The characterization of scenarios with combined NB and FW injection will provide a valuable dataset to benchmark RF codes (e.g. AORSA, TORIC and CQL3D-FOW), which have been considerably improved in the past years. NSTX-U will provide the required data for extensive validation before their use for scenario predictions in future devices such as ITER and FNSF.
31

## Slide 32: FY14-18 Wave heating and current drive research timeline (assuming baseline funding)
FY13
14
15
16
17
18
Physics
Assess performance of 12-strap double-feed FW antenna and compatibility with NBI H-modes at higher BT
5 year plan period
Develop plasma scenarios with fully non-inductive ramp-up and H-mode sustainment that utilize RF heating and current drive, and determine the validity of advanced RF codes.
5 year goal
5 year plan period
Measure and mitigate RF power flows in the SOL and to the divertors in the H-mode regime
Study FW interaction with NBI fast-ions
Simulate/mockup reduced- strap FW antenna performance
Validate advanced RF codes that include SOL, realistic antenna geometry, accurate modeling of fast-ion interaction and effect of edge fluctuations by comparing to NSTX-U data
Use advanced RF codes to predict RF performance in FNSF and ITER
Generate 100% NI Ip ~ 500 kA FW H-mode using inductively generated target
28 GHz EC heated CHI start-up
Assess FW electron heating during NBI NI current ramp-up
Thrust 1
Supporting HHFW Research for Thrusts
28 GHz EBW
start-up
Test O-X-B heating with "fixed" horn
300 kA to 500 kA
NI ramp-up with FW
Complete simulation of FW heating during Ip ramp-up and flat top
Assess effect of cryo-pumping and 3-D fields on FW antenna performance
Complete simulation of 28GHz EC/EBW heating during Ip ramp-up and flat top
Measure B-X-O coupling
Upgrade advanced RF codes to include SOL, realistic antenna, and accurate fast-ion modeling
Thrust 2
Upgrade Outage

## Slide 33: FY14-18 upgrades that support wave heating and current drive research (assuming baseline funding)
FY13
14
15
16
17
18
5 year plan period
5 year plan period
Tools
Theory
Facility
Add high-fidelity realistic antenna geometry to AORSA-3D
1 MW 28 GHz EC/EBW heating system with fixed horn antenna
Compliant HHFW feedthroughs
Full finite-orbit-width CQL3D and AORSA/ORBIT-RF for simulation of RF acceleration of NBI ions
Use RF operator in NUBEAM to accurately model fast-ion absorption
Test FW straps to excite EHO
TORIC with SOL and SPIRAL modeling of RF power loss to divertor
Diagnostics
Diagnostics for measuring HHFW and EBW power deposition and current drive (eg. Upgraded MPTS, ME-SXR, MSE-LIF, MSE-CIF)
GENRAY with SOL edge fluctuations and wave scattering for RF coupling
AORSA 3D high-resolution SOL
Include RF operator in NUBEAM
10-40 GHz edge reflectometer for SOL measurements in front of antenna
Fast IR for RF power SOL power losses
RF magnetic and Langmuir probes to measure RF power flow to divertor
Tangential FIDA and upgraded ssNPA for measuring RF acceleration of NBI ions
SAMI - microwave imaging diagnostic
Upgrade Outage