## Slide 1: Overview of NSTX-U Research Program Progress and Plans
J. Menard, PPPL
For the NSTX-U Research Team
NSTX-U PAC 37
PPPL B318
January 26-28, 2016

## Slide 2: Outline
Events since PAC-35
Charge Questions
Mission and Capabilities of NSTX-U
Research Goals and Milestones
Key Scientific Issues NSTX-U Will Address
Organizational Structure
Run Coordination
Support for FESAC / FES Strategic Goals
Summary

## Slide 3: NSTX-U Research Team Has Been Scientifically Productive Very Active in Scientific Conferences, Publications, and Collaborations
Strong APS meeting participation
  2014: 1 ST review talk, 5 NSTX invited talks, 44 posters
  2015: 3 NSTX invited talks (+4 by team-members), 54 posters
L. Delgado-Aparicio: DOE Early Career Award for research on impurity transport and control
Multitude of technical NSTX-U / next-step presentations at 2015 SOFE, Li Symposium, IAEA-TM on divertors
International ST Workshop: 78 talks+posters, 50% international
45 refereed publications for FY2015
34 IAEA FEC 2016 synopses on NSTX-U + ST-FNSF

## Slide 4: NSTX-U Research Team Has Been Scientifically Productive Very Active in Scientific Conferences, Publications, and Collaborations
Collaborative research contributions made in range of topics directly relevant to NSTX-U program
  DIII-D: Pedestal transport, fast-ions instabilities, RWM / RFA, QH-mode TEM particle transport, Li dropper, granule injector, snowflake/X divertors
  EAST: Lithium coating / wall physics, flowing liquid Li limiter
  KSTAR: NTV rotation damping, error fields, RMP
  C-Mod: ELM cycle / pedestal structure, high-Z spectroscopy
  MAST / York: Momentum transport studies / SAMI diagnostic
  QUEST: CHI + ECH start-up research, EBW-CD start-up modelling (new)
  ITPA halo current data / studies: DIII-D, AUG, C-Mod (+ NSTX / NSTX-U)

## Slide 5: Reminder: Project / Program events since PAC-35
Successful vessel pump-down (December 2014)
Team-wide Research Forum (February 2015)
Commissioning for 1st plasma, OH arc fault (April)
PAC-36 - program letter, arc fault discussion (June)
Arc recovery, corrective actions (May)
First test plasma: 110140kA, 0.5T (August)
Bake, facility / diagnostic commissioning (Fall)
Plasma commissioning: 800kA, 0.6T (late December)
Diverted NBI H-mode achieved (January 2016)
Just begun operating! PAC input very timely, valuable

## Slide 6: Presentations / agenda organized to aid you / PAC-37 in addressing charge questions
Please assess the research planned to be carried out for the NSTX-U FY2016 experimental campaign
  Are there any major missing elements, or new opportunities?
Please assess the alignment between the NSTX-U research plans and goals and the FESAC / FES initiatives, research opportunities, and ITER urgent research needs.
Please comment on the progress and plans for the NSTX-U / PPPL theory partnership, and how well this partnership and the broader NSTX-U research activities support “integrated predictive capability”.
Please comment on the present team prioritization of planned facility enhancements including:
  Divertor cryo-pump, non-axisymmetric control coils (NCC), 28GHz gyrotron, conversion to high-Z PFCs + liquid metals research
Menard, Ono, Maingi, Kaye, Gerhardt
Key Presentations:
All (except Ono)
Bhattacharjee, Boyer, Poli
Menard, Ono, Maingi, Kaye, Gerhardt, Jaworski, Sabbagh

## Slide 7: Outline
Events since PAC-35
Charge Questions
Mission and Capabilities of NSTX-U
Research Goals and Milestones
Key Scientific Issues NSTX-U Will Address
Organizational Structure
Run Coordination
Support for FESAC / FES Strategic Goals
Summary

## Slide 8: NSTX-U Mission Elements:
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
Develop solutions for plasma- material interface (PMI)
Advance ST as Fusion Nuclear Science Facility and Pilot Plant
Liquid metals / Lithium
Snowflake/X
ST-FNSF /
Pilot-Plant
ITER

## Slide 9: NSTX-U will access new physics with 2 major new tools:
Higher T, low n* from low to high 
 Unique regime, study new transport and stability physics
Full non-inductive current drive
 Not demonstrated in ST at high-T
Essential for any future steady-state ST
2. Tangential 2nd Neutral Beam
1. New Central Magnet

## Slide 10: NSTX-U will have major boost in performance
2× toroidal field (0.5  1T)
2× plasma current (1  2MA)
5× longer pulse (1  5s)
2× heating power (5  10MW)
Tangential NBI  2× current drive efficiency
4× divertor heat flux ( ITER levels)
Up to 10× higher nTE (~MJ plasmas)
2. Tangential 2nd Neutral Beam
1. New Central Magnet

## Slide 11: Outline
Events since PAC-35
Charge Questions
Mission and Capabilities of NSTX-U
Research Goals and Milestones
Key Scientific Issues NSTX-U Will Address
Organizational Structure
Run Coordination
Support for FESAC / FES Strategic Goals
Summary

## Slide 12: 5 year goal: Establish core physics/scenarios for ST 10 year goal: Integrate high-performance core + metal walls
First 5 years
Lower A or higher A?
Standard, snowflake, Super-X (MAST-U)?
Inform choice of
FNSF configuration:
Confinement vs. b , collisionality
Sustain high b with advanced control
Non-inductive start-up, ramp-up
Mitigate high heat fluxes
Test high-Z divertor, Li vapor shielding
Establish ST physics / scenarios:
High-Z consequences? need high-Z + Li?
Assess for both divertor and first-wall
Inform choice of FNSF / DEMO
plasma facing materials:
Second 5 years
Convert all PFCs from C to high-Z
Static  flowing Li divertor module(s), full toroidal flowing Li divertor, high Twall
5s  10-20s for PFC/LM equilibration
Assess ST with high-Z, high-Z + Li
High-performance + metal walls

## Slide 13: Summary of FY2016-18 NSTX-U Research Milestones
FY2016
  Obtain 1st data at 60% higher field/current, 2-3× longer pulse:
    Re-establish sustained low li / high-k operation above no-wall limit
    Study thermal confinement, pedestal structure, SOL widths
    Assess current-drive, fast-ion instabilities from new 2nd NBI
FY2017
  Extend NSTX-U performance to full field, current (1T, 2MA)
    Assess divertor heat flux mitigation, confinement at full parameters
  Access full non-inductive, small current over-drive
  First 2D high-k scattering, test prototype high-Z tiles, HHFW
FY2018
  Study low-Z and high-Z impurity transport
  Assess causes of core electron thermal transport
  Test advanced q profile and rotation profile control
  Assess CHI plasma current start-up performance
  Divertor power and momentum balance (vapor shielding)
R16-3
R16-1
R16-2
R17-1,3
R17-2
IR17-1
R17-4
R18-1
IR18-2
R18-2
R18-3
IR18-1
Milestone #

## Slide 14
NSTX-U Milestone Schedule for FY2016-18
FY2017
FY2016
18
16
Develop physics + operational tools for high-performance: k, d, b, EF/RWM
Assess H-mode confinement, pedestal, SOL characteristics at higher BT, IP, PNBI
Assess disruption mitigation, initial
tests of real-time warning, prediction
Develop high-non-inductive fraction NBI H-modes for sustainment and ramp-up
Assess fast-wave SOL losses, core thermal and fast ion interactions at increased field and current
Run Weeks:
FES 3 Facility Joint Research Target (JRT)
Integrated Scenarios
Core Science
Boundary Science
+ Particle Control
C-Mod leads JRT
Assess effects of NBI injection on fast-ion f(v) and NBI-CD profile
Assess scaling, mitigation of steady-state, transient heat-fluxes w/ advanced divertor operation at high power density
R17-1
Assess high-Z divertor PFC performance and impact on operating scenarios
R17-2
Assess impurity sources and edge and core impurity transport
R18-1
Assess role of fast-ion driven instabilities versus micro-turbulence in plasma thermal energy transport
IR18-2
Control of current and rotation profiles to improve global stability limits and extend high performance operation
R18-2
Assess transient CHI current start-up potential in NSTX-U
R18-3
Investigation of power and momentum balance for high density and impurity fraction divertor operation
IR18-1
FY2018
16
12
IR17-1
R17-4
R16-1
R16-2
R16-3
Incremental
Examine effect of configuration on operating space for dissipative divertors
DIII-D leads JRT
18
Assess E and local transport and turbulence at low * with full confinement and diagnostic capabilities
R17-3
TBD
NSTX-U leads JRT
Begin ~1 year outage for
major facility enhancement(s) sometime during FY2018

## Slide 15: Motivations for next major facility enhancements One (maybe 2) enhancement(s) feasible / affordable for FY18-19 outage
1. Divertor cryo-pump with high-Z baffle
  Control density and n* without Li, compare to Li
  Accelerate transition to high-Z PFCs, support liquid metal tests with bakeable baffle
2. Non-axisymmetric control coils (NCC)
  Resonant, non-resonant NTV rotation control
  RMP ELM suppression (not yet achieved in ST)
  Enhanced RWM/EF control
NCC
Existing
RWM
coils
Full toroidal NCC array (2 x 12)
3. 28GHz / 1MW gyrotron (Tsukuba)
  Heat CHI target w/ ECH for HHFW
  EC/EBW-only CD for start-up
  Longer-term: EBW CD for sustainment

## Slide 16: Favorable confinement trend with collisionality and  found in ST experiments
Promising scaling to ST-FNSF / Pilot, will trend continue on NSTX-U / MAST-U?
ST scaling observed in NSTX and MAST: tE, th µ n*e-0.8 b-0.0
Tokamak empirical scaling (ITER 98y,2): tE, th µ n*e-0.1 b-0.9
Role of enhancements:
Vary n*  cryo, b, Wf  NCC
See Bhattacharjee and Kaye talks for more details

## Slide 17: NBI-heated STs excellent testbed for -particle physics
-particles couple to Alfvénic modes when V > VAlfvén~ -0.5 Csound
Vfast > VA condition easily satisfied in high-b ST with NBI heating
NSTX-U: large fast-ion dynamic range spanning ST and conventional A
  Toroidal field 2× NSTX  Vfast < VA  stabilize modes
  Tangential 2nd NBI  very flexible fast-ion distribution
    Vary pitch angle, pressure profile
Can we find TAE-quiescent, high-performance regimes in NSTX-U?
Role of enhancements:
Vary bfast / btot  cryo, Wf  NCC

## Slide 18: NSTX-U aims to play leading role in disruption prediction, avoidance, and mitigation (DPAM) for ITER and FNSF
Advanced non-linear MHD modelling of vertical displacement events (VDE) + halo currents with M3D-C1
Enhance measurements of halo-current dynamics
FY16
FY17-18
Test ITER-like Massive Gas Injection (MGI) valves
  Test poloidal dependence of density assimilation
  First data expected FY16
RBT t = 2900
RBT t = 2918
NSTX Discharge 132859
RBT t = 2875
RBT t = 2850
University of Washington
NSTX-U / PPPL
Theory Partnership
See Bhattacharjee and Sabbagh talks for more details
Role of enhancements:
Control n*  cryo, b, Wf  NCC

## Slide 19: Design studies show ST potentially attractive as Fusion Nuclear Science Facility (FNSF) or Pilot Plant
FNSF with copper TF coils
A=1.7, R0 = 1.7m, x = 2.7
Fluence = 6MWy/m2, TBR ~ 1
FNSF / Pilot Plant with HTS TF coils
A=2, R0 = 3m, x = 2.5
6MWy/m2, TBR ~ 1, Qeng ~ 1
FNSF: Provide neutron fluence for material/component R&D (+ T self-sufficiency?)
Pilot Plant: Electrical self-sufficiency: Qeng = Pelec / Pconsumed ≥ 1 (+ FNSF mission?)

## Slide 20: Steady-state operation required for ST/AT FNSF or Pilot Plant
NSTX achieved 70% “transformer-less” current drive
NSTX-U designed to achieve 100% (TRANSP):
IP=1 MA, BT=1.0 T, PNBI=12.6 MW
H98y2
ITER H-mode confinement scaling multiplier
Will NSTX-U achieve 100% as predicted by simulations?
Role of enhancements:
Control ne / ngw  cryo, b, Wf  NCC
See Boyer and Gerhardt talks for more details

## Slide 21: ST-FNSF may need solenoidless current start-up method Coaxial Helicity Injection (CHI) effective for current initiation
CHI developed on HIT, HIT-II
Transferred to NSTX / NSTX-U
NSTX: 150-200kA closed flux current
R. Raman et al., PRL 2006
NSTX-U: CHI projects to 300-400kA
2
2
2
R (m)
R (m)
0
Z (m)
1.0 ms 1.6 ms 2.7 ms
R (m)
0
0
2
0
-2
Role of enhancements:
High-Z divertor tiles  reduce low-Z Prad
TSC axisymmetric simulation of CHI startup

## Slide 22: 1MW 28GHz ECH / EBW gyrotron is game-changer for solenoid-free start-up
CHI can form IP=300-400kA, but:
  Te too low for HHFW absorption
  Density too low and IP decay too fast for NBI absorption in CHI plasma
Good ECH first pass absorption predicted  “bridge the Te gap”
Strong ECH + High-Harmonic Fast-Wave (HHFW) synergy found in TRANSP simulations of non-inductive start-up
  Sustain IP enough for NBI to couple (not shown)
EBW-only start-up also promising
  High hCD ~1 A/W in MAST, QUEST
No ECH
With ECH
HHFW phasing: k|| = 3m-1 (CD)
See Poli and Gerhardt talks for more details
Role of enhancements:
Gyrotron, also ne control  cryo

## Slide 23: Dedicated tokamak + ST experiments found power exhaust width varies as 1 / Bpoloidal
ST data breaks aspect ratio degeneracy of data set
Will 1/Bpoloidal variation continue at higher IP? What about detached conditions?
Role of enhancements:
Control ne and detachment  cryo
3D/RMP effects in divertor  NCC

## Slide 24: NSTX-U will test ability of radiation and advanced divertors to mitigate very high heat-fluxes
NSTX: reduced heat flux 2-4×via radiation (partial detachment)
Additional null-point in divertor expands field, reduces heat flux
Snowflake/X Divertor
Standard Divertor
NSTX-U has additional coils for up-down symmetric snowflake/X, improved control
NSTX-U peak heat fluxes will be up to 4-8× higher than in NSTX
SFD: V. Soukhanovskii (LLNL)
XD: M. Kotschenreuther (UT)

## Slide 25: Plasma confinement increased continuously with increasing Li coatings in NSTX – what is limit?
Global parameters improve
  H98y2 increases ~0.9  1.4
  No core Li accumulation
High H critical for compact FNSF / Pilot Plants
NSTX-U will double Li-wall coverage with upward evaporators
Will further assess contributors to confinement improvement:
  Lower-recycling / reduced neutral source / higher Te
  Edge profile / turbulence changes
  Influence of (low-Z) impurities in pedestal region
Energy Confinement Time (ms)
Pre-discharge lithium evaporation (mg)
R. Maingi, et al., PRL 107 (2011) 145004
Role of enhancements:
Compare Li-wall pumping to conventional pumping  cryo

## Slide 26: NSTX-U boundary / PFC plan: add divertor cryo-pump, transition to high-Z wall, study flowing liquid metal PFCs
5yr goal: Integrate high E and T with 100% non-inductive
10yr goal: Assess compatibility with high-Z & liquid lithium PFCs
Cryo + full lower outboard high-Z divertor
Lower OBD
high-Z row of tiles
B+C BN
Li High-Z
2016
2017-18
2018-19
Heatable high-Z PFCs for liquid Li (including pre-filled)
Cryo + high-Z FW
and OBD
+ liquid Li divertor (LLD)
2020-21
High-Z tile row
Up + downward Li evaporator, possible pre-filled Li tiles (FY18)
High-Z tile row
All high-Z FW +
divertors
+ flowing LLD
module
2022-23
or
Flowing Li module (Concept, location, size TBD)
Cryo-pump
Downward Li evaporator +
Li granule injector
See Maingi, Jaworski talks for more details

## Slide 27: Outline
Events since PAC-35
Charge Questions
Mission and Capabilities of NSTX-U
Research Goals and Milestones
Key Scientific Issues NSTX-U Will Address
Organizational Structure
Run Coordination
Support for FESAC / FES Strategic Goals
Summary

## Slide 28: New NSTX-U Science organizational structure for 2015-16: 3 Science Groups, 9 Topical Science Groups, 1 Task Force
Each TSG has a leader, deputy, theory rep, and at least 1 university rep to enhance university participation
12 collaborating institutions engaged in NSTX-U science program leadership
Topical Science Group (TSG)
Science Group (SG)
Task Force (TF)
Task Force focuses resources on particle control – important for NSTX-U research goals, addresses PAC recommendations

## Slide 29: Motivations for restructuring science program
TSGs provide expertise in broad range of topics, but program would benefit from better coordination between TSGs
  SG leader responsibility: Coordinate TSG physics research plans, experimental/shot plans, diagnostic coverage & usage
Efficient shot usage especially important during first run year (many systems need to be re-commissioned)
  Experiments that engage multiple TSGs receive more run-time
Incorporate much wider set University researchers/PIs in planning + coordination of research program (FES/PPPL goal)
New - Task Force for long-pulse particle control
New - Working Groups: Disruption PAM (Sabbagh, Raman), NCC performance spec (Park, Canik), data frameworks (Tritz, Yuh, Smith)
  Task Forces have dedicated run-time, Working Groups do not, but recommend Program/SG/TSG actions

## Slide 30: NSTX-U university collaborators spearheaded new outreach seminar effort –11 talks given so far
J. Berkery (CU), D. Smith (UW)

## Slide 31: Research Forum held February 2015 Experimental proposals prioritized using several criteria:
Viability of proposal given available NSTX-U capabilities
OFES Joint Research Targets / Milestones
NSTX-U Research Milestones, Facility Enhancement design
ITER: Direct IO requests, ITPA: NSTX-U is leader / prominent
Experiments leading to high-profile publications/presentations:
  PRL, Science, Nature Invited talks: IAEA, APS, EPS, Sherwood, …
Career development: PhD thesis, post-doctoral research
Any good idea generated during run – potential “break-thru” ?
Maximize institutional / researcher breadth of XP leadership

## Slide 32: Very strong interest in NSTX-U research Requested research time exceeds available time by factor of 4
Requested / Available Run Time:
  Total: 273 / 90 = ~3×
  Research: 243 / 60 = ~4×
84 unique lead author names
~85% of requested time
Forum guidance / plan (Feb 2015): 16 run weeks
Recently incremented to 18 run weeks = 90 total run days
TSG / TF run-time guidance for FY16:

## Slide 33: Experimental proposal preparation and execution well underway
29 eXperimental Machine Proposals (XMP) for commissioning / calibration identified and/or written
  11 of the 29 already being executed (see Battaglia listing)
  Expect ~5-6 run weeks of XMP
27 eXperimental Proposals (XPs) written, reviewed for highest priority (P1a) experiments ~6 run weeks
►~1/2-2/3 of FY16 run-time has XMP/XP ready
Additional allocations:
  High priority experiments - P1b,c ~3.5-4 run weeks
  Priority P2a,b ~ 1.5-2 run weeks
  Reserve ~1 run week
For more info see: Master Spreadsheet of XMPs and XPs

## Slide 34: Research Operations Goals for first 2 run-months (still consistent with Forum guidance / assumptions)
Machine Commissioning – ~1 month (run weeks 1-4)
  Develop basic breakdown, current ramp, shape/position control, diverted plasmas, H-mode access, basic fuelling optimizations.
  Diagnostic commissioning
  Boronized PFCs
  Mostly XMPs
  Goal: 1 MA, 0.5 T, NBI-heated H-mode (i.e. ~NSTX fiducial levels)
1st Month of Science Campaign (run weeks 5-8)
  Boronized PFCs, possibly begin Li coatings (end of period)
  Operations and basic profile diagnostics, neutron rate,…
  HHFW available for commissioning
  6 beam sources up to 90 kV
  Operation up to 1.4 MA and 0.65 T, 2 seconds
We are here at
~2.5 run weeks
M. Ono talk will cover operational readiness

## Slide 35: Outline
Events since PAC-35
Charge Questions
Mission and Capabilities of NSTX-U
Research Goals and Milestones
Key Scientific Issues NSTX-U Will Address
Organizational Structure
Run Coordination
Support for FESAC / FES Strategic Goals
Summary

## Slide 36: Substantial leadership and participation in FES workshops by NSTX-U, collaborators, PPPL
Transients: 36% of 67 whitepapers: 13 for disruptions, 11 for ELMs
  Co-chair: R. Nazikian
  Disruptions: D. Brennan (co-lead), S. Sabbagh, D. Gates
  ELMs: R. Nazikian (lead), J. Canik (co-lead), O. Schmitz, W. Solomon
PMI: 29% of 56 whitepapers - evenly split among topical areas
  Chair: R. Maingi  hosted by PPPL
  SOL / Div: R. Goldston, J. Myra, V. Soukhanovskii
  PMI / Div. Simulators: J.P. Allain (leader), M. Jaworski, B. Wirth
  Engineering Innovation: C. Kessel (leader), R. Ellis, R. Majeski
  Core-edge Integration: J. Canik, M. Kotschenreuther, R. Majeski, R. Wilson
  Cross-cutting: R. Maingi, J. Menard, H. Neilson
Integrated Modeling: 24% of 119 whitepapers – Disruptions, WDM
  Disruptions: D. Brennan (co-lead), S. Gerhardt, S. Jardin
  Boundary: J. Canik, C-S Chang, G. Hammett
  Whole Device Modelling: C. Kessel (co-lead), B. Grierson, S. Kaye, F. Poli
  Multi-Physics, multi-scale: G. Fu, G. Hammett
  Data Management / Software Integration: S. Kaye / F. Poli

## Slide 37: NSTX-U research program well aligned with FESAC / FES strategic priorities
Advancing predictive capability, model validation
  See NSTX-U / Theory Partnership and Science Group talks
Supporting integrated modeling, exascale computing
  See TRANSP + Integrated Scenarios talks, XGC applications
Mitigating / avoiding transients (disruptions, ELMs)
  See Boundary and Core Science Group talks, DPAM talk
Taming the PMI (Divertor, SOL, first wall, PFCs)
  See Boundary Science and high-Z / liquid metal plan talk
Establishing physics basis for FNSF / next-steps
  Contributions from all talks
Supporting discovery science, basic plasma physics
  Reconnection / plasmoids in Partnership, Integrated Scenarios talks

## Slide 38: Summary: NSTX-U will make fundamental and world-leading contributions to toroidal fusion science
Investigate unique high-b, low collisionality regime for understanding transport and stability
Explore advanced divertors, high-Z and Li walls
Inform optimal configuration for next-steps
FY2016 run campaign is now underway!
  Thank you for your attention!

## Slide 39: Backup

## Slide 40: Run Time Guidance for XP Prioritization (January 2016) Similar to Research Forum, but +1 week for XMP, +1 week for XP

## Slide 41: NSTX-U 5 year plan: Develop physics/scenario understanding needed to assess ST viability as FNSF/DEMO, support ITER
Snowflake and radiative divertor exhaust location
Pheat [MW] with
qpeak < 10MW/m2
Lower
Lower or Upper
Lower + Upper
8
10
15
20
Divertor heat-flux control
2016 | 2017 | 2018 | 2019 | 2020 | 2021
NBI+BS IP ramp-up: initial  final [MA]
CHI closed-flux
current [MA]
0.15 – 0.2
0.2 – 0.3
0.3 – 0.5
0.4 – 0.6
0.6  0.8
0.5  0.9
0.4  1.0
Sustained bN
n* / n* (NSTX)
Non-inductive
fraction (Dt ≥ tCR)
4 – 6
5 – 6
3 – 5
0.6
0.4
0.3 – 0.2
0.2 – 0.1
70 – 90%
80 – 110%
90 – 120%
100 – 140%
NCC
ECH / EBW
Cryo
Structural force
and coil heating
limit fractions
Max BT [T], IP [MA]
Nominal tpulse [s]
1 – 2
2 – 4
0.5, 0.5
1.0, 0.75
0.8, 1.6
1, 2
4 – 5
1.0, 1.0
Off-midplane non-axisymmetric control coils (NCC): rotation profile control (NTV), sustain high bN
Cryo: access lowest n*, compare to Li
ECH / EBW: bridge Te gap from start-up to ramp-up
Inform choice
of FNSF/DEMO
aspect ratio
and divertor

## Slide 42: NSTX-U engaged in 31 ITPA joint experiments / activities
 | Advanced Scenarios and Control
IOS-1.2 | Divertor heat flux reduction in ITER baseline scenario (considering)
IOS-1.3 | Operation near PLH (considering)
IOS-2.1 | Compare helium H-modes in different devices (considering)
IOS-3.3 | Core confinement for q(0)=2 (considering)
IOS-5.2 | Maintaining ICRH coupling in expected ITER regime
 | Boundary Physics
PEP-26 | Critical edge parameters for achieving L-H transition
PEP-28 | Physics of H-mode access with different X-point height (considering)
PEP-29 | Vertical jolts/kicks for ELM triggering and control
PEP-30 | ELM control by pellet pacing in ITER-like conditions and consequences for plasma confinement
PEP-31 | Pedestal structure and edge relaxation mechanisms in I-mode (considering)
PEP-37 | Effect of low-Z impurity on pedestal and global confinement
DSOL-31 | Leading edge power loading and monoblock shaping
DSOL-34 | Far-SOL fluxes and link to detachment (considering)
DSOL-35 | In-out divertor ELM energy density asymmetries (consdiering)
 | Macroscopic Stability
MDC-1 | Disruption mitigation by massive gas jets
MDC-8 | Current drive prevention/stabilization of NTMs (considering)
MDC-15 | Disruption database development
MDC-17 | Active disruption avoidance
MDC-18 | Evaluation of axisymmetric control aspects
MDC-19 | Error field control at low plasma rotation
MDC-21 | Global mode stabilization physics and control
MDC-22 | Disruption prediction for ITER
 | Transport and Turbulence
TC-9 | Scaling of intrinsic plasma rotation with no external momentum input (considering)
TC-10 | Experimental identification of ITG, TEM and ETG turbulence and comparison with codes
TC-11 | He and impurity profiles and transport coefficients
TC-14 | RF rotation drive (considering)
TC-15 | Dependence of momentum and particle pinch on collisionality
TC-17 | r* scaling of intrinsic torque (considering)
TC-19 | Characteristics of I-mode plasmas (considering)
TC-24 | Impact of resonant magnetic perturbations on transport and confinement (considering)
 | Energetic Particles
EP-6 | Fast ion losses and associated heat loads from edge perturbations (ELMs and RMPs)

## Slide 43: Roles / Responsibilities for Task Forces
Address specific operational and/or scientific goal that cuts across or impacts multiple SGs / TSGs
Goal must be very high priority within research program
Receives dedicated run-time, and has dedicated session at Research Forum
  Similar to a TSG, but may not necessarily have theory/modelling or university representatives – depends on duration or scope
Organizes experimental proposals to achieve goal
Finite duration - nominally 1-2 years, renewable if necessary
TF leadership should nominally have a leader and a deputy, and should include at least 1 collaborator if possible
Reports directly to Program / Project
Long-pulse particle control

## Slide 44: Roles / Responsibilities for Working Groups
Respond to specific programmatic or technical charge from NSTX-U Program or Project
Addresses issues that cross-cut more than one SG or TSG
Nominal lifetime = 1-2 years, can be extended/renewed
Provides points of contact between NSTX-U and other groups as necessary (e.g. PPPL theory, FESAC, ITPA, ITER)
Does not have dedicated NSTX-U run time, but provides recommendations on XP prioritization, other resource needs
WG leadership should nominally have a leader and a deputy, and should include at least 1 collaborator if possible
DPAM: Prep for JRT-16, understand then avoid causes of disruptions in NSTX-U
Multi-facility and multi-institutional effort

## Slide 45: NSTX-U = National Spherical Torus eXperiment - Upgrade Highly collaborative research program
402 team members
290 scientists
(~70% non-PPPL)
55 institutions
22 US Universities
Domestic (33)
International (22)