## Slide 1: Overview of the Disruption Prediction, Avoidance, and Mitigation Working Group and Initial Results
NSTX-U PAC 37 Meeting
PPPL, Princeton, NJ
January 27th, 2016
V1.6
S.A. Sabbagh1, R. Raman2
For the NSTX-U DPAM Working Group
1Columbia University, New York, NY
2University of Washington, Seattle, WA

## Slide 2: Overview of the NSTX-U Disruption Prediction, Avoidance, and Mitigation (DPAM) Working Group - OUTLINE
Motivation and connection to DOE FES priorities
Mission statement and Scope
Disruption Prediction: Characterization and forecasting approach, implementation, and development
Disruption Avoidance: Mode stabilization and control
Disruption Mitigation: Preparation of NSTX-U MGI system
Connection to JRT-16 Joint Research Target Milestones

## Slide 3: Disruption avoidance is a critical need for future tokamaks; NSTX-U is focusing stability research on this
The new “grand challenge” in tokamak stability research
  Can be done! (JET: < 4% disruptions w/C wall, < 10% w/ITER-like wall)
    ITER disruption rate: < 1 - 2% (energy load, halo current); << 1% (runaways)
Strategic plan: utilize/expand stability/control research success
  Synergize and build upon disruption prediction and avoidance successes attained in present tokamaks (don’t just repeat them!)
FESAC 2014 Strategic Planning report defined “Control of Deleterious Transient Events” highest priority (Tier 1) initiative
  Working group members had significant leadership roles in the 2015 DOE Workshops on solving issues of “Transient Events in Tokamaks”
NSTX-U will produce focused research on disruption avoidance with quantitative measures of progress
  Long-term goal: many sequential shots (~3 shot-mins) without disruption

## Slide 4: DPAM Working Group - Mission Statement and Scope
Mission statement
  Satisfy gaps in understanding prediction, avoidance, and mitigation of disruptions in tokamaks, applying this knowledge to move toward acceptable levels of disruption frequency/severity using quantified metrics
Scope
  Location: Initiate and base the study at NSTX-U, expand to a national program and international collaboration (multi-tokamak data)
  Timescale: Multi-year effort, planning/executing experiments of various approaches (leveraging the 5 NSTX-U Year Plan) to reduce plasma disruptivity/severity at high performance
  Breadth: High-level focus on quantified mission goal, with detailed physics areas expected to expand/evolve within the group, soliciting research input/efforts from new collaborations as needed
More than 50 members presently on email list; 3 meetings held to date

## Slide 5
Disruption Prediction

## Slide 6: Disruption event chain characterization capability started for NSTX-U as next step in disruption avoidance plan
Approach to disruption prevention
  Identify disruption event chains and elements
  Predict events in disruption chains
  Cues disruption avoidance systems to break event chains
    Attack events at several places with active control
  Synergizes and builds upon both physics and control successes of NSTX
t
Disruption prediction/avoidance framework (from upcoming DOE “Transient Events” report)
  New Disruption Event Characterization and Forecasting (DECAF) code created

## Slide 7
Disruption Event Characterization And Forecasting Code (DECAF) yielding initial results (pressure peaking example)
PRP warnings
PRP
VDE
IPR
SCL
Detected at: 0.4194s
0.4380s
0.4522s
0.4732s
NSTX
142270
Disruption
10 physical events presently defined in code with quantitative warning points
  Builds on manual analysis of de Vries
  Builds on warning algorithm of Gerhardt
  New code written (in Python), easily expandable, portable to other tokamaks (recent capability to process DIII-D data)
Example: Pressure peaking (PRP) disruption event chain identified by code before disruption
  (PRP) Pressure peaking warnings identified first
  (VDE) VDE condition subsequently found 19 ms after last PRP warning
  (IPR) Plasma current request not met
  (SCL) Shape control warning issued
Event chain
P.C. de Vries et al., Nucl. Fusion 51 (2011) 053018
S.P. Gerhardt et al., Nucl. Fusion 53 (2013) 063021
J.W. Berkery, S.A. Sabbagh, Y.S. Park (Columbia U.)
and the NSTX-U Disruption PAM Working Group

## Slide 8: DECAF is structured to ease parallel development of disruption characterization, event criteria, and forecasting
Physical event modules encapsulate disruption chain events
  Development focused on improving these modules
  Structure eases development
    E.g. separate code by C. Myers that improved disruption timing definition was quickly imported
Physical events are objects in physics modules
  e.g. VDE, LOQ, RWM are objects in “Stability”
  Carry metadata, event forecasting criteria, event linkages, etc.
Main data structure
Code control workbooks
Density Limits
Confinement
Stability
Tokamak dynamics
Power/current handling
Technical issues
Physical event modules
Output processing

## Slide 9: Initial DECAF results detect disruption chain events when applied to dedicated 44 shot NSTX RWM disruption database
Several events detected for all shots
  RWM: RWM event warning
  SCL: Loss of shape control
  IPR: Plasma current request not met
  DIS: Disruption occurred
  LOQ: Low edge q warning
  VDE: VDE warning (40 shots)
Others:
  PRP: Pressure peaking warning
  GWL: Greenwald limit
  LON: Low density warning
  LTM: Locked tearing mode
Occur with or after RWM

## Slide 10: Initial DECAF results detects disruption chain events when applied to dedicated 44 shot NSTX RWM disruption database
Most RWM near major disruption
  61% of RWM occur within 20 tw of disruption time (tw = 5 ms)
  Earlier RWM events NOT false positives – cause large decreases in bN with recovery (minor disruptions)
VDE
60
40
20
0
0
2
4
6
BPLn=1 (G)
bN
0.2
0.4
0.6
0.8
1.0
0.0
t(s)

## Slide 11: Initial DECAF analysis already finding common disruption event chains (44 shot NSTX disruption database)
Common disruption event chains (52.3%)
  Related chains
    RWM  SCL  VDE  IPR  DIS
    VDE  RWM  SCL  IPR  DIS
    VDE  RWM  IPR  DIS  SCL
    RWM  SCL  VDE  GWL  IPR  DIS
Disruption event chains w/o VDE (11.4%)
New insights being gained
  Chains starting with GWL are found that show rotation and bN rollover before RWM (6.8%)
  Related chains
    GWL  VDE  RWM  SCL  IPR  DIS
    GWL  SCL  RWM  IPR  DIS
Disruption event chains with RWM
VDE
SCL
IPR
RWM
DIS
Event chains with RWM and VDE
(52.3%)
No
VDE
(11.4%)
Other
(29.5%)
GWL start
(6.8%)

## Slide 12: First DECAF results for NSTX-U replicate the triggers found in new real-time state machine shutdown capability
Important capability of DECAF to compare analysis using offline vs. real-time data
  Simple, initial test
PCS Shut-down conditions are analogous to DECAF events
  PCS loss of vertical control  DECAF
DECAF comparison:VDE event
  Matches PCS when r/t signal used (1 criterion)
  VDE event 13 ms earlier using offline EFIT signals (3 criteria)
See talk by S. Gerhardt (next) for detail of new NSTX-U automated shutdown capability
VDE
PCS trigger
For VDE
(t = 0.733s)
VDE
Using r/t data (t = 0.733s) Using EFIT (t = 0.720s)
DECAF
EFIT offline reconstruction
of Z position
Zaxis (m)
Ip (MA)
PCS trigger
0
0.4
0.8
0.2
0.4
0.6
0.8
1.0
0.0
t(s)
0
0.4
-0.4
0
2
4

## Slide 13
Disruption Avoidance

## Slide 14
Predictor/Sensor (CY available) | Control/Actuator (CY available) | Modes | REFER TO
Rotating and low freq. MHD (n=1,2,3) 2003 | Dual-component RWM sensor control (closed loop 2008) | NTM RWM | - Menard NF 2001 - Sabbagh NF 2013; + backup slides
Low freq. MHD spectroscopy (open loop 2005); Kinetic RWM modeling (2008) | Control of βN (closed loop 2007) | Kink/ball RWM | - Sontag NF 2007 - Berkery (2009–15) - Gerhardt FST 2012
r/t RWM state-space controller observer (2010) | Physics model-based RWM state-space control (2010) | NTM, RWM Kink/ball, VDE | - THIS TALK - Sabbagh NF 2013; + backup slides
Real-time Vf measurement (2016) | Plasma Vf control (NTV 2004) (NTV + NBI rotation control closed loop ~ 2017) | NTM Kink/ball RWM | - Podesta RSI 2012 - Zhu PRL 06 +backup - THIS TALK
Kinetic RWM stabilization real-time model (2016-17) | Safety factor, li control (closed loop ~ 2016-17) | NTM, RWM Kink/ball, VDE | - Berkery, NF 2015 - D. Boyer’s TALK
MHD spectroscopy (real-time) (in 5 Year Plan) | Upgraded 3D coils (NCC): improved Vf and mode control (in 5 Year Plan) | NTM, RWM Kink/ball, VDE | - NSTX-U 5 Year Plan - THIS TALK
NSTX-U is building on past strength, creating an arsenal of capabilities for disruption avoidance

## Slide 15: Joint NSTX / DIII-D experiments and analysis gives unified kinetic RWM physics understanding for disruption avoidance
RWM Dynamics
  RWM rotation and mode growth observed
  No strong NTM activity
  Some weak bursting MHD in DIII-D plasma
    Alters RWM phase
  No bursting MHD in NSTX plasma
DIII-D (bN = 3.5)
NSTX (bN = 4.4)
DBpn=1(G)
fBpn=1(deg)
(arb)
Frequency (kHz)
t (s)
t (s)
amplitude
phase
Da
toroidal magnetics
rotation
growth
rotation
growth
amplitude
phase
Da
toroidal magnetics
S. Sabbagh et al., APS Invited talk 2014

## Slide 16: Evolution of plasma rotation profile leads to kinetic RWM instability as disruption is approached
DIII-D (minor disruption)
NSTX (major disruption)
MISK
MISK
unstable
stable
unstable
stable
increasing time
increasing time
gtwall
gtwall
S. Sabbagh et al., APS Invited talk 2014
Kinetic RWM stabilization occurs from broad resonances between plasma rotation and particle precession drift, bounce/circulating, and collision frequencies

## Slide 17: State space rotation controller designed for NSTX-U using non-resonant NTV and NBI to maintain stable profiles
Momentum force balance – wf decomposed into Bessel function states
NTV torque:
yN
NBI, -NTV torque density (N/m2)
NBI
Torque
(NSTX)
0.0
0.5
1.0
1.5
0.0
0.2
0.4
0.6
0.8
1.0
NBI and NTV torque profiles for NSTX-U
Momentum Actuators
New NBI
(broaden rotation)
3D Field Coil
(shape wf profile)
-NTV
Torque
I. Goumiri, et al., submitted to NF (2016)

## Slide 18: State space rotation controller designed for NSTX-U using non-resonant NTV and NBI to maintain stable profiles
Momentum force balance – wf decomposed into Bessel function states
NTV torque:
NBI, -NTV torque density (N/m2)
NBI
Torque
(NSTX)
0.0
0.5
1.0
1.5
NBI and NTV torque profiles for NSTX-U
NBI Torque
(NSTX-U)
Momentum Actuators
New NBI
(broaden rotation)
3D Field Coil
(shape wf profile)
-NTV
Torque
yN
0.0
0.2
0.4
0.6
0.8
1.0
I. Goumiri, et al., submitted to NF (2016)

## Slide 19: State space rotation controller designed for NSTX-U can evolve plasma rotation profile toward global mode stability
I. Goumiri (Princeton student), S.A. Sabbagh (Columbia U.), C. Rowley (P.U.), D.A. Gates, S.P. Gerhardt (PPPL)
Recall:
NSTX (major disruption)
MISK
unstable
stable
stable
gtwall
Plasma rotation (kHz)
0
15
20
10
5
yN
0.0
0.2
0.4
0.6
0.8
1.0
NSTX-U (6 NBI sources and n = 3 NTV)
marginally
stable
Steady-state reached in ~ 3tm
Marginally stable profile
Broader stable
profile
NBI, -NTV torque density (N/m2)
0.0
0.5
1.0
1.5
2.0
Plasma rotation (krad/s)
NBI
NTV

## Slide 20: With planned NCC coil upgrade, rotation controller can reach desired rotation profile faster, with greater fidelity
I. Goumiri (Princeton student), S.A. Sabbagh (Columbia U.), C. Rowley (P.U.), D.A. Gates, S.P. Gerhardt (PPPL)
NSTX-U wf control with
  6 NBI sources
  Greater core NTV from planned NCC upgrade
Better performance
  Faster to target t ~ 0.5tm
  Matches target wf better
Planned NCC upgrade
Marginally stable profile
Broader stable
profile
NBI
NTV
Plasma rotation (kHz)
0
15
20
10
5
NBI, -NTV torque density (N/m2)
0.0
0.5
1.0
1.5
2.0
0.0
0.2
0.4
0.6
0.8
1.0
yN

## Slide 21: Active RWM control design study for proposed NSTX-U 3D coil upgrade (NCC coils) shows superior capability
NCC 2x12 with favorable sensors, optimal gain
NCC 2x6 odd parity, with favorable sensors
Full NCC coil set allows control close to ideal wall limit
  NCC 2x6 odd parity coils: active control to bN/bNno-wall = 1.58
  NCC 2x12 coils, optimal sensors: active control to bN/bNno-wall = 1.67
NCC (plasma facing side)

## Slide 22: NSTX RWM state space controller sustains high bN, low li plasma – available for NSTX-U with independent coil control
RWM state space feedback (12 states)
n = 1 applied field suppression
  Suppressed disruption due to n = 1 field
Feedback phase scan
  Best feedback phase produced long pulse, bN = 6.4, bN/li = 13
NSTX Experiments
(from 2010)
Ip (MA)
(A)
Run time has been allocated for continued experiments on NSTX-U in 2016
S. Sabbagh et al., Nucl. Fusion 53 (2013) 104007

## Slide 23: In addition to active mode control, the NSTX-U RWM state space controller can be used for real-time disruption warning
Sensor
data
Controller
(observer)
The controller “observer” produces a physics model-based calculation of the expected sensor data – a synthetic diagnostic
If the real-time synthetic diagnostic doesn’t match the measured sensor data, a r/t disruption warning signal can be triggered
  Technique will be assessed using the DECAF code
RWM Sensor Differences (G)
RWM Sensor Differences (G)
137722
t (s)
40
0
80
0.56
0.58
0.60
137722
t (s)
0.56
0.58
0.60
0.62
dBp90
dBp90
-40
0.62
40
0
80
-40
Effect of 3D Model Used
No NBI Port
With NBI Port
RWM

## Slide 24
Disruption Mitigation

## Slide 25: NSTX-U Disruption Mitigation Research Aims to Develop MGI and EPI Technologies in Support ITER and FNSF
Massive Gas Injection (MGI): (starting 2016)
  ITER-type MGI valve will be used on NSTX-U in a configuration to do nearly exact comparison experiments
  Experimental results to be studied using M3D-C1 (A. Fil, S. Jardin, et al.)
    Develop understanding of gas assimilation fraction by the plasma
    Use to project to ITER plasmas
  Similar plasma poloidal size, shape of DIII-D and NSTX-U allows multi-machine comparison studies
Electromagnetic Particle Injector (EPI): (in 5 Year Plan)
  Motivation: Handle fast disruptions
    For warning times < 10 ms, MGI may not be a viable option
  Rapid delivery of impurities deeper into plasma with fast time-response
    Under 5ms from trigger to delivery at 7m from plasma
    Efficiency of system improves in a magnetic field environment

## Slide 26: New double solenoid valve design (zero net JxB torque) pass tests for reliability and magnetic field limits
MGI
Valve
Magnets
Magnets
Test stand
Fast Baratron
Baratron traces with and without magnetic field
MGI
Valve
MGI
Valve
University of Washington Test Stand
R. Raman, et al., RSI 85 (2014) 11E801

## Slide 27: NSTX-U MGI will study poloidal injection location variation using identical MGI valves and gas transit piping
Assess benefits of injection into the private flux region & the high-field side vs. LFS midplane
Quantify MGI gas assimilation fractions and extend model to larger machines
Model gas penetration and assimilation results using 3D MHD codes (incl. M3D-C1)
First plasma tests April, experiment May 2016
1a: Private flux region
1b: Lower SOL, Lower divertor
3: Upper divertor
2: mid-
plane
4: future position

## Slide 28: DPAM Working Group is fulfilling DOE Joint Research Target JRT-16 milestones to start NSTX-U 5 YP research goals
FY16 DOE Joint Research Target summary (1 page)
  http://nstx.pppl.gov/DragNDrop/Working_Groups/DPAM/Repository/JRT16QuarterlyMilestones-V9.pdf
Prediction / Avoidance
  Use disruption prediction algorithm to characterize the reliability of predicting a few types of common disruptions from at least two devices
  Report on capability to reduce disruption rate through active improvement of plasma stability
  Test on at least one facility to detect in real time an impending disruption and take corrective measures to safely terminate the plasma discharge
Mitigation
  Test newly-designed ITER-type massive gas injection valve to study benefits of private flux region massive gas injection vs. mid-plane inj.
Culminating Milestones for 2016

## Slide 29: NSTX-U Research is building upon physics understanding and synergizing control for disruption PAM in tokamaks
Disruption PAM Working Group Mission
  Satisfy gaps in understanding disruption prediction, avoidance, mitigation
  Apply knowledge to demonstrate acceptable levels of disruption frequency/severity using quantified metrics
PAC charges are directly addressed
  FESAC/FES Initiatives: NSTX-U DPAM Working group effort was born from 2015 FES effort - is identically aligned with it. Urgent ITER need.
  Research: Disruption Event Characterization And Forecasting effort started to unify physics understanding for disruption avoidance (5 YP Committee member recommendation); MGI to start in 2016.
  Facility enhancements: Quantified disruptivity metrics will assess new capabilities (e.g. plasma rotation, q, active mode control ) and guide future improvements (e.g. planned NCC 3D coil upgrade, et al.)
  PPPL Theory partnership: Is highly leveraged in this effort (10 members)
(see talk by A. Bhattacharjee)

## Slide 31
Supporting Slides Follow

## Slide 32: NSTX is a spherical torus equipped to study passive and active global MHD control
RWM active stabilization coils
RWM poloidal
sensors (Bp)
RWM radial sensors (Br)
Stabilizer
plates
High beta, low aspect ratio
  R = 0.86 m, A > 1.27
  Ip < 1.5 MA, Bt = 5.5 kG
  bt < 40%, bN > 7
Copper stabilizer plates for kink mode stabilization
Midplane control coils
  n = 1 – 3 field correction, magnetic braking of wf by NTV
  n = 1 RWM control
Combined sensor sets now used for RWM feedback
  48 upper/lower Bp, Br
3D Conducting Structure Model

## Slide 33
Initially used for NSTX since simple critical scalar wf threshold stability models did not describe RWM stability
Kinetic modification to ideal MHD growth rate
  Trapped / circulating ions, trapped electrons, etc.
  Energetic particle (EP) stabilization
Stability depends on
  Integrated wf profile: resonances in dWK (e.g. ion precession drift)
  Particle collisionality, EP fraction
Trapped ion component of dWK (plasma integral over energy)
collisionality
wf profile (enters through ExB frequency)
Hu and Betti, Phys. Rev. Lett 93 (2004) 105002
Sontag, et al., Nucl. Fusion 47 (2007) 1005
precession drift
bounce
Modification of Ideal Stability by Kinetic theory (MISK code) is used to determine proximity of plasmas to stability boundary
J. Berkery et al., PRL 104, 035003 (2010)
S. Sabbagh, et al., NF 50, 025020 (2010)
J. Berkery et al., PRL 106, 075004 (2011)
S. Sabbagh et al., NF 53, 104007 (2013)
J. Berkery et al., PoP 21, 056112 (2014)
J. Berkery et al., PoP 21, 052505 (2014)
J. Berkery et al., NF 55, 123007 (2015)
Some NSTX / MISK analysis references

## Slide 34: Kinetic RWM stability evaluated for DIII-D and NSTX plasmas, reproduces experiments over wide rotation range
Summary of results
  Plasmas free of other MHD modes can reach or exceed linear kinetic RWM marginal stability
  Bursting MHD modes can lead to non-linear destabilization before linear stability limits are reached
  Extrapolations of DIII-D plasmas to different Vf show marginal stability is bounded by 1.6 < qmin < 2.8
Kinetic RWM stability analysis for experiments (MISK)
Plasma rotation [krad/s] (yN = 0.5)
Normalized growth rate (gtw)
major disruption
minor disruption
DIII-D
NSTX
stable
unstable
extrapolation
qmin = 2.8
qmin = 1.6
“weak stability” region
J.W. Berkery, J.M. Hanson, S.A. Sabbagh (Columbia U.)
S. Sabbagh et al., APS Invited talk 2014
Extensive NSTX / MISK analysis references spanning ~ 7 years
(8 references given in supporting slides)

## Slide 35
JET disruption event characterization provides framework to follow for understanding / quantifying DPAM progress
P.C. de Vries et al., Nucl. Fusion 51 (2011) 053018
JET disruption event chains
Related disruption event statistics
JET disruption event chain analysis performed by hand, desire to automate
General code written (DECAF) to address the first step – initial analysis started using NSTX data

## Slide 36
Disruption Characterization Code now yielding initial results: disruption event chains, with related quantitative warnings (2)
J.W. Berkery, S.A. Sabbagh, Y.S. Park
This example: Greenwald limit warning during Ip rampdown
  (GWL) Greenwald limit warning issued
  (VDE) VDE condition then found 0.6 ms after GWL warning
  (IPR) Plasma current request not met
GWL warnings
NSTX
138854
GWL
VDE
IPR
Detected at: 0.7442s
0.7448s
0.7502s
Disruption during
Ip ramp-down
Event chain

## Slide 37: NTV physics studies for rotation control: measured NTV torque density profiles quantitatively compare well to theory
TNTV (theory) scaled to match peak value of measured -dL/dt
  Scale factor ((dL/dt)/TNTV) = 1.7 and 0.6 for cases shown above – O(1) agreement
KSTAR n = 2 NTV experiments do not exhibit hysteresis
n = 2 coil configuration
Experimental
-dL/dt
yN
NSTX
NTVTOK
x1.7
n = 3 coil configuration
Experimental
-dL/dt
NTVTOK
yN
NSTX
x0.6
See recent NTV review paper: K.C. Shaing, K. Ida, S.A. Sabbagh, et al., Nucl. Fusion 55 (2015) 125001

## Slide 38: Active RWM control: dual Br + Bp sensor feedback gain and phase scans produce significantly reduced n = 1 field
Favorable Bp + Br feedback (FB) settings found (low li plasmas)
Time-evolved theory simulation of Br+Bp feedback follows experiment
Dt (s) (model)
Radial field n = 1 (G)
180 deg FB phase
90 deg FB phase
0 deg FB phase
Vacuum error field
Vacuum error field
+ RFA
Simulation of Br + Bp control (VALEN)
Feedback on
Br Gain = 1.0
140124
140122
139516
No Br feedback
t (s)
bN
li
6
4
2
0
0.8
0.6
0.2
0.0
6
4
2
0
0.0
0.2
0.4
0.6
0.8
1.0
1.2
1.4
Br Gain = 1.50
Brn = 1 (G)
bN
li
0.4
6
4
2
Br gain scan
Br FB phase scan
S. Sabbagh et al., Nucl. Fusion 53 (2013) 104007

## Slide 39: Model-based RWM state space controller including 3D model of plasma and wall currents used at high bN
Controller model can compensate for wall currents
  Includes linear plasma mode-induced current model (DCON)
Potential to allow control coils to be moved further from plasma, and be shielded (e.g. for ITER)
  Straightforward inclusion of multiple modes (n = 1, or n > 1)
Balancing transformation
~3000+ states
Full 3-D model
…
RWM eigenfunction(2 phases, 2 states)
State reduction (< 20 states)
Controller reproduction of n = 1 field in NSTX
100
150
50
0
-50
-100
-150
Sensor Difference (G)
0.4
0.6
0.8
1.0
0.2
t (s)
118298
118298
100
150
50
0
-50
-100
-150
Sensor Difference (G)
Measurement
Controller
(observer)
5 states
used
10 states
used
(only wall states used)
Katsuro-Hopkins, et al., NF 47 (2007) 1157

## Slide 40: State Derivative Feedback Algorithm needed for Current Control
Previously published approach found to be formally “uncontrollable” when applied to current control
State derivative feedback control approach
  new Ricatti equations to solve to derive control matrices – still “standard” solutions for this in control theory literature
Control vector, u; controller gain, Kc
Observer est., y; observer gain, Ko
Kc , Ko computed by standard methods
(e.g. Kalman filter used for observer)
Advance discrete state vector
(time update)
(measurement
update)
e.g. T.H.S. Abdelaziz, M. Valasek., Proc. of 16th IFAC World Congress, 2005
State equations to advance
General (portable) matrix output file for operator
Written into the PCS

## Slide 41: NSTX RWM state space controller sustains high bN, low li plasma – available for NSTX-U with independent coil control
RWM state space feedback (12 states)
n = 1 applied field suppression
  Suppressed disruption due to n = 1 field
Feedback phase scan
  Best feedback phase produced long pulse, bN = 6.4, bN/li = 13
NSTX Experiments
(from 2010)
Ip (MA)
(A)
Run time has been allocated for continued experiments on NSTX-U in 2016
S. Sabbagh et al., Nucl. Fusion 53 (2013) 104007

## Slide 42: RWM state space controller sustains otherwise disrupted plasma caused by DC n = 1 applied field
n = 1 DC applied field test
  Generate resonant field amplication, disruption
  Use of RWM state space controller sustains discharge
RWM state space controller sustains discharge at high bN
  Best feedback phase produced long pulse, bN = 6.4, bN/li = 13
140025
140026
Control
applied
Control not applied
bN
IRWM-4 (kA)
wf/2p~q=2
(kHz)
Bpn=1 (G)
Ip (MA)
n = 1 field on
0.0
0.2
0.4
0.6
0.8
1.0
t(s)
1.2
0.6
0.0
6
3
0
10
5
0
0.5
0.0
12
8
4
0
RWM state space feedback (12 states)
n = 3 correction
S. Sabbagh et al., Nucl. Fusion 53 (2013) 104007

## Slide 43: Open-loop comparisons between measurements and RWM state space controller show importance of states and model
Improved agreement with sufficient number of states (wall detail)
A) Effect of Number of States Used
dBp180
100
200
0
-100
RWM Sensor Differences (G)
137722
t (s)
40
0
80
0.56
0.58
0.60
137722
t (s)
0.56
0.58
0.60
0.62
dBp180
dBp90
dBp90
-40
0.62
t (s)
0.56
0.58
0.60
0.62
t (s)
0.56
0.58
0.60
0.62
100
200
0
-100
40
0
80
-40
7 States
B) Effect of 3D Model Used
No NBI Port
With NBI Port
2 States
RWM
3D detail of model important to improve agreement
Sensor data
Controller (observer)
RWM sensors
Sensor
data
Controller
(observer)
RWM

## Slide 44: In addition to active mode control, the NSTX-U RWM state space controller can be used for r/t disruption warning
Sensor
data
Controller
(observer)
The controller “observer” produces a physics model-based calculation of the expected sensor data – a synthetic diagnostic
If the real-time synthetic diagnostic doesn’t match the measured sensor data, a r/t disruption warning signal can be triggered
  Technique will be assessed using the DECAF code
RWM Sensor Differences (G)
RWM Sensor Differences (G)
137722
t (s)
40
0
80
0.56
0.58
0.60
137722
t (s)
0.56
0.58
0.60
0.62
dBp90
dBp90
-40
0.62
40
0
80
-40
Effect of 3D Model Used
No NBI Port
With NBI Port
RWM

## Slide 45: In addition to active mode control, the NSTX-U RWM state space controller can be used for real-time disruption warning
Sensor
data
Controller
(observer)
The controller “observer” produces a physics model-based calculation of the expected sensor data – a synthetic diagnostic
If the real-time synthetic diagnostic doesn’t match the measured sensor data, a r/t disruption warning signal can be triggered
  Technique will be assessed using the DECAF code
RWM Sensor Differences (G)
RWM Sensor Differences (G)
137722
t (s)
40
0
80
0.56
0.58
0.60
137722
t (s)
0.56
0.58
0.60
0.62
dBp90
dBp90
-40
0.62
40
0
80
-40
Effect of 3D Model Used
No NBI Port
With NBI Port
RWM

## Slide 46: Bounce resonance stabilization dominates for DIII-D vs. precession drift resonance for NSTX at similar, high rotation
DIII-D experimental rotation profile
NSTX experimental rotation profile
|δWK| for trapped resonant ions vs. scaled experimental rotation (MISK)
133103 @ 3.330 s
stable plasma
133776 @ 0.861 s
stable plasma
precession
resonance
bounce / circulating
resonance
precession
resonance
bounce / circulating
resonance
DIII-D
NSTX

## Slide 47: Increased RWM stability measured in DIII-D plasmas as qmin is reduced is consistent with kinetic RWM theory
|δWK| for trapped resonant ions vs. scaled experimental rotation (MISK)
Measured plasma response to 20 Hz, n = 1 field vs qmin
n = 1 |dBp | (G/kA)
qmin
DIII-D experimental rotation profile
precession drift
resonance
bounce /
circulating
resonance
DIII-D (qmin = 1.2)
DIII-D (qmin = 1.6)
DIII-D (qmin = 2.8)
Bounce resonance dominates precession drift resonance for all qmin examined at the experimental rotation
less stable

## Slide 48: When Ti is included in NTV rotation controller model, 3D field current and NBI power can compensate for Ti variations
t (s)
t (s)
3D coil current and NBI power (actuators)
yN
NBI, NTV torque density (N/m2)
Plasma rotation (rad/s)
NTV
torque
104
desired wf
t1
t3
NBI
torque
t1 = 0.59s
t2 = 0.69s
t3 = 0.79s
NTV torque profile model for feedback dependent on ion temperature
Rotation evolution and NBI and NTV torque profiles
K1 = 0, K2 = 2.5
3D Coil Current (kA)
0.5
0.7
0.9
1.0
0.8
1.2
1.4
1.6
1.8
2.0
0.5
0.7
0.9
Ti (keV)
0.6
1.2
1.8
0.0
t (s)
0.5
0.7
0.9
0.8
0.6
0.4
NBI power (MW)
7
1
0
6
5
4
3
2
t2
t1
t3
t2
t1
t2
t3
0
6
8
4
2
10
0.0
0.2
0.4
0.6
0.8
1.0
0.0
0.5
1.0
1.5
2.0
2.5
t1
t3
t2

## Slide 49: NSTX-U: RWM active control capability increases as proposed 3D coils upgrade (NCC coils) are added
Partial 1x12 NCC coil set significantly enhances control
  Present RWM coils: active control to bN/bNno-wall = 1.25
  NCC 1x12 coils: active control to bN/bNno-wall = 1.52
Existing
RWM
coils
NCC upper (1x12) (plasma facing side)
Using present midplane RWM coils
Partial NCC 1x12 (upper), favorable sensors

## Slide 50: ITER High Priority need: What levels of plasma disturbances (dBp; dBp/Bp(a)) are permissible to avoid disruption?
NSTX RWM-induced disruptions analyzed
  Same database analyzed by DECAF in prior slides
Compare maximum dBp (n = 1 amplitude) causing disruption vs Ip
Maximum dBp increases with Ip
Next step: add results from other devices
NSTX
RWM-induced
Disruptions
(n = 1 global
MHD mode)

## Slide 51: Maximum dBp might follow a de Vries-style engineering scaling Ipp1lip2/ap3q95p4
NSTX RWM-induced disruptions
Compare maximum dBp causing disruption to de Vries locked NTM scaling
  engineering parameters
  Data shows significant scatter (as does de Vries’ analysis for NTM)
NSTX
RWM-induced
Disruptions
(n = 1 global
MHD mode)

## Slide 52: Maximum dBp/<Bp(a)> might follow a de Vries-style scaling lip1/q95p2
NSTX RWM-induced disruptions
Compare maximum dBp causing disruption vs. de Vries locked NTM scaling
  Normalized parameters
NSTX analysis uses kinetic EFIT reconstructions
  li instead of li(3)
  <Bp(a)>fsa used
NSTX
RWM-induced
Disruptions
(n = 1 global
MHD mode)

## Slide 53: In contrast, maximum dBp/<Bp(a)> seems independent of scaling on (li) or (Fp) (or (Fp/li))
Fp = ptot(0)/<ptot>vol (from kinetic equilibrium reconstructions)
Dependence on li, Fp expected for RWM marginal stability points
NSTX
RWM-induced
Disruptions
(n = 1 global
MHD mode)
internal inductance
total pressure peaking factor