## Slide 1: Advanced Scenarios and Control
Devon Battaglia for the NSTX-U team
NSTX-U PAC 39
January 9-10, 2018

## Slide 2: Research Thrusts of the Advanced Scenarios and Control Topical Science Group (TSG)
Demonstrate non-inductive sustainment for multiple τR
  NSTX-U designed to be world-leading in investigating 100% NI scenarios in a low-aspect ratio configuration
Develop partially inductive scenarios and advanced control to support the broad scientific program
Advance real-time control and scenario modeling for fusion energy research and next-step devices

## Slide 3: Research Thrusts of the Advanced Scenarios and Control Topical Science Group (TSG)
Demonstrate non-inductive sustainment for multiple τR
  NSTX-U designed to be world-leading in investigating 100% NI scenarios in a low-aspect ratio configuration
Develop partially inductive scenarios and advanced control to support the broad scientific program
Advance real-time control and scenario modeling for fusion energy research and next-step devices

## Slide 4: Non-inductive operation on an ST provides crucial information needed to optimize the A of next-step devices
Non-inductive (NI) current sustainment is required for a continuous tokamak reactor
  NI operation at low-A will have unique challenges and opportunities
NSTX-U will have world-leading capabilities for investigating stationary NI scenarios at low-A
  Largest Ip, BT NI operation in an ST
  Real-time control of J, P, vϕ profiles
Non-inductive current fraction
NSTX-U TRANSP
Projections
NSTX data
Gerhardt et al., NF 52 (2012) 083020

## Slide 5: STs can access a non-inductive (NI) regime with broad pressure and current profiles at high βN
Performance of non-inductive scenarios in tokamaks improves with lower qcyl
  NSTX accesses large βN/li  offset lower qcyl in fBS
  Broad J (low li) aligns with large edge JBS from broad P
STs achieve naturally large κ, δ
STs can operate with stability margin at large values of global βN
  NSTX-U NI target: βN ~ 5 - 6, li ~ 0.5
S.A. Sabbagh, NF 46 (2006) 635
Do the potential benefits exceed the challenges of large BT at low-A?

## Slide 6: BT = 1T operation will enable unique high-performance NI scenarios at high β
Chart: Ip (MA)
| 0.87 | 0.75
 | 0.032745 | 0.022248
 | 0.016803 | 0.014715
Ip and <nT> of 100% NI increase with BT
  βN limited by qmin > 1 at BT=0.75T
  βN limited by confinement at BT = 1T
nτeT 1020 m-3 s keV
100% NI NSTX-U TRANSP
BT = 0.75 T
PNBI = 6.8 MW
βN = 4.3 – 4.9
Peaked
Broad
Peaked
Broad
BT = 1.0 T
PNBI = 10.2 MW
βN = 4 – 4.3
fGW = 0.72
tpulse = 5 s
H98y,2 = 1
Adapted from Gerhardt et al., NF 52 (2012) 083020

## Slide 7: BT = 1T operation will enable unique high-performance NI scenarios at high β
Chart: Ip (MA)
| 0.87 | 0.75
 | 0.032745 | 0.022248
 | 0.016803 | 0.014715
 | 0.034093 | 0.031176
 | 0.13361 | 0.1378
Ip and <nT> of 100% NI increase with BT
  βN limited by qmin > 1 at BT=0.75T
  βN limited by confinement at BT = 1T
Performance scales with confinement
  ST scaling projects to larger sustained NI Ip
    H98y,2 ~ Ip1.34 BT0.15 fGW.41
    HST ~ Ip1.01 BT1.08 fGW.44
  Differences in performance between scaling relations becomes larger as BT increases
    See T&T TSG presentation (Guttenfelder)
nτeT 1020 m-3 s keV
100% NI NSTX-U TRANSP
fGW = 0.72
tpulse = 5 s
HST = 1
BT = 0.75 T
PNBI = 6.8 MW
βN = 4.8 – 5.3
H98y,2 = 1.05
BT = 1.0 T
PNBI = 10.2 MW
βN = 4.9 – 5.3
H98y,2 = 1.2
Adapted from Gerhardt et al., NF 52 (2012) 083020

## Slide 8: BT = 1T operation will enable unique high-performance NI scenarios at high β
Chart: Ip (MA)
| 0.87 | 0.75
 | 0.032745 | 0.022248
 | 0.016803 | 0.014715
 | 0.034093 | 0.031176
 | 0.13361 | 0.1378
 | 0.15126 | 0.076418
Ip and <nT> of 100% NI increase with BT
  βN limited by qmin > 1 at BT=0.75T
  βN limited by confinement at BT = 1T
Performance scales with confinement
  ST scaling projects to larger sustained NI Ip
    H98y,2 ~ Ip1.34 BT0.15 fGW.41
    HST ~ Ip1.01 BT1.08 fGW.44
  Differences in performance between scaling relations becomes larger as BT increases
    See T&T TSG presentation (Guttenfelder)
βN transport limited at BT = 1T
  Achieve qmin > 1 with global stability margin at highest PNBI (tpulse = 1.5 s ~ τR)
nτeT 1020 m-3 s keV
100% NI NSTX-U TRANSP
fGW = 0.72
BT = 1.0 T
HST = 1
βN = 5.7
PNBI = 15.6 MW
BT = 1.0 T
H98y,2 = 1
βN = 4.8
PNBI = 15.6 MW
Adapted from Gerhardt et al., NF 52 (2012) 083020

## Slide 9: BT = 1T operation will enable unique high-performance NI scenarios at high β
Chart: Ip (MA)
| 0.87 | 0.75
 | 0.032745 | 0.022248
 | 0.016803 | 0.014715
 | 0.034093 | 0.031176
 | 0.13361 | 0.1378
 | 0.15126 | 0.076418
Ip and <nT> of 100% NI increase with BT
  βN limited by qmin > 1 at BT=0.75T
  βN limited by confinement at BT = 1T
Performance scales with confinement
  ST scaling projects to larger sustained NI Ip
    H98y,2 ~ Ip1.34 BT0.15 fGW.41
    HST ~ Ip1.01 BT1.08 fGW.44
  Differences in performance between scaling relations becomes larger as BT increases
    See T&T TSG presentation (Guttenfelder)
βN transport limited at BT = 1T
  Achieve qmin > 1 with global stability margin at highest PNBI (tpulse = 1.5 s ~ τR)
NSTX-U has potential for demonstrating NI performance similar to A=3 devices
nτeT 1020 m-3 s keV
100% NI NSTX-U TRANSP
fGW = 0.72
BT = 0.75 T
H98y,2 = 1
BT = 0.75 T
HST = 1
BT = 1.0 T
HST = 1
BT = 1.0 T
H98y,2 = 1
DIII-D 100% NI demonstrated
βN = 3, BT ~ 2T
H98y,2 ≥ 1.2
Adapted from Gerhardt et al., NF 52 (2012) 083020

## Slide 10: NSTX-U has a suite of real-time control capabilities for optimizing NI scenarios
Six NBI lines 65 - 100 keV at different Rtang
Real-time profile measurements
  rtCHERS (RTV): vϕ control
  rtMSE: J and q control (in progress)
  rtMPTS: P constraint, ne feedback (in progress)
Flexible plasma control system (PCS) with parallelized real-time EFIT
  Profile control algorithms developed and tested via integration with TRANSP
  Parallelized PCS architecture accelerates rtEFIT solution with profile constraints
    FY16 run: rtEFIT convergence interval maintained while doubling fitting constraints and resolution

## Slide 11: NSTX-U has a suite of real-time control capabilities for optimizing NI scenarios
Six NBI lines 65 - 100 keV at different Rtang
Real-time profile measurements
  rtCHERS (RTV): vϕ control
  rtMSE: J and q control (in progress)
  rtMPTS: P constraint, ne feedback (in progress)
Flexible plasma control system (PCS) with parallelized real-time EFIT
  Profile control algorithms developed and tested via integration with TRANSP
  Parallelized PCS architecture accelerates rtEFIT solution with profile constraints
    FY16 run: rtEFIT convergence interval maintained while doubling fitting constraints and resolution
Comparison of real-time CHERS system to standard CHERs
M. Podesta and R.E. Bell, PPCF 58 (2016) 125016

## Slide 12: NSTX-U has a suite of real-time control capabilities for optimizing NI scenarios
Six NBI lines 65 - 100 keV at different Rtang
Real-time profile measurements
  rtCHERS (RTV): vϕ control
  rtMSE: J and q control (in progress)
  rtMPTS: P constraint, ne feedback (in progress)
Flexible plasma control system (PCS) with parallelized real-time EFIT
  Profile control algorithms developed and tested via integration with TRANSP
  Parallelized PCS architecture accelerates rtEFIT solution with profile constraints
    FY16 run: rtEFIT convergence interval maintained while doubling fitting constraints and resolution
100% NI TRANSP Simulation
M.D. Boyer et al., NF 57 (2017) 066017
+10% density
Control on

## Slide 13: NSTX-U will have unique capabilities for developing NI scenarios compared to MAST-U
NSTX-U can access higher BT, Pheat in NI scenarios
  Access high density (fGW = 0.5 - 1), large fBS (> 70%) in stationary conditions for multiple τR at Ip ≥ 1 MA
Real-time NBI deposition control via outer gap and beam selection
Wall-stabilization for operation at βN above no-wall limit concurrently with broad J (low li)
MAST-U NSTX-U
 | MAST-U (2018) Planned | NSTX-U (2016) Achieved | MAST-U (stage 1) Planned | NSTX-U (full field) Planned
Max Ip (MA) | 1.0 | 1.0 | 2.0 | 2.0
Max BT at 0.936 m (T) | 0.513 | 0.635 | 0.684 | 1.0
NBI (MW) (Beam voltage) | 3.5 (75 keV) | 12 (90 keV) | 7.5 (75 keV) | 12 (90 keV)
tpulse at full field (s) | 1 | 1 | 5 | 5

## Slide 14: Realization and optimization of fully NI scenarios integrates research and development from multiple TSGs
Particle and impurity control in long pulse via wall conditioning, ELM control and RF heating
  Div-SOL TSG + Pedestal TSG + T&T TSG, Wave H&CD (Particle control task force)
NI scenario intimately linked to confinement and shape of the profiles
  Transport and Turbulence TSG + Pedestal TSG
Access to high-β requires stabilization of MHD modes
  Macroscopic Stability TSG
Core performance depends on deposition and transport of fast ions
  T&T TSG + Energetic Particles TSG
Compatibility of NI scenarios with heat flux control
  PFC WG + Materials TSG + Div-SOL TSG

## Slide 15: Research Thrusts of the Advanced Scenarios and Control Topical Science Group (TSG)
Demonstrate non-inductive sustainment for multiple τR
  NSTX-U designed to be world-leading in investigating 100% NI scenarios in a low-aspect ratio configuration
Develop partially inductive scenarios and advanced control to support the broad scientific program
Advance real-time control and scenario modeling for fusion energy research and next-step devices

## Slide 16: Progress in FY16 toward developing inductive low-li, high-κ H-mode scenario
NSTX
0.44 T
H-mode
NSTX-U
0.62 T
Week 3
No EFC
Week 5
EFC v1
Week 7
EFC v2
140702
202946
203679
204112
Demonstrated stable operation at κ similar to NSTX despite higher aspect ratio for li > 0.8
NSTX 10 years
NSTX-U 10 weeks
Elongation
Internal inductance
NSTX-U target
J.E. Menard Nucl. Fusion 2017

## Slide 17: MHD-quiescent H-mode discharges sustained with H98y,2 ≥ 1 and βN/βno-wall ≥ 1
n = 1
n = 2
n = 3
n = 4
204112
Minimal core MHD
  H98y,2 ≥ 1
βN/βno-wall ≥ 1
J. Berkery PoP 24 (2017) 056103
J.E. Menard Nucl. Fusion 2017
D.J. Battaglia Nucl. Fusion 2018
204112
Ip = 0.9 MA
BT = 0.63 T
PNBI = 5.5 MW
H-mode scenario was difficult to reliably repeat during final two weeks of operations

## Slide 18: Present ASC focus is modeling and analysis to accelerate scenario development at restart
FY17-19 ASC research milestones: develop reliable ramp-up to low-li, high-κ, high-Ip
  FY17 milestone identified constraints on elongation, stability and the L-H transition
  FY18-19 develop a framework for predictive modeling for the breakdown and rampup
    Primary tools: TOKSYS and TRANSP
Initiated collaboration with MAST-U for developing shared tools and analysis
  Example: start-up modeling of MAST-U
    See Stan Kaye’s Collaboration talk
  Focus is development of similar startup and ramp-up modeling tools and experiments
Overshooting the 2cm inner gap target is bad for vertical stability
Solution: active control of the inner gap

## Slide 19: Research Thrusts of the Advanced Scenarios and Control Topical Science Group (TSG)
Demonstrate non-inductive sustainment for multiple τR
  NSTX-U designed to be world-leading in investigating 100% NI scenarios in a low-aspect ratio configuration
Develop partially inductive scenarios and advanced control to support the broad scientific program
Advance real-time control and scenario modeling for fusion energy research and next-step devices

## Slide 20: PPPL leads development of TRANSP as a tool for modeling and testing of scenarios and control
Predictive modeling with assumed transport properties
  Identify scenarios with relaxed J profile
  Minimize flux consumption of ramp-up (backup)
Integrate control algorithm into TRANSP for testing and development (slide 8 and )
Use TRANSP database to develop linearized or neural network control model (backup)
  Planned expansion of PCS computation power to enable “faster than real-time prediction”
  Disruption avoidance and real-time scenario optimization
Coupled q0, βN feedback controller in TRANSP
M.D. Boyer, Nucl. Fusion (2015)
q0
βN
NBI Power
(MW)
Outer Gap
(cm)

## Slide 21: Real-time control development enables science and contributes to broader effort of tokamak control
State machine logic in PCS enables future expansion of disruption avoidance and protection
  FY16 demonstrated controlled ramp-down triggered by disruption warnings (backup)
NSTX-U researchers contribute to the development of advanced shape control algorithms and actuator sharing
  Involved in collaborations on MIMO shape control including snowflake divertor (Pat Vail, Princeton PhD)
Heat flux management with fish-scaled surfaces
  Integrate flaring or sweeping with angle-of-incidence control into target scenarios
  Possible future investment in heat flux measurements and control

## Slide 22: Summary: Recent results and new plans
Steady progress in FY16 toward developing low-li, high-κ H-mode scenario
  Matched NSTX κ for li > 0.8 despite larger A
  H-mode with MHD-free periods, H98y,2 ~ 1, βN/βN-no-wall ~ 1
Real-time control capabilities commissioned that enable scientific mission
  Real-time velocity diagnostic, parallelized rtEFIT …
Applying TRANSP to develop scenarios and real-time control
  Detailed investigations of access and control of 100% NI scenarios
  Developing and testing reduced models for control and real-time forecasting
Increased emphasis on angle-of-incidence control with new PFC design
  See Matt Reinke’s talk
  Integrate control into target scenarios and other heat flux mitigation methods

## Slide 23: Summary: Addressing critical issues
NSTX-U will be world-leading in the demonstration of fully non-inductive scenarios in an ST
  High field (BT = 1T), high power (PNBI = 10 – 15 MW) enables Ip ≥ 1 MA at high density (fGW ~ 0.5 - 1) and fBS > 70% for multiple τR
  Real-time measurement and control of J, P, vϕ profiles via 6 NBI injectors + outer gap with parallelized rtEFIT
Development of NI scenarios is a priority of the FY20 campaign
  Modeling, analysis and collaborations aim to accelerate the progress at restart
NSTX-U will continue to contribute to the development of critical control capabilities for tokamaks
  Profile control, disruption avoidance, actuator sharing, RWM control, real-time forecasting, machine protection …

## Slide 24: Back up

## Slide 25: Partially inductive scenarios expand the accessible regimes for scientific discovery
Non-inductive current fraction
NSTX-U
NSTX
Low ν*: BT = 2.0T, 15 MW, Ip ~ 2MA
High βN: BT = 0.55 T, 10 MW most off-axis,
Ip ~ 1 MA
Gerhardt et al., NF 52 (2012) 083020
(Trapezoids scan H98y,2  HST and broad  peaked profiles)

## Slide 26: First demonstration of stationary long-pulse sawtoothing L-mode on an ST used for first experiments on NSTX-U
0.7s
1.5s

## Slide 27: State machine logic in PCS enables future expansion of disruption avoidance and protection
FY16 run demonstrated controlled ramp-down triggered by disruption warnings
Notes: Ramp down should go to backup

## Slide 28: Non-inductive scenarios will access Ip > 1 MA within the stability envelop of NSTX
NSTX
A = 1.7
NSTX
TRANSP Simulations
S.P. Gerhardt et al., NF 52 (2012) 083020

## Slide 29: Modeling and future experiments focus on reducing inductive current in ramp-up scenarios
Investigate potential of HHFW + NBI for reducing OH flux consumption
  Couple reduced OH ramp-up to NI scenarios
  Work aims to determine current drive needs for next-step devices
  See Roger Raman’s talk
F.M. Poli et al., NF 55 (2015) 123011

## Slide 30: Recent work: Developing neural net models from TRANSP database of NSTX-U
“Faster than real-time” forecasting requires reduced models
  NUBEAM calculations can not be completed in real-time
  Solution is to develop a neural net model for the beam heating and current drive
Neural net model derived from NSTX-U BEAST database will be integrated into rtEFIT and forecasting algorithms
  BEAST: Between and Among Shots TRANSP
NN prediction
Testing shot
Dan Boyer, NSTX-U Monday Science Meeting 12/5/17