## Slide 1: NSTX-U PAC-39 Program Overview
J. Menard
For the NSTX-U Research and Recovery Teams
PPPL
January 9, 2018

## Slide 2: Outline
PAC Members and charge questions
ST and NSTX-U research goals
Program impacts from extended outage
Key questions addressed by NSTX-U
World-leading ST capabilities during initial ops
Summary

## Slide 3: Outline
PAC Members and charge questions
ST and NSTX-U research goals
Program impacts from extended outage
Key questions addressed by NSTX-U
World-leading ST capabilities during initial ops
Summary

## Slide 4: Thank you to PAC-39 members
new
new
new
Remote
Unavailable
Unavailable

## Slide 5: Process for this PAC
We request “real-time” PAC assistance in helping our team put forward the most compelling arguments for NSTX-U – the mission, program, facility / Recovery
  We encourage the PAC to request improved arguments and slide content homework - overnight especially, longer-term
  It would be most valuable to have any PAC consensus and endorsement of NSTX-U major strengths in the PPT debrief
Technical discussions should focus on the charges
Keep questions until end of talks to help stay on time

## Slide 6: PAC-39 Charge Questions
The NSTX-U research program requests PAC-39 comments and recommendations on:
Quality and importance of recent NSTX / NSTX-U research results
Uniqueness / timeliness of important questions NSTX-U will answer for fusion science
How / whether NSTX-U will be world-leading when operation resumes in 2020
Important scientific and technological findings since:
  Original physics design of NSTX-U (2009)
  And/or since the last 5 year plan was written (2014)
  And how such findings influence the impact of medium-term research on NSTX-U (2020-2025) and the long-term NSTX-U vision (2025-2030).

## Slide 7: Outline
PAC Members and charge questions
ST and NSTX-U research goals
Program impacts from extended outage
Key questions addressed by NSTX-U
World-leading ST capabilities during initial ops
Summary

## Slide 8: Low aspect ratio “Spherical Torus / Tokamak” (ST) vital for predictive capability for toroidal science and fusion energy
ST accesses unique regime of high normalized p
  Fundamental changes in nature of turbulence, MHD stability  Enhanced electromagnetic and super-Alfvénic effects
  STs can more easily study electron-scale turbulence at high temperature  Important for all toroidal configurations
  Neutral beam fast-ions in present STs mimic ITER DT fusion products  Study burning plasma science
If physics results favorable, STs could provide more economical fusion development & energy systems
  Potentially reduced magnet and device size and cost
ITER
Electromagnetic turbulence
Pilot Plant
FNSF / CTF

## Slide 9: High-current-density rare earth barium copper oxide (REBCO) superconductors motivate consideration of low-A pilot plants
Base cable: 50 tapes YBCO Tapes with 38 mm substrate
(Van Der Laan, HTS4Fusion, 2015)
Conductor on Round Core Cables (CORC): High winding pack current density at high magnetic field
JWP ~ 70MA/m2 at 19T
Higher current densities, B likely possible…
10 mm
10 mm
6 mm
7 kA CORC (4.2K, 19 T) cable
Chart: Pnet [MWe]
| 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.25 | 2.5 | 2.75 | 3 | 3.5 | 4
0.3 | -42.5779 | 36.6802 | 100.5919 | 110.8791 | 110.5433 | 103.3192 | 95.5508 | 81.2005 | 65.435 | 45.4267 | 5.1489 | -28.8353
0.4 | -72.7603 | -5.8829 | 57.8131 | 79.5166 | 90.225 | 92.7252 | 95.2754 | 81.181 | 65.4314 | 45.4256 | 5.1487 | -28.8353
0.5 | -125.2658 | -73.5657 | 5.2089 | 25.8632 | 37.2943 | 41.5085 | 49.304 | 57.3246 | 59.7178 | 45.4267 | 5.1489 | -28.8353
0.6 | -138.5857 | -118.0805 | -81.9554 | -56.7195 | -34.8841 | -17.8912 | 11.4901 | 26.6647 | 30.4871 | 25.6367 | 4.5439 | -28.8353
0.7 | -144.7239 | -139.4112 | -129.7223 | -122.6517 | -116.3479 | -111.3445 | -102.4945 | -87.7336 | -74.4052 | -66.6135 | -63.162 | -68.8654
20 | -144.7239 | -139.4112 | -129.7223 | -122.6517 | -116.3479 | -111.3445 | -102.4945 | -91.1684 | -96.1049 | -102.0119 | -113.118 | -121.7794
JWP [MA/m2]
12T
19T
Increasing JWP
R = 3m
TBR ~ 1
PNBI = 50MW
100% non-inductive
bN (A) at no-wall limit
A ~ 2 attractive at high JWP

## Slide 10: Example: A=2, R0 = 3m HTS-TF Pilot Plant
Cryostat volume ~ 1/3 of ITER
BT = 4T, IP = 12.5MA
k = 2.5, d = 0.55
bN = 4.2, bT = 9%, fgw = 0.8
H98 = 1.75, HPetty-08 = 1.3
HST = 0.7-0.9
fNI = 100%, fBS = 0.76
Startup IP (OH)~2MA
JWP = 70MA/m2
BT-max = 17.5T
No joints in TF
Vertical maintenance
Pfusion = 520 MW
PNBI = 50 MW
ENBI=0.5MeV
QDT = 10.4
Qeng = 1.35
Pnet = 73 MW
Wn = 1.3 MW/m2
Peak n-flux = 2.4 MW/m2
Peak n-fluence: 7MWy/m2
TBR  1
J. Menard, et al., Nucl. Fusion 56 (2016) 106023
ST confinement scaling uncertain, but potentially favorable
ST non-inductive sustainment at high performance remains to be demonstrated

## Slide 11: NSTX-U vital for predictive capability, fusion science Will access new physics with 2 new tools:
High normalized pressure at high T
 Unique regime, study new transport and stability physics
Sustain plasma without transformer
 Not yet achieved at high-T, low n*
Essential for any future steady-state ST
1. New Central Magnet
2. Tangential 2nd Neutral Beam

## Slide 12: NSTX / MAST confinement increased at higher Te Will confinement trend continue, or look like conventional A?
Normalized electron collisionality ne*  ne / Te2
BTtE
[T-s]
Low n*  need higher plasma current, toroidal field, heating power, density control
Continued favorable confinement trends could lead to more compact ST reactors
ST scaling: tE, th µ n*e-0.8 b-0.0
ITER 98y,2: tE, th µ n*e-0.1 b-0.9

## Slide 13: NSTX-U will access and measure novel regimes of electron turbulent transport driven by high beta
Energy confinement scaling from “micro-tearing” modes simulated to be similar to NSTX results
simulation
Guttenfelder, PRL (2011), PoP (2012)
Visualization courtesy F. Scotti (LLNL)
Normalized collision frequency
Normalized transport rate
ce (rs2cs/a)
NSTX experiment
0.1
1
10
0.1
1
10
NSTX-U regime
Dissipative trapped electron modes (DTEM)  similar scaling

## Slide 14: NSTX-U design enables access to 3× higher plasma pressure, temperature than MAST-U
MAST-U
NSTX-U
Conducting plates suppress kink instabilities,
1.5× higher bN, bT
NSTX-U design provides 1.4× higher BT and
2× higher BT2
p ∝ bT BT2
3× higher

## Slide 15: NSTX-U will test whether high-performance STs can be sustained for future fusion applications
Non-inductive current fraction
NSTX-U projections
NSTX data
New
2nd
NBI
1st
NBI
Gerhardt,
NF (2012)
NSTX-U greatly expands plasma current operating space:
100% non-inductive at ~1MA, 5s
Plasma current up to 2MA for 5s
NSTX ≤ 65% non-inductive
IP = 1MA for ~1s, 1.3MA for 0.2s
RTAN [cm]
__________________
50, 60, 70, 130
60, 70,120,130
70,110,120,130
n
e
/
n
Greenwald
0.95
0.72
IP=0.95MA, bN=5, bT = 10%, BT = 1T, PNBI = 10MW
Vary & control qmin via:
beam source
plasma density
outer gap (not shown)
Boyer, NF (2015)

## Slide 16: NSTX-U will be leading (only) ST able to access and study kinetic RWM physics in-depth
NSTX showed that resonant damping can stabilize resistive wall mode (RWM)
Reduced drift-kinetic MHD
RWM stability map
gtwall
Torque Profiles From 6
Different NBI Sources
Neutral
Beams
(TRANSP)
Largest Rtan
Smallest Rtan
Use neutral beams, rotation damping from 3D fields, other actuators to control rotation for RWM stability
Passive stabilizing plates:
bN  4 (no-wall)  6 (with-wall)
J. Berkery, Phys. Plasmas (2017)

## Slide 17: NSTX-U at high plasma current will play important role in understanding power exhaust width scaling
Significant uncertainty (factor of 2) in projected scrape-off layer heat flux width lq at full performance NSTX-U (2MA, 1T, 10MW)
Heuristic Drift Scaling [Eich, PRL 2011]: 1.9 [mm]
(used for Recovery PFC re-design – see Gerhardt presentation)
Multi-machine Eich Scaling (Eich, NF 2013): 2.0 [mm]
NSTX scaling (Gray, JNM 2011): 3.0 [mm]
MAST scaling (Thornton, PPCF 2014): 4.1 [mm]
XGC-1 simulation (unpublished – see backup): 3.0 [mm]
See M. Reinke presentation for more detail

## Slide 18: Outline
PAC Members and charge questions
ST and NSTX-U research goals
Program impacts from extended outage
Key questions addressed by NSTX-U
World-leading ST capabilities during initial ops
Summary

## Slide 19: REMINDER: In FY2016 NSTX-U had scientifically productive 1st year, but had to cease operations due to failed divertor PF coil
Achieved H-mode on 8th day of 10 weeks of operation
Surpassed magnetic field and pulse-duration of NSTX
Matched best NSTX H-mode performance at ~1MA
Identified, corrected dominant error fields (more to do…)
Commissioned all magnetic and kinetic profile diagnostics
New 2nd NBI suppresses Global Alfven Eigenmodes (GAE)
  Fredrickson – APS invited, PRL 2017
Implemented techniques for controlled plasma shut down, disruption detection, commissioned new tools for mitigation
PF1A upper coil failed very slowly over ~1000 pulses
Section of failed PF1AU
Several papers on NSTX-U results published, in-press, or submitted

## Slide 20: NSTX-U targeting major increase in performance
2× toroidal field (0.5  1T)
2× plasma current (1  2MA)
5× longer pulse (1  5s)
2× heating power (5  10MW)
Tangential NBI  2× current drive efficiency
Up to 10× higher nTE (~MJ plasmas)
4× divertor heat flux ( ITER levels)
2. Tangential 2nd Neutral Beam
1. New Central Magnet
Ultimate Performance Goals:

## Slide 21: Achieving NSTX-U Ultimate Performance Goals requires Recovery Project (see S. Gerhardt presentation)
FY2017: DOE requested PPPL to review “Extent of Condition” of entire NSTX-U facility including reliability, submit Corrective Action Plan (CAP)
Recovery = Implement CAP using operations funding: $48M base + $15M contingency
Normal / planned maintenance and run preparation: $34M base + $4M contingency
Recovery following DOE 413.3b guidelines

## Slide 22: Major program impacts due to Recovery (1)
Research operations delayed until sometime in FY20
  Several FY17 and FY18-19 research Milestones redirected toward Recovery / future operations
  In April, FES redirected NSTX-U funded “science” collaborators to new FES “ST” solicitation (international) and DIII-D solicitation
  NSTX-U University and Industry diagnostic collaborations remain funded in FY18, but smaller diagnostics can be relocated to other facilities
    Modest Recovery scope/funding for collaborating national labs – PFCs, diagnostics
  Within PPPL, NSTX-U researchers redirected to find collaboration opportunities – preferably aligned with NSTX-U research goals
  S. Kaye helped coordinate DIII-D National Campaign (FY17 only)
    S. Kaye also coordinating PPPL MAST-U collaborations, M. Ono for QUEST

## Slide 23: Major program impacts due to Recovery (2)
Improved / more in-depth understanding of divertor heat and halo loads requires re-design of some plasma facing components (Gerhardt presentation)
Changes to “polar regions” to minimize vacuum and magnet risk eliminate lower insulator, reduce inboard-outboard gap  no Coaxial Helicity Injection (Gerhardt presentation)
  Non-inductive start-up research carried out through collaborations  NSTX-U implementation deferred (Raman presentation)
No high-harmonic fast-wave (HHFW) enhancement scope in Recovery + budget uncertainty
  HHFW program on hiatus, retaining staff for re-start (budget-dependent)
  Recovery: modeling / projections of antenna limiter heat loading
  Possible future activities: Design of dedicated non-HHFW outboard limiter, RF test-stand activities to improve voltage stand-off / RF power coupling

## Slide 24: NSTX-U researchers actively engaged in Recovery
Aided Extent of Condition reviews:
  Aided in System Design Description (SDD) formulation, edits
  Design Validation and Verification Reviews (DVVRs)
    Aided in preparation of presentations, chit submission, chit response
New PFC requirements working group (click here for more info)
  Extent of Condition review process identified PFC power handling issues
    Narrower SOL width not incorporated in General Requirements Document (2009-2012)
    Increased halo peaking on IBDH  T-bar design insufficient
  Extensive equilibrium & heat-flux scans performed, more to come
Topical Science Group contributions:
  Re-assessed scenario needs: first 2yrs of ops + 5/7 year plan
    Magnetic balance and d variations influence PFC design considerations
  Assessed impact of polar region mods on research plans

## Slide 25: Overall NSTX-U goals balanced and coordinated across Recovery and Research departments
Experimental
Research
Operations
S. Gerhardt
RF Operations
R. Perkins
Physics Operations
D. Battaglia
Diagnostic
Operations & R&D
B. Stratton
Boundary Physics
Operations
M. Jaworski
Theory &
Simulation
A. Bhattacharjee
Publications &
Presentations
Computational
Support
G. Tchilinguirian
Integrated Scenarios
S. Gerhardt
Core Science
S. Kaye
Science Groups, Task Forces,
Working Groups
PFC Requirements Working Group
M. Reinke
(Oak Ridge National Lab)
Physics Analysis
S. Kaye
Disruption PAM Working Group
S. Sabbagh
(Columbia University)
Run Coordination
TBD for next run
Deputy: TBD
Systems Engineering
and Integration
S. Gerhardt
Integrated
Analysis
P. Titus
Diagnostics
R. Ellis III
Central I&C
G. Tchilinguirian
Real Time Control
& Protection
F. Hoffmann
Power Systems
J. Dellas
Heating Systems
T. Stevenson
Vacuum & Fueling
Systems
D. Cai
VV & Internal Hdwe
M. Smith
Magnets
S. Raftopoulos
Cooling & Bakeout
Systems
J. Petrella
Test Cell
N. Atnafu
Planning & Control
S. Langish
COEs
Plasma Facing
Components
M. Jaworski
Tokamak
Core
D. Loesser
Responsible Engineers
Project Administration
K. Lukazik
Operations, ASO
T. Stevenson
Red = OBS
Construction
L. Dudek
CAD
Integration
J. Mitchell
Work Control
Center
F. Jones
Project Manager
R. Feder
NSTX-U Recovery
Director: J. Menard
Deputy: S. Gerhardt
Quality Assurance
F. Malinowski
ES&H
J. Levine
Chief Engineer
V. Riccardo
Procurement Liaison
A. White
Project Engineer
C. Neumeyer
Planning & Control
T. Egebo
NSTX-U Research
Director: J. Menard
Deputy: S. Kaye
Deliver reliable facility to support science goals within available resources
Requirements to achieve operational scenarios (example: magnet alignment vs error-fields)
PFC RE is physicist ensuring requirements and research goals are met
Particle Control
Task Force - TBD
Boundary Science
R. Maingi

## Slide 26: FY18 Recovery Notable Outcomes (Notable Outcome = annual DOE management contract goal)
Complete final design reviews for the 6 PF1 coils 3/31/2018
Prepare Recovery project to be ready for baselining (4/30/2018)
Build at least one prototype PF1A coil (7/15/2018)
  Qualify coil by operating at both max required current, max heating
  Verify the quality of the coil's insulation system through electrical testing followed by destructive sectioning and inspection
Build and test at least one of each type (PF1A, B, C) of production inner poloidal field coil (9/30/2018)
  Qualify a PF1A coil by operating at both max required current, max heating

## Slide 27: FY18 Research Milestones
Notable Outcome: Provide leadership, coordination, support to FES joint research target (JRT) with goal of testing predictive models of fast-ion transport by multiple Alfven eigenmodes.
Research:
  Develop/benchmark reduced heat flux & thermo-mech. models for PFC monitoring
  Develop simulation framework for ST breakdown and current ramp-up
  Validate & further develop reduced transport models for electron thermal transport
  Optimize energetic particle distribution function for improved plasma performance
Facility: Evaluate PFC operational limits and develop integrated diagnostic plans for operations

## Slide 28: Outline
PAC Members and charge questions
ST and NSTX-U research goals
Program impacts from extended outage
Key questions addressed by NSTX-U
World-leading ST capabilities during initial ops
Summary

## Slide 29: Science Group presentations address key questions
Key research questions: First 1-3 years, 3-5 years, 5-10 years
Can a high-performance ST have 100% non-inductive current, equilibrated?
Does “ST” confinement scaling persist to (3× to 6×) lower collisionality n*?
Can Alfvénic instabilities be modelled/understood, manipulated to control core?
Can passive & active RWM stabilization be achieved at low n* and sustained?
How will pedestal transport & turbulence vary vs lower n*, higher IP, Li coatings
How does heat-flux width scale? Can ne control be sustained? (see backup)
Can heat fluxes be mitigated consistent with high core performance?
Can liquid metals provide a solution for higher confinement, power exhaust?
Can high-harmonic fast-waves provide reliable heating and CD in H-mode?
Can NSTX-U demonstrate solenoidal-free initiation, ramp-up, and flat-top?
Core
W. Guttenfelder
M. Podesta
S. Sabbagh
Boundary
A. Diallo
M. Reinke
M. Jaworski
Scenarios
D. Battaglia
Scenarios
R. Perkins
R. Raman
Science Group and presenter

## Slide 30: NSTX-U will be world-leading ST in several research areas when operations resume
Access up to 3× higher ST pressure, temperature
Study transport physics in unique regime: high b, low n*
  Advanced diagnostics for electron and ion-scale turbulence
  Li-coatings (on C) for confinement vs. recycling in large ST
Only ST to access to wall-stabilized regime, highest b values through kinetic stabilization, advanced control
High-power NBI heating and current drive tools ready to:
  Pursue 100% non-inductive scenarios at high-performance
  Study high divertor heat flux mitigation (sweep, flare, detach, …)
  Explore fast-ion instabilities and control for burning plasmas
Complement DIII-D higher-A, MAST-U boundary emphasis

## Slide 31: Summary: NSTX-U will address key scientific issues to accelerate fusion science understanding, performance
Fusion Technology and Performance
High-temperature superconductors for compact and efficient ST fusion core
Liquid metal blankets for high thermal efficiency
ST Pilot Plant for
net electricity
NSTX Explored ST stability & confinement
Provide steady-state fusion neutron environment for nuclear material and component R&D
ST-based fusion neutron source
ST = Spherical Torus:
A magnetic confinement configuration that could lead to a smaller and more cost-competitive fusion energy source
Demonstrate sustainment for future steady-state operation
Longer-term: High-power tests of liquid metals as transformative wall solution
Advanced diagnostics + computation provide fundamental understanding and basis for next-step ST devices
Extend ST confinement understanding to fusion-relevant temperatures
NSTX Upgrade Facility and Research Program
Fundamental Plasma and Materials Science

## Slide 32: NSTX-U Backup

## Slide 33: NSTX-U Mission Elements
Explore unique ST parameter regimes to advance predictive capability for burning plasmas and beyond
Develop solutions for plasma- material interface challenge
Advance ST as Fusion Nuclear Science Facility and Pilot Plant
Liquid metals / Lithium
Snowflake / X
ST-FNSF /
Pilot-Plant

## Slide 34: NSTX-U and DIII-D are powerful and complementary tools enabling U.S. leadership in core fusion science
Variation of aspect ratio A provides robust physics validation
  Understand tokamak MHD stability, thermal and fast ion transport, pedestal structure
Together, NSTX-U and DIII-D provide the U.S. world-leading and complementary capabilities to address core physics issues
  Both have excellent diagnostics, strong and flexible beam and wave heating systems
  Complementary boundary approaches: cryo-pumping vs. lithium, solid vs. liquid
  Together, can identify optimal aspect ratio for possible fusion next-steps
DIII-D
A = 3
San Diego, CA
NSTX-U
A = 1.6
Princeton, NJ

## Slide 35: NSTX-U and MAST-U are the most capable ST devices in a world-wide ST research program
MAST-U – emphasis on boundary
  Designed with world’s most flexible, well-diagnosed power exhaust system (super-X divertor) for heat-flux mitigation studies
NSTX-U
Princeton, NJ
NSTX-U – emphasis on core
  Designed to access highest ST plasma pressure, temperature by 3×, bT & bN by 1.5×
  Diagnose, understand core transport and turbulence, stability, sustainment
Together, NSTX-U and MAST-U will provide majority of ST physics basis
Complementary Research:
MAST-U
Culham, UK

## Slide 36: NSTX-U excellent testbed for -particle physics
NSTX-U: larger fast-ion dynamic range spanning ST and conventional A
  Toroidal field 2× NSTX  can stabilize modes (Vf < VA )
  Tangential 2nd NBI  highly flexible fast-ion distribution
    Vary pitch angle, pressure profile
Are fast-ions well confined in high-performance ST regimes?
Can we predict fast-ion confinement for burning plasmas / ITER?

## Slide 37: NSTX-U experiments at higher plasma current will play important role in understanding power exhaust width
2MA NSTX-U
XGC1 simulations predict turbulence will widen edge heat flux in ITER
Preliminary XGC1 shows deviation from lq ~ IP-1 for full current (2MA) NSTX-U
Need additional simulations and analysis to better understand underlying physics, implications for STs
C.S. Chang et al 2017 Nucl. Fusion 57 116023
1MA NSTX-U

## Slide 38: NSTX-U will study confinement improvement from Li wall coatings, and power exhaust on liquid metal divertors
D.P. Boyle, et al., J. Nucl. Mater. 438 (2013) S979
H98~1
NSTX-U: Will double Li deposition, increase confinement
Test liquid metals for power handling
Example: Capillary Porous System
M. Jaworski, PPCF (2013)
NSTX: Higher lithium deposition  higher confinement

## Slide 39: STs leading advanced divertor development NSTX-U / MAST-U collaborating on 1st plasma, scenarios, divertors
MAST-U: world-leading tests of long-leg/super-X w/ variable flaring
E. Havlickova, et al., Plasma Phys. Control. Fusion 56 (2014) 075008
NSTX-U: Flared divertor using “snowflake / X” + radiation
New PF1 coils in NSTX-U central magnet

## Slide 40: Motivations for future facility enhancements
Divertor cryo-pump (graphite  high-Z PFCs)
  Control density and n* without Li, compare to Li wall-coatings
  Use bakeable baffle + high-Z PFCs for initial liquid metal tests
NCC
Existing
RWM/EFC coils
Full toroidal
array (2×12)
28GHz / 1-2MW gyrotron (Tsukuba)
  EC/EBW-only current-drive for start-up
  Heat helicity injection target with ECH for HHFW/NBI
  Longer-term: EBW CD for sustainment
Non-axisymmetric control coils (NCC)
  Resonant/non-resonant NTV rotation control, enhanced RWM/EF control
  Assess RMP ELM suppression (not yet achieved in ST)
Transition from all graphite to W/TZM PFCs
  Assess integration of high-performance ST with reactor-relevant wall
  Implement wall compatible with bulk / flowing liquid metals
  Extend LTX-b liquid-Li confinement experiments to higher performance

## Slide 41: FNSF / Pilot Plant Backup

## Slide 42: Design studies show ST potentially attractive as Fusion Nuclear Science Facility (FNSF) or Pilot Plant
FNSF with copper TF coils
A=1.7, R0 = 1.7m, x = 2.7
Fluence = 6MWy/m2, TBR ~ 1
FNSF / Pilot Plant with HTS TF coils
A=2, R0 = 3m, x = 2.5
6MWy/m2, TBR ~ 1, Qeng ~ 1
FNSF: Provide neutron fluence for material/component R&D (+ T self-sufficiency?)
Pilot Plant: Electrical self-sufficiency: Qeng = Pelec / Pconsumed ≥ 1 (+ FNSF mission?)

## Slide 43: At lower A, high TF winding-pack current density enables access to maximum allowed BT at coil
12T: ITER-like TF coil limit
(Nb3Sn, 11.8T)
19T: Present CORC HTS limit
Chart: Max BT at TF coil [T]
| 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.25 | 2.5 | 2.75 | 3 | 3.5 | 4
160 | 18.3214 | 18.7622 | 19 | 19 | 19 | 19 | 19 | 19 | 19 | 19 | 19 | 19
80 | 16.433 | 17.1602 | 17.7576 | 18.1294 | 18.4409 | 18.7044 | 18.9935 | 18.9996 | 18.9999 | 19 | 19 | 19
40 | 11.266 | 13.8912 | 16.0357 | 16.4935 | 16.8683 | 17.1797 | 17.6277 | 18.277 | 18.8214 | 19 | 19 | 19
30 | 8.4495 | 10.4184 | 12.1777 | 13.3057 | 14.277 | 15.1135 | 16.3799 | 17.2829 | 17.8659 | 18.3192 | 18.9755 | 19
20 | 5.633 | 6.9456 | 8.1185 | 8.8704 | 9.518 | 10.0757 | 10.9199 | 12.2231 | 13.3857 | 14.3299 | 15.7496 | 16.7393
20 (12T) | 5.633 | 6.9456 | 8.1185 | 8.8704 | 9.518 | 10.0757 | 10.9199 | 12 | 12 | 12 | 12 | 12
Coil structure sized to maintain ≤ 0.3% strain on winding pack
Effective inboard tungsten carbide (WC) neutron shield thickness = 60cm
JWP [MA/m2]
(12T)

## Slide 44: A = 1.8-2.3 maximizes TF magnet utilization, and TF will be significant fraction of core cost
0.3m
0.4m
0.5m
0.6m
0.7m
Eff. shield
thickness:
JWP = 70MA/m2
A=4 utilization ~1/3-1/2 of maximum at low A
Optimal range

## Slide 45: A ≥ 3 maximizes blanket volume utilization
JWP = 70MA/m2
0.3m
0.4m
0.5m
0.6m
0.7m
Eff. shield
thickness: