## Slide 1: Solenoid-Free Plasma Start-Up & Ramp-Up
1R. Raman, 2D. Mueller, 2M. Ono, 2F. Poli, 2F. Ebrahimi
1 University of Washington
2 Princeton Plasma Physics Laboratory
NSTX-U PAC-39
Princeton Plasma Physics Laboratory
January 9-10, 2018

## Slide 2: Solenoid-free Start-up and Ramp-up are Critical Issues for Compact ST and Tokamak-based Reactors
ECH / EBW – Utilize 1 – 2 MW 28 GHZ gyrotron
CHI – Coaxial Helicity Injection up to ~ 400 kA
LHI – Local Helicity Injection up to ~ 400 kA
HHFW - ~ 4 MW 30 MHZ high Harmonic Fast Wave
NBI - ~ 10 MW NBI
NSTX-U
IP [MA]
NBI
Time
HHFW
ECH/EBW, CHI, LHI
Solenoid-free
Start-up phase
Current ramp-up
phase
0 MA 0.4 MW 1 MA
ST has been addressing critical issue of solenoid-free start-up
  A compact ST has little space for a central solenoid
  Solenoid-free start-up is also attractive for tokamak designs
Maximizing solenoid-free start-up currents reduces reliance on less developed non inductive current ramp-up scenarios
Few MA start-up current is projected for reactors
  Higher currents may be feasible

## Slide 3: Solenoid-Free Start-Up / Ramp-Up Present Plans
NSTX-U can start with Ramp-Up studies using inductively generated targets with HHFW & NBI, as in original plan.
  Eventual goal is to transfer this capability to CHI/LHI/ECH started targets when one or more of these are implemented on NSTX-U
NSTX-U SFPS experiments deferred in the near term; progress will be made through collaborations and theory/modeling:
  Supporting ECH / EBW start-up studies being conducted on QUEST
  Pegasus has been investigating Local Helicity Injection
  Supporting CHI work being conducted on QUEST in Japan

## Slide 4: On NSTX-U, Non-inductive Ramp-Up from ~0.4MA to ~1MA Projected to be Possible With New CS + More Tangential 2nd NBI
2nd NBI provides 3-4x higher CD at low IP:
  2x higher absorption (4080%) at low IP = 0.4MA
    Will test on NSTX-U during YRS 1 & 2
  1.5-2x higher current drive efficiency
First NBI
More tangential
2nd NBI
First NBI
2nd NBI
NBI
HHFW
NBCD
bootstrap
FWCD
ohmic
non-inductive
plasma
TRANSP
Simulations
F. Poli, PPPL

## Slide 5: High Current Helicity Injection Start-Up can Reduce Reliance on Less Understood Current Ramp-Scenarios
Method | Device | Current Scaling | Present Demonstrations
ECH / EBW | MAST QUEST | Current scaling not understood | <100 kA on QUEST & MAST (Not coupled to induction)
Local Helicity Injection (LHI) [Small area electrodes / high voltage] | Pegasus | Dynamo Current Drive models need development | 200 kA on Pegasus (Coupled to induction)
Steady State CHI [Large area electrodes / lower voltage] | HIT-II HIST | Dynamo Current Drive models need development | 400 kA on NSTX 200 kA on HIT-II (Not coupled to induction)
Transient CHI [Short 2-3ms pulse discharge] | HIT-II NSTX QUEST | Scaling to large devices well understood | 200kA on NSTX 100 kA on HIT-II Demonstrated flux saving on NSTX by ramping to 1MA with inductive drive

## Slide 6: QUEST Has an On-Going Active Program on ECH NSTX-U is Contributing via. Theory and Diagnostic Support
Current efficiency increased from 66kA/270kW to 85kA/230kW using new wave guides and polarizer
Further polarizer improvements should enable higher power (available up to 400 kW) operations.
Model validation of non-thermal electron tail created by the ECCD being carried out by PPPL researchers (Bertelli, Poli, Taylor)
X-ray camera from PPPL together with modeling to improve understanding of physics of ECCD (Delgado-Aparicio)
Initial 28 GHz plasma current ramp-up experiments on QUEST
Target

## Slide 7: 28GHz-34.8GHｚ Two Frequency Gyrotron Development by University of Tsukuba, Japan
• High power test to be conducted in 2018 for > 1.5 MW at 28 GHz.
• CPD (Cathode Potential Depressor) increased the tube efficiency to ~ 50%
• Double disk window developed for long-pulse/steady-state operations
• High power tube should be technically available for NSTX-U within two years
T. Kariya, NF 2017

## Slide 8: Local Helicity Injection (LHI) Providing High-Ip Start-Up being Developed on Pegasus ST (Univ. of Wisconsin)
LHI Injector Geometries Vary Dominant Drive on Pegasus
LHI-Driven Ip ~ 0.2 MA Scenarios Test Predictive Ip(t) Model
Outboard: VIND Dominant
Inboard: VLHI Dominant
J.A. Reusch,et. al, PoP (submitted)
LHI provides non-solenoidal startup and sustainment:
  Ip ≤ 0.2MA to date (with less than 8 kA of injected current)
  Inboard and outboard injection location investigated
LHI also enables access to interesting physics regimes:
  The current drive mechanism does appear to fundamentally be due to edge localized reconnection activity
  Strong edge drive provides access to low ℓi and very high bT plasmas at relatively high Ip discharges at very low 𝐵T

## Slide 9: Transient CHI: High Fraction of Open to Closed Flux Conversion in NIMROD Simulations & in Experiments
F. Ebrahimi, PPPL
Transient CHI injects poloidal magnetic flux from divertor area into vessel on a 1-3ms time scale
  Injector flux shaping and injector current ramp-down causes open flux to form closed flux surfaces (like in a soap bubble)
Promising PoP level tests on NSTX-U motivated us (during the NSTX-U construction period) to examine and develop CHI implementation concepts for a reactor (R. Raman, et al., Fus. Sci. Technol. 68, 674 (2015))
Encouraged QUEST to implement & test reactor-relevant CHI capability
Significantly ramped up computational modeling work to understand CHI scaling
Theory and NSTX-U/HIT-II Experimental work has resulted in simple scaling relation for transient CHI to project to reactor scale devices (Ip Injected flux)
NSTX

## Slide 10: QUEST (in Japan) is Developing Reactor-Relevant CHI Configuration & Will Test ECH Heating of a Transient CHI Plasma
Injector
Flux
Current injection
In reactor concept insulator can be shielded from neutrons
Insulator not part of vacuum boundary as on NSTX
  Needs experimental test / verification
CHI system on QUEST is similar in concept to the one planned for NSTX-U
CHI Insulator
QUEST CHI is a NSTX-U CHI Team Led Effort
Initial injector current direction
Plasma growth

## Slide 11: Transient CHI Discharges Successfully Established in QUEST
ECH heating to be tested during 2018

## Slide 12: Solenoid-Free Start-Up / Ramp-Up NSTX-U Plans Utilize Multiple Facilities
NSTX-U Ramp-Up studies will continue using inductively generated targets with HHFW & NBI, as in original plan.
NSTX-U solenoid-free start-up activities will be conducted in other ST facilities in the near term:
    Supporting CHI work being conducted on QUEST in Japan
    Supporting ECH / EBW start-up studies being conducted on QUEST
    Pegasus is studying LHI
Preparation toward NSTX-U CDRs:
    NSTX-U ~ 1.5 MW, 28 GHz gyrotron CDR completed
    NSTX-U reactor-relevant CHI CDR to be ready in ~ 3 years via QUEST and other experiments/modeling

## Slide 13: Back-Up Slides

## Slide 14: Transient CHI Start-Up

## Slide 15: CHI start-up to ~0.4MA is projected for NSTX-U, and is projected to scale favorably to next-step STs
Conceptual concept for “QUEST– like” CHI electrode in NSTX-U upper divertor
Utilizes full injector flux capability in NSTX-U
  Ip > 400 kA
  1MA Start-up potential

## Slide 16: QUEST ECH current start-up generates forward fast electrons NSTX-U plans to install x-ray camera to elucidate ECCD physics
QUEST
TOP VIEW
28GHzRF 2nd
Resonance layer
(R ≈ 320 mm)
Detector (CdTe)
Ip
e-
FWD
BWD
• NSTX-U multi-energy soft x-ray camera to be used to measure the QUEST ECH induced high energy electrons with high spatial and time resolutions.
• Developing a new synthetic diagnostic tool for multi-energy soft x-ray camera with UT.
• On-going modeling with GENRAY and CQL3D for ECH fast electron generations.

## Slide 17: QUEST New ECH Beam Steering, Focusing and Polarization Capability Enabled High Current Access and Physics Study
Quasi-optic Polarizer System
QO Polarizer
System
Coupling Mirror
HE11HE11
λ/8
polarizer
λ/4
polarizer
Ti02 Coating
Absorber
• Steering and focusing mirror launcher system together with quasi-optic waveguide enables incident polarization, N//, and deposition profile scanning
• ECH power is presently limited by arcing in the quasi-optic waveguide. Improvements are being made for next campaign for higher power (and higher current) operations.
• Current ramp-up and sustainment mechanisms will be also investigated via parameter scanning.
in
out
To mirror launcher system