## Slide 1: Non-Milestone Research Results; Collaborations/Public-Private Partnerships
A. Diallo for NSTX-U Team
NSTX-U PAC-40 – Sept. 11, 2019

## Slide 2: Non-Milestone research results that can impact NSTX-U, ITER and tokamak research
NSTX-U scientists are involved in NSTX-U-related research activities as well as collaborations during the Recovery outage
  PPPL researchers carrying out research in both areas
  Collaborator research funding primarily through collaborations
Collaborations can be on topics that can impact future NSTX-U operations
  NSTX-U can capitalize on the DoE investment in research that is independent of NSTX-U

## Slide 3: Researchers are actively engaging in other domestic and international collaborations during Recovery
LTX-β (PPPL): Spectroscopy, plasma surface interaction, impurity transport
DIII-D (US): Pedestal physics, 3D physics, plasma materials interactions
EAST (China): edge physics, plasma materials interactions, effect of lithium
ASDEX-U, W7-X (Germany): wall conditioning using boron powder
QUEST (Japan): Full non-inductive startup (CHI, ECCD)
Urunia (UW): CHI
HL-2A (China): LH stabilization of ELMs, effects of NTMs on fast ions
KSTAR (S. Korea): Core MHD, rotation physics, plasma control
MAST-U and ST40 (UK): See next slide
MST (WIPPPL): ME-SXR for profiles and impurity transport
New collaborations (recent International proposal awards - JET, WEST, KSTAR, and COMPASS-U)

## Slide 4: Collaboration on MAST Upgrade will afford opportunities with direct connection to the NSTX-U research program
Plasma startup, rampup and control
  Confinement and transport, including TRANSP and gyrokinetic analyses, L-H threshold (PPPL), turbulence (UCLA)
  Equilibrium and stability including EF and tearing physics (PPPL), RWM, disruptions, equilibrium codes (Columbia U.)
  Divertor physics – diagnostics and data analysis (ORNL, LLNL)
  Energetic particles, modeling, FIDA support, ssNPA, fusion products (PPPL, UC Irvine, Florida Int. Univ., UCLA)
  Pedestal physics (PPPL)
  First physics campaign planned for Spring 2020

## Slide 5: ST40 collaboration has been approved and will be funded in FY20
Public-private partnership with Tokamak Energy Ltd., UK
  Collaboration funded for three years through CRADA (Cooperative Research and Development Agreement)
  PPPL, ORNL, UC Irvine, U. Washington, Columbia U.
ST40 is a high-TF (up to 3 T) Spherical Tokamak with Business Milestone by end of third year to “establish fusion conditions” (Ti(0)>10 keV, ne>1020 m-3)
  2-4 MW NBI
  Will not have full diagnostic set; research, and time for it, will have limitations
Areas of collaboration include:
  Pedestal physics – PBLS (PPPL), Divertor physics (ORNL)
  Confinement scaling, TRANSP, EP physics, EF and tearing physics (PPPL, UC Irvine)
  Disruption prediction algorithm development (Columbia U)
  RF modeling for startup/rampup (EC/EBW), possible ICRH (PPPL, ORNL)
  Scoping for turbulence diag. (PPPL), CHI (U. Washington), Li injection (PPPL)

## Slide 6: This talk addresses PAC-40 charge #1
Edge/pedestal physics
Energetic particle physics
Macrostability
Scenario development
Diagnostics development
1. Please comment on the quality and importance of recent research results, including collaborative activities, and how they advanced the NSTX-U Mission and Milestones

## Slide 7: Outline
Edge/pedestal physics
    Explore dynamic processes in the edge region for understanding pedestal/SOL structure (NSTX/NSTX-U)
    Utilize different wall conditioning techniques to optimize plasma performance (EAST, DIII-D, AUG, KSTAR)

## Slide 8: First detailed measurements of high-k (electron-scale) turbulence across L-H transition in NSTX reveal broad spectral changes
Multiple turbulence phases are identified across the L-H transition
Suppression of high-k turbulence at lower wavenumbers, i.e. k┴ρs ≤ 9-10 (higher wavenumbers unaffected); similar with turbulence changes at ion scale (BES)
L-H transition
Quasi-stationary phase
Intermittent phase
Quiet phase
Recovery phase
High-k turbulence frequency spectrum evolution
Before L-H transition
after intermittent phase
Further into H-mode
High-k turbulence wavenumber spectrum evolution
Total scattering power
Ren et al., Nucl. Fusion (2019)

## Slide 9: Fast camera imaging of the divertor provides new insights into SOL turbulence
Divertor leg fluctuations observed by fast imaging in NSTX-U
  Intermittent; localized to bad curvature side
    Simulations with ArbiTER code find unstable resistive ballooning mode [Baver, CCP (2016)]
Disconnection of midplane turbulence from divertor plate due to X-point
  Consistent with expectation from two-region blob model [Myra, PoP (2005)]
Images in CIII emission
[Scotti, Nuc. Fusion (2018)]
normalized collisionality
normalized blob size
Resistive
X-point
Resistive
Ballooning
Sheath connected
Ideal Interch

## Slide 10: Mechanisms leading to Enhanced Pedestal (EP) H-mode are being better understood
EP H-mode is an attractive ELM-free regime for compact reactors
      H98y,2 typically 1.5
      Slower density and impurity accumulation
Reduced edge ion collisionality drives reduction in neocl. ion energy and momentum transport
      Decrease in edge density following an ELM initiates a period of reduced edge ion collisionality
      Positive feedback loop: Improved neo. energy confinement compensates for larger anom. particle transport loss
          Faster loss of colder ions, slower loss of hotter ions
      “Locks in” lower collisionality
Access to lower collisionality may enable routine access to EPH for NSTX-U
Battaglia, 2019 APS invited, PoP to be submitted

## Slide 11: Wall conditioning and ELM control studied with low-Z impurity powder injection on EAST and DIII-D
Impurity powder dropper compatible with many materials deployed on EAST & DIII-D
  Original version using Li was first deployed on NSTX
EAST: compare ELM suppression with Li powder injection (reduced recycling) with B powder (low freq. edge mode)
DIII-D: B powder injection successfully used for wall conditioning to reduce recycling and density
No Li powder
Li powder
EAST
No B powder
B powder
EAST
Dα
WMHD [kJ]
ne [1019 m-3]
R. Maingi, Nucl. Fusion 58 (2018) 024003
A. Diallo, H-mode workshop 2019
DIII-D
A. Bortolon, APS 2018, NME in prep

## Slide 12: ELM control and enhanced power exhaust studied with low-Z impurity powder injection on KSTAR and AUG
KSTAR: BN powder injection led to periods of ELM quiescence
  Dependence on injection rate
AUG: BN powder injection led to enhanced radiated power, reduced heat flux, improved stored energy
  Similar to N2 gas injection
Powder dropper is being considered for early deployment in NSTX-U
No B powder
BN powder
KSTAR
E. Gilson, EPS 2019 P5.126
No B powder
BN powder - lo
BN powder - hi
AUG
A. Bortolon, Nucl. Mater. Energy 19 (2019) 384

## Slide 13: Outline
Energetic particle physics
    Novel ICE observation on NSTX-U
    Effect of EP on NTV on DIII-D
      Potential effects on plasma rotation/performance
    Effect of RF on EP distribution
      Impact on NB heating and current drive

## Slide 14: Ion Cyclotron Emission (ICE) from NSTX/NSTX-U scenarios shows features uncommon in larger R/a devices
[E. Fredrickson, PoP 2019]
  NSTX(-U): ICE frequency maps to fci deeper in the core
    ICE maps to a region of strong local density gradient
    Frequency doesn’t follow Alfvénic scaling (but scales with B)
  Complement data from larger R/a devices
  More theory work needed to explain the observations
Contours of electron density (black) with the magnetic spectrogram overlaid (red)
  Understanding ICE would provide a reactor-relevant fast ion diagnostic for ITER and beyond
      Neutron rate generally proportional to ICE amplitude [JET]
      Simple measurements (coils)
      ICE typically associated with fast ions

## Slide 15: Energetic Particles found to Induce neoclassical toroidal viscosity on DIII-D
EP-induced NTV, predicted by theory was verified in n=1 DIII-D plasma response experiments
    Experimental measured NTV torque is varied with beam voltage and injection angle
    Simulated EP NTV agrees with experiments
EP NTV, due to precession resonance, can be much stronger than thermal NTV, when ExB rotation is comparable to the precession frequency
Energetic particles, as one of major plasma species, may contribute significant NTV torque in NSTX-U and ITER operation
    Can impact plasma rotation and thus confinement and stability
NSTX-U flexible beams can help to further verify EP NTV and improve NTV modelling
Torque Density (a.u.)
Radial
Radial
Tangential
MARS-K
Experiments
MARS-K Simulated NTV
Z.R. Wang, EPS 2019
EP-NTV
Thermal Electron-NTV
Thermal ion-NTV

## Slide 16: 3D RF field (from Petra-M) combined with following particle code SPIRAL to study the interaction of FW with fast ions
Strong interaction
20k particles
E = 80 keV
vII0=0 m/s
R = 43-155 cm (2 cm step )
= 0-2π
(1 deg step)
Z = 50 cm
Blue
Yellow
3D vs. 2D field can affect the interaction between FW and
fast ions
Energy gained
by fast ions from RF
Strong
Weak
Extending to 3D enables accurate core-edge coupling with the antenna

## Slide 17: Outline
Macrostability: Study being performed to understand and mitigate processes that impact plasma stability
      EF correction (KSTAR and ITER)
      Impact on the magnetic footprints on the divertor plates due to the misalignment of NSTX-U equilibrium coils
      RWM and effect of wall (MAST - no wall, NSTX - wall)
      Disruptions and VDEs

## Slide 18: NSTX-U researchers continue to develop and test error field correction (EFC) strategy in tokamaks and for ITER
Developing unified n=1+2 resonant EFC criteria to avoid disruptive MHD modes*
  Using IPEC to calculate resonant field threshold for locked modes
  Investigating multi-modal aspects of HFS EF effects as seen with NSTX-U TF errors and COMPASS HFS coils
Predicting non-resonant NTV correction capabilities of existing and designed coils
  Using self-consistent NTV response matrix in GPEC
  Assessing Top/Bottom coil utilities in ITER*, and designing coils to couple NTV dominant response structure in KSTAR
  * As a part of ITPA MHD activity (MDC-19)
n=1+2 resonant EF scaling in tokamaks
ITER T/B coil correction against NTV by mid-coils

## Slide 19: Study the precision needed to install the equilibrium coils of NSTX-U in terms of plasma footprints on the divertor plates
Study predicted that error fields in NSTX-U will not expand footprints outside of divertor PFCs
A 5 mm shift of the TF coils produces 10 cm wide footprints on the outer divertor plates
The footprint size is linearly proportional to the misalignment magnitude of TF and PF5.
Munaretto Nucl. Fusion 59(2019) 076039
“s” is defined as the distance from inner midplane along the wall clockwise
Upper-Inner
Upper-Outer
Lower-Outer
Lower-Inner

## Slide 20: Studies of observed global modes in MAST & NSTX allow for understanding the effect of wall proximity on mode structure
Fast camera image
(MAST 21436, t ~ 0.280s)
VALEN analysis (n = 1 RWM)
(using MAST 7090)
NSTX 114147, t ~ 0.268s
VALEN analysis (n = 1,2,3 RWM)
(reconstructed 114147)
Sabbagh, et al., Nucl. Fusion 46 (2006) 635
“egg shape event”
VALEN code analysis produces similar distortions to MAST and NSTX observations
Images of plasma distortion due to global modes
MAST
NSTX

## Slide 21: DECAF MHD events are now producing early disruption warnings for KSTAR
DECAF* is a physics-based disruption algorithm
Mode locking at reduced plasma rotation
Key notables of MHD warning
  “Safe”/“unsafe” MHD periods
  Early disruption warning (300 ms) ➔ on transport timescale
MHD warning level
Safe
KSTAR
16299
MHD-n1
MHD-n2
DECAF automated MHD objects
frequency (kHz)
warning level
n
1
2
3
*D. Humphreys, et al., PoP 22 (2015) 021806
S.A. Sabbagh, APS DPP Invited talk (2018)

## Slide 22: Outline
Scenario development
    Optimize non-inductive startup and ramp up, including active controls plasma (QUEST, URANIA, MAST (+U), NTSX(+U), KSTAR, DIII-D)
    Assess impact of H species in HHFW heated plasma

## Slide 23: QUEST ECH provides unique opportunity to understand and optimize ECH based tokamak/ST start-up/ramp-up concept
N. Bertelli, invited talk at the 23rd Topical RF Conf. (China, 2019)
Transient CHI on QUEST has shown reliable discharge initiation, and plasma growth in biased electrode configuration
  CHI to be tested also on URANIA
ECCD Phase
• Increasing X-ray – energetic electrons
• Ip ∝ IX-ray ∝ neh
• Minority energetic particle population
Initial pressure driven current phase
• No X-ray
• No ECCD
Experiment and modeling of 2nd harmonic electron cyclotron heating and current drive solenoid-free start-up in QUEST
gyrotron - 28 GHz

## Slide 24: Exploring optimized HHFW with H species
W/cm3/MW
10% H concentration case & nφ = -12, f=30MHz, and BT = 1T
Could provide an attractive path for 2nd harmonic H minority heating in NSTX-U (perhaps in the ramp-up phase)
H power deposition
Electron power deposition
2D power deposition obtained by AORSA full wave code
2nd Harmonic
N. Bertelli, invited talk at the 23rd Topical RF Conf. (China, 2019)
Performed through the RF SciDAC collaboration

## Slide 25: Outline
Diagnostics development
    Comprehensive measurements for EP distribution and impurity studies
    Implementation of real-time capable DECAF

## Slide 26: New/Upgraded Fast Ion Diagnostics/Tools to Improve Phase Space Coverage and Accuracy
FIDA Imaging
On DIII-D
M. A. Van Zeeland
PPCF (2009)
UC Irvine
INPA on DIII-D X.D. Du NF(2018)
Fast-Ion D-Alpha Imaging
    Much better spatial resolution
    Simultaneously get FIDA energy spectra with beam splitter
Imaging Neutral Particle Analyzer (INPA) provides radially resolved image
    Gyroradius ➡️ energy
    Line-of-sight ➡️ radius
Test NSTX-U neutron electronics at DIII-D
Inference of fast-ion distribution function with all available fast-ion diagnostics (software development)

## Slide 27: ME-SXR diagnostic tested at MST: originally designed to be installed on NSTX-U for impurity transport experiments
MST
SXR-inferred Te(r,t) measurement @ MST
Large # of viewing chords & high energy resolution
Total count

## Slide 28: Disruption prediction and avoidance research on KSTAR moving to real-time application in 2019
Disruption Prediction
First real-time computation of DECAF MHD analysis planned for 2019
New KSTAR r/t MHD computer and test stand (Columbia U. / PPPL)
  Real-time computer now online at KSTAR; r/t DAQ tests start on 9/10/19
Plasma Stability and Disruption Avoidance
  Resistive wall mode active control system with required r/t sensor compensation completed, ready for initial use in 2019
  New U.S. DOE funding granted to greatly expand real-time capability
S.A. Sabbagh, et al.

## Slide 29: Summary
During the recovery, NSTX-U Team remains actively engaged in research activities on NSTX/U and other devices
Ongoing activities and collaborations address many issues common to NSTX-U and conventional aspect ratio tokamaks
ST collaborations (MAST-U, URANIA, QUEST, ST40) can target ST specific issues necessary to advance tokamaks physics as well as impact and facilitate NSTX-U research

## Slide 30: Backup

## Slide 31: First full 3D torus simulation including realistic antenna geometry
Performed using the Petra-M code developed by RF SciDAC team
Extending to 3D enables accurate core-edge coupling with the antenna
N. Bertelli, invited talk at the 23rd Topical RF Conf. (China, 2019)
Ez component for 90 degree antenna phasing

## Slide 32: Novel Phenomenon: Blob Wakes in NSTX
Blobs sometimes break up into trailing small-scale “wakes”
  Direction: poloidally in the opposite direction to the blobs (i.e. wakes move in electron diamagnetic direction)
Theory : blob wakes consistent with to drift or drift-Alfven waves instabilities
2D GPI images vs. time (2.5 µsec/frame)
Single column of 2D data vs. time showing poloidal propagation
of wakes (upward) vs. blobs (downward)
Zweben, Myra, Diallo et al, Phys. Plasmas 26, 072502 (2019)

## Slide 33: Characterization of SOL and divertor turbulence in NSTX/NSTX-U via imaging of divertor fluctuations
Reduction in Vrad with respect to upstream Vrad approaching separatrix in disconnected region
  Midplane poloidal velocities in agreement with target filament velocity
~2x larger poloidal corr. length on divertor target
Radial velocity reduction consistent with reduction in polarization drive due to X-point
Imaging of diverter localized intermittent field-aligned filamentary structures is support by modeling
  Consistent with unstable resistive ballooning modes (ArbiTER code)
Scotti, Nucl. Fusion 58(2018) 126028

## Slide 34: Enable external steering of TRANSP for control and scenario development
e.g., Boyer, et al., Nuclear Fusion 2017.
Predictive modeling helps control
Control improved the predictive modeling
Socket connection for TRANSP enables passing of information between actuators (NTV, beam, shape, ne, etc…) and controlled parameters (q, li, betaN etc..)
Builds upon previous work on NSTX-U as well as KSTAR collaboration

## Slide 35: Collaboration with MAST-U led to development of novel, time-dependent model for evaluating startup on Spherical Tokamaks
Vacuum calculation producing 2D, time-dependent E, B able to predict timing of startup in MAST-U and NSTX-U
    Includes reduced models describing Townsend Avalanche as well as particle loss on open field lines
    Model developed and tested against shared database of MAST and NSTX(-U)
    Applied model to scenario development to assist in MAST-U commissioning activities during summer 2018 appointment at CCFE
Supports broader effort to develop startup models for future tokamaks, such as ITER and is supporting experiments on DIII-D (summer, 2019)
Battaglia, D. J. accepted, 2019 Nucl. Fusion

## Slide 36: Apparent global mode “egg shape event” has been noted by A. Kirk regarding loss of H-mode ➔ RWM on MAST
Several shots display asymmetric, global events
  Consider that the “egg shape events” are global MHD ➔kink/ballooning/resistive wall modes (RWM) Q: does this follow “standard” theory? A: yes
disruption
courtesy A. Kirk
Fast camera images
(21436, t ~ 0.280s)
Mode locked toroidally,
expands radially

## Slide 37: DECAF MHD events are now producing early disruption warnings for KSTAR
DECAF* is a physics-based analysis paradigm that meets all disruption predictor requirement metrics
Mode locking at reduced plasma rotation
Key notables of MHD warning
  “Safe”/“unsafe” MHD periods
  Early disruption warning (300 ms) ➔ on transport timescale
DECAF “heat map” (for MHD)
Very low frequency mode ➔
Plasma rotation profile
and dynamics
High amplitude mode ➔
}
Decreasing βN ➔
condition
time (s)
MHD warning level
Safe
KSTAR
16299
MHD-n1
MHD-n2
DECAF automated MHD objects
frequency (kHz)
warning level
n
1
2
3
*D. Humphreys, et al., PoP 22 (2015) 021806
S.A. Sabbagh, APS DPP Invited talk (2018)

## Slide 38: Successful benchmark of nonlinear MHD codes based on NSTX Vertical Displacement Event
Axisymmetric VDE simulations with M3D-C1, NIMROD & JOREK
  Based on NSTX #139536 with simplified resistive wall
  Excellent agreement of linear growth rates & nonlinear evolution including halo currents between all three codes
Krebs to be submitted; http://arxiv.org/abs/1908.02387]

## Slide 39: Three distinct turbulence mechanisms predicted by local, single-scale GYRO simulations
Low-k turbulence (ρi scale)
  Different dominant mode active at different radii
    (ρ=0.75) ITG dominates
    (ρ=0.45) MTM dominates
High-k turbulence (ρe scale)
(ρ=0.45-0.65) ETG dominates (where E×B shear suppresses low-k)
Also expect non-local & possibly multi-scale effects to matter ➙ need robust global EM gyrokinetic codes + multi-scale simulations
W. Guttenfelder et al., Nucl. Fusion 59, 056027 (2019)
exp.
Provides low-A complement to numerous R/a=3 transport validation studies

## Slide 40: Exploring the Regime of Validity of Delta-f Global Gyrokinetic Simulations with Spherical Tokamak Plasmas
GTS simulations cannot explain the factor of 2 change in heat flux before and after RF cessation (in L-mode)
    Due to the gradient driven nature of GTS
However, GTS simulations demonstrate decent agreement in ion thermal transport with a set of NBI-heated NSTX H-mode
More GTS simulations are needed to understand the above discrepancy and to quantify the regime of validity of the GTS code
RF-heated NSTX L-mode plasma
NBI-heated NSTX H-mode plasma

## Slide 41: NSTX-U L-mode operation provides valuable flexibility for physics validation studies
New centerstack enables stationary L-mode studies over range of Ip, BT, ne, PNBI (was not possible in NSTX)
[D. Battaglia, Nucl. Fusion 58, 046010 (2018)]
Provides low-A complement to numerous R/a=3 transport validation studies
Extending validation of gyrokinetics & transport models to low-A helps unify physics basis for operation & optimization of next-step facilities (ITER and beyond)
NSTX-U L-mode

## Slide 42: CHI on QUEST Aims to Develop Reactor-relevant CHI Electrodes and Test ECH Heating and Sustainment of CHI Started plasma

## Slide 43: Transient CHI on QUEST has Shown Reliable Discharge Initiation, and Plasma Growth in Biased Electrode Configuration
CHI insulator on QUEST is not part of the vacuum vessel
Objectives
  Current persistence
  Closed flux current generation
Future objectives
  Heat CHI plasma with ECH
  Impurity reduction
  Increase current magnitude & sustain with ECH

## Slide 44: Three new PPPL x-ray diagnostics will be implemented at WEST for Te, nZ, Zeff and ne.fast measurements
Modest-resolution compact x-ray imaging crystal spectrometer (cXICS) for nZ & δZeff profile measurements
Broadband multi-energy SOFT x-ray (ME-SXR) for nZ, δZeff and Te profile measurements
Sample Ar, Mo, Xe, W emission to constrain nZ & transport
Broadband multi-energy HARD x-ray (ME-HXR) for Te & ne,fast measurements
New DECTRIS CdTe detector
Si
New camera design
New compact spectrometer is a spin-off PPPL’s collaboration with MIT’s PSFC
New multi energy SXR and HXR systems are upgrades of diagnostic tested at WiPPL

## Slide 45: NSTX-U High Harmonic Fast Wave (HHFW) “Scenarios” considered
NSTX-U plasma
  B = 1T
  Ion species: D, H, C, DBEAM
R [m]
Z [m]
ρpol
ρpol
ne
nD
Te
TD

## Slide 46: NSTX-U “Scenarios” considered
NSTX-U plasma
      B = 1T
H concentration scan:
      nH/ ne = 1%, 2%, 5%, 10%
Te & ne scans at βe constant
nNBI scan
B scan:
      B = 0.53, 0.63, 0.76, and 1 T
w/ and w/o NBI
Two antenna frequencies:
  30 MHz and 60 MHz
Three nφ values: -5, -12, -21
Employed full wave code AORSA (Maxwellian plasma)
N. Bertelli et al 2019 Nucl. Fusion 59 086006

## Slide 47: Hydrogen concentration scan: H power absorption increases with larger H concentration and decreases for larger nφ
W/ NBI: dominant electron & fast ions absorption (except for nφ = -5)
W/O NBI: significant H absorption at lower nφ
nφ = -12
nφ = -5
nφ = -21
With
NBI
NO
NBI
f = 30MHz
H concentration
H concentration
H concentration

## Slide 48: Lower antenna phasing has stronger interaction with SOL plasma
Ez component of the wave field
30 degree
90 degree
150 degree
Strong interaction with the SOL

## Slide 49: Anomalous electron losses dominate; strong ion-scale turbulence measured
Observed neoclassical ion losses (in L-mode), anomalous electron losses
However, ion scale turbulence data (BES) shows large amplitude, broadband fluctuations & bi-modal poloidal phase velocity
    Bi-modal phase velocities suggestive of two distinct turbulence types (observed in DIII-D & TFTR)
BES cross-power spectra
ρ=0.58-0.86
BES poloidal cross-phase
BES fluctuation amplitudes
e-dia direction
i-dia direction
W. Guttenfelder et al., Nucl. Fusion 59, 056027 (2019)

## Slide 50: Control-oriented modeling for NSTX-U with machine learning based on TRANSP and experimental data
Machine learning algorithms are being used to develop fast simulation capabilities for scenario optimization and real-time control
  Builds upon neural network development for NSTX-U beam heating
  E.g., magnetic diffusion: Neural network models for equilibrium dependent geometric quantities, bootstrap current, and resistivity, kinetic profiles: electron pressure/density profile shapes
Solid: Expected (TRANSP/NSTX-U)
Dashed: Neural net prediction
Boyer, et al., Nuclear Fusion 2019.

## Slide 51: “Predict-first” KSTAR TRANSP analysis shows expected high performance plasmas at > 80% NICF
High non-inductive current fraction for 6.5, 7.5, 8.5 MW NBI
  βN from 3.0 – 3.5; based on KSTAR plasmas with NICF ~70%
Generate substantial database of long pulse, high βN plasmas in the 2019 KSTAR run for disruption prediction studies
Predicted high non-inductive current fraction (NICF) current profiles
81.5% NICF
93% NICF
101% NICF
J.-H. Ahn, S.A. Sabbagh, et al. (Columbia U.)