## Slide 1: MS TSG Effect of Polar Changes
Jack Berkery
Columbia University
PPPL
May 24, 2017
*This work supported by the US DOE contracts DE-AC02-09CH11466 and DE-FG02-99ER54524

## Slide 2: MS TSG five year plans
Thrust MS-1: Understand and advance passive and active feedback control to sustain macroscopic stability
  RWM kinetic stability, state space control, rotation control
Thrust MS-2: Understand 3D field effects and provide the physics basis for optimizing stability through equilibrium profile control by 3D fields
  Error fields, NTM, NTV
Thrust MS-3: Study and develop techniques for disruption prediction, avoidance, and mitigation, and understand disruption dynamics and in high-performance ST plasmas
  DECAF disruption avoidance, Halo currents, MGI

## Slide 3: MS TSG concerns
Many experiments in MS TSG purposefully make disruptions
  This ability needs to be maintained, mitigated and unmitigated, up to 1T 2MA
  Direct impact forces and halo current forces exerted on the tiles
  Strikepoints move during disruptions – should be studied
  Conversely, disruption avoidance XPs need long pulse to demonstrate stability
3D fields utilized by the MS TSG will impact the polar region
  By changing the heat flux pattern and field line angles
  Rotating 3D fields for diagnostic purposes requires long pulse
Plasma shapes for continuity with tearing studies requested
  NSTX and DIII-D similar shapes, κ up to 2.2, upper δ up to 0.45, lower δ up to 0.7
L-modes (~1s) and controlled shutdown (0.5s) limited on CS
Co- vs counter-Ip XPs require BT reversal; new EP loss pattern

## Slide 4: MS TSG concerns
Access to high beta is critical for MS TSG
  Ability to operate all 6 NBI should be retained
  Pulse lengths long enough for magnetic braking and to trigger NTMs
Access to low collisionality is required for stability studies
  Glow discharge cleaning, bakeout, tile material (outgassing) important
Massive gas injection experiments are planned
  NSTX-U only machine for private flux vs. midplane injection study – retain holes
  Injection from private flux region may help radiate/protect divertor tiles in VDE

## Slide 5: MS TSG concerns
Necessary magnetics should not be affected
  Coverage for equilibrium reconstruction, including polar region for snowflake
  Capacity for upgraded halo current sensors should be retained… (next slides)
  Extended magnetic sensors in the divertor region have long been planned
    If ceramic break for CHI is removed, could in principle consider another channel at even lower major radius
New sensor locations
Present sensor locations
BR sensors (nominally normal, Bnorm)
Bp sensors (nominally tangential, Btan)

## Slide 6
Sketch of present NSTX-U configuration (FY16)
Multi-axis B sensors
Normal-current shunt tiles
Single axis B sensors
Dense Langmuir probes

## Slide 7
Sketch of planned enhancements
Multi-axis B sensors
Normal-current shunt tiles
Single axis B sensors
Dense Langmuir probes

## Slide 8: Existing configuration (FY16)
Upper
Lower

## Slide 9: Enhanced configuration
Upper
Lower