## Slide 1: Progress and Plans for NSTX Upgrade and Kinetic Resistive Wall Mode Stability
Jack Berkery, Columbia University
and the NSTX-U team
Georgia Institute of Technology,
Atlanta, GA
April 14, 2016

## Slide 2: Outline
National Spherical Torus Experiment – Upgrade
  ST Overview and Motivation, NSTX-U Mission
  NSTX-U Upgrades, Status
  NSTX-U Research Focus
Modifications to Ideal Stability by Kinetic Effects
  Includes rotation, collisionality, and energetic particle effects
  Benchmarked MISK code calculations can explain experimental stability
Summary

## Slide 3
ST
“Spherical” tokamak (ST) has aspect ratio A < 2
A ~ 1.2-2,
k = 2-3,
q95 = 6-20,
bT = 10-40%
A ~ 3-4,
k = 1.5-2,
q95 = 3-4,
bT = 3-10%
Tokamak
Toroidal beta bT = p / (BT02/2m0)
Aspect Ratio A = R /a
Elongation k = b/a
IP ~ ITF (1 + k2) / (2 A2 q*)
Energy confinement time tE ∝ IP
Access high pressure, rapid rotation, low collisionality
• ST has high IP, economically, due to high κ and low A
• Favorable average curvature improves stability at high beta

## Slide 4: Design studies show ST potentially attractive as Fusion Nuclear Science Facility (FNSF)
Projected to access high neutron wall loading at moderate R, Pfusion
  Wn ~ 1-2 MW/m2 , Pfus ~ 50-200MW, R ~ 0.8-1.8m
Modular, simplified maintenance
FNSF: Provide neutron fluence for material/component R&D
FNSF with
copper TF coils
A=1.7, R0 = 1.7m Fluence = 6MWy/m2
Tritium breeding ratio ~ 1

## Slide 5: Tokamaks are not presently steady-state, but in the future will operate without transformer
Conventional Tokamak
Primary transformer coils drive toroidal current in plasma
Must stop when transformer coils reach current/force limits
Inner Poloidal Field Coils
(Primary transformer circuit)
Plasma electric current
(Secondary transformer circuit)
Advanced Tokamak
External: wave and beam current drive
Self-generated: high pressure plasmas make “bootstrap” current

## Slide 6: Outline
National Spherical Torus Experiment – Upgrade
  ST Overview and Motivation, NSTX-U Mission
  NSTX-U Upgrades, Status
  NSTX-U Research Focus
Modifications to Ideal Stability by Kinetic Effects
  Includes rotation, collisionality, and energetic particle effects
  Benchmarked MISK code calculations can explain experimental stability
Summary

## Slide 7
NSTX-U (2015-)
NSTX (1999-2011)
The National Spherical Torus Experiment Upgrade (NSTX-U) at the Princeton Plasma Physics Lab

## Slide 8: NSTX-U will access new physics with 2 major new tools:
Higher T, low n* from low to high 
 Unique regime, study new transport and stability physics
Full non-inductive current drive
 Not demonstrated in ST at high-T
Essential for any future steady-state ST
2. Tangential 2nd Neutral Beam
1. New Central Magnet

## Slide 9: NSTX-U will have major boost in performance
2× toroidal field (0.5  1T)
2× plasma current (1  2MA)
5× longer pulse (1  5s)
2× heating power (5  10MW)
Tangential NBI  2× current drive efficiency
4× divertor heat flux ( ITER levels)
Up to 10× higher nTE (~MJ plasmas)
2. Tangential 2nd Neutral Beam
1. New Central Magnet
2017-2018 goals:

## Slide 10
NSTX-U Facility Is Now Operational
Upgrade Project Completed on Schedule and Cost
HHFW System
1st NBI
2nd NBI
NSTX-U
All six NBI sources are now operational, supporting high performance H-mode experiments

## Slide 11: NSTX-U plasma commissioning status
~7 run weeks of ops, IP = 0.5–1MA, boronized PFCs
Nearly all shots at BT = 0.6-0.65T > NSTX max = 0.55T
All 6 NBI injected into plasmas, 4-6MW routinely available
Approaching NSTX WTOT record ~ 430kJ
NSTX record
Exceeded NSTX L & H-mode pulse-lengths
using 1MW L-modes (0.65, 0.8MA)
NSTX record

## Slide 12: Examples of high-performance L and H-modes achieved thus far
Optimal n=1 error field correction amplitude and phase identified to maximize pulse length, discharge performance

## Slide 13
Path to high IP without tearing modes: elevate qmin via early heating + H-mode
  Utilizing real-time EFIT / ISOFLUX and improved vertical motion detection
  Near-term: li = 0.5-0.6, κ = 2.5 – 2.7, IP = 1.1 – 1.3MA
NSTX-U has matched NSTX highest flat-top pressures for plasma currents up to 0.9MA

## Slide 14: Outline
National Spherical Torus Experiment – Upgrade
  ST Overview and Motivation, NSTX-U Mission
  NSTX-U Upgrades, Status
  NSTX-U Research Focus
Modifications to Ideal Stability by Kinetic Effects
  Includes rotation, collisionality, and energetic particle effects
  Benchmarked MISK code calculations can explain experimental stability
Summary

## Slide 15: NSTX achieved favorable confinement and current drive results; Will trends continue in NSTX-U?
Steady-state operation required for FNSF
IP=1 MA, BT=1.0 T, PNBI=12.6 MW
TRANSP Contours of Non-Inductive Fraction
H98y2 confinement
parameter
ITER-like scaling
ST-FNSF
?
constant q, b, r*
NSTX Upgrade
NSTX
Favorable confinement results could lead to more compact ST reactors
NSTX achieved 70% “transformer-less” current drive Will NSTX-U achieve 100% as predicted?
NSTX observed confinement increase at higher Te!
Will trend continue, or look like conventional A?
Normalized electron collisionality ne*  ne / Te2

## Slide 16
Compact ST-FNSF has no/small central solenoid
Plasma current start-up/ramp-up critical issue for FNSF
ST-FNSF Scenarios
IP [MA]
NBI
Time
HHFW
RF and/or HI
Solenoid-free
Start-up
Current ramp-up and profile control
~ 1-2 MA of solenoid-free start-up current needed for FNSF
• Two novel techniques for solenoid-free start-up and ramp-up will be investigated
  Radio-frequency power
  Helicity Injection

## Slide 17: NSTX-U will test ability of advanced divertors to mitigate very high heat-fluxes
Power / particles contact target plates here
Power exhaust width outside main plasma can be very narrow (few mm)
NSTX-U has additional coils for improved control of snowflake
NSTX-U peak heat fluxes will be up to 4-8× higher than in NSTX
Snowflake Divertor
Standard Divertor

## Slide 18: Outline
National Spherical Torus Experiment – Upgrade
  ST Overview and Motivation, NSTX-U Mission
  NSTX-U Upgrades, Status
  NSTX-U Research Focus
Modifications to Ideal Stability by Kinetic Effects
  Includes rotation, collisionality, and energetic particle effects
  Benchmarked MISK code calculations can explain experimental stability
Summary

## Slide 19: An unstable RWM is an exponential growth of magnetic field line kinking that can cause disruptions
The resistive wall mode (RWM) is a kinking of magnetic field lines slowed by penetration through vessel structures
where
Bp
RWMs can cause a collapse in β, disruption, and termination of the plasma
NSTX 130235
[S. Sabbagh et al., Nucl. Fusion 46, 635 (2006)]

## Slide 20: RWM dispersion relation evaluated with ideal and kinetic components allows for passive stabilization of the RWM
Resistive Wall Mode (RWM) fluid dispersion relation:
τw-1 is slow enough for active stabilization (feedback)
However, experiments operate above the no-wall limit without active control!
βNno-wall
βNwith-wall
unstable
stable
0
Ideal Kink Mode
Resistive Wall Mode
~τw-1

Ideal Stability

## Slide 21: RWM dispersion relation evaluated with ideal and kinetic components allows for passive stabilization of the RWM
Resistive Wall Mode (RWM) fluid dispersion relation:
τw-1 is slow enough for active stabilization (feedback)
[B. Hu et al., Phys. Rev. Lett. 93, 105002 (2004)]
However, experiments operate above the no-wall limit without active control!
Passive stabilization
  Collisional dissipation
  Rotational stabilization
    Models with scalar “critical rotation” for stability could not explain experiments
[S. Sabbagh et al., Nucl. Fusion 50, 025020 (2010)]
βNno-wall
βNwith-wall
unstable
stable
0
Ideal Kink Mode
Resistive Wall Mode
~τw-1

Ideal Stability
Kinetic Effects

## Slide 22
Precession Drift
~ Plasma Rotation
Bounce
Rotational resonance effect
NSTX 121083
unstable
(marginal stability)
unstable
Precession drift resonance stabilization
Bounce/transit resonance stabilization
Plasma evolution
Marginal stability
νeff/νexp (marginal stability)
instability
(experiment)
ωφ/ωφexp (marginal stability)
MISK code calculations for NSTX γτw contours vs. ν and ωφ
[J. Berkery et al., Phys. Rev. Lett. 104, 035003 (2010)]
Kinetic RWM theory consistent with RWM destabilization at intermediate plasma rotation; stability altered by collisionality
Destabilization appears between:
precession resonance at low ωφ
bounce resonance at high ωφ

## Slide 23: Collisionality affects the strength of kinetic resonances
~ Plasma Rotation
Collisionality
Collisionality effect
on-resonance
more stable
 ~ -1/ν
off-resonance
less stable
 ~ constant
MISK calculations
unstable
stable
Early theory predicted RWM stability should decrease at low ν
Kinetic RWM stability theory at low ν:
  Stabilizing resonant kinetic effects enhanced
[J. Berkery et al., Phys. Rev. Lett. 106, 075004 (2011)]
0.2
1.2
1.4
0.4
0.6
0.8
1.0

## Slide 24: Energetic particles provide a stabilizing force that is nearly independent of rotation and collisionality
Precession Drift
~ Plasma Rotation
Collisionality
Bounce
Energetic particle effect
[J. Berkery et al., Phys. Plasmas 17, 082504 (2010)]
NSTX 121083 @ 0.475 s
δWK
ωφ/ωφexp
Large for EPs
Small for EPs
Significant Re(δWK), but nearly independent of ωφ
Energetic particles are not in mode resonance
Effect is not energy dissipation, but rather a restoring force

## Slide 25: Outline
National Spherical Torus Experiment – Upgrade
  ST Overview and Motivation, NSTX-U Mission
  NSTX-U Upgrades, Status
  NSTX-U Research Focus
Modifications to Ideal Stability by Kinetic Effects
  Includes rotation, collisionality, and energetic particle effects
  Benchmarked MISK code calculations can explain experimental stability
Summary

## Slide 26: Kinetic RWM theory has been benchmarked between codes and applied to multiple devices
fluid growth rates
fluid plus kinetic growth rates
unstable
stable
low rotation
precession resonance
high rotation
bounce resonance
[J. Berkery et al., Phys. Plasmas 21, 052505 (2014)]
Benchmarking with MARS-K (Yueqiang Liu) supports the understanding that RWM stability can be increased by kinetic effects
  At low rotation through precession drift resonance
  At high rotation by bounce resonance
[H. Reimerdes et al., Phys. Rev. Lett. 106, 215002 (2011)]
Active measurements in DIII-D (Holger Reimerdes) support the importance of kinetic effects in stable plasma behavior as well
  Plasma response is enhanced where kinetic effects and RWM stability are weak
  MISK calculations match experiments
ITER test case
DIII-D

## Slide 27: MISK calculations validated against unstable experimental plasmas; reproduce approach towards marginal stability
MISK calculations (at tMISK) including kinetic effects, have been tested against many marginally stable NSTX experimental cases
[J. Berkery et al., Nucl. Fusion 55, 123007 (2015)]
The calculations trend towards instability (γτw = 0) approaching time of RWM instability growth
unstable
stable
NSTX
NSTX

## Slide 28: Summary
NSTX-U project recently completed on cost and schedule
  Physics research began December 2015, making great progess
NSTX began, and NSTX-U will extend, opportunities to study toroidal confinement physics in novel regimes:
  Low aspect ratio, strong shaping, high β, low collisionality
  Advanced divertors, lithium walls, unique start-up solutions
  Will inform optimal configuration for next-step FNSF device
Kinetic RWM stability theory modifies ideal stability
  Includes rotation, collisionality, and energetic particle effects
  Benchmarked MISK calculations can explain experiments

## Slide 29: Backup

## Slide 30: NSTX Upgrade mission elements
ITER
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
Develop solutions for the plasma-material interface (PMI) challenge
Advance ST as candidate for Fusion Nuclear Science Facility (FNSF)
Develop ST as fusion energy system
Lithium
“Snowflake”
ST-FNSF / Pilot-Plant

## Slide 31: Low collisionality operation achieved on NSTX using lithium wall coatings
Lithium coatings on carbon tiles reduced gas source from wall
  Lead to a larger H-mode pedestal, larger core temperature
  Confinement continued to improve with reduced collisionality
Longer discharges will address first wall solutions
  New diagnostics and campaigns with different wall materials will advance studies of plasma-wall interaction
R. Maingi, PRL 2011

## Slide 32: Plasma confinement increased continuously with increasing Li coatings in NSTX – what is limit?
Global parameters improve
  H98y2 increases ~0.9  1.4
  No core Li accumulation
High H critical for compact FNSF / Pilot Plants
NSTX-U will double Li-wall coverage with upward evaporators
Will further assess contributors to confinement improvement:
  Lower-recycling / reduced neutral source / higher Te
  Edge profile / turbulence changes
  Influence of (low-Z) impurities in pedestal region
Energy Confinement Time (ms)
Pre-discharge lithium evaporation (mg)
R. Maingi, et al., PRL 107 (2011) 145004
Role of enhancements:
Compare Li-wall pumping to conventional pumping  cryo

## Slide 33: Kinetic effects arise from the perturbed pressure, are calculated in MISK from the perturbed distribution function
Force balance:
leads to an energy balance:
Kinetic Energy
Change in potential energy due to perturbed kinetic pressure is:
Fluid terms
is solved in MISK by using from the drift kinetic equation for

## Slide 34: Kinetic effects arise from the perturbed pressure, are calculated in MISK from the perturbed distribution function
Force balance:
leads to an energy balance:
Kinetic Energy
Change in potential energy due to perturbed kinetic pressure is:
Fluid terms
is solved in MISK by using from the drift kinetic equation for
Precession Drift
~ Plasma Rotation
Collisionality
Bounce

## Slide 35: A realistic projection of ITER stability requires including all kinetic effects
expected ωφ
expected
βα
precession resonance
Collisionality and rotation will be low in ITER: strong precession resonance
Alpha particle calculations agree between MISK and MARS-K, are crucial to ITER stability
Comparing trapped alpha particle calculation
Real
Imag
unstable
stable
Rotational resonance effect
Collisionality effect
Energetic particle effect
+
+

## Slide 36: NSTX-U developing a range of profile control actuators for physics studies, scenario optimization
NTV torque density (N/m2)
Plasma rotation (rad/s)
Radial coordinate
NTV
region
0
2
4
6
104
desired wf
t1
t2
t3
Variations in Outer Gap
Variations in Beam Sources
800 kA Partial Inductive, 87% < fNI < 100%
27 22 17 12 7 2
Outer Gap
800 kA and 1 T
[50,60,70,130] cm
[50,60,120,130] cm
[60,70,110,120] cm
[70,110,120,130] cm
q-Profile Actuators
Torque Profiles From 6 Different NB Sources
Neutral
Beams
(TRANSP)
Rotation Profile Actuators
Largest Rtan
Smallest Rtan
S. Gerhardt,
NF 2012
NSTX-U state-space ωφ controller w/NTV as actuator
S. Sabbagh, IAEA 2014

## Slide 37
  High βN for fusion performance, high non-inductive fraction for continuous operation
    High bootstrap current fraction -> Broad current profile -> Low li = <Bp2>/<Bp>ψ2
  Unfavorable for ideal stability since low li reduces the ideal n = 1 no-wall beta limit
The highest βN/li is not the least stable in NSTX
  Passive stability of the resistive wall mode (RWM) must be explained
Record bN and bN / li accessed in NSTX using passive + active resistive wall mode stabilization
Major NSTX-U mission is to achieve fully non-inductive operation at high b
ST-FNSF
Unstable RWM
Stable / controlled RWM
S. Sabbagh, NF 2013; J. Berkery, POP 2014

## Slide 38: Real-time models can be used for stability estimation
[J.W. Berkery et al., Nucl. Fusion 55, 123007 (2015)]
Modeled estimates for NSTX no-wall limit
NSTX 138556
DCON
Above no-wall
limit
Below
Internal inductance
Pressure peaking
Aspect ratio
Composite no-wall limit model
Growth rate
Kinetic effects
Fluid terms
RWM dispersion relation
Reduced RWM kinetic stability model
Rotation
Full MISK code too complex for real-time
Reduced model including: rotation, collisionality, EPs being implemented

## Slide 39: State space rotation controller designed for NSTX-U can evolve plasma rotation profile toward global mode stability
I. Goumiri (Princeton student), S.A. Sabbagh (Columbia U.), C. Rowley (P.U.), D.A. Gates, S.P. Gerhardt (PPPL)
Recall:
NSTX (major disruption)
MISK
unstable
stable
stable
γτwall
Plasma rotation (kHz)
0
15
20
10
5
ΨN
0.0
0.2
0.4
0.6
0.8
1.0
NSTX-U (6 NBI sources and n = 3 NTV)
marginally
stable
Steady-state reached in ~ 3τm
Marginally stable profile
Broader stable
profile
NBI, -NTV torque density (N/m2)
0.0
0.5
1.0
1.5
2.0
Plasma rotation (krad/s)
NBI
NTV

## Slide 40: DCON confirms NSTX-U above the no-wall limit; NSTX-based model gives good estimate
NSTX-U H-mode discharges: 204112
DCON
Above no-wall limit
Below
Composite no-wall limit model
DCON
Above no-wall limit
Below
204118 (April 2016)
Composite no-wall limit model
NSTX no-wall limit model ([J.W. Berkery et al., Nucl. Fusion 55, 123007 (2015)]) includes internal inductance, pressure peaking, and aspect ratio, predicts NSTX-U DCON no-wall limit
J.W. Berkery, S.A. Sabbagh (Columbia University)

## Slide 41: NSTX-U device performance progression
1st year: Limit forces to ½ way between NSTX and NSTX-U, and ½ of the design-point heating of any coil
  Presently operating at BT ~ 0.65T
  Increase to BT ~ 0.8T after completing engineering analysis
2nd year goal: Full field and current, coil heating to ¾ of limit
3rd year goal: Full capability
Parameter | NSTX (Max.) | Year 1 NSTX-U Operations | Year 2 NSTX-U Operations | Year 3 NSTX-U Operations | NSTX-U Ultimate Goal
IP [MA] | 1.2 | ~1.6 | 2.0 | 2.0 | 2.0
BT [T] | 0.55 | ~0.8 (0.65) | 1.0 | 1.0 | 1.0
Allowed TF I2t [MA2s] | 7.3 | 80 | 120 | 160 | 160
IP Flat-Top at max. allowed I2t, IP, and BT [s] | ~0.4 | ~3.5 | ~3 | 5 | 5
41

## Slide 42: Examples of high-performance L and H-modes achieved thus far
(motivates cryo-pump)
NEXT: Increase k to avoid tearing, active RWM control, trigger ELMs (DRsep, granule injector)