## Slide 1
Kinetic Resistive Wall Mode Stabilization in Tokamaks and Initial Results from NSTX-U*
S.A. Sabbagh1, J.W. Berkery1, Y. Liu2, J.E. Menard3, H. Reimerdes4, and the NSTX-U Research Team
1Dept. of Applied Physics and Applied Mathematics, Columbia U., New York, NY, USA
2CCFE, Culham Science Centre, Abingdon OX14 3DB, UK
3Princeton Plasma Physics Laboratory, Princeton, NJ, USA
4Ecole Polytechnique Fédérale de Lausanne (EPFL), Swiss Plasma Center (SPC), CH-1015 Lausanne, Switzerland
Supported by
*This work supported by the US DOE contract DE-AC02-09CH11466, DE-FC02-04ER54698, and DE-FG02-99ER54524
KTH Research Seminar
8 February 2017
Stockholm, Sweden
V1.2
NSTX-U

## Slide 2: Outline
Importance of global MHD stability and early RWM theory
Experimental inconsistencies provoking new understanding
Kinetic RWM stability physics summary
Corroborative experiments in stable and unstable plasmas in NSTX and DIII-D, and implications for ITER
NSTX-U: Plan aimed toward understanding confinement in ST, disruption avoidance, etc; initial device operation

## Slide 3: The research shown here verified understanding of resistive wall mode (RWM) stability physics using kinetic MHD theory
Importance: Strongly growing RWMs cause disruptions
  Also cause large stored energy collapse (minor disruption) with DWtot ~ 60% (~ 200 MJ in ITER)
    For comparison, large ELMs have DWtot ~ 6% (20 MJ in ITER)
NSTX
  RWM: a global kink/ballooning mode with growth rate, rotation slowed by conducting wall (~ 1/twall)
  RWM typically doesn’t occur when strong tearing modes (TM) appear
    But, what happens when TMs are avoided / controlled (as is planned for ITER)?
  RWM evolution is also dangerous as it can itself trigger TMs
RWM stability physics must be understood to best assess techniques for disruption avoidance
Experimental RWM reconstruction in NSTX
(S.A. Sabbagh, et al., Nucl. Fusion 46 (2006) 635)

## Slide 4: Early theoretical investigations provided initial hypotheses for global kink/ballooning/RWM mode stabilization physics
Conducting wall stabilizes global kink/ballooning mode
  Global kink growth rate ~ 1/tAlfven ~ ms
  Mode transforms into slower growing resistive wall mode (RWM)
RWM physical characteristics
  Growth rate gRWM ~ 1/twall ~ ms
  RWM less stable when wall is closer
  RWM stabilized at plasma critical rotation of a few % of Alfven speed
 Bondeson and Ward, PRL 72 (1994) 2709
Early experiments looked to determine the plasma critical rotation speed
- Experiments initially found consistency with critical rotation at few % of VA
Unstable
Global kink/ballooning
mode
RWM
Stable
gtw
Wall / plasma radius

## Slide 5
Ideal MHD stabilization physics
  Sound wave continuum damping
  Shear Alfven resonance damping
Non-ideal MHD stabilization physics
  Resistive layer damping
  Viscous boundary layer damping
Kinetic stabilization physics
  Parallel viscous force model for sound wave damping
  Semi-kinetic model: mode resonance with thermal ion bounce motion
Therefore, early global mode stabilization physics models related to plasma rotation were investigated
- Bondeson, et al., PRL 72 (1994) 2709
- Betti, et al., PRL 74 (1995) 2949
- Y. Liu, et al., 45 (2005) 1131
- Bondeson, et al., PRL 72 (1994) 2709
- Zheng, et al., PRL 95 (2005) 255003
- Finn, Phys. Plasmas 2 (1995) 3782
- Gimblett & Hastie, Phys. Plasmas 7
(2000) 258
- Fitzpatrick & Aydemir NF 36 (1996) 11
- Chu, et al., Phys. Plasmas 2 (1995) 2236
- Bondeson & Chu (Phys. Plasmas 3 (1996) 3013
- Bondeson, Y. Liu, PPCF 45 (2003) A253

## Slide 6
  Early theory did not find general quantitative agreement with experimental RWM marginal stability
Low-li plasma yields Wcrit tA ~ 0.02 with weak b dependence
Low internal inductance plasma
Moderate internal inductance plasma
Critical rotation
Critical rotation
(β − βno-wall)/(βideal-wall−βno-wall)
(β − βno-wall)/(βideal-wall−βno-wall)
- R. LaHaye, …, Y. Liu, H. Reimerdes, et al., NF 44 (2004) 1197
- H. Reimerdes, J. Bialek, M.Chance, …, Y.Liu, et al., NF 45 (2005) 368
Moderate-li scenario yields significantly lower Wcrit
   Kinetic damping generally underestimates Wcrit
MARS code: Y. Liu

## Slide 7
  Key transitional period 2006–08: Several experiments showed key inconsistencies with early stability physics models
Results from earlier critical rotation experiments using resonant magnetic braking (n = 1 field) rescinded – explained by torque bifurcation, not RWM (Garofalo, et al., IAEA Fusion Energy Conference (FEC) 2006, paper EX/7-1Ra)
New hypotheses were now needed to explain mode stabilization physics – that is where this story begins…
NSTX
 Conclusion: simple critical rotation hypothesis is NOT sufficient to explain stability, new theory needed
  NSTX using non-resonant (n = 3) magnetic braking by NTV yielded a growing RWM instability (Sabbagh, et al., PRL 97 (2006) 045004) and did not produce torque bifurcation (Sontag, Sabbagh, et al. NF 47 (2007) 1005)
  DIII-D with balanced NBI: RWM stable at plasma rotation less than 1% VA (Reimerdes PPCF 49 (2007) B349)
  NSTX: Berkery/Sabbagh showed RWM instability at higher plasma rotation (Sabbagh IAEA FEC 2008 paper EX/5-1; Berkery, et al. PRL 104 (2010) 035003
NSTX

## Slide 8
Kinetic modification to ideal MHD
Stability depends on
  Trapped / circulating ions, trapped electrons
  Particle collisionality
  Energetic particle (EP) population
  Integrated wf profile matters!!! : broad rotation resonances in dWK
plasma integral over particle energy
collisionality
wf profile (enters through ExB frequency)
precession drift
bounce
Drift kinetic theory energy functional (Hu/Betti) includes key precession drift resonance as stabilizing mechanism
ion gyro-orbit
and trajectory
(Fig. adapted from R. Pitts et al., Physics World (Mar 2006))
Trapped particle orbit precession drift
Trapped particle
orbit
EP integral component is dominated by precession drift term
Trapped orbit 2D
projections
(Hu, Betti, et al., PoP 12 (2005) 057301)

## Slide 9: Kinetic modifications show decrease in RWM stability at relatively high wf – consistent with experiment (MISK code)
S.A. Sabbagh, J.W. Berkery, et al., IAEA Fusion Energy Conference (FEC) 2008 (paper EX/5-1)
Marginal stable experimental plasma reconstruction, rotation profile wfexp
Variation of wf away from marginal profile increases stability
Unstable region at low wf
Theoretical variation of wf
Marginally stable
experimental
profile
121083
RWM stability vs. Vf (contours of gtw)
y/ya
wf/wfexp
2.0
1.0
0.2
wf/2p (kHz)
Im(dWK)
Re(dWK)
wf/wfexp
gtw
experiment
2.0
1.0
0.2
unstable
wf/wfexp
NSTX

## Slide 10: MISK calculations for NSTX consistent with RWM destabilization at intermediate plasma rotation; stability altered by collisionality
Destabilization appears between precession drift resonance at low wf, bounce/transit resonance at high wf
Destabilization moves to increased wf as n decreases
J.W. Berkery, et al., PRL 104 (2010) 035003 S.A. Sabbagh, et al., NF 50 (2010) 025020
NSTX 121083
unstable
(marginal stability)
unstable
Precession drift resonance stabilization
Bounce/transit resonance stabilization
Plasma evolution
Marginal stability
neff/nexp (marginal stability)
gtw contours vs. ν and wf
instability
(experiment)
wf/wfexp (marginal stability)
NSTX

## Slide 11
Kinetic modifications completely change the understanding and scaling of mode stability at reduced collisionality
- J.W. Berkery, S.A. Sabbagh, et al., Phys. Rev. Lett. 106 (2011) 075004
- J.W. Berkery, S.A. Sabbagh, et al., Phys. Plasmas 21 (2014) 056112
Ion precession drift resonance
stabilization
stable
unstable
Past models/ideas
  Collisions provide mode stabilization
  So, stability decreased with decreasing n
  Unfavorable for ITER
Present model
  Collisions spoil broad stabilizing resonances
  Mode stabilization vs. n depends on wf
    At strong resonance: mode stability increases with decreasing n
2.0
weak resonance
NSTX
unstable
stable

## Slide 12: Further kinetic RWM analysis showed importance of fast particles to refine quantitative marginal stability evaluation
Rotation profile scans in NSTX and DIII-D
Inclusion of fast particles more accurately determines mode stability
- Reimerdes, et al., APS 2008
- Sabbagh, Berkery, et al., APS DPP 2010 GI2.00001(invited talk)
- Berkery, Sabbagh, et al., PoP 21 (2014) 056112
NSTX 140132, t = 0.704s
unstable
Marginal stability in experiment
Stability vs. wf (contours of gtw) - NSTX
2.0
1.0
wf/wfexp
thermal
w/fast particles
125701
NSTX
Stable rotation profile scan - DIII-D
unstable
stable

## Slide 13: Kinetic RWM calculations for DIII-D are consistent with MHD spectroscopy results when energetic particles are included
Technique
  Low frequency MHD spectroscopy measures resonant field amplification (RFA) of applied n=1 field
  Yields RWM growth rate in a stable plasma
Results show
  Kinetic model requires fast ions to explain experimental stability
  Plasma rotation dependence of RFA matches kinetic RWM theory
    Similar finding in NSTX plasmas
    Recently re-confirmed in DIII-D
Reimerdes, Berkery, …, Sabbagh et al., PRL 106 (2011) 215002
Less stable
 H. Reimerdes, et al., PRL 93 (2004) 135002
Rotation
Rotation
(Wang, Lanctot, Liu, et al., PRL 114 (2015) 145005)

## Slide 14
Experiments directly measuring global stability using MHD spectroscopy (RFA) understood by kinetic RWM theory
(trajectories of 20 experimental plasmas)
Stability vs. bN/li
  decreases up to bN/li = 10, increases at higher bN/li
  Consistent with kinetic resonance stabilization
Resonant Field Amplification vs. bN/li
unstable
RWM
S. Sabbagh, et al., NF 53 (2013) 104007
J. Berkery, et al., PoP 21 (2014) 056112
RFA vs. rotation (wE)
Stability vs. rotation
  Largest stabilizing effect from ion precession drift resonance with wf
Minimize |<ωD> + ωE|
NSTX
Most
stable
RFA Amp. (G/G)
RFA Amp. (G/G)
Less stable

## Slide 15: 2014: Dedicated DIII-D experiments directly probed RWM marginal stability boundary, compared to NSTX results
Candidates for steady-state, high bN operation
Can have high probability of significant RWM activity with qmin > 2
  RWMs and TMs cause strong b collapses in 82% of a database of 50 shots examined, with an average of 3 collapses every 2 shots
  RWMs cause collapse 60% of the time, TMs 40% of the time
Employ high qmin > 2 to avoid 2/1 TM instability (TM precludes RWM)
  Used ECCD control of 3/1 TM to provide further control of strong n = 1 TMs
Unique 1 ms resolution of wf and Ti measurement captures profile detail in timescale < RWM growth time
DIII-D High bN, qmin plasmas
NSTX
Strong RWM drive: Maximum bN > 7, bN /li > 13.5
Strong TMs eliminated by high elongation (> 2.6) or Li wall conditioning
NSTX
S.A. Sabbagh, J.W. Berkery, J. Hanson, et al. APS DPP Invited Talk VI2.0002 (2014)

## Slide 16: 2014: Kinetic RWM marginal stability boundaries were directly probed over wide range of plasma rotation profiles
RWM marginal stability examined for major and minor disruptions
  Found at high bN and high rotation
  Found at high bN and low rotation
    Low rotation expected in ITER
  At moderate bN and high rotation with increased profile peaking
    similar loss of profile broadness might easily occur in ITER
1.
2.
3.
Wide range of DIII-D toroidal plasma
velocity profiles
Plasma toroidal rotation (km/s)
R (m)
1.7
1.8
1.9
2.0
2.1
2.2
2.3
400
300
200
100
0
-100
S.A. Sabbagh, J.W. Berkery, J. Hanson, et al. APS DPP Invited Talk VI2.0002 (2014)

## Slide 17: Comparison of RWM growth and dynamics in high bN shots with high plasma rotation
Elements
  RWM rotation and mode growth observed
  No strong NTM activity
  Some weak bursting MHD in DIII-D plasma
    Alters RWM phase
  No bursting MHD in NSTX plasma
DIII-D (bN = 3.5)
NSTX (bN = 4.4)
1.
DBpn=1(G)
fBpn=1(deg)
(arb)
Frequency (kHz)
t (s)
t (s)
amplitude
phase
Da
toroidal magnetics
rotation
growth
rotation
growth
amplitude
phase
Da
toroidal magnetics
NSTX

## Slide 18: Evolution of plasma rotation profile leads to linear kinetic RWM instability as disruption is approached
DIII-D (minor disruption)
NSTX (major disruption)
MISK
MISK
unstable
stable
unstable
stable
increasing time
increasing time
gtwall
gtwall
NSTX

## Slide 19: Kinetic RWM stability analysis evaluated for DIII-D and NSTX plasmas
Summary of results
  Plasmas free of other MHD modes can reach or exceed linear kinetic RWM marginal stability
Plasma rotation [krad/s] (yN = 0.5)
Normalized growth rate (gtw)
major disruption
minor disruption
DIII-D
NSTX
unstable
Kinetic RWM stability analysis for experiments (MISK)
1.
2.
3.
1.
stable
NSTX
S.A. Sabbagh, J.W. Berkery, J. Hanson, et al. APS DPP Invited Talk VI2.0002 (2014)

## Slide 20: Kinetic RWM stability analysis evaluated for DIII-D and NSTX plasmas
Summary of results
  Plasmas free of other MHD modes can reach or exceed linear kinetic RWM marginal stability
  Bursting MHD modes can lead to non-linear destabilization before linear stability limits are reached
Plasma rotation [krad/s] (yN = 0.5)
Normalized growth rate (gtw)
major disruption
minor disruption
DIII-D
NSTX
unstable
Kinetic RWM stability analysis for experiments (MISK)
“weak stability” region
- Present analysis can quantitatively define
a “weak stability” region below linear instability
Strait, et al., PoP 14 (2007) 056101
stable
NSTX
S.A. Sabbagh, J.W. Berkery, J. Hanson, et al. APS DPP Invited Talk VI2.0002 (2014)

## Slide 21: Bounce resonance stabilization dominates for DIII-D vs. precession drift resonance for NSTX at similar, high rotation
DIII-D experimental rotation profile
NSTX experimental rotation profile
|δWK| for trapped resonant ions vs. scaled experimental rotation (MISK)
133103 @ 3.330 s
stable plasma
133776 @ 0.861 s
stable plasma
precession
resonance
bounce / circulating
resonance
precession
resonance
bounce / circulating
resonance
DIII-D
NSTX
NSTX
Rotation

## Slide 22: Reduced RWM stability measured in DIII-D plasmas as qmin is increased is consistent with kinetic RWM theory
|δWK| for trapped resonant ions vs. scaled experimental rotation (MISK)
Measured plasma response to 20 Hz, n = 1 field vs qmin
n = 1 |dBp | (G/kA)
qmin
DIII-D experimental rotation profile
precession drift
resonance
bounce /
circulating
resonance
DIII-D (qmin = 1.2)
DIII-D (qmin = 1.6)
DIII-D (qmin = 2.8)
Bounce resonance dominates precession drift resonance for all qmin examined at the experimental rotation
less stable

## Slide 23
Key analysis codes MARS-K and MISK were brought into agreement in γτw vs ωE for analysis of ITER
fluid growth rates
fluid plus kinetic growth rates
unstable
stable
low rotation
precession
resonance
high rotation
bounce/transit
resonance
- J.W. Berkery, Y. Liu, … S.A. Sabbagh et al.
Phys. Plasmas 21 (2014) 052505
  Case: bN = 2.9 (20% > no-wall limit – advanced scenario)
  Alpha particles are required for RWM stabilization at all wf
  Near RWM marginal stability at ba/btotal = 0.1 at expected rotation
expected ωφ
expected βα
unstable
stable
MISK calculation for ITER
Code benchmarking (growth rate vs. rotation)
Rotation
MARS-K code/analysis: Y. Liu, Z. Wang
unstable
stable

## Slide 24
Predictor/Sensor (CY available) | Control/Actuator (CY available) | Modes | REFER TO
Rotating and low freq. MHD (n=1,2,3) 2003 | Dual-component RWM sensor control (closed loop 2008) | NTM RWM | - Menard NF 2001 - Sabbagh NF 2013
Low freq. MHD spectroscopy (open loop 2005); Kinetic RWM modeling (2008) | Control of βN (closed loop 2007) | Kink/ball RWM | - Sontag NF 2007 - Berkery (2009–15) - Gerhardt FST 2012
r/t RWM state-space controller observer (2010) | Physics model-based RWM state-space control (2010) | NTM, RWM Kink/ball, VDE | - Sabbagh IAEA 2010 - Sabbagh NF 2013 - THIS TALK
Real-time Vf measurement (2016) | Plasma Vf control (NTV 2004) (NTV + NBI rotation control closed loop ~ 2018-19) | NTM Kink/ball RWM | - Podesta RSI 2012 - Zhu PRL 06 - THIS TALK
Reduced kinetic RWM stabilization (2016) (aimed at real-time) | Safety factor, li control (closed loop ~ 2018-19) | NTM, RWM Kink/ball, VDE | - Berkery, NF 2015 (+ THIS TALK) - D. Boyer, NF 2015
MHD spectroscopy (real-time) (in 5 Year Plan) | Upgraded 3D coils (NCC): improved Vf and mode control (in 5 Year Plan) | NTM, RWM Kink/ball, VDE | - NSTX-U 5 Year Plan
NSTX-U is building on past strength, creating an arsenal of capabilities for disruption avoidance (available / future)

## Slide 25: A reduced kinetic RWM model in new Disruption Event Characterization And Forecasting (DECAF) code
Ideal component dW
  Equilibrium quantities including li, p0/<p>, A, used in beta limit models for dWb, dWinf
Kinetic component dWk
  Functional forms (mainly Gaussian) used to reproduce precession and bounce/transit resonances
  Height, width, position of peak depend on collisionality
J.W. Berkery, S.A. Sabbagh, R.E. Bell, et al., NF 55 (2015) 123007
Bounce/transit resonances
Precession resonances
<n> = 1 kHz
DCON calculation of n=1 no-wall limit
Elements: mode growth rate calculation
NSTX

## Slide 26: Reduced kinetic RWM model in DECAF results in a calculation of gtw vs. time for each discharge
Favorable characteristics
  Stability contours CHANGE for each time point (last time point shown left frame)
  Possible to compute growth rate prediction in real time
ideal
Ideal + kinetic
unstable
stable
gtw contours vs. ν and wf
Normalized growth rate vs. time
gtw
gtw
Increasing time
139514
disruption
predicted instability
J.W. Berkery, S.A. Sabbagh, R. Bell, et al., submitted to Phys. Plasmas (2017)
NSTX

## Slide 27: DECAF reduced kinetic model results initially tested on a database of NSTX discharges with unstable RWMs
86% of shots are predicted unstable
54% predicted unstable < 300 ms (approx. 60tw) before current quench
32% predicted unstable < 450 ms before current quench
  Mostly earlier cases are minor disruptions
Predicted instability statistics (44 shots)
Normalized growth rate vs. time
Chart: 
| < 300ms | > 300ms | no warning
 | 24 | 14 | 6
Stable
(14%)
Instability < 450 ms
before disruption
(32%)
Instability < 300 ms
before disruption
(54%)
unstable
stable
NSTX

## Slide 28: State space rotation controller designed for NSTX-U using non-resonant NTV and NBI to maintain stable profiles
Momentum force balance – wf decomposed into Bessel function states
Neoclassical Toroidal Viscosity (NTV) torque:
yN
NBI, -NTV torque density (N/m2)
NBI
Torque
(NSTX)
0.0
0.5
1.0
1.5
0.0
0.2
0.4
0.6
0.8
1.0
NBI and NTV torque profiles for NSTX-U
Momentum Actuators
New NBI
(broaden rotation)
3D Field Coil
(shape wf profile)
-NTV
Torque
NSTX

## Slide 29: State space rotation controller designed for NSTX-U using non-resonant NTV and NBI to maintain stable profiles
Momentum force balance – wf decomposed into Bessel function states
Neoclassical Toroidal Viscosity (NTV) torque:
NBI, -NTV torque density (N/m2)
NBI
Torque
(NSTX)
0.0
0.5
1.0
1.5
NBI and NTV torque profiles for NSTX-U
NBI Torque
(NSTX-U)
Momentum Actuators
New NBI
(broaden rotation)
3D Field Coil
(shape wf profile)
-NTV
Torque
yN
0.0
0.2
0.4
0.6
0.8
1.0
NSTX

## Slide 30: NTV physics studies for rotation control: measured NTV torque density profiles quantitatively compare well to theory
TNTV (theory) scaled to match peak value of measured -dL/dt
  Scale factor ((dL/dt)/TNTV) = 1.7 and 0.6 for cases shown above – O(1) agreement
n = 2 coil configuration
Experimental
-dL/dt
yN
NSTX
NTVTOK
x1.7
n = 3 coil configuration
Experimental
-dL/dt
NTVTOK
yN
NSTX
x0.6
Also, see recent NTV review paper: K.C. Shaing, K. Ida, S.A. Sabbagh, et al., Nucl. Fusion 55 (2015) 125001
For NTV experiment/theory see: W. Zhu, S.A. Sabbagh, R.E. Bell, et al., PRL 96 (2006) 225002
NSTX

## Slide 31
Application of kinetic RWM physics understanding from present research will now be used for disruption avoidance
I. Goumiri, C. Rowley, S.A. Sabbagh, et al. Nucl. Fusion 56 (2016) 036023
Recall:
NSTX (major disruption)
MISK
unstable
stable
stable
gtwall
Plasma rotation (kHz)
0
15
20
10
5
yN
0.0
0.2
0.4
0.6
0.8
1.0
Planned rotation control in NSTX-U
(actuators: 6 NBI sources, n = 3 NTV)
marginally
stable
Steady-state reached in ~ 3tm
Marginally stable profile
Broader stable
profile
NBI, -NTV torque density (N/m2)
0.0
0.5
1.0
1.5
2.0
Plasma rotation (krad/s)
NBI
-NTV
NSTX

## Slide 32: Model-based RWM state space controller including 3D model of plasma and wall currents used at high bN
Controller model can compensate for wall currents
  Includes linear plasma mode-induced current model (DCON)
  Includes plasma response model
  Straightforward inclusion of multiple modes (n = 1, or n > 1)
Potential to allow control coils to be moved further from plasma, and be shielded (e.g. for ITER)
Balanced truncation
~3000+ states
Full 3-D model
…
RWM eigenfunction(2 phases, 2 states)
State reduction (< 20 states)
Controller reproduction of n = 1 field in NSTX
100
150
50
0
-50
-100
-150
Sensor Difference (G)
0.4
0.6
0.8
1.0
0.2
t (s)
118298
118298
100
150
50
0
-50
-100
-150
Sensor Difference (G)
Measurement
Controller
(observer)
5 states
used
10 states
used
(only wall states used)
O. Katsuro-Hopkins, et al., NF 47 (2007) 1157
A. Boozer, Phys. Plasmas 10 (2003) 1458
NSTX

## Slide 33: NSTX RWM state space controller sustains otherwise disrupted plasma caused by DC n = 1 applied field
n = 1 DC applied field test
  Generate resonant field amplication, disruption
  Use of RWM state space controller sustains discharge
RWM state space controller sustains discharge at high bN
  Best feedback phase produced long pulse, bN = 6.4, bN/li = 13
140025
140026
Control
applied
Control not applied
bN
IRWM-4 (kA)
wf/2p~q=2
(kHz)
Bpn=1 (G)
Ip (MA)
n = 1 field on
0.0
0.2
0.4
0.6
0.8
1.0
t(s)
1.2
0.6
0.0
6
3
0
10
5
0
0.5
0.0
12
8
4
0
RWM state space feedback (12 states)
n = 3 correction
S. Sabbagh et al., Nucl. Fusion 53 (2013) 104007
S. Sabbagh et al., IAEA FEC (2010) Paper EXS/5-5
NSTX

## Slide 34: NSTX RWM state space controller sustains high bN, low li plasma – available for NSTX-U with independent coil control
RWM state space feedback (12 states)
n = 1 applied field suppression
  Suppressed disruption due to n = 1 field
Feedback phase scan
  Best feedback phase produced long pulse, bN = 6.4, bN/li = 13
NSTX Experiments
(from 2010)
Ip (MA)
(A)
S. Sabbagh et al., Nucl. Fusion 53 (2013) 104007
S. Sabbagh et al., IAEA FEC (2010) Paper EXS/5-5
NSTX

## Slide 35: Open-loop comparisons between measurements and RWM state space controller show importance of states and model
Improved agreement with sufficient number of states (wall detail)
A) Effect of Number of States Used
dBp180
100
200
0
-100
RWM Sensor Differences (G)
137722
t (s)
40
0
80
0.56
0.58
0.60
137722
t (s)
0.56
0.58
0.60
0.62
dBp180
dBp90
dBp90
-40
0.62
t (s)
0.56
0.58
0.60
0.62
t (s)
0.56
0.58
0.60
0.62
100
200
0
-100
40
0
80
-40
7 States
B) Effect of 3D Model Used
No NBI Port
With NBI Port
2 States
RWM
3D detail of model important to improve agreement
Sensor data
Controller (observer)
RWM sensors
Sensor
data
Controller
(observer)
RWM
NSTX

## Slide 36: In addition to active mode control, the NSTX-U RWM state space controller can be used for real-time disruption warning
Sensor
data
Controller
(observer)
The controller “observer” produces a physics model-based calculation of the expected sensor data – a synthetic diagnostic
If the real-time synthetic diagnostic doesn’t match the measured sensor data, a r/t disruption warning signal can be triggered
  Technique will be assessed using new Disruption Event Characterization and Forecasting (DECAF) code
RWM Sensor Differences (G)
RWM Sensor Differences (G)
137722
t (s)
40
0
80
0.56
0.58
0.60
137722
t (s)
0.56
0.58
0.60
0.62
dBp90
dBp90
-40
0.62
40
0
80
-40
Effect of 3D Model Used
No NBI Port
With NBI Port
RWM
NSTX

## Slide 37: In addition to active mode control, the NSTX-U RWM state space controller can be used for real-time disruption warning
Sensor
data
Controller
(observer)
The controller “observer” produces a physics model-based calculation of the expected sensor data – a synthetic diagnostic
If the real-time synthetic diagnostic doesn’t match the measured sensor data, a r/t disruption warning signal can be triggered
  Technique will be assessed using new Disruption Event Characterization and Forecasting (DECAF) code
RWM Sensor Differences (G)
RWM Sensor Differences (G)
137722
t (s)
40
0
80
0.56
0.58
0.60
137722
t (s)
0.56
0.58
0.60
0.62
dBp90
dBp90
-40
0.62
40
0
80
-40
Effect of 3D Model Used
No NBI Port
With NBI Port
RWM
NSTX

## Slide 38
Higher T, low n* from low to high 
 Unique regime, study new transport and stability physics
Full non-inductive current drive
 Not demonstrated in ST at high-T
Essential for any future steady-state ST
2. Tangential 2nd Neutral Beam
1. New Central Magnet
NSTX-U will access new physics with 2 major new tools

## Slide 39
NSTX-U designed for major performance boost
2. Tangential 2nd Neutral Beam
1. New Central Magnet
2× toroidal field (0.5  1T)
2× plasma current (1  2MA)
5× longer pulse (1  5s)
2× heating power (5  10MW)
Tangential NBI  2× current drive efficiency
4× divertor heat flux ( ITER levels)
Up to 10× higher nTE (~MJ plasmas)

## Slide 40
NSTX Upgrade Device and Test Cell – Interior (inset) and Aerial View
HHFW System
1st NBI
2nd NBI
NSTX-U

## Slide 41
NSTX-U will address key physics questions in first 3 years leveraging unique capabilities
What role do electromagnetic effects play in electron energy transport? (High b, lower n*)
Can fast-ion instabilities be predicted and controlled for ITER and beyond? (Vary vf /vA, bf, anisotropy)
Can ST operate disruption-free near with-wall limit, aiming to be 100% non-inductive?
  Only ST in world capable of this research critical for steady-state FNSF / Pilot Plant
What physics determines SOL heat flux width? (Low-A, 2× IP , Li wall)
How do advanced divertors and Li impact edge transport, scenarios?
Confinement vs. b , collisionality
Sustain high b w/ advanced control
Non-inductive start-up, ramp-up
Mitigate high heat fluxes
Test high-Z divertor, Li vapor shielding
Establish ST physics / scenarios:

## Slide 42: NSTX / MAST confinement increased at higher Te (!) Will confinement trend continue, or look like conventional A?
Normalized electron collisionality ne*  ne / Te2
ITER-like scaling
ST-FNSF
?
constant q, b, r*
NSTX Upgrade
NSTX
Favorable confinement results could lead to more compact ST reactors
Low n*  need higher plasma current, toroidal field, heating power, density control

## Slide 43: NSTX-U has surpassed maximum pulse duration and magnetic field of NSTX
Compare similar NSTX / NSTX-U Boronized L-modes, PNBI=1MW
NSTX-U L-mode duration
exceeds longest NSTX H-mode
4x longer
NSTX-U BT > highest NSTX BT

## Slide 44: Accessed high elongation k using progressively earlier H-mode and heating + optimized EFC
L-mode flattop
H-mode flattop
NSTX-U (5 run weeks)
NSTX (10 years)
Future goal
Goal: Internal inductance li = 0.5-0.7  k = 2.4-2.7

## Slide 45: Recovered ~1MA H-modes that reached / exceeded the ideal n = 1 no-wall limit
H98 ≥ 1, βN ~ 3.5-4 ≥ n=1 no-wall limit
202946 – no EFC 204112 – EFC v2
203679 – EFC v1 204118 – EFC v2

## Slide 46: H-mode confinement > ITER scaling, consistent with ST scaling (so far) – need higher IP, BT to test

## Slide 47: Most tangential NBI generates counter-propagating Toroidal Alfvén Eigenmodes (TAEs)
Counter-propagating TAE predicted for hollow fast-ion profiles
H.V. Wong, H. Berk, Phys. Lett. A 251 (1999) 126.
TRANSP: As current builds up beam fast-ion beta profile predicted to become hollow
1st evidence of off-axis NBI in NSTX-U

## Slide 48: Tangential 2nd neutral beam suppresses Global Alfven Eigenmode (GAE) – consistent with simulation
t ci
HYM code simulation of #204707, n=10
|dBn |2
t=0.44s
t=0.47s
New 2nd NBI already powerful tool for fast-ion mode physics
HYM code: growth of n=10 counter-GAE from 1st NBI
HYM: suppression of n=10 counter-GAE by 2nd NBI
Most unstable n-number, mode w consistent with HYM

## Slide 49: NSTX-U had scientifically productive 1st year
Achieved H-mode on 8th day of 10 weeks of operation
Surpassed magnetic field and pulse-duration of NSTX
Matched best NSTX H-mode performance at ~1MA
Identified and corrected dominant error fields
Exceeded the n = 1 ideal MHD no-wall beta limit
Injected up to 12MW NBI power into armor by end of run
Discovered new 2nd NBI modifies several fast-ion modes
Implemented techniques for controlled plasma shut down, disruption detection, commissioned new tools for mitigation
2016 run ended prematurely due to fault in divertor PF coil
  Coil forensics, Extent of Condition  new coil fab, other repairs
  Aim to resume plasma operation during 2018 – but timing still TBD

## Slide 50: Research established verified understanding of kinetic MHD theory to determine global mode stability in tokamaks
  Early theory did not find general agreement with experimental global mode (RWM) marginal stability; simple “critical rotation” hypothesis inadequate
  Drift kinetic theory modification to ideal stability criterion can explain mode stability results in experiments when precession drift physics is included
Computed kinetic RWM marginal stability limits can describe disruptive limits in plasmas free of other MHD modes
Stabilization physics complementarity found: at similar high rotation, kinetic RWM stabilization physics dominated by ion precession drift resonance in NSTX, and bounce orbit resonance in DIII-D
Unification of theoretical understanding and joint experimental verification allows stability research to progress to next step: disruption avoidance
  Expanded use of present theory for disruption prediction
  Disruption avoidance via plasma rotation profile control
- Berkery, Sabbagh, et al. submitted to PoP (2017)
- Goumiri, Rowley, Sabbagh, et al. NF 56 (2016) 036023

## Slide 51: Goals for future NSTX-U operation
Increase field to 0.8-1T, current to 1.6-2MA, extend flat-top duration (H-mode) to 2-5s
Characterize 2nd beam: heating, current drive, torque / rotation profiles, fast-ion instabilities
Characterize and forecast events leading to disruptions; demonstrate disruption-free operation
Assess energy confinement, pedestal height/structure, edge heat-flux width
Push toward full non-inductive current drive
Test advanced divertor heat flux mitigation

## Slide 52
Supporting Slides Follow

## Slide 53: Modification of Ideal Stability by Kinetic theory (MISK code) has sufficiently broad physics to determine RWM stability
Energy balance
Kinetic Energy
Change in potential energy due to perturbed kinetic pressure is:
Fluid terms
is solved numerically by using from the drift kinetic equation to solve for
Precession drift resonance
~ Plasma Rotation
Collisionality
Bounce orbit resonances
(Hu, Betti, et al., PoP 12 (2005) 057301)

## Slide 54
Plasma response to external n=1 field is determined by the RWM damping rate gRWM and mode rotation frequency wRWM
Dependence of the plasma response dBplas on the frequency wext of an externally applied n=1 field described by single mode model
  Perturbed field at wall:
  Plasma response at wall:
  with complex growth rate
  g0=gRWM+iwRWM
  and coupling coefficient Msc between coil c and sensor s
*
H. Reimerdes et al., PRL (2004)

## Slide 55: A classic, simple RWM model illustrates basic mode dynamics
Simulation with error field, and increasing mode drive
Stable RWM amplifies error field (resonant field amplification (RFA))
When RWM becomes unstable, it first unlocks, rotates in co-NBI direction
  Amplitude is not strongly growing during this period
Eventually unstable mode amplitude increase causes RWM to re-lock, mode grows strongly
RWM growth rate, rotation frequency is O(1/twall)
R. Fitzpatrick, Phys. Plasmas 9 (2002) 3459
log10(mode amplitude)
mode phase (arb)
plasma velocity (arb)
RWM stable, amplifies 3D field
RWM unstable
mode rotating
mode growth
30
60
0
time (normalized to twall)
2
1
0
-1
-2
1
0
-1
0.4
0.2
0
10
20
40
50

## Slide 56: Kinetic RWM stability analysis evaluated for DIII-D and NSTX plasmas
Summary of results
  Plasmas free of other MHD modes can reach or exceed linear kinetic RWM marginal stability
  Bursting MHD modes can lead to non-linear destabilization before linear stability limits are reached
  Extrapolations of DIII-D plasmas to different Vf show marginal stability is bounded by 1.6 < qmin < 2.8
Kinetic RWM stability analysis for experiments (MISK)
Plasma rotation [krad/s] (yN = 0.5)
Normalized growth rate (gtw)
major disruption
minor disruption
DIII-D
NSTX
stable
unstable
extrapolation
qmin = 2.8
qmin = 1.6
“weak stability” region
NSTX

## Slide 57: The earliest potential indication of a locking island (from CER) comes after the n = 1 RWM has fully grown
1 ms CER indicates that an island may be forming and locking by 1.510s
Magnetics show that n = 1 RWM reaches full amplitude by 1.509s
Conclude that this dynamic is not caused by an island-induced loss of torque balance
Earliest indication of island
RWM growth
starts
RWM growth
ends

## Slide 58
INITIAL RESULT | rwall/a | Ideal dW/-dW¥ | Re(dWk) /dW¥ | Im(dWk)/ (dW¥) | gtwall | wtwall | dWk/-dW¥ (wE = ¥)
Solov’ev 1 (MARS-K) (MISK) | 1.15 | 1.187 1.122 | 0.0256 0.0243 | -0.0121 0.0280 | 0.804 0.850 | -0.0180 -0.0452 | 
Solov’ev 3 (MARS-K) (MISK) | 1.10 | 1.830 2.337 | 0.208 0.371 | -0.343 0.0601 | 0.350 0.232 | -0.228 -0.0273 | 
ITER (MARS-K) (MISK) | 1.50 | 0.682 0.677 | 141.5 0.665 | 2.286 -0.548 | -0.988 0.0709 | 0.00019 0.437 | 
FINAL RESULT |  |  |  |  |  |  | 
Solov’ev 1 (MARS-K) (MISK) | 1.15 | 1.187 1.122 | 0.0218 0.0208 | -0.0121 -0.0068 | 0.803 0.861 | 0.0180 0.0189 | 0.157 0.154
Solov’ev 3 (MARS-K) (MISK) | 1.10 | 1.830 2.337 | 0.0794 0.0892 | -0.147 -0.090 | 0.471 0.374 | 0.114 0.051 | 1.98 1.09
ITER (MARS-K) (MISK) | 1.50 | 0.682 0.677 | 0.241 0.367 | -0.046 -0.133 | 0.817 0.581 | 0.090 0.202 | 6.11 6.72
Due to benchmarking effort, alterations to both MARS-K and MISK codes produced agreement in all categories
Green = good

## Slide 59: State Derivative Feedback Algorithm needed for Current Control
Previously published approach found to be formally “uncontrollable” when applied to current control
State derivative feedback control approach
  new Ricatti equations to solve to derive control matrices – still “standard” solutions for this in control theory literature
Control vector, u; controller gain, Kc
Observer est., y; observer gain, Ko
Kc , Ko computed by standard methods
(e.g. Kalman filter used for observer)
Advance discrete state vector
(time update)
(measurement
update)
e.g. T.H.S. Abdelaziz, M. Valasek., Proc. of 16th IFAC World Congress, 2005
State equations to advance
General (portable) matrix output file for operator
Written into the PCS
NSTX

## Slide 60
The ITPA process greatly aided our unified EU and US effort
(example: code benchmarking and implications for ITER)
ITPA allowed a common basis and goals for research
  Reimerdes, Sabbagh, Liu were/are ITPA joint experiment leaders/co-leaders
Significant kinetic RWM analysis code benchmarking effort
  Two Solov’ev, and ITER Advanced Scenario case tested
  Leading codes tested: MARS-K, MISK (PENT code written during this process)
Key components of the analyses separately compared
  Ideal MHD stability functional dW (with and without stabilizing wall)
  Kinetic MHD stability functional dWk (Real & Imaginary components)
Yielded a direct comparison of kinetic RWM growth rate and natural rotation rate (gtwall, wtwall)
ITPA joint experiments: MDC-2 Reimerdes, Liu, Sabbagh; and MDC-21: Sabbagh, Liu

## Slide 61: The 2016 Landau-Spitzer Award recipients are greatly thankful for this fine honor
The awardees especially thank
  The 2016 Award committee
  The EPS and the APS
  Prof. Riccardo Betti (U. Rochester) for his enthusiastic, and selfless nomination
The awardees
  Appreciate the joint, collaborative, nature of this research between the EU and US, aided by the ITPA
  Acknowledge the experimental teams on NSTX and DIII-D; scientific exchanges with JET, JT-60U, RFX, HBT-EP
  Convey that the research meriting the award comprises an ~decade-long effort
S.A. Sabbagh
J.W. Berkery
Y.Q. Liu
H. Reimerdes
Landau
Spitzer

## Slide 62
1st year: Limit forces to ½ way between NSTX and NSTX-U, and ½ of the design-point heating of any coil
  Presently operating at BT ~ 0.63T
  Increase to BT ~ 0.8T after completing engineering analysis
2nd year goal: Full field and current, coil heating to ¾ of limit
3rd year goal: Full capability
Parameter | NSTX (Max.) | Year 1 NSTX-U Operations | Year 2 NSTX-U Operations | Year 3 NSTX-U Operations | NSTX-U Ultimate Goal
IP [MA] | 1.2 | ~1.6 | 2.0 | 2.0 | 2.0
BT [T] | 0.55 | ~0.8 (0.65) | 1.0 | 1.0 | 1.0
Allowed TF I2t [MA2s] | 7.3 | 80 | 120 | 160 | 160
IP Flat-Top at max. allowed I2t, IP, and BT [s] | ~0.4 | ~3.5 | ~3 | 5 | 5
NSTX-U device performance progression

## Slide 63: Fast-ion confinement measured to be at / near predicted values at low total NBI power ~1-2MW
Good agreement between neutron measurement and TRANSP prediction
Need small anomalous fast ion diffusivity (Daf=0.3m2/s) for agreement
Neutron rate
ENBI = 85keV
ENBI = 65keV