## Slide 1: Columbia U. Group - Collaborative Research on NSTX-U for Disruption Avoidance
S.A. Sabbagh – for the Columbia U. / NSTX-U Group
(J.W. Berkery, J.M. Bialek, Y.S. Park)
Report to DOE and NSTX-U Program
PPPL
7/23/15
V1.1

## Slide 2: Near 100% disruption avoidance is a critical need for future tokamaks; Columbia Research on NSTX-U is focused on this
The new “grand challenge” in tokamak stability research
  Can be done! (JET: < 4% disruptions w/C wall, < 10% w/ITER-like wall)
    ITER disruption rate: < 1 - 2% (energy load, halo current); << 1% (runaways)
Strategic plan: utilize/expand stability/control research success
  Disruption prediction, avoidance, and mitigation (DPAM) is multi-faceted, best addressed by a focused, (inter)national effort (multiple devices/institutions)
FESAC 2014 Strategic Planning report defined “Control of Deleterious Transient Events” highest priority (Tier 1) initiative
NSTX-U is a world-leading laboratory for focused research on disruption avoidance with quantitative measures of progress
  Columbia U. group endorsed by NSTX-U Program in a leadership role for this research, building on past success in MHD stability and control research

## Slide 3: Columbia Group Research at PPPL provides key disruption avoidance research, emphasis on global mode stabilization
Physics Elements
  Kinetic RWM stabilization physics - unification between NSTX / DIII-D
  NTV used in plasma rotation control (supports NSTX-U Vf control)
  Physics model-based active RWM state-space controller
  Dual-component sensor RWM PID control
  RWM control analysis of upgraded 3D coils for NSTX-U
  NSTX-U equilibrium reconstruction – key basis for stability analysis
  Planned real-time MHD spectroscopy for NSTX-U (in 5 Year Plan)
  Related high normalized beta and NTV experiments on KSTAR
Research synergism
  These elements now being brought together as part of a disruption prediction/avoidance system; NSTX-U DPAM working group formed)
  New Disruption Characterization and Prediction code / initial results
Response to DOE call for enhanced university participation
  CU-PPPL group outreach to Columbia U. APAM department; new diagnostic proposal to be submitted (Volpe/Sabbagh)
Princeton
student

## Slide 4: Joint NSTX / DIII-D experiments and analysis gives unified kinetic RWM physics understanding for disruption avoidance
RWM Dynamics
  RWM rotation and mode growth observed
  No strong NTM activity
  Some weak bursting MHD in DIII-D plasma
    Alters RWM phase
  No bursting MHD in NSTX plasma
DIII-D (bN = 3.5)
NSTX (bN = 4.4)
DBpn=1(G)
fBpn=1(deg)
(arb)
Frequency (kHz)
t (s)
t (s)
amplitude
phase
Da
toroidal magnetics
rotation
growth
rotation
growth
amplitude
phase
Da
toroidal magnetics
S. Sabbagh et al., DIII-D/NSTX experiments
S. Sabbagh et al., APS Invited talk 2014

## Slide 5: Evolution of plasma rotation profile leads to linear kinetic RWM instability as disruption is approached
DIII-D (minor disruption)
NSTX (major disruption)
MISK
MISK
unstable
stable
unstable
stable
increasing time
increasing time
gtwall
gtwall
S. Sabbagh et al., DIII-D/NSTX experiments; S. Sabbagh et al., APS Invited talk 2014

## Slide 6: Kinetic RWM stability evaluated for DIII-D and NSTX plasmas, reproduces experiments over wide rotation range
Summary of results
  Plasmas free of other MHD modes can reach or exceed linear kinetic RWM marginal stability
  Bursting MHD modes can lead to non-linear destabilization before linear stability limits are reached
  Extrapolations of DIII-D plasmas to different Vf show marginal stability is bounded by 1.6 < qmin < 2.8
Kinetic RWM stability analysis for experiments (MISK)
Plasma rotation [krad/s] (yN = 0.5)
Normalized growth rate (gtw)
major disruption
minor disruption
DIII-D
NSTX
stable
unstable
extrapolation
qmin = 2.8
qmin = 1.6
“weak stability” region
Reduced models of kinetic RWM stability now being investigated to support real-time disruption avoidance (e.g. by rotation profile control)
J.W. Berkery, J.M. Hanson, S.A. Sabbagh (Columbia U.)

## Slide 7: Rotation feedback controller designed for NSTX-U using non-resonant NTV and NBI used as actuators
3D coil current and NBI power (actuators)
t (s)
t (s)
3D Coil Current (kA)
feedback on
feedback on
0.5
0.6
0.7
0.8
0.5
0.6
0.7
0.8
2
1
0
NBI power (MW)
7
1
0
6
5
4
3
2
yN
NBI, NTV torque density (N/m2)
Plasma rotation (rad/s)
NTV
torque
0
6
8
10
104
desired wf
t1
t4
4
2
NBI
torque
t1 = 0.00t
t2 = 0.68t
t3 = 1.99t
t4 = 4.78t
0.0
0.5
1.0
1.5
2.0
2.5
0.0
0.2
0.4
0.6
0.8
1.0
Rotation evolution and NBI and NTV torque profiles
I. Goumiri (P.U. student), S.A. Sabbagh (Columbia U.), C. Rowley (P.U.), D.A. Gates, S.P. Gerhardt (PPPL)
Momentum force balance – wf decomposed into Bessel function states
NTV torque:
(non-linear)

## Slide 8: NTV physics studies for rotation control: measured NTV torque density profiles quantitatively compare well to theory
TNTV (theory) scaled to match peak value of measured -dL/dt
  Scale factor ((dL/dt)/TNTV) = 1.7 and 0.6 for cases shown above – O(1) agreement
n = 2 coil configuration
Experimental
-dL/dt
yN
NSTX
NTVTOK
x1.7
n = 3 coil configuration
Experimental
-dL/dt
NTVTOK
yN
NSTX
x0.6
S. Sabbagh et al., IAEA FEC 2014 (EX/1-4)

## Slide 9: Model-based RWM state space controller including 3D model of plasma and wall currents used at high bN
Controller model can compensate for wall currents
  Includes plasma mode-induced current
Potential to allow more flexible control coil positioning
  May allow control coils to be moved further from plasma, and be shielded (e.g. for ITER)
  Straightforward inclusion of multiple modes (with n = 1, or n > 1) in feedback
Balancing transformation
~3000+ states
Full 3-D model
…
RWM eigenfunction(2 phases, 2 states)
State reduction (< 20 states)
Katsuro-Hopkins, et al., NF 47 (2007) 1157
Controller reproduction of n = 1 field in NSTX
100
150
50
0
-50
-100
-150
Sensor Difference (G)
0.4
0.6
0.8
1.0
0.2
t (s)
118298
118298
100
150
50
0
-50
-100
-150
Sensor Difference (G)
Measurement
Controller
(observer)
5 states
used
10 states
used
(only wall states used)

## Slide 10: NSTX RWM state space controller sustains high bN, low li plasma
RWM state space feedback (12 states)
n = 1 applied field suppression
  Suppressed disruption due to n = 1 field
Feedback phase scan
  Best feedback phase produced long pulse, bN = 6.4, bN/li = 13
NSTX Experiments
Ip (MA)
(A)
S. Sabbagh et al., Nucl. Fusion 53 (2013) 104007
Run time has been allocated for continued experiments on NSTX-U

## Slide 11: Active RWM control: dual Br + Bp sensor feedback gain and phase scans produce significantly reduced n = 1 field
Favorable Bp + Br feedback (FB) settings found (low li plasmas)
Time-evolved theory simulation of Br+Bp feedback follows experiment
Dt (s) (model)
Radial field n = 1 (G)
180 deg FB phase
90 deg FB phase
0 deg FB phase
Vacuum error field
Vacuum error field
+ RFA
Simulation of Br + Bp control (VALEN)
Feedback on
Br Gain = 1.0
140124
140122
139516
No Br feedback
t (s)
bN
li
6
4
2
0
0.8
0.6
0.2
0.0
6
4
2
0
0.0
0.2
0.4
0.6
0.8
1.0
1.2
1.4
Br Gain = 1.50
Brn = 1 (G)
bN
li
0.4
6
4
2
Br gain scan
Br FB phase scan
S. Sabbagh et al., Nucl. Fusion 53 (2013) 104007

## Slide 12: Active RWM control design study for proposed NSTX-U 3D coil upgrade (NCC coils) shows superior capability
NCC 2x12 with favorable sensors, optimal gain
NCC 2x6 odd parity, with favorable sensors
Full NCC coil set allows control close to ideal wall limit
  NCC 2x6 odd parity coils: active control to bN/bNno-wall = 1.58
  NCC 2x12 coils, optimal sensors: active control to bN/bNno-wall = 1.67
NCC (plasma facing side)

## Slide 13
Plasma parameters
  q95 ~4.5
  PNBI = 2.7 - 4 MW (2 or 3 beam sources)
bN/li > 6 (50% increase from the highest values in previous operations)
  A high value for advanced tokamaks
  bN up to 4.3
  li ranging 0.66 - 0.87 with bN > 4
  Discharge bN was not limited by n > 0 events
bN /li = 6
bN /li = 5
n = 1 with-wall
limit
n = 1 no-wall limit***
First H-mode
Previous
Operation*,**
MP2014-05-02-007
by Sabbagh and Y.S. Park
Recent operation
having bN > bNno-wall
KSTAR design target
operating space
Columbia U. experiments yield record bN for KSTAR, significantly surpassed the ideal MHD n = 1 stability limit
Y.S. Park, S.A. Sabbagh, et al., KSTAR Conference 2015
Normalized beta vs. internal inductance from KSTAR EFIT
*Y.S. Park, et al., Nucl. Fusion 53 (2013) 083029
**Y.S. Park, et al., Phys. Plasmas 21 (2014) 012513
** O. Katsuro-Hopkins, et al., Nucl. Fusion 50 (2010) 025019

## Slide 14: Disruption event chain characterization capability started for NSTX-U as next step in disruption avoidance plan
Approach to disruption prevention
  Identify disruption event chains and elements
  Predict events in disruption chains
    Attack events at several places
    Give priority to early events
  Provide cues to avoidance system to break the chain
  Provide cue to mitigation system if avoidance deemed untenable
t
General code written (Python) to address the first step – initial test runs started using NSTX data

## Slide 15
JET disruption event characterization provides framework to follow for understanding / quantifying DPAM progress
P.C. de Vries et al., Nucl. Fusion 51 (2011) 053018
JET disruption event chains
Related disruption event statistics
JET disruption event chain analysis performed by hand, need to automate
NSTX-U DPAM Working Group formed (w/ Columbia U. Group leadership): List of disruption chain events defined, interested individuals identified

## Slide 16
Disruption Characterization Code now yielding initial results: disruption event chains, with related quantitative warnings
PRP warnings
PRP
VDE
SCL
IPR
0.420s
0.440s
0.475s
0.485s
NSTX
142270
Disruption
J.W. Berkery, S.A. Sabbagh, Y.S. Park (Columbia U.)
10 physical disruption chain events and related quantitative warning points are presently defined in code
  Code is easily expandable, portable to other tokamaks
This example: Pressure peaking (PRP) disruption even chain identified by code
  (PRP) Pressure peaking warnings identified first
  (VDE) VDE condition subsequently found 20 ms after last PRP warning
  (SCL) Shape control warning issued
  (IPR) Plasma current request not met

## Slide 17: NSTX-U is a world leading program on disruption avoidance, Columbia U. Group Research providing a leadership role
Physics Elements
  Kinetic RWM stabilization physics
  NTV physics for plasma rotation control (for instability avoidance)
  Active RWM control (physics-based RWM state-space controller)
  RWM control analysis of upgraded 3D coils for NSTX-U
  NSTX-U equilibrium reconstruction – key basis for stability analysis
  Planned real-time MHD spectroscopy for NSTX-U (in 5 Year Plan)
  Related high normalized beta and NTV experiments on KSTAR
Research synergism
  Elements now being brought together as part of a disruption prediction/avoidance system; NSTX-U DPAM working group leadership
  Disruption Characterization/Prediction code initiated
Action to enhance university / student / post-doc participation
  New diagnostic proposal to be submitted (Volpe/Sabbagh)

## Slide 18
Supporting slides follow

## Slide 19
Initially used for NSTX since simple critical scalar wf threshold stability models did not describe RWM stability
Kinetic modification to ideal MHD growth rate
  Trapped / circulating ions, trapped electrons, etc.
  Energetic particle (EP) stabilization
Stability depends on
  Integrated wf profile: resonances in dWK (e.g. ion precession drift)
  Particle collisionality, EP fraction
Trapped ion component of dWK (plasma integral over energy)
collisionality
wf profile (enters through ExB frequency)
Hu and Betti, Phys. Rev. Lett 93 (2004) 105002
Sontag, et al., Nucl. Fusion 47 (2007) 1005
precession drift
bounce
Modification of Ideal Stability by Kinetic theory (MISK code) is used to determine proximity of plasmas to stability boundary
J. Berkery et al., PRL 104, 035003 (2010)
S. Sabbagh, et al., NF 50, 025020 (2010)
J. Berkery et al., PRL 106, 075004 (2011)
J. Berkery et al., PoP 21, 056112 (2014)
J. Berkery et al., PoP 21, 052505 (2014)
(benchmarking paper)
Some NSTX / MISK analysis references

## Slide 20: Bounce resonance stabilization dominates for DIII-D vs. precession drift resonance for NSTX at similar, high rotation
DIII-D experimental rotation profile
NSTX experimental rotation profile
|δWK| for trapped resonant ions vs. scaled experimental rotation (MISK)
133103 @ 3.330 s
stable plasma
133776 @ 0.861 s
stable plasma
precession
resonance
bounce / circulating
resonance
precession
resonance
bounce / circulating
resonance
DIII-D
NSTX

## Slide 21: Increased RWM stability measured in DIII-D plasmas as qmin is reduced is consistent with kinetic RWM theory
|δWK| for trapped resonant ions vs. scaled experimental rotation (MISK)
Measured plasma response to 20 Hz, n = 1 field vs qmin
n = 1 |dBp | (G/kA)
qmin
DIII-D experimental rotation profile
precession drift
resonance
bounce /
circulating
resonance
DIII-D (qmin = 1.2)
DIII-D (qmin = 1.6)
DIII-D (qmin = 2.8)
Bounce resonance dominates precession drift resonance for all qmin examined at the experimental rotation
less stable

## Slide 22: Experiments directly measuring global stability using MHD spectroscopy (RFA) support kinetic RWM stability theory
(trajectories of 20 experimental plasmas)
Stability vs. bN/li
  decreases up to bN/li = 10, increases at higher bN/li
  Consistent with kinetic resonance stabilization
Resonant Field Amplification vs. bN/li
unstable
RWM
S. Sabbagh, et al., NF 53 (2013) 104007
RFA vs. rotation (wE)
Stability vs. rotation
  Largest stabilizing effect from ion precession drift resonance with wf
Most
stable
Minimize |<ωD> + ωE|
Stability at lower n
  Collisional dissipation is reduced
  Stabilizing resonant kinetic effects are enhanced
  Stabilization when near broad ωφ resonances; almost no effect off-resonance
J. Berkery, et al., PoP 21 (2014) 056112
NSTX experiments

## Slide 23: NSTX is a spherical torus equipped to study passive and active global MHD control
RWM active stabilization coils
RWM poloidal
sensors (Bp)
RWM radial sensors (Br)
Stabilizer
plates
High beta, low aspect ratio
  R = 0.86 m, A > 1.27
  Ip < 1.5 MA, Bt = 5.5 kG
  bt < 40%, bN > 7
Copper stabilizer plates for kink mode stabilization
Midplane control coils
  n = 1 – 3 field correction, magnetic braking of wf by NTV
  n = 1 RWM control
Combined sensor sets now used for RWM feedback
  48 upper/lower Bp, Br
3D Structure Model

## Slide 24: Open-loop comparisons between measurements and RWM state space controller show importance of states and model
Improved agreement with sufficient number of states (wall detail)
A) Effect of Number of States Used
dBp180
100
200
0
-100
RWM Sensor Differences (G)
137722
t (s)
40
0
80
0.56
0.58
0.60
137722
t (s)
0.56
0.58
0.60
0.62
dBp180
dBp90
dBp90
-40
0.62
t (s)
0.56
0.58
0.60
0.62
t (s)
0.56
0.58
0.60
0.62
100
200
0
-100
40
0
80
-40
7 States
B) Effect of 3D Model Used
No NBI Port
With NBI Port
2 States
RWM
3D detail of model important to improve agreement
Measurement
Controller (observer)

## Slide 25: When Ti is included in NTV rotation controller model, 3D field current and NBI power can compensate for Ti variations
t (s)
t (s)
3D coil current and NBI power (actuators)
yN
NBI, NTV torque density (N/m2)
Plasma rotation (rad/s)
NTV
torque
104
desired wf
t1
t3
NBI
torque
t1 = 0.59s
t2 = 0.69s
t3 = 0.79s
NTV torque profile model for feedback dependent on ion temperature
Rotation evolution and NBI and NTV torque profiles
K1 = 0, K2 = 2.5
3D Coil Current (kA)
0.5
0.7
0.9
1.0
0.8
1.2
1.4
1.6
1.8
2.0
0.5
0.7
0.9
Ti (keV)
0.6
1.2
1.8
0.0
t (s)
0.5
0.7
0.9
0.8
0.6
0.4
NBI power (MW)
7
1
0
6
5
4
3
2
t2
t1
t3
t2
t1
t2
t3
0
6
8
4
2
10
0.0
0.2
0.4
0.6
0.8
1.0
0.0
0.5
1.0
1.5
2.0
2.5
t1
t3
t2

## Slide 26: NSTX-U: RWM active control capability increases as proposed 3D coils upgrade (NCC coils) are added
Partial 1x12 NCC coil set significantly enhances control
  Present RWM coils: active control to bN/bNno-wall = 1.25
  NCC 1x12 coils: active control to bN/bNno-wall = 1.52
Existing
RWM
coils
NCC upper (1x12) (plasma facing side)
Using present midplane RWM coils
Partial NCC 1x12 (upper), favorable sensors

## Slide 27: Real-time MHD spectroscopy, model-based active control, and kinetic physics will be used for disruption avoidance
safe
too high
too low
Ip (MA)
MHD Spectroscopy
  Use real-time measurement of plasma global mode stability to “steer” toward increased stability
Advanced active control
  Combined Br + Bp feedback reduces n = 1 field amplitude, improves stability
  RWM state space controller sustains low li, high βN plasma
Simplified kinetic physics models
  “steer” profiles (e.g. plasma toroidal rotation) toward increased stability in real-time
NSTX
NSTX
DIII-D

## Slide 28: NSTX-U DPAM Working Group meeting: List of disruption chain events defined, interested individuals identified
Impurity control (NC)
  bolometry-triggered shutdown (SPG); "tailoring” radiation-induced TM onset (LD, DG)
  change plasma operational state / excite ELMs, etc. (TBD – perhaps JC)
Greenwald limit (GWL)
  density/power feedback, etc. (DB)
Locked TM (LTM)
  TM onset and stabilization conditions, locking thresholds (JKP,RLH,ZW)
  TM entrainment (YSP)
Error Field Correction (EFC)
  NSTX-U EF assessment and correction optimization (CM,SPG)
  NSTX-U EF multi-mode correction (SAS, YSP, EK)
Current ramp-up (IPR)
  Active aux. power / CD alteration to change q (MDB, SPG)
Shape control issues (SC)
  Active alteration of squareness, triangularity, elongation – RFA sensor (SPG,MDB)
Transport barrier formation (ITB)
  Active global parameter, Vf, etc. alteration techniques (SAS,JWB,EK)
H-L mode back-transition (HLB)
  Active global parameter, Vf, etc. alteration techniques (SAS,JWB,EK)
Approaching vertical instability (VSC)
  Plasma shape change, etc. (SPG, MDB)
Resistive wall mode (RWM)
  Active global parameter, Vf, etc. alteration techniques (SAS,JWB)
  Active multi-mode control (SAS,YSP,KT)
Ideal wall mode (IWM)
  Active global parameter, Vf, etc. alteration techniques (JEM)
Internal kink/Ballooning mode (IKB)
  Active global parameter, Vf, etc. alteration techniques (SAS,JWB)
  Active multi-mode control (SAS, YSP, KT)
Abbreviations:
JWB: Jack Berkery
AB: Amitava Bhattacharjee
DB: Devon Battaglia
MDB: Dan Boyer
JC: John Canik
LD: Luis Delgado-Aparicio
DG: Dave Gates
SPG: Stefan Gerhardt
MJ: Mike Jaworski
EK: Egemen Kolemen
RLH: Rob La Haye
JEM: Jon Menard
CM: Clayton Myers
JKP: Jong-Kyu Park
YSP: Young-Seok Park
RR: Roger Raman
SAS: Steve Sabbagh
KT: Kevin Tritz
ZW: Zhirui Wang
TBD: (To be decided)
Interest from Theory
  Amitava Bhattacharjee, Allen Boozer, Dylan Brennan, Bill Tang have requested involvement
Interested? contact:
sabbagh@pppl.gov
raman@pppl.gov

## Slide 29
Disruption Characterization Code now yielding initial results: disruption event chains, with related quantitative warnings (2)
J.W. Berkery, S.A. Sabbagh, Y.S. Park
This example: Greenwald limit warning during Ip rampdown
  (GWL) Greenwald limit warning issued
  (VDE) VDE condition then found 7 ms after GWL warning
  (IPR) Plasma current request not met
GWL warnings
NSTX
138854
GWL
VDE
IPR
0.746s
0.753s
0.753s
Disruption during
Ip ramp-down