## Slide 1
NSTX
Supported by
College W&M
Colorado Sch Mines
Columbia U
CompX
General Atomics
INEL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Nova Photonics
New York U
Old Dominion U
ORNL
PPPL
PSI
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Washington
U Wisconsin
Culham Sci Ctr
U St. Andrews
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Hebrew U
Ioffe Inst
RRC Kurchatov Inst
TRINITI
KBSI
KAIST
POSTECH
ASIPP
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
U Quebec
Thermography analysis of transient events in NSTX
K.Gan(ASIPP)
R.Maingi, J-W.Ahn, T.K.Gray(ORNL), A.G.McLean(LLNL)

## Slide 2
Outline
2
Calculate the 2D heat flux distribution with TACO code
  How to choose the α parameter
  Comparison of the Taco and Theodor results
The characteristics of ELM divertor heat flux
  Type III ELM
  Type V ELM
  Type I ELM
  Different situation ELM heat flux
Survery the power load with 2D heat flux distribution
  Toroidal asymmetry on divertor heat flux
  Strange edge transport during L-H transition
  Different 2D heat flux between type V and type III ELM

## Slide 3
Outline
3
Calculate the 2D heat flux distribution with TACO code
  How to choose the α parameter
  Comparison of the Taco and Theodor results
The characteristics of ELM divertor heat flux
  Type III ELM
  Type V ELM
  Type I ELM
  Different situation ELM heat flux
Survery the power load with 2D heat flux distribution
  Toroidal asymmetry on divertor heat flux
  Strange edge transport during L-H transition
  Different 2D heat flux between type V and type III ELM

## Slide 4
Physical LLD model for numerical temperature calculation
Physical LLD model for numerical temperature calculation
Taco code
4
Taco is a inversion algorithm on a 3D Fourier method which solve the heat transfer equation and get 2D heat flux data.
previous Taco did not consider the heat transmission coefficient, α parameter (Herrmann)
Negative heat flux was often calculated after transient event
Negative heat flux can be removed with α parameter
α parameter has large impact on the calculation of peak heat fluxes
Without α

## Slide 5
Choose the α value
5
MAST
NSTX
IN MAST, the optimum value of α for the LWIR case sits at the knee of the curve while in the MWIR case, it sits in the steepest part of the curve
IN NSTX, Choose the α value to keep the energy deposition constant after discharge
G De Temmerman, PPCF, 52 (2010) 095005 (14pp)

## Slide 6
Comparison of TACO and THEODOR results
6
Good consistent q on a single radial line between TACO and THEODOR
The heat flux distribution almost the same between TACO and THERDOR on a single radial line

## Slide 7
Outline
7
Calculate the 2D heat flux distribution with TACO code
  How to choose the α parameter
  Comparison of the Taco and Theodor results
The characteristics of ELM divertor heat flux
  Type III ELM
  Type V ELM
  Type I ELM
  Different situation ELM heat flux
Survery the power load with 2D heat flux distribution
  Toroidal asymmetry on divertor heat flux
  Strange edge transport during L-H transition
  Different 2D heat flux between type V and type III ELM

## Slide 8
Divertor heat flux during type III ELM
8
Intermittent (2KHZ) type V ELM existed between type III ELM
ELM filament happened during ELM, λq will be smaller after ELM filament
λq increase (decrease) with ELM for shot 132460 (132401).
132401
132460

## Slide 9
Divertor heat flux during type V ELM with high δ
9
Type V ELM will Increase the transport and reduce the peak heat flux with large λq
A strange heat flux region existed between 0.25-0.30s
Fx_osp~18

## Slide 10
10
During 0.201-0.208s, the qpeak increased and λq decreased and power deposition seems constant
the qpeak is 0.62MW/m2 at 0.24s, 1.93MW/m2 at 0.21s. It almost decreased 70% qpeak
During type V ELM, the qpeak decreased and increased with almost constant power deposition
Type v ELMs(0.24s) reduced the 40% qpeak compare to ELM free phase
132406
Divertor heat flux during type V ELM with low δ

## Slide 11
Divertor heat flux during type I ELM
11
Shot # | Time (s) | λq (m) | fx_osp | λqn (m)
132403 | 264.928ms, type v ELM | 0.175m | 5.3 | 0.033
132406 | 204.809ms,ELM-free phase | 0.056m | 5.4 | 0.01
132438 | 266.337ms, inter-type I ELM | 0.06m | 1.85 | 0.032
λq decrease ~40% during type I ELM filament
6KHZ energy transport between type I
ELM (GPI)
λqn is similar between type v ELM
(# 132403) and inter type I ELM.

## Slide 12
Heat flux research in JET and ASDEX
12
was defined as ELM rise time
In the first phase,( )the target temperature and the power increase up to a peak value
In the second phase,( )the target temperature decays back to the Inter-ELM value
T. Eich, JNM, 337–339 (2005) 669–676

## Slide 13
Different situation ELM heat flux
13
Maximum power load in ELM filament, Maximum qpeak after ELM filament
(situation II ELM)
Triggered ELM
Maximum power load and qpeak appeared at
ELM filament
Maximum power and qpeak
Appeared after ELM filament
(situation I ELM)
(situation III ELM)

## Slide 14
The relationship between situation I,II ELM and βp
14
square represent the situation I ELM heat flux, triangle represent the situation II ELM heat flux
The maximum qpeak will appeared at ELM filament with a low β
With βp increase, the number of situation I ELM begun to decrease, and the situation II ELM appeared.
The real physical mechanism is still unknown

## Slide 15
Outline
15
Calculate the 2D heat flux distribution with TACO code
  How to choose the α parameter
  Comparison of the Taco and Theodor results
The characteristics of ELM divertor heat flux
  Type III ELM
  Type V ELM
  Type I ELM
  Different situation ELM heat flux
Survery the power load with 2D heat flux distribution
  Toroidal asymmetry on divertor heat flux
  Strange edge transport during L-H transition
  Different 2D heat flux between type V and type III ELM

## Slide 16
2D divertor heat flux distribution on NSTX
16

## Slide 17
Toroidal asymmtry on divertor heat flux
17
According to the toroidal asymmetry
The reason of toroidal asymmetry is still unclear, toroidal ripple, 3D structure of filaments, misalign divertor tile or inconsistent surface property (α value)

## Slide 18
Numerical Modeling of ELM Filaments on Divertor Plates
18
Add 300A on Flux tube 1
A. Wingen, PRL, 104, 175001 (2010)
The initial heat pulse during an ELM generate thermoelectric current between two divertor plate
typical ELM stripe structures can be correctly modeled

## Slide 19
ELM power load in MAST
α was set to 100k, the Ts is closer to the LLD
temperature measured by dual-band IR camera
19
Filament at different radial position and different toroidal angle generate the striated divertor heat flux
A Kirk, PPCF, 49 (2007) 1259–1275

## Slide 20
Striated heat flux in NSTX
α was set to 100k, the Ts is closer to the LLD
temperature measured by dual-band IR camera
20
The striated heat flux (R>0.61m) was generated by filaments
It’s unclear the reason which cause the striated divertor heat flux
(R<0.57m)
Question: Did the filaments and magnetic topology generate the striated divertor heat fluxes together?

## Slide 21
Outline
21
Calculate the 2D heat flux distribution with TACO code
  How to choose the α parameter
  Comparison the Taco and Theodor results
The characteristics of ELM divertor heat flux
  Type III ELM
  Type V ELM
  Type I ELM
  Different situation ELM heat flux
Survery the power load with 2D heat flux distribution
  Toroidal asymmetry on divertor heat flux
  Strange edge transport during L-H transition
  Different 2D heat flux between type V and type III ELM

## Slide 22
Strange edge transport during L-H transition
α was set to 100k, the Ts is closer to the LLD
temperature measured by dual-band IR camera
22
Increasing Pload before L-H transition was caused by decreased Drsep
During L-H transition , the qpeak first decrease then increase
A delayed time existed between qpeak and Awet during L-H transition

## Slide 23
2D heat flux distribution during L-H transition
α was set to 100k, the Ts is closer to the LLD
temperature measured by dual-band IR camera
23
During L-H transition, the heat flux around the out strike point first become very small, then increase to ELM-free phase

## Slide 24
Filaments during L-H transition
α was set to 100k, the Ts is closer to the LLD
temperature measured by dual-band IR camera
24
Filaments generated the striated heat flux(R>0/61m)
Separate the power deposition with two parts:
(filaments)

## Slide 25
The power load during L-H transition
α was set to 100k, the Ts is closer to the LLD
temperature measured by dual-band IR camera
25
Pin decrease fast to a low value then increase
Pout decrease slower than Pin
Pout can be several times bigger than Pin
During L-H transition

## Slide 26
Heat flux evolution during L-H transition
α was set to 100k, the Ts is closer to the LLD
temperature measured by dual-band IR camera
26
132406 (6.3khz)
The intermittent filaments still happen during L-H transition
~3KHZ heat flux oscillation appeared before L-H transition
During L-H transition, the heat flux near the OSP first decrease then increase

## Slide 27
2D heat flux distribution during ELM
α was set to 100k, the Ts is closer to the LLD
temperature measured by dual-band IR camera
27
The Power deposition seems just increase ~13% during Type V ELM peak than between ELMs
The plasma wetting area decrease with type v ELM
There is a delay time between Pin and Pout during type V ELM

## Slide 28
2D heat flux distribution during type V ELM
α was set to 100k, the Ts is closer to the LLD
temperature measured by dual-band IR camera
28
During ELM-free , the heat flux region is close to the OSP
During type V ELM, the heat flux region is far from the OSP
The heat flux inside the CHI gap increase first

## Slide 29
2D heat flux during type III ELM
α was set to 100k, the Ts is closer to the LLD
temperature measured by dual-band IR camera
29
The position of qpeak can be 34cm far from the OSP at pre-ELM
The Pin and Pout increase together during type III ELM

## Slide 30
Summary
TACO has been applied successful on heat flux calculation in NSTX
A criteria to choose the α value: Modify α until the energy deposition is kept constant after discharge
The width of power deposition on divertor (λq) will decrease with type III ELM due to the obvious type v ELM during inter-type III ELM.
Type v ELM will increase the transport and decrease the peak heat flux
Compare to ELM phase phase
Situation II ELM will appeared under high βp
It was first time to analyze the power load with 2D heat flux distribution in NSTX
  Divertor heat flux is toroidal asymmetry
  Strange edge transport has been reported during L-H transition
  There is a delay time between Pin and Pout during type V ELM, Pin and Pout increase together during type III ELM
30