## Slide 1: XP on L-H Power Threshold Scan
S. M. Kaye, M. Churchill et al.

## Slide 2: Motivation
Conventional aspect ratio indicates PLH~neBTS (not exactly but pretty close)
NSTX exhibited a strong dependence of PLH on plasma current
  Correlated with depth of Er well as determined by XGC
No dedicated BT scans performed in NSTX
PLH did show an anecdotal density dependence both in NBI and RF
Will help establish transition conditions for Smith/Churchill XP

## Slide 3: Plan
Perform current and field scans to determine PLH
  Ip = 600, 800, 1000 kA
  BT = 0.4, 0.52, 0.65 T
Use 1B as primary source, with 2C and 2A as needed
  Vary voltage using “binary search” (as in NSTX) to determine threshold
Most likely an XP that could be performed very soon, with present machine conditions
  Low field startup has been achieved, but discharge needs to be lengthened
  Some issues with higher current L-mode shots on last run day (4/8)
Require MHD-free periods at time of transition
  Don’t care about after!
Require transitions after current flattops

## Slide 4: Baseline discharges
204202: 700 kA L-mode shot used for BEAST/NUBEAM validation (4/8)
  Used three sources, L-H transition at 0.67 s
  Move beam on times earlier towards start of flattop

## Slide 5: Baseline discharges
Vary current and field
1 day XP (20-24 shots): 3.08e15 neutrons
Condition | Ip (MA) | BT (T)
1 | 1.0 | 0.65
2 | 0.8 | 0.65
3 | 0.6 | 0.65
4 | 0.6 | 0.52
5 | 0.6 | 0.40

## Slide 6: Misc
Diagnostics – interested in global behavior
  Required: Da, IR cameras, magnetics and Mirnovs, neutrons, TV, MPTS, estimate of Zeff
  Desired: CHERS, BES, FIDA, high-f Mirnovs
Analysis:
  Equilibrium reconstruction, TRANSP, XGC
Publication
  IAEA, NF letter or equivalent (PPCF?)