## Slide 1
Overview of Results and Analysis from the National Spherical Torus Experiment
S. A. Sabbagh
Columbia University
for the NSTX-U Research Team
NSTX-U
Supported by
Culham Sci Ctr
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Inst for Nucl Res, Kiev
Ioffe Inst
TRINITI
Chonbuk Natl U
NFRI
KAIST
POSTECH
Seoul Natl U
ASIPP
CIEMAT
FOM Inst DIFFER
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
Coll of Wm & Mary
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Lehigh U
Nova Photonics
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Tennessee
U Tulsa
U Washington
U Wisconsin
X Science LLC
54th Meeting of the APS Division of Plasma Physics
October 30th, 2012
Providence, Rhode Island
V1.4s

## Slide 2: NSTX research targets predictive physics understanding needed for fusion energy development facilities
ST Pilot Plant
Outline
New center-stack
NSTX-U
2nd neutral beam
Develop key physics understanding to be tested in unexplored, hotter ST plasmas
  Study high beta plasma transport and stability at reduced collisionality, for extended pulse
  Prototype methods to mitigate very high heat/particle flux
  Move toward fully non-inductive operation
BT
Ip
PNBI
pulse
1 T
2 MA
12 MW
5 s
ITER
Enable devices: ST-FNSF, ST-Pilot/DEMO, ITER
  Leveraging unique ST plasmas provides new understanding for tokamaks, challenges theory
0.5
1
6
1
Fusion Nuclear Science Facility (FNSF)

## Slide 3: BES measured low-k turbulence in ELM-free H-mode pedestal steep gradient region is most consistent with TEMs
Beam emission spectroscopy (BES) array
R
Z
Poloidal Correlation Length vs. Parameters
Smith YI3.04 (Invited – Friday)
Multivariate linear scaling coefficients ak
  Fitting results are robust
  Scalings are most consistent with Trapped Electron Modes
Measurements during MHD quiet periods, in steep gradient region
  kq ≈ 0.2-0.4 cm-1 and kqri ≈ 0.2
Large poloidal correlation lengths
  Lc ≈ 10 ri

## Slide 4: Pedestal width scaling differs from other devices; turbulence correlation measurements consistent with theory
3 cm | 2 – 4 cm (reflecto-metery)
11 cm | 10 – 14 cm (BES)
4
4
Pedestal width scaling bqa applies to multiple machines
In NSTX, observed ped. width is larger
  Data indicates stronger scaling: bq vs. bq0.5
  Initial ballooning critical pedestal analysis indicates scaling ~ bq0.8 for NSTX
Measured correlation lengths at pedestal top are consistent with theory
  spatial structure exhibits ion-scale microturbulence (k⊥ri ~ 0.2 - 0.7)
  Compatible with ITG modes and/or KBM
Pedestal width scaling
Turbulence correlation lengths
Theory
(non-linear XGC1 code)
R = 1.38m
Experiment
80% - 99% ELM cycle
radial
poloidal
139047
  (During inter-ELM period, at pedestal top)
C-Mod
DIII-D
0.1
0.9
0.04
0.08
0.12
0.16
0.00
Pedestal width (yN)
0.3
0.5
0.7
~ 0.08 (bqped)
0.5
0.4 (bqped)
1.05
NSTX
Diallo PP8.010 (We)
P. Snyder, IAEA 2012
Notes: 4
4

## Slide 5: Investigations underway to understand positive aspects of lithium wall coating; plasmas reach kink/peeling limit
Energy confinement improves, ELMs stabilize - with no core Li accumulation
  Partially due to high neoclassical particle diffusivity
Chang PO7.07 (We)
New bootstrap current calculation (XGC0 code) agrees with profile reaching kink/peeling limit before ELM
Norm. surface avg. current
0.5
0.6
0.7
0.8
0.9
1.0
1.0
0.8
0.6
0.4
0.2
0.0
yN
XGC0 model
Sauter model
Maingi PP8.007 (We)
Bootstrap current profile
Carbon
Lithium
NEO (solid)
NCLASS (dash)
Surface analysis experiments show oxide coverage of Li plasma facing components (PFCs) expected in 20 – 200s
  Short reaction times motivate flowing Li PFCs
  Oxygen plays important role in D retention
Jaworski PP8.032 (We)
Capece GO6.08 (Tu)
Scotti GI2.05 (Invited – Tu 11:30 AM)
r/a
Particle diffusivity (m2/s)
130725

## Slide 6: Experiments measuring global stability further support kinetic RWM stability theory, provide guidance for NSTX-U
Two competing effects at lower n
  Collisional dissipation reduced
  Stabilizing resonant kinetic effects enhanced (contrasts early theory)
Expectations at lower n
  More stabilization near ωφ resonances; almost no effect off-resonance
Berkery GO6.09 (Tu)
RFA =
Bapplied
Bplasma
Resonant Field Amplification (RFA) vs n
on resonance
off resonance
(trajectories of 20 experimental plasmas)
Mode stability directly measured in experiments using MHD spectroscopy
  Stability decreases up to bN/li = 10, increases at higher bN/li
  Consistent with kinetic resonance stabilization
Resonant Field Amplification (RFA) vs. bN/li
unstable
mode
Bialek PP8.013 (We)

## Slide 7: Disruptivity studies and warning analysis of NSTX database are being conducted for disruption avoidance in NSTX-U
Disruption warning algorithm shows high probability of success
  Based on combinations of single threshold based tests
Results
  ~ 98% disruptions flagged with at least 10ms warning, ~ 4% false positives
  False positive count dominated by near-disruptive events
Disruptivity
Physics results
  Low disruptivity at relatively high bN ~ 6; bN / bNno-wall(n=1) ~ 1.3-1.5
    Consistent with specific disruption control experiments, RFA analysis
  Strong disruptivity increase for q* < 2.5, and at very low rotation
Warning Algorithms
S.P. Gerhardt
All discharges since 2006
bN
li
q*

## Slide 8: Fast ion redistribution associated with low frequency MHD measured by fast ion Da (FIDA) diagnostic
Caused by n = 1 global kink instabilities
Redistribution can affect stability of *AE, RWMs, other MHD
Full-orbit code (SPIRAL) shows redistribution in real and velocity space
  Radial redistribution from core plasma
  Particles shift towards V||/V = 1
Core localized CAE/GAEs measured in H-mode plasmas
CAE/GAE-simulated core electron thermal transport matches experiment
Simulations of NBI-driven CAEs show coupling to KAWs
0.9
1.0
1.1
1.2
1.3
1.4
1.5
R(m)
Fast ion density reduction during kink
Change in distribution due to kink mode
Z [m]
R [m]
Energy [keV]
V||\V
CAE resonances
SPIRAL code
Crocker GO6.03 (Tu)
Bortolon JI2.02 (Invited – Tuesday PM)
Tritz GO6.04 (Tu)
Belova PP8.022 (We)

## Slide 9: Significant HHFW power deposited in the SOL in front of the antenna flows to divertor region
Visible camera image of edge RF power flow to divertor
RF power loss profile (divertor, and mapped to midplane)
HHFW
Antenna
Divertor
Perkins GO6.012 (Tu)
R. Perkins, et al., PRL 109 (2012) 045001
RF power couples to field lines across entire scrape-off layer (SOL) width, not just to field lines connected to antenna components
  Midplane mapping shows strong losses close to antenna and separatrix
Shows importance of quantitatively understanding RF power coupling to the SOL for prediction to future devices
Power flux (MW/m2)
Data mapped to midplane
R (m)
Divertor
0.4
0.6
0.8
1.0
1.2
3
2
1
0
4
LCFS
Antenna

## Slide 10: Radiative snowflake divertor greatly reduces heat flux during ELMs; toroidal asymmetry of 2D heat flux studied
Divertor heat flux significantly reduced both during and between ELMs
  during ELMs: 19 to ~ 1.5 MW/m2
  steady-state: 5-7 to ~ 1 MW/m2
Achieved by a synergistic combination of detachment + radiative snowflake
Snowflake divertor in NSTX
Soukhanovskii PP8.027 (We)
Divertor heat flux (MW/m2)
CHI gap
R (m)
Heat flux at peak ELM time
eDA(qpeak)
,2D
Toroidal asymmetry of 2D heat flux
Ahn GO6.06 (Tu)
2D fast IR camera measurement (6.3kHz)
Toroidal asymmetry becomes largest at the peak heat flux for usual Type-I ELMs
Toroidal asymmetry
Meier PP8.028 (We)

## Slide 11: 100% non-inductive scenarios projected over wide range of NSTX-U operation; coaxial helicity injection (CHI) scales well
Raman GO6.011 (Tu)
In NSTX, Ip ramp to 1 MA requires 35% less inductive flux when CHI is used
  Plasmas with favorable high k, low li, ne
TSC modeling predicts a doubling of closed flux current > 400kA in NSTX-U
  Suitable for hand-off to NBI heating/current drive
TSC simulation of CHI startup
0
1.0 ms
1.6 ms
2.7 ms
1
2
0
1
2
0
1
2
R (m)
R (m)
R (m)
0
-2
1
2
-1
Z (m)
NSTX-U projected scenarios
Ono PP8.06 (We)
S. Gerhardt, et al., Nucl. Fusion 52 (2012) 083020
In NSTX
  Sustained non-inductive fraction of 65% with NBI at IP = 0.7 MA
  70 - 100% non-inductive reached using HHFW current drive (IP = 0.3 MA)

## Slide 12: Rapid Progress is Being Made on NSTX Upgrade
2nd neutral beam moved into place
TF OD = 40cm
TF OD = 20cm
TF quadrant assembled
NEW Center Stack
(first plasma anticipated Summer 2014)
Ono PP8.06 (We)
Old center stack

## Slide 13: NSTX Presentations at the 54th APS DPP Meeting
Poster Session
Contributed Talks
Tuesday |  | 
Modifications of impurity transport and divertor sources with lithium wall conditioning in NSTX | Scotti | GI2.005
Interplay between coexisting MHD instabilities mediated by energetic ions in NSTX H-mode plasmas | Bortolon | JI2.002
Thursday |  | 
Physics of tokamak plasma start-up | Mueller | UT3.001
Friday |  | 
Assessing low wavenumber pedestal turbulence in NSTX with measurements and simulations | Smith | YI3.004
Session PP8: Wednesday Afternoon (Room: Hall BC)
(11:30 AM – 12:00 PM)
(2:30 PM – 3:00 PM)
(2:00 PM – 3:00 PM)
Tuesday |  | 
NSTX Overview | Sabbagh | GO6.001
Ohmic H-mode intrinsic rotation | J-K. Park | GO6.002
CAE/GAE structure and ID | Crocker | GO6.003
CAE/GAE-induced transport | Tritz | GO6.004
Divertor heat asymmetry | Ahn | GO6.006
Impurity effects on lithium wall | Capece | GO6.008
RWM control / physics | Berkery | GO6.009
Co-axial helicity injection | Raman | GO6.011
RF power flow in SOL | Perkins | GO6.012
2D ELM precursor studies | Sechrest | GO6.013
Wednesday |  | 
Bootstrap current model | Chang | PO7.007
Invited / Tutorial Talks
(11:00 AM – 11:30 AM)