## Slide 1
Active resistive wall mode and plasma rotation control for disruption avoidance in NSTX-U
S. A. Sabbagh1, J.W. Berkery1, R.E. Bell2,
J.M. Bialek1, D.A. Gates2, S.P. Gerhardt2,
I.R. Goumiri3, Y.S. Park1, C.W. Rowley3,Y. Sun4
1Department of Applied Physics, Columbia University, New York, NY
2Princeton Plasma Physics Laboratory, Princeton, NJ
3Princeton University, Princeton, NJ
4ASIPP, Hefei Anhui, China
NSTX-U
Supported by
Culham Sci Ctr
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Inst for Nucl Res, Kiev
Ioffe Inst
TRINITI
Chonbuk Natl U
NFRI
KAIST
POSTECH
Seoul Natl U
ASIPP
CIEMAT
FOM Inst DIFFER
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
Coll of Wm & Mary
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Lehigh U
Nova Photonics
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Tennessee
U Tulsa
U Washington
U Wisconsin
X Science LLC
55th Meeting of the APS Division of Plasma Physics
November 12th, 2013
Denver, Colorado
V2.3

## Slide 2: Near-complete disruption avoidance in long-pulse tokamak devices is a new “grand challenge” for stability research
Outline (approaches discussed here)
  MHD spectroscopy at high beta
  Kinetic RWM stabilization physics criteria
  Plasma rotation feedback control using NTV
  Model-based active RWM control and 3D coil upgrade
Disruption avoidance is an urgent need for the spherical torus (ST), ITER, and tokamaks in general
  Preparing several physics-based control approaches for disruption prediction / avoidance (P&A) in NSTX-U
Disruption categorization (NSTX database)
% Having strong low frequency n = 1 magnetic precursors
55%
% Associated with large core rotation evolution
46%
S. Gerhardt et al., NF 53 (2013) 063021

## Slide 3: MHD spectroscopy, to be used for disruption P&A, reveals non-intuitive stability dependencies at high bN
MHD spectroscopy experiments
  measured resonant field amplification (RFA) of applied n = 1 tracer field in high bN plasmas at varied wf
  Higher RFA shows reduced mode stability
Counter-intuitive results:
  Highest bN, lowest wf (green): most stable
  Lowest bN, medium wf (blue): unstable
Physics understanding given by kinetic RWM theory (simplified here):
1
2
Precession Drift
~ Plasma Rotation
Collisionality
RFA = Bplasma/Bapplied

## Slide 4: Experiments directly measuring global stability using MHD spectroscopy (RFA) support kinetic RWM stability theory
(trajectories of 20 experimental plasmas)
Stability vs. bN/li
  decreases up to bN/li = 10, increases at higher bN/li
  Consistent with kinetic resonance stabilization
Resonant Field Amplification vs. bN/li
unstable
RWM
Berkery TI2.002 (Th)
S. Sabbagh et al., NF 53 (2013) 104007
RFA vs. rotation (wE)
Stability vs. rotation
  Largest stabilizing effect from ion precession drift resonance with wf
Most
stable
Minimize |<ωD> + ωE|
Stability at lower n
  Collisional dissipation is reduced
  Stabilizing resonant kinetic effects are enhanced
  Stabilization when near broad ωφ resonances; almost no effect off-resonance

## Slide 5: Model-based, state-space rotation controller designed to use Neoclassical Toroidal Viscosity (NTV) profile as an actuator
Momentum force balance – wf decomposed into Bessel function states
NTV torque:
133743
Goumiri NP8.040 (We)
radius
t(s)
Plasma rotation
t(s)
State-space model
TRANSP run
(non-linear)
Feedback using NTV: “n=3” dB(r) spectrum
Desired
Plant
w/ Observer
NTV
region

## Slide 6: Expanded NTV torque profile model for control being developed from theory/comparison to experimental data
NSTX 3D coils used for rotation control
NTV torque profile (n = 3 configuration)
130723
(t=0.583s)
New analysis: NTVTOK code
  Shaing’s connected NTV model, covers all n, and superbanana plateau regimes
  Past quantitative agreement with theory found in NSTX for plateau, “1/n ” regimes
  Full 3D coil specification, ion and electron components considered, no A assumptions
NTV torque profile (n = 2 configuration)
(Shaing, Sabbagh, Chu, NF 50 (2010) 025022)
(Sun, Liang, Shaing, et al., NF 51 (2011) 053015)
(Zhu, Sabbagh, Bell, et al., PRL 96 (2006) 225002)
x(m)
y(m)
z(m)
Experimental
-dL/dt
(scaled)
NTVTOK
NTVTOK
-NTV torque density
-NTV torque density
133726
(t=0.555s)
Experimental
-dL/dt
(scaled)

## Slide 7: Model-based RWM state space controller including 3D plasma response and wall currents used at high bN in NSTX
Potential to allow more flexible control coil positioning
  May allow control coils to be moved further from plasma, and be shielded (e.g. for ITER)
Katsuro-Hopkins, et al., NF 47 (2007) 1157
RWM state space controller in NSTX at high bN
137722
t (s)
40
0
80
0.56
0.58
0.60
137722
t (s)
0.56
0.58
0.60
0.62
dBp90
dBp90
-40
0.62
40
0
80
Effect of 3D Model Used
No NBI Port
With NBI Port
3D detail of model is important to improve sensor agreement
S.A. Sabbagh, et al., Nucl. Fusion 53 (2013) 104007
Controller
(observer)
Measurement

## Slide 8: RWM active control capability will increase significantly when Non-axisymmetric Control Coils (NCC) are added to NSTX-U
Performance enhancement
  Present RWM coils: active control to bN/bNno-wall = 1.25
  Add NCC 2x12 coils, optimal sensors: active control to bN/bNno-wall = 1.67
  Partial NCC options also viable
Existing
RWM
coils
Full NCC
2x12 coils
Using present midplane RWM coils
J.-K. Park NP8.003 (We)
NCC 2x12 with favorable sensors, optimal gain
VALEN (J. Bialek)

## Slide 9: NSTX-U is addressing disruption prediction and avoidance of global modes with a multi-faceted physics and control plan
MHD spectroscopy at high beta
  Resonant field amplification shows an increase in stability at very high bN/li > 10 in NSTX
  Stability dependence on collisionality supports kinetic stabilization theory: lower n can improve stability (contrasts early theory)
Kinetic RWM stability physics models
  Broad precession drift resonance condition to minimize |ωE + ωD| yields increased stability
Plasma rotation control
  First closed-loop feedback of model-based state-space controller successful using NTV as sole actuator
  Expanded NTV profile quantitative modeling underway
Active RWM control
  Demonstrated model-based RWM state space control at high bN > 6
  Planned expansion of 3D coil set on NSTX-U computed to significantly enhance control performance

## Slide 10: Supporting Slides Follow

## Slide 11: Highly successful disruption P&A needs to exploit several phases to avoid mode-induced disruption
Pre-instability
  RFA to measure stable g
  Profile control to reduce RFA
  Real-time stability modeling for disruption prediction
Instability growth
  Profile control to reduce RFA
  Active instability control
Large amplitude instability
  Active instability control
Instability saturation
  Profile control to damp mode
DBpn=1(G)
IA(kA)
DBn=odd(G)
fBpn=1(deg)
RFA
RFA reduced
Mode rotation
Co-NBI direction
RWM
NSTX 128496
t (s)
0.606
0.610
0.614
0.618
0.5
0
-1.0
0
10
20
300
200
100
0
10
0
-10
-0.5
-1.5
S.A. Sabbagh, et al., Nucl. Fusion 50 (2010) 025020
A
B
C
D
A
B
C
D
Active RWM control in NSTX

## Slide 12: Research shown here is part of a sophisticated disruption prediction-avoidance-mitigation framework for NSTX-U
Plasma Operations
Avoidance Actuators
PF coils
2nd NBI: (q, p, vf control)
3D fields (upgraded + NCC):
(EF, RWM control,
wf control via NTV)
Divertor gas injection
Mitigation
Early shutdown
Massive gas injection
Pellet injection
Control Algorithms: Steer Towards Stable Operation
Isoflux and vertical position control
LM, NTM avoidance
wf state-space controller (by NTV, NBI)
RWM, EF state-space controller
Divertor radiation control
Disruption Warning
System
Predictors (measurements, models)
Shape/position
Eq. properties (b, li, Vloop,…)
Profiles (p(r), j(r), wf(r),…..)
Plasma response (n=0-3, RFA, …)
Divertor heat flux
Loss of Control
General framework & algorithms applicable to ITER

## Slide 13: Research shown here is part of a sophisticated disruption prediction-avoidance-mitigation framework for NSTX-U
Plasma Operations
Avoidance Actuators
PF coils
2nd NBI: (q, p, vf control)
3D fields (upgraded + NCC):
(EF, RWM control,
vf control via NTV)
Divertor gas injection
Mitigation
Early shutdown
Massive gas injection
Pellet injection
Control Algorithms: Steer Towards Stable Operation
Isoflux and vertical position control
LM, NTM avoidance
Vf state-space controller (by NTV, NBI)
RWM, EF state-space controller
Divertor radiation control
Disruption Warning
System
Predictors (measurements, models)
Shape/position
Eq. properties (b, li, Vloop,…)
Profiles (p(r), j(r), vf(r),…..)
Plasma response (n=0-3, RFA, …)
Divertor heat flux
Loss of Control
General framework & algorithms applicable to ITER

## Slide 14: Dedicated MHD spectroscopy reveal stability dependencies that are non-intuitive based on early RWM stabilization theory
MHD spectroscopy experiments
  measured resonant field amplification (RFA) of high bN plasmas at varied plasma rotation
Counter-intuitive results:
  Highest bN, lowest wf (green): most stable
  Lowest bN, highest wf (red): less stable
  Higher bN, highest wf (cyan): less stable
  Lowest bN, medium Vf (blue): unstable
γ contours
Control Algorithms
Disruption Warning System
Predictors
Mitigation
Plasma Operations
Avoidance actuators (2nd NBI, 3D fields, for q, vφ , βN control)
1
2
3
4

## Slide 15: Simple models derived from kinetic RWM physics being developed for real-time disruption prediction / avoidance
Criteria to increase stability based on kinetic RWM physics
  Real-time measurement of wf (and bN) alone is insufficient!
  Precession drift stabilization criterion (minimize |ωE + ωD|) provides better guidance for global mode stability
    Corresponds to <ωE> ~ 4 - 5 kHz
  Avoid disruption by controlling plasma rotation profile toward this condition
    obtain <ωE> from real-time wf and modeled n and T profiles
high
low
safe
Berkery TI2.002 (Th)
Core rotation time evolution
<wE> time evolution

## Slide 16: 2. Simple models derived from kinetic RWM physics being developed for real-time for disruption prediction / avoidance
Criterion to increase stability based on kinetic RWM physics
  Real-time measurement of wf (and bN) alone is insufficient!
  Simplified precession drift stabilization criterion (minimize |ωE + ωD|) provides better guidance for global mode stability
    Corresponds to <ωE> ~ 5kHz in the range (0.5 < yN < 0.9)
  Avoid disruption by controlling plasma rotation profile toward this condition
    obtain <ωE> from real-time wf and modeled n and T profiles
too high
too low
Avoidance Actuators (q, vφ , βN control)
γ contours
Control Algorithms
Disruption Warning System
Predictors
Mitigation
Plasma Operations
safe
Berkery TI2.002 (Th)

## Slide 17: Experiments directly measuring global stability (RFA) using MHD spectroscopy support kinetic RWM stability theory
Stability at lower n
  Collisional dissipation reduced
  Stabilizing resonant kinetic effects enhanced
  Stabilization near ωφ resonances; almost no effect off-resonance
RFA vs collisionality
(trajectories of 20 experimental plasmas)
Stability vs. bN/li
  decreases up to bN/li = 10, increases at higher bN/li
  Consistent with kinetic resonance stabilization
Resonant Field Amplification vs. bN/li
unstable
mode
Berkery TI2.002 (Th)
S. Sabbagh et al., NF 53 (2013) 104007
on resonance
off resonance
RFA vs collisionality (theory)
MISK calculations
on resonance
off resonance
unstable

## Slide 18: Experiments measuring global stability vs. n further support kinetic RWM stability theory, provide guidance for NSTX-U
RWM growth rate (γτw)
unstable
Marginal
stability
J. Berkery et al., PRL 106 (2011) 075004
Two competing effects at lower n
  Collisional dissipation reduced
  Stabilizing resonant kinetic effects enhanced (contrasts early theory)
Expectations at lower n
  More stabilization near ωφ resonances; almost no effect off-resonance
Collisionality
Plasma Rotation
Theory: RWM growth rate vs. n and wf
MISK code
RFA =
Bapplied
Bplasma
Exp: Resonant Field Amplification (RFA) vs n
Mode stability directly measured in experiment using MHD spectroscopy
  Decreases with n at lower RFA (“on resonance”)
  Independent of n at higher RFA (“off resonance”)
on resonance
off resonance
(trajectories of 20 experimental plasmas)
off-resonance
on resonance
Berkery #I#.## (Th)
S. Sabbagh et al., NF 53 (2013) 104007

## Slide 19: 1. MHD spectroscopy, to be used for disruption P&A, reveals non-intuitive stability dependencies
MHD spectroscopy experiments
  measured resonant field amplification (RFA) of high bN plasmas at varied wf
  Higher RFA shows reduced mode stability
Counter-intuitive results:
  Highest bN, lowest wf (green): most stable
  Lowest bN, highest wf (red): less stable
  Higher bN, highest wf (cyan): less stable
  Lowest bN, medium wf (blue): unstable
Physics understanding given by kinetic RWM theory (simplified here):
1
2
3
4
Precession Drift
~ Plasma Rotation
Collisionality
RFA = Bplasma/Bapplied

## Slide 20: Model-based RWM state space controller including 3D plasma response and wall currents used at high bN
Controller model includes
  plasma response
  plasma mode-induced current
Potential to allow more flexible control coil positioning
  May allow control coils to be moved further from plasma, and be shielded (e.g. for ITER)
Balancing transformation
~4000 states
Full 3-D model
…
RWM eigenfunction(2 phases, 2 states)
State reduction (< 20 states)
Katsuro-Hopkins, et al., NF 47 (2007) 1157
RWM state space controller in NSTX at high bN

## Slide 21: Comparisons between sensor measurements and state space controller show importance of states and 3D effects
Improved agreement with sufficient number of states (wall detail)
A) Effect of Number of States Used
dBp180
100
200
0
-100
RWM Sensor Differences (G)
137722
t (s)
40
0
80
0.56
0.58
0.60
137722
t (s)
0.56
0.58
0.60
0.62
dBp180
dBp90
dBp90
-40
0.62
t (s)
0.56
0.58
0.60
0.62
t (s)
0.56
0.58
0.60
0.62
100
200
0
-100
40
0
80
7 States
B) Effect of 3D Model Used
No NBI Port
With NBI Port
2 States
RWM
3D detail of model important to improve agreement
Measurement
Controller (observer)
137722
137722
S.A. Sabbagh, J.-W. Ahn, J. Allain, et al., Nucl. Fusion 53 (2013) 104007

## Slide 22: MHD spectroscopy, to be used for disruption P&A, reveals non-intuitive stability dependencies
MHD spectroscopy experiments
  measured resonant field amplification (RFA) of high bN plasmas at varied wf
  Higher RFA shows reduced mode stability
Counter-intuitive results:
  Highest bN, lowest wf (green): most stable
  Lowest bN, medium wf (blue): unstable
Physics understanding given by kinetic RWM theory (simplified here):
1
2
Precession Drift
~ Plasma Rotation
Collisionality
RFA = Bplasma/Bapplied