## Slide 1: Advanced divertor magnetic configurations for tokamaks: concepts, status, future.
Vlad Soukhanovskii
Edge Coordinating Committee Fall 2014 Technical Meeting
29 October 2014
New Orleans, Louisiana

## Slide 2: Acknowledgements
Dmitri Ryutov, LLNL
Dale Meade, Princeton, NJ

## Slide 3: This talk to discuss poloidal magnetic divertor configurations for tokamaks
Outline
Introduction
  Poloidal magnetic divertor configuration
  Perspectives on advanced magnetic divertor configurations: physics, engineering, history
Status of experiments
Research plans

## Slide 4: Other Plasma-Material Interface areas are as important, however, not discussed in this talk
Core and pedestal integration
Plasma facing components
  Divertor target geometry
  Continuously moving divertor plates
  Liquid metal divertors
  Pebble divertors
  Solid divertor targets with active cooling
Operating scenarios
  Particle control with cryo
  Radiative regimes
  Ergodic divertors
  3D fields
Numerical plasma and material models

## Slide 5: Poloidal X-point divertor enabled progress in tokamak physics studies in the last 30 years
Critical divertor tasks
  Power exhaust
  D/T and He pumping
  Impurity source reduction
  Impurity screening
C. S. Pitcher and P. Stangeby, PPCF 39, 779 (1997)
National Spherical Torus Experiment,
Princeton Plasma Physics Lab
Advanced magnetic configurations: potential to perform the divertor tasks better than the standard X-point divertor

## Slide 6: Significant gaps exist between present divertor solutions and future device requirements
Pheat/R
  Present experiments: ≤ 14 MW/m
  ITER: ≤ 20 MW/m DEMO: 80-100 MW/m
  Proposed solution: radiate up to 80-90%
Steady-state heat flux
  Technological limit qpeak ≤ 5-15 MW/m2
  ITER: qpeak ≤ 10 MW/m2 (Mitigated)
  DEMO: qpeak ≤ 150 MW/m2 (Unmitigated)
ELM energy, target peak temperature
  Melting limit 0.1-0.5 MJ/m2
  DEMO: Unmitigated, ≥ 10 MJ/m2
Impurity erosion (divertor target plasma temperature)
Greenwald report, Toroidal Alternate Panel Report, ReNeW
IAEA DEMO Workshops

## Slide 7: Advanced magnetic divertor configurations can improve standard divertor properties and performance
Divertor physics is inherently 2D or even 3D
  Parallel / cross-field transport and turbulence
  Radiation front (detachment) stability
  Neutral pressure / density distribution
Radiated power loss
Increase via Vdiv, LII
Number of
Divertors / legs
Poloidal Target
Inclination, etc
Increase plasma-wetted area
Increase lq via
increased
radial transport, LII
N
Increase divertor area at large RSP
Increase plasma-wetted area via increasing fexp

## Slide 8: Engineering and technology aspects define divertor configuration options
Plasma equilibria, shaping and control
  Magnetic coils – inside or outside TF magnet
  Neutron shielding
  Cooling
  Electromagnetic forces
  Maintenance and remote handling

## Slide 9: Advanced divertor magnetic configurations (classified by appearance)
Multiple divertors, each with one X-point
Higher order (2nd, 3rd) null divertors
Divertor with multiple X-points
Long-legged divertors with multiple X-points
Note on early concepts
  Envisioned before H-mode discovery (1982)
  Some concepts envisioned divertor for particle and impurity control only

## Slide 10: 1. Multiple divertors: triple-null, quadruple-null to share heat and particle fluxes
D-shaped plasma, high triangularity
Increased local shear
Enhanced kink stbility
J. Kesner, Nucl. Fusion 30, 548 (1990)
K. Bol et.al, Nucl. Fusion 25, 1149 (1985)
Poloidal Divertor Experiment tokamak at PPPL (1979 – 1983)
Significant contribution to divertor physics with double-null configuration

## Slide 11: 2. Higher order null divertors : larger region of very low Bp to affect geometry and transport
Snowflake, 2nd order null
  Bp ~ 0, grad Bp ~ 0 (Cf. first-order null: Bp ~ 0)
  Bp(r)~r2 (Cf. first-order null: Bp ~ r )
  Four divertor legs
Cloverleaf, 3rd order null
  Bp(r)~r3
  Six divertor legs
Strong plasma convection
D. D. Ryutov, Phys. Plasmas 14 (2007), 064502
D. D. Ryutov et. al, Phys. Plasmas 20 (2013), 092509

## Slide 12: 3. Divertor with multiple X-points: expand SOL in the divertor region
Poloidal Bundle + Expanded Boundary
Analysis of radiation, H-mode compatibility, neutron shielding, coil currents
N. Ohyabu, J. Plasma Fus. Res. 5 525 (1991)
N. Ohyabu et. al, Nucl. Fusion 5 519 (1981)
Doublet III Expanded Boundary

## Slide 13: 3. Divertor with multiple X-points: expand SOL in the divertor region
Cusp-like divertor configuration
  Coil currents acceptable for ITER-like parameters
H. Takase, J. Phys. Soc. J. 70, 609, 2001
M. Kotschenreuther et. al, IAEA FEC 2004;
Phys. Plasmas 14, 072502 (2007)
X-Divertor
  Small dipole coils under each divertor leg, inside the TF
  Potential to stabilize rad. front

## Slide 14: 4. Long-legged divertors with multiple X-points: increase connection length, expand SOL
F. H. Tenney et.al,
J. Nucl. Mater. 53 43 (1974)
Conceptual divertor design for Princeton Reference Design Reactor.
A.V. Georgievsky et.al, 6th Symp Eng Prob of Fus Energy, p 583, 1975, IEEE 75CH1097-5-NPS, Copyright 1976
F. H. Tenney,
PPPL Report 1284, 1976
Long-legged double null poloidal divertor
Long-legged high flux expansion poloidal divertor

## Slide 15: Long-legged divertors with multiple X-points
R. W. Conn et.al, U. Wisc. Report UWFDM-114, 1974
B. Badger et.al, U. Wisc. Report UWFDM-150, 1975
G. L. Kulcinski et.al, U. Wisc. Report UWFDM-173, 1976
UWMAK-II
UWMAK-III
Tokamak Enginering Test Reactor
UW Fusion Technology Institute conceptual reactor systems studies

## Slide 16: 4. Long-legged divertors with multiple X-points
D. Meade, Private Communication
T. F. Yang et.al, Westinghouse Corp. WFPS-TME-055 1977
TNS reactor (w/ ORNL)
Divertor heat flux 1-3 MW/m2
Flowing liquid lithium targets for heat and particle removal
PDX Modification proposal

## Slide 17: 4. Long-legged divertors remove interaction zone away from plasma
Conceptual design Engineering Test Facility
R=5.6 m
a=1.3 m
Bt=5.5 T
Ip=6.1 MA
PNBI=60 MW
Poloidal divertor
  W target plates
  Cryo-panels for particle control
P. H. Sager et. al, J. Vac. Sci. Tech. 18, 1081 (1981)

## Slide 18: 4. Long-legged divertors with multiple X-points
M. Peng, Steady-state Spherical tokamak TST,
Workshop on Edge Plasma for BPX and ITER, 1991
B. LaBombard et.al, APS 2013,
IAEA 2014
P. M. Valanju et.al, Phys.
Plasmas 16, 056110 (2009)
Super-X divertor
X-point target divertor
ADX tokamak proposal

## Slide 19: Advanced magnetic divertor configurations: status of experiments
Dedicated experimental devices (1979-1986)
    PDX
    Doublet III Expanded boundary
Snowflake divertor configuration (existing devices with existing coils, 2008-present)
    TCV, 2008
    NSTX, 2009
    DIII-D, 2012
    EAST, 2014
Long leg divertor physics (2010-present)

## Slide 20: 1. Doublet III Expanded Boundary was the first advanced magnetic divertor configuration experiment
Stability of divertor configuration with outside PF coils
Integrated power and particle exhaust
  Reduction of intrinsic impurities in the core
  Radiative divertor plasma cooling with seeded argon
  Argon screening from main plasma
Compatibility with core confinement
A. Mahdavi et. al, J. Nuc. Mater. 111 (1982) 355
N. Ohyabu et. al, Nucl. Fusion 5 519 (1981)

## Slide 21: 2. Snowflake configuration has been realized in several devices using existing PF coils
TCV
  Ip≤1 MA
  Bt≤1.5 T
  16 PF coils, Pre-programmed currents
NSTX
  Ip=0.8-1.0 MA
  Bt≤0.45 T
  3 divertor coils, pre-programmed currents
DIII-D
  Ip=0.8-1.0 MA
  Bt=2 T
  3 divertor coils w/control

## Slide 22: Divertor heat flux significantly reduced due to snowflake divertor geometry effects
NSTX
DIII-D
SOL
Standard Snowflake
Standard Snowflake
snowflake

## Slide 23: Snowflake divertor enables power and particle sharing over multiple strike points
GSP3
qSP3
qSP1
Standard Snowflake
W. Vijvers et.al, IAEA FEC 2012
V. A. Soukhanovskii et.al, IAEA FEC 2014

## Slide 24: Divertor heat transport affected by snowflake geometry
EMC3-IRENE modeling under-predicts power in additional strike points
Suggests additional transport channel in the null region
Increased lq may imply increased transport
  Increased radial spreading due to L||
  SOL transport affected by null-region mixing
lq = 2.40 mm
lq = 3.20 mm
Parallel heat flux (MW/m2)
H. Reimerdes et al. PPCF 2013, T. Lunt et al. PPCF 2014
V. A. Soukhanovskii et.al, IAEA FEC 2014

## Slide 25: Snowflake configuration favorably affects radiative divertor and detachment
Standard Snowflake
Standard Snowflake
PSOL = 3-4 MW
Natural partial detachment in NSTX snowflake otherwise inaccessible with standard divertor
Broader radiated power distribution, nearly complete power detachment in DIII-D
V. A. Soukhanovskii et.al, IAEA FEC 2014
V. A. Soukhanovskii et.al, NF 2011; POP 2011

## Slide 26: 3. Recent DIII-D experiments demonstrated benefits of the increased connection length
Longer connection length vs shorter connection length
  Divertor peak heat flux reduced
  Divertor Te reduced
  Divertor radiation increased
T. Petrie et.al, APS 2013, PSI2014, IAEA FEC 2014, APS 2014

## Slide 27: Advanced magnetic divertor configuration development
Near-term plans (5 years)
  Clarify effects of 2nd order null, extra X-points and long legs on
    Pedestal stability
    Steady-state and transient transport (heat, ion, impurity)
    Impurity radiation limits
Tokamaks
  Upgraded: TCV, NSTX-U, HL-2M, MAST-U
  Existing: DIII-D, EAST
Long-term plans (5-15 years) ?

## Slide 28: MAST Upgrade to test advanced divertor configurations
Bt=0.8 T
Ip ≤ 2 MA
PNBI ≤ 7.5 MW
8 divertor PF coils
Extensive diagnostic set
Radial and parallel transport, stability of detachment
Pedestal formation, structure, 3D fields
Super-X Snowflake
G. Fishpool et.al, J. Nucl. Mater. 2013

## Slide 29
Snowflake divertor is a leading heat flux mitigation candidate for NSTX-Upgrade
New center-stack
2nd neutral beam
BT
Ip
PNBI
pulse
1 T
2 MA
12 MW
5 s
NSTX-U Mission elements:
  Advance ST as candidate for Fusion Nuclear Science Facility
  Develop solutions for the plasma-material interface challenge
  Explore unique ST parameter regimes to advance predictive capability for ITER
  Develop ST as fusion energy system
J. E. Menard et. al, Nucl. Fusion 52 (2012) 083015

## Slide 30: HL-2M tokamak enables a number of advanced magnetic configurations
jj
Major radius R = 1.78 m
Minor radius a = 0.65 m
Toroidal field Bt = 2.2 T
Plasma current IP = 2.5 MA
Pin=32 MW (Design)
Snowflake Snowflake-plus Snowflake-minus Tripod
G.Y. Zheng et.al, Fus. Eng. Design 89 (2014) 2621

## Slide 31: Many pre-DEMO and DEMO designs include snowflake and Super-X configurations
Y. Wan, SOFE 2013
China Fusion Experimental Reactor
Z. Luo et.al, IEEE TRANSACTIONS ON PLASMA SCIENCE, V42, 2014, 1021
R Albanese et. al,
PPCF, 56 (2014) 035008
Snowflake for DEMO
N. Asakura et.al, Trans. Fus. Sci. Tech. 63, 2013, 70.
Super-X and Snowflake for DEMO
Super-X for Aries Slim CS
M. Kotschenreuther et. al, ARIES Workshop 2010

## Slide 32: Everything New Is Actually Well-Forgotten Old (Новое – это хорошо забытое старое, the Russian saying).
A number of potentially attractive magnetic divertor configurations exist
Much research remains to be done to qualify them as
  Advanced magnetic divertor configurations
  Divertor candidates for a fusion reactor

## Slide 33: Backup

## Slide 34: Abstract
The present vision for controlling the plasma–material interface of a tokamak is an axisymmetric poloidal magnetic X-point divertor. The divertor must enable access to high core and pedestal plasma performance metrics while keeping target plate heat loads and erosion within the operating limits of plasma-facing component cooling technology and target plate materials. The proposed ITER divertor is based on standard X-point geometry designs tested in large tokamak experiments and uses tilted vertical targets to generate partial radiative detachment of the strike points. However, the standard divertor approach is likely to be insufficient for next step advanced tokamak and spherical tokamak devices such as the proposed fusion nuclear science facilities and for the DEMO reactor.
Novel magnetic divertor configuration development and optimization has always been an active area in fusion plasma research. In this talk, advanced poloidal divertor concepts and experimental performance will be reviewed. Advanced divertors have the capability to modify steady-state and transient power exhaust via modifications to parallel and perpendicular transport and dissipative loss channels. The basic physics principles of these concepts will be summarized, from the first divertor for impurity control proposed by L. Spitzer for the stellarator, to long legged divertors, expanded boundaries, multiple X-point divertors, and multipole divertors for tokamaks. Many of the these divertor configurations face practical limitations on magnetic coil layout and construction. In recent years, two advanced divertor concepts have been pursued experimentally: snowflake (2nd order null) divertors, implemented in the TCV, NSTX, DIII-D and EAST tokamaks with existing magnetic coils, and the (long-legged) Super-X divertor, which is presently being implemented in MAST Upgrade using specially designed additional coils. The status and plans for research in these areas will be summarized.
Several outstanding physics and engineering problems need to be addressed in order to qualify an advanced divertor concept for a next step tokamak reactor. This talk will discuss the general issues and motivations, including coil design and placement, equilibria design and plasma real-time control, plasma-facing component design, compatibility with highly radiative scenarios, and integration with high-performance core and pedestal plasma.
This work is supported by the US Department of Energy under DE-AC5207NA27344.

## Slide 35: Conventional divertor history…
A. D. Sanderson et.al, J. Nucl. Mater. 76 530 (1978)
First proposal of a magnetic divertor
  L. Spitzer, Phys. Fluids 1 (1958) 253 (for impurity control in a stellarator)
First use of a poloidal divertor
  JFT-2a (DIVA), Japan, 1975 (approx.)
First demonstration of impurity control using a divertor
  JFT-2a, Japan, 1975 (approx.)
First demonstration of H-mode with a poloidal divertor
  ASDEX, Germany 1982
Poloidal bundle divertor