## Slide 1
Recent Progress on Spherical Torus Research and Implications for Fusion Energy Development Path
Masayuki Ono
PPPL, Princeton University
On behalf on the world ST community!
APS-DPP 2014
October 27 – 31, 2014
Session FR1
Spherical Torus
Notes: Thank you chairman and I would like to thank the Program Committee for giving us the opportunity to present to you the recent….

## Slide 2
Acknowledgements
For more detail, M. Ono and R. Kaita, ST review paper for PoP
US Institutions:
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Nova Photonics
New York U
ORNL
Princeton U
*PPPL
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Tennessee
*U Washington
*U Wisconsin
International Institutions:
*Culham Sci Ctr
U St. Andrews
York U
*Tokamak Energy
Chubu U
Fukui U
Hiroshima U
*Hyogo U
*Kyoto U
*Kyushu U
Kyushu Tokai U
NIFS
Niigata U
*U Tokyo
Tsukuba U
JAEA
Hebrew U
*Ioffe Inst
RRC Kurchatov Inst
TRINITI
D.V.Efremov Inst
INTEKHMASH
NFRI
KAIST
POSTECH
*Seoul National U
*Beijing National L
ASIPP
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
• At present, over 500 researchers and 140 graduate students are engaged in ST research worldwide.
• Over 1,000 ST related refereed publications since 2000.
* With ST Facility
Notes: I would like to acknowledge the world ST community with researchers from a large number of institutions.
At present there are over 500 researchers engaged in the ST research.
I should also note that there is a strong educational component of ST research with over 140 graduate students performing research.
There are over 1000 ST related refereed publications since 2000 so I can only mention just a small fraction of the work.
I also borrowed heavily from the recent review paper written for PoP.

## Slide 3
Unique ST properties
ST Fusion Energy Development Path
World ST Facilities
Unique ST Physics Regimes
ST-FNSF Relevant Experiments
ST Facility Upgrade Status
Summary
Talk Outline
Notes: Here is the outline of this review to give you an overview of the world ST research.

## Slide 4
ST is a low aspect ratio tokamak with A < 2
Natural elongation makes its spherical appearance
Y-K.M. Peng, D.J. Strickler, NF (1986)
A. Sykes, et al., Nucl. Fusion (1999).
Camera image from START
Aspect Ratio A = R /a
Elongation k = b/a
“natural” = “without active shaping”
ITF
ITF
BTF ∝ ITF/R
Ip
Ip
Ip
x
Ip
x
x
Ip
Ip
Note: ST differs from FRC, spheromak due to BTF

## Slide 5
A ~ 3,
k = 1.5-2,
q95 = 3-4,
bT = 3-10%
A ~ 1.5,
k = 2-3,
q95 = 8-12,
bT = 10-40%
Tokamak
ST
A spherical tokamak (ST) is a high beta tokamak
Favorable average curvature improves stability at high beta
Toroidal Beta bT = p / (BT02/ 2m0)
Aspect Ratio A = R /a
Elongation k = b/a
Notes: A spherical tokamak is a low aspect ratio tokamak. Tokamak is a donut like aspect ratio of about 3 where as ST is aspect ratio of about 1.5. As the aspect ratio is reduced, the hole of the donut is reduced and it disappears entirely at A = 1. As the aspect ratio is reduced, the plasma elongate naturally takes on the spherical shape due to self fields. Another important property is the magnetic field line. The tokamak magnetic field line goes around torus at relatively constant pitch where as the ST geometry, the field line transit the outboard unstable region quickly but spend many toroidal transits in the inboard stable region. This makes ST plasma stable for high beta and also makes the edge safety factor high ~ 10 compared to ~ 3 for tokamak.
As a result, there are a number of new unique physics regimes which can be accessed at low aspect ratio, which can be utilized to enhance the understanding of toroidal confinement physics and improve predictive capabilities for ITER and future fusion facilities.

## Slide 6
ST can be compact, high beta, and high confinement
Higher elongation k and low A lead to higher Ip, bT and tE
Toroidal Beta bT = p / (BT02/ 2m0)
Aspect Ratio A = R /a
Elongation k = b/a
Ip ~ ITF (1 + k2 / (2 A2 q*)
bTº bN Ip / (aBT0)
S. Jardin et al., FS&T (2003)
D.A. Gates et al., NF (2007).
High κ ∼ 3.0 equilibrium in NSTX.
tE ∝ Ip
Ip ~ ITF for ST due to low A and high k
• ST has high Ip due to high κ and low A
• Ip increases tokamak performance
• ST can achieve high performance cost effectively
$
Notes: A spherical tokamak is a low aspect ratio tokamak. Tokamak is a donut like aspect ratio of about 3 where as ST is aspect ratio of about 1.5. As the aspect ratio is reduced, the hole of the donut is reduced and it disappears entirely at A = 1. As the aspect ratio is reduced, the plasma elongate naturally takes on the spherical shape due to self fields. Another important property is the magnetic field line. The tokamak magnetic field line goes around torus at relatively constant pitch where as the ST geometry, the field line transit the outboard unstable region quickly but spend many toroidal transits in the inboard stable region. This makes ST plasma stable for high beta and also makes the edge safety factor high ~ 10 compared to ~ 3 for tokamak.
As a result, there are a number of new unique physics regimes which can be accessed at low aspect ratio, which can be utilized to enhance the understanding of toroidal confinement physics and improve predictive capabilities for ITER and future fusion facilities.

## Slide 7
  Lower A  increased toroidicity  higher b, strong shaping
  Higher b  electromagnetic effects in turbulence, EP-modes, RF heating and CD
  Higher fraction of trapped particles (low A), increased normalized orbit size (high b), and flow shear (due to low B, low A) broad range of effects on transport and stability
  Increased normalized fast-ion speed (high b)  simulate fast-ion transport/losses of ITER
  Compact geometry (small R)  high power/particle/neutron flux relevant to ITER, reactors
New physics regimes are accessed at low aspect ratio, enhancing the understanding of toroidal confinement physics
Notes: A spherical tokamak is a low aspect ratio tokamak. Tokamak is a donut like aspect ratio of about 3 where as ST is aspect ratio of about 1.5. As the aspect ratio is reduced, the hole of the donut is reduced and it disappears entirely at A = 1. As the aspect ratio is reduced, the plasma elongate naturally takes on the spherical shape due to self fields. Another important property is the magnetic field line. The tokamak magnetic field line goes around torus at relatively constant pitch where as the ST geometry, the field line transit the outboard unstable region quickly but spend many toroidal transits in the inboard stable region. This makes ST plasma stable for high beta and also makes the edge safety factor high ~ 10 compared to ~ 3 for tokamak.
As a result, there are a number of new unique physics regimes which can be accessed at low aspect ratio, which can be utilized to enhance the understanding of toroidal confinement physics and improve predictive capabilities for ITER and future fusion facilities.

## Slide 8
Unique ST properties
ST Fusion Energy Development Path
World ST Facilities
Unique ST Physics Regimes
ST-FNSF Relevant Experiments
ST Facility Upgrade Status
Summary
Talk Outline
Notes: Here is the outline of this review to give you an overview of the world ST research.

## Slide 9
Extend Predictive Capability for ITER and Toroidal Science
  High b physics, rotation, shaping for MHD, transport
  Non-linear Alfvén modes, fast-ion dynamics, Electron gyro-scale turbulence at low n*
Unique ST properties support and accelerate a range of development paths toward fusion energy
Burning Plasma Physics - ITER

## Slide 10
Enable Compact Fusion Nuclear Science Facility
  High neutron wall loading
  Potentially smaller size, cost
  Smaller tritium (T) consumption at fixed neutron wall loading
  Accessible / maintainable
Goal: 100% non-inductive + high b
Plasma-Material Interface Research
  Strong heating + smaller R  high P/R, P/S
  Novel solutions: snowflake, liquid metals, Super-X, hot high-Z walls
STs Narrow Gaps to FNSF/Pilot/DEMO:

## Slide 11
If the cost of volume neutron source (FNSF) facility is “modest” << ITER, DEMO, it becomes highly attractive development step in fusion energy research. M.A. Abdou, et al., FTS (1996)
Fusion needs FNSF(s) (modest cost, low T, and reliable) to Test and Qualify Fusion Components
FNSFs
Without R&D, fusion components could fail prematurely which often requires long repair/down time. This would cripple the DEMO operation.
FNSF can help develop reliable fusion components.
Such FNSF facilities must be modest cost, low T, and reliable.
Fusion needs to develop reliable/qualified components which are unique to fusion:
Divertor/PFC
Blanket and Integral First Wall
Vacuum Vessel and Shield
Tritium Fuel Cycle
Remote Maintenance Components
FNSF-ST
FNSF-AT

## Slide 12: There have been several studies of ST-FNSF showing the potential attractiveness of this approach
Projected to access high neutron wall loading at moderate R0, Pfusion
  Wn ~ 1-2 MW/m2 , Pfus ~ 50-200MW, R0 ~ 0.8-1.8m
Modular, simplified maintenance
Tritium breeding ratio (TBR) near 1
  Requires sufficiently large R0, careful design
R&D Needs for an ST-FNSF
  Non-inductive start-up, ramp-up, sustainment
    Low-A  minimal inboard shield  no/small transformer
  Confinement scaling (especially electrons)
  Stability and steady-state control
  Divertor solutions for high heat flux
  Radiation-tolerant magnets, design
Culham (UK)
UT Austin
ORNL
PPPL
Example ST-FNSF concepts

## Slide 13
Unique ST properties
ST Fusion Energy Development Path
World ST Facilities
Unique ST Physics Regimes
ST-FNSF Relevant Experiments
ST Facility Upgrade Status
Summary
Talk Outline
Notes: Here is the outline of this review to give you an overview of the world ST research.

## Slide 14
Operating ST Research Facilities Since 2000
NSTX and MAST: MA-class STs, Smaller STs addressing topical issues
z
NSTX/LTX
PEGASUS
KTM
GLOBUS-M
SUNIST
VEST
HIT-II
QUEST
HIST
LATE
TST-2
TS3/4
UTST
ETE
NSTX, USA
R0 ~ 0.85 m
MAST, UK
R0 ~ 0.75 m
HIT-II, USA
QUEST/CPD, Japan
VEST, Korea
ETE, Brazil
LATE, Japan
TS3/4, Japan
SUNIST, China
HIST, Japan
UTST, Japan
TST-2, Japan
GLOBUS-M, Russia
LTX/CDX-U, USA
PEGASUS, USA
STs operated since 2000
z
MAST
ST25(HTS)
z
ST25, UK
Notes: NSTX and MAST are MA class STs so they are the flag ships of ST research. They are at present undergoing upgrades for 1 T operation. Globus-M is a medium size ST and it is undergoing upgrade to 1 T operation. There a large number of STs in Japan. And the QUEST device is the largest and their flagship device. It aim is to operate steady-state. There are also STs in China, Korean, Kazakhstan, and Brazil. One recent addition is ST25 which is the first all high temperature SC magnet tokamak by Tokamak Energy which is private funded enterprise. You can see quite a range of aspect ratio. The lowest one is PEGASUS with A = 1.15 with extremely slender center post. LTX is a lithium dedicated machine with A = 1.5. I do not have the time to cover the lithium research but there are companion papers at this conference for those interested. NSTX and MAST are 1.32. The ST devices spans quite broad range to make sure we capture necessary low A physics.

## Slide 15
MA-Class ST Research Started in 2000
Complementary Physics Capabilities of NSTX and MAST
NSTX
MAST
A. Sykes, et al., IAEA 2000, NF 2001
M. Ono, et al., IAEA 2000, NF 2001
NSTX
R = 85 cm
A ≥ 1.3
= 1.7 - 3.0
BT = 5.5 kG
Ip ≤ 1.5 MA
Vp ≤ 14 m3
PNBI = 7.4 MW
Similar Capabilities
MAST
R = 80 cm
A ≥ 1.3
= 1.7 – 2.5
BT ~ 5.0 kG
Ip ≤ 1.5 MA
Vp ≤ 10 m3
PNBI = 4.0 MW
Comprehensive diagnostics
Physics integration
Scenario development
Passive Plates
Heilicity Injection
HHFW
1 x 6 RWM Coils
Large divertor volume
Merging/Compression
ECH
2 x 12 ELM coils
Complementary Capabilities

## Slide 16
Unique ST properties
ST Fusion Energy Development Path
World ST Facilities
Unique ST Physics Regimes
ST-FNSF Relevant Experiments
ST Facility Upgrade Status
Summary
Talk Outline
Notes: Here is the outline of this review to give you an overview of the world ST research.

## Slide 17
Higher bT enables higher fusion power and compact FNSF for required neutron wall loading
Tokamak
bN = 6
5
4
3
2
Ip/aBT0 (MA/mT)
Toroidal b (%)
ITER
0
20
40
0
4
8
ST-FNSF
Data base from START, MAST, PEGASUS and NSTX
Pfusion ∝ p 2 x Vol
Pfusion ∝ bT2 BT04 x Vol
$
Physics Knob
Product
Investment
Wn ∝ Pfusion / Area
High neutron wall loading Wn possible in a compact ST
Wn ∝ bT2 BT04 a (not strongly size dependent)
Wn ~ 1 MW/m2 with R ~ 1 m FNSF feasible!

## Slide 18
S.A. Sabbagh PRL(2006)
Record bN and bN/li accessed using resistive wall mode stabilization
J. W. Berkery, PRL (2011)
W. Zhu, PRL (2006)
S.A. Sabbagh at this APS
High bN regime is important for bootstrap current generation.
High bN/li regime important since high fBS regime has low li.
Major mission of NSTX-U is to achieve fully non-inductive operations at high b
ST-FNSF
Unstable RWM
Stable / controlled RWM

## Slide 19
Favorable Confinement Trend with Collisionality and b found
Important implications for future STs and Demo with much lower n
M. Valovic et al., NF (2011)
Fig. 70. (a) Normalized confinement time as a function of collisionality at mid-radius in NSTX. Blue points are from discharges that used HeGDC+B wall conditioning, while red points are from discharges that used Li. Reprinted with permission from S.M. Kaye et al., Nucl. Fusion 53 063005 (2013). Copyright (2013). Institute of Physics.
(b) Collisionality scan of thermal energy confinement time in MAST. Reprinted with permission from M. Valovic et al., Nucl. Fusion 51 073045 (2011). Copyright (2011) Institute of Physics.
NSTX
Very promising ST scaling to reactor condition, if continues on NSTX-U/MAST-U
NSTX
tE, th µ n-0.1 b-0.9 tokamak empirical scaling (ITER98y,2)
tE, th µ n-0.8 b-0.0 ST scaling
S.M. Kaye et al., NF (2007) (2013)
MAST
B tE,th [ T s]
~ n*e -0.82
n*e

## Slide 20
Microtearing-driven (MT) transport may explain ST collisionality scaling
Microtearing-driven ce vs. nei using the GYRO code.
W. Guttenfelder, et al., PoP(2012)
MT growth rate decreases with reduced collisionality in qualitative agreement with the NSTX experiment.
Futher electron confinement improvement expected for NSTX-U and MAST-U due to reduced collisionality.
NSTX-U /MAST-U

## Slide 21
ETGs measured for the first time with high-k scattering
High be or larger re ∝ be0.5 of ST plasma enabled measurement of ETGs.
E. Mazzucato et al., NF (2009)
H.Y. Yuh et al., PoP (2009)
J.L. Peterson, et al., PoP(2011).
ETG Suppression in Reversed Shear
Electron Temperature Gradient Mode (ETG) Excitation with Core Electron Heating
Shear stabilization of ETGs D. R. Smith, et al., PRL (2009)
Density gradient stabilization of ETGs Y. Ren, et al., PRL (2011)
Note: Here we call electron gyro-scale turbulence as ETGs
Calculated ETG ce by GTS code agrees with experiment
S. Ethier et al., IAEA (2010)
ce (m2/sec)
ce (m2/sec)
time (Vth/LTe)
ce (GTS)

## Slide 22
H-mode / ELM physics: High Priority Research Goal
Unmitigated ELMs could cause PFC damage in reactors
ST is in strongly shaped ELM regimes
P.B. Snyder et al., PoP (2002).
Video images of MAST plasmas showing a filamentary ELM structure.
NSTX, PEGASUS
(Type I)
MAST
(Type I)
  N. Ben Ayed et al., PPCF (2009).
K.E. Thome et al., EPR (2014)
FNSF
L-H power threshold scaling extended for low A
• NSTX/MAST/PEGASUS accessed H-mode at very low heating power < 1 MW and also in ohmic plasmas
• NSTX-U and MAST-U will provide H-mode access scaling for FNSF

## Slide 23
Divertor heat flux in Low-A regime
ST power flux width clearly shows 1/Bp variation
Most divertor power arrives at outboard side in MAST and NSTX!
Ratio of outboard power flux vs. inboard in MAST
STs data breaks A degeneracy of power flux width study.
* Unfavorable for large size, Ip devices such as ITER and Demo
"P B / R" as the new heat flux metric which is favorable for STs
Outboad heat flux
POB >> PIB
Inboad heat flux
PIB (kW)
POB (kW)
POB/PIB
Time (s)
G.F. Counsell et al., PPCF (2002)
Heuristic model by R.J. Goldston, NF (2012).
~ 40 kW
~ 2 MW
~ 50
T. Eich et al., NF (2013).

## Slide 24
NBI heated ST plasmas provide an excellent testbed for a-particle physics
Alfvenic modes readily accessed due to high Va > VAlf
EP parameter space
a-particles couples to Alfven-type mode strongly when Va > VAlf ~ b-0.5 Cs
Va > VAlf in ITER and reactors
In STs, the condition is easily satisfied due to high beta
A prominent instabilities driven by fast particles are global and called toroidal Alfven eigenmodes (TAE).
NSTX-U/MAST-U will also explore Va < VAlf regime giving more flexibility
  M.P. Gryaznevich et al. PPCF (2004)
Stabilization of TAEs at high β in MAST
TAEs significantly modified at high b as VAlf Cs
  E. D. Fredrickson et al., NF (2013)

## Slide 25
“TAE avalanche” shown to cause energetic particle loss
Uncontrolled a-particle loss could cause reactor first wall damage
Time (ms)
(a)
Multi-mode TAE avalanche can cause significant EP losses as in “sea”of TAEs expected in ITER
D.S. Darrow et al., NF (2013).
  E. D. Fredrickson et al., NF (2013)
Progress in simulation of neutron rate drop
due to TAE avalanche
Time (ms)
Neutron rate (a.u.)
Fast ion loss rate (a.u.)
Frequency (kHz)

## Slide 26
Unique ST properties
ST Fusion Energy Development Path
World ST Facilities
Unique ST Physics Regimes
ST-FNSF Targeted Experiments
ST Facility Upgrade Status
Summary
Talk Outline
Notes: Here is the outline of this review to give you an overview of the world ST research.

## Slide 27
Compact ST-FNSF has no/small central solenoid
STs Addressing Critical Issues for FNSF and Demo
ST-FNSF Scenarios
IP [MA]
NBI
Time
HHFW
EC/EBW, HI, PF
Solenoid-free
Start-up
high bT, bN, k, disruption avoidance, high H, heat flux mitigation
Current ramp-up and profile control
• Three novel techniques for solenoid-free start-up and ramp-up investigated
  ECH/EBW
  Helicity Injection
  Merging-compression
~ 1-2 MA of solenoid-free start-up current needed for FNSF
Notes: ST has been addressing critical issues for FNSF: A compact FNSF facility does not have solenoid. So, the solenoid-free start-up is a critical issue for ST-FNSF. But solenoid-free start-up is attractive for tokamak reactor design as well. Other issues are ramp-up….

## Slide 28
Efficient ECH/EBW start-up and sustainment demonstrated
RF start-up investigated in CDX, TST-2, LATE, MAST, QUEST, VEST, SUNIST
T.S. Bigelow et al., ISTW 2013
55 kA sustained with 270 kW in QUEST, Japan
H. Idei, et al., IAEA 2014
ECH/EBW start-up to be tested at MW level in QUEST, NSTX-U and MAST-U.
TST-2
LATE ECH/EBW
Initial Open Field Line Phase
Evolution Phase
ST formation Phase
M. Uchida et al., PRL (2010).
72 kA start-up current achieved with 75 kW in MAST, UK

## Slide 29
Helicity Injection Is an Efficient Method for Current Initiation
Coaxial Helicity Injection (CHI) Concepts Being Devloped
CHI developed on HIT and HIT-II and transferred to NSTX
Discharge evolution of 160 kA closed flux current produced by CHI alone in NSTX
R. Raman et al., PRL (2006)

## Slide 30
Helicity Injection Is an Efficient Method for Current Initiation
Local Helicity Injection (LHI) Concepts Being Seveloped
Long-Pulse Startup Demonstrated in PEGASUS with LHI
CHI and LHI startup to be tested at higher current ~ 0.5-1.0 MA in NSTX-U.
  3-6 kA current injector array in plasma SOL
Improving predictive capability for both CHI and LHI
J. O’Bryan, PhD. Thesis, UW Madison 2014

## Slide 31
Merging Start-Up Yielded High Current STs
Rapid ion heating observed from magnetic reconnection
Y. Ono, et al., NF (2003)
Merging-compression start-up in MAST
Ultra high b STs produced by mergings in TS-3 Device
Fig. 22. Schematic of UTST. Reprinted with permission from Y. Ono.
Y. Ono, et al., this APS
CS Induction
A. Sykes et al., NF (2001)

## Slide 32
Current Ramp-Up and Profile Control Crucial for FNSF
Major Research Topics for MAST-U and NSTX-U
G. Taylor et al., PoP (2010), (2012)
Efficient HHFW electron heating due to high be achieved in NSTX.
HHFW current ramp-up will be tested in NSTX-U at higher power ~ 4 MW.
NSTX
Near sustained discharges obtained with modest HHFW power.

## Slide 33
Current Ramp-Up and Profile Control Crucial for FNSF
Major Research Topics for MAST-U and NSTX-U
  M. Turnyanskiy et al., NF (2009)
G. Taylor et al., PoP (2010), (2012)
Efficient HHFW electron heating due to high be achieved in NSTX.
HHFW current ramp-up will be tested in NSTX-U at higher power ~ 4 MW.
NSTX
Off-axis NBI CD Required for Profile Control Demonstrated in MAST
Off-axis current drive for profile control will be tested in both MAST-U and NSTX-U with major NBI upgrades.
Near sustained discharges obtained with modest HHFW power.

## Slide 34
NSTX has accessed A, bN, k needed for ST-based FNSF
Requires fBS ≥ 50% for plasma sustainment
fBS º IBS / Ip = CBS bp / A0.5 = (CBS/20) A0.5 q* bN µ A5 (1+k2) bN2/ bT
SC-ST
NSTX achieved fBS ~ 50% and fNI ~ 65-70% with beams.
NSTX-U expects to achieve fNI ~100% with the more tangential (~ x1.5- 2 more current drive efficient) NBI.
S.P. Gerhardt et al., NF (2011)

## Slide 35
Example: Disruptivity is reduced with strong shaping of the plasma boundary.
NSTX Data Demonstrates a Favorable Operations Window For Reduced Disruptivity in an ST-FNSF
No strong increase in disruptivity as bN increases
Reduction in disruptivity also with:
  Decreasing li (broader current profile)
  Decreasing pressure peaking
S=37
S=20
Upgrades will test and improve these favorable trends in a systematic way
S.P. Gerhardt et al., NF (2013)
ST-FNSF
(S=q95IP/aBT)

## Slide 36
High Confinement Needed for Compact FNSF
High confinement H-mode in the range of FNSF obtained
Y. Ren.
Fusion gain Q depends strongly on “H”, Q µ H 5-7
Higher H enables compact ST-FNSF H = 1.2 – 1.3
Higher H gives more reactor design flexibility and margins.
• Ion energy transport in H-mode ST plasmas near neoclassical level due to high shear flow and favorable curvature.
• Electron energy transport anomalous
S. Gerhardt NF (2014)
FNSF
H-mode confinement in STs H ~ 1 (ITER98y,2) but enhanced pedestal H-mode (EPH) has 50% higher H up to H ~ 2
R. Maingi, PRL (2010)
EPH
H-mode
NSTX
NSTX

## Slide 37
ST-FNSF has high P/R due to small R
Innovative Heat Flux Mitigation via Divertor Flux Expansion
D. Ryutov, et al., PoP (2007)
P.M. Valanju, et al., PoP (2009).
Kotschenreuther, et al., PoP (2007)
Lower toroidal field of outboard divertor leg of STs facilitates heat flux mitigation by divertor flux expansion solutions
X-Divertor: CREST
Snow-flake
Super-X: MAST-U
Major mission of MAST-U is to investigate up-down symmetric Super-X configuration. NSTX explored Snow-flake / X-divertor.

## Slide 38
Divertor flux expansion of ~ 50 achieved with
Snow Flake Divertor with large heat flux reduction in NSTX
NSTX-U will investigate novel divertor heat flux mitigation concepts needed for FNSF and Demo.
• Up-and-down symmetric Snow Flake / x-Divertors
• Lithium + high-z metal PFCs
Divertor heat flux (MW/m2)
Snowflake divertor in NSTX
OSP
V. A. Soukhanovskii et al., PoP (2012)

## Slide 39
Unique ST properties
ST Fusion Energy Development Path
World ST Facilities
Unique ST Physics Regimes
ST-FNSF Relevant Experiments
ST Facility Upgrade Status
Summary
Talk Outline
Notes: Here is the outline of this review to give you an overview of the world ST research.

## Slide 40
NSTX and MAST are undergoing major upgrades
~ x 2 BT, Ip, PNBI and ~ x5 pulse length from NSTX/MAST
NSTX-U
MAST-U
Super X-divertor configuration for FNSF divertor solution
Highly tangential 2nd NBI for non-inductive operations

## Slide 41
• New Center Column for higher BT and Ip
• Super-X Divertor for divertor heat flux mitigation
• Vertically off-axis NBI for current profile control.
MAST-U to support novel exhaust concepts, ITER, and FNSF
Completed MAST operation in 2013 and began construction
First plasma scheduled in 2016
End Plate Modules (LEP)
J. Milnes SOFT 2014
Centre Column (CC) Module
Super X Divertors
Conventional
Super-X
Off-Axis NBI

## Slide 42
NSTX-U to provide data base to support
ST-FNSF designs and ITER operations
TF OD = 40cm
Previous
center-stack
TF OD = 20cm
New 2nd NBI
Present NBI
New
center-stack
~ X 5 - 10 increase in ntT from NSTX
NSTX-U average plasma pressure ~ Tokamaks
Key NSTX-U research topics for FNSF and ITER
Stability and steady-state control at high b
Confinement scaling (esp. electron transport)
Non-inductive start-up, ramp-up, sustainment
Divertor solutions for mitigating high heat flux
J. Menard, et al., NF (2012)
New CS provides higher x2 TF (improves stability), 3-5s needed for J(r) equilibration
More tangential injection provides 3-4x higher CD at low IP:
  2x higher absorption (4080%) at low IP
  1.5-2x higher current drive efficiency
Research operation to resume in Apr. 2015

## Slide 43
NSTX Upgrade Project Is Nearly Complete
Recent aerial view of NSTX-U Test Cell (Oct. 27, 2014)
CS Casing
HHFW System
1st NBI
2nd NBI
NSTX-U

## Slide 44
New Center-Stack Installed In NSTX-U (October 24, 2014)
First plasma scheduled in Feb. 2015
M. Ono, et al., at this APS

## Slide 45
Summary of Spherical Torus Research
World-wide effort with over 500 researchers and 140 students
• ST is a member of tokamak family with aspect ratio ≤ 2.0
• Unique ST features include natural elongation, compact geometry, and high beta which would be suitable for compact FNSF and PMI solutions.
• Extreme ST physics parameters exercise tokamak theory/modeling to validate and improve predictive capability needed for ITER and beyond where large extrapolations are needed.
• MA-class ST research began in 2000 with NSTX and MAST together with smaller ST facilities worldwide. Today, 16 ST facilities are operational.
• STs contributed strongly to fusion research program in all fusion energy science areas
• STs performed FNSF relevant experiments achieving many of the key plasma parameters and research objectives.
• Next phase of ST research begins shortly as 1T-2MA-class MAST-U and NSTX-U Facilities are coming on line for FNSF and ITER

## Slide 46
ST Related Presentations at this APS Meeting
Invited Talks
  BI1.00001 (Mon): The effects of impurities and core pressure on pedestal stability in JET and MAST, Samuli Saarelma
  GI1.00003 (Tue): Broadening of the divertor heat flux footprint with increasing number of ELM filaments in NSTX, Joon-Wook Ahn
  NI2.00003 (Wed): High Power Heating of Magnetic Reconnection in Tokamak Merging Experiments, Yasushi Ono
  TI1.00001 (Thu): Simulation of 3D effects on partially detached divertor conditions in NSTX and Alcator C-Mod. Jeremy Lore
  TI1.00003 (Thu): Drift Kinetic Effects on 3D Plasma Response in High-beta Tokamak Resonant Field Amplification Experiments, Z.R. Wang
  VI2.00002 (Thu): Unification of Kinetic Resistive Wall Mode Stabilization Physics in Tokamaks. S.A. Sabbagh
  YI1.00006 (Fri): Energy Channeling and Coupling of Neutral-beam-driven Compressional Alfv’en Eigenmodes to Kinetic Alfv’en Waves in NSTX, Elena Belova
  YI2.00003 (Fri) : High Performance Discharges in the Lithium Tokamak eXperiment (LTX) with Liquid Lithium Walls, John Schmitt
Oral Session GO3 (Tue): MAST-U, PEGASUS, NSTX-U, LTX
Poster Session PP8 (Wed): NSTX-U, LTX, PEGASUS, MAST-U, QUEST, TS-4

## Slide 47: Back-up slides

## Slide 48
Nearly self-sustained ST-Demo regimes identified
q-profile appears to be a differentiating feature for ST and AT
J. Menard et al., PPPL Report, 2003
fBS º IBS / Ip = CBS bp / A0.5 µ A5 (1+k2) bN2/ bT
ST
AT
Reversed shear AT likely suffers from infernal modes and/or double tearing at high beta, and we can potential reduce or eliminate reverse shear in ST due to higher edge q-shear from low-A
Notes: Number of ST power plant /DEMO studies showing generally competitive COE.

## Slide 49
Extend Predictive Capability
  Non-linear Alfvén modes, fast-ion dynamics
  Electron gyro-scale turbulence at low n*
  High b, rotation, shaping, for MHD, transport
Fusion Nuclear Science Facility
  High neutron wall loading
  Potentially smaller size, cost
  Smaller T consumption
  Accessible / maintainable
Burning Plasma Physics - ITER
Steady-State, Plasma-Material Interface R&D
VULCAN
NHTX
KSTAR
EAST
JT-60SA
W7-X, LHD
QUASAR
Pilot Plant or DEMO
ARIES-ST
ARIES-CS
ARIES-AT
FNSF-ST
FNSF-AT
Fusion Nuclear Science Facility
Goal: 100% non-inductive + high b
Plasma-Material Interface Research
  Strong heating + smaller R  high P/R, P/S
  Novel solutions: snowflake, liquid metals, Super-X, hot high-Z walls
STs Narrow Gaps to Pilot/DEMO:
ST research program supports and accelerates a range of development paths toward fusion energy
ST Research
J. Menard

## Slide 50
ST Fusion Power Plants
Copper vs. Superconducting Coils
ARIES-ST
Cu Power Plant
JUST
SC ST Power Plant
R0 ~ 3.2 m
R0 ~ 4.5m
Copper design – Compact but due to larger recirculating power leading to higher fusion power needing aggressive bT, bN, k. designs..
SC design – Larger size due to SC shielding requirement. But smaller recirculating power provides more flexibility in design such as operating at lower fusion power, more moderate bT, bN, k, etc.
Y. Nagayama et al., IEEJ (2012)
B.G. Hong, Yet al.,NF (2011)
K. Gi IAEA(2014)
F. Najmabadi et al., FED (2003)
H. R. Wilson, et al., NF (2004)
Nearly fully self-sustained ST/Tokamal reactor requires high k and bN
fBS º IBS / Ip = CBS bp / A0.5 = (CBS/20) A0.5 q* bN µ A5 (1+k2) bN2/ bT
All of the ST power plant designs have q95 ~ 10 which could give needed MHD stability

## Slide 51
Non-conventional ST Fusion Power Reactors
Taking advantage of compact and light weight ST fusion core
M. Kotschenreuther et al., FE&D (2009).
The Discovery II
C.H. Williams, et al., NASA/TM-2005-213559
ST Fusion Core
ST Fusion-Fission Hybrid
A. Sykes, SOFT 2014
ST135
R = 1.35m
Qfus ~ 5 Pilot Plants
front view
aft view
Realizing "2001: A Space Odyssey": Piloted Spherical Torus Nuclear Fusion Propulsion
ST-FNSF-like Q ~ 1 facility producing net energy by “burning” highly toxic long-live nuclear waste
With HTS magnet operating at 3.7T/7 MA Pfusion = 185 MW

## Slide 52
ELM Stabilization and Mitigation
Through application of lithium and 3-D fields
D.K. Mansfield, et al., JNM (2009)
ELMs stabilized with edge pressure modification with Li in NSTX
R. Maingi, et al., PRL (2009).
ELM mitigation with n=3
3-D fields (ELM Coils) in MAST
Increasing Type I ELM freq. by x 8 (900 Hz) has reduced heat flux
A. Kirk et al., NF (2013)