## Slide 1: Global MHD Mode Stabilization and Control for Tokamak Disruption Avoidance
57th Annual Meeting of the APS Division of Plasma Physics, Savannah, Georgia
11/18/15
V1.5
S.A. Sabbagh1, J.W. Berkery1, J.M. Bialek1, J.M. Hanson1, C. Holcomb2,
M. Austin3, D. Battaglia4, R.E. Bell4, K. Burrell3, R. Buttery3, N. Eidietis3,D.A. Gates4, S.P. Gerhardt4, B. Grierson4, I. Goumiri5, G. Jackson3, R. La Haye3, J. King3, E. Kolemen4, M.J. Lanctot2, M. Okabayashi4, T. Osborne3, Y.S. Park1, C. Rowley5, E. Strait3
1Department of Applied Physics, Columbia University, New York, NY, 2Lawrence Livermore National Laboratory, Livermore, CA, 3General, Atomics, San Diego, CA, 4Princeton Plasma Physics Laboratory, Princeton, NJ, 5Princeton University, Princeton, NJ

## Slide 2: Disruption avoidance is a critical need for future tokamaks; NSTX-U is focusing stability research on this
The new “grand challenge” in tokamak stability research
  Can be done! (JET: < 4% disruptions w/C wall, < 10% w/ITER-like wall)
    ITER disruption rate: < 1 - 2% (energy load, halo current); << 1% (runaways)
Strategic plan: utilize/expand stability/control research success
  Synergize and build upon disruption prediction and avoidance successes attained in present tokamaks
FESAC 2014 Strategic Planning report defined “Control of Deleterious Transient Events” highest priority (Tier 1) initiative
NSTX-U will allow focused research on disruption prediction and avoidance with quantitative measures of progress

## Slide 3
Sensor/predictor (CY available) | Control/Actuator (CY available)
Low frequency MHD (n=1,2,3): 2003 | Dual-component RWM sensor control (closed loop: 2008)
Low frequency MHD spectroscopy (open loop: 2005) | Control of βN (closed loop: 2007)
r/t RWM state-space controller observer (2010) | Physics model-based RWM state-space control (2010)
Real-time rotation measurement (2016) | Plasma rotation control (NTV rotation control open loop: 2003) (+NBI closed loop ~ 2017)
Kinetic RWM stabilization initial real-time model (2016-17) | Safety factor control (closed loop ~ 2016-17)
MHD spectroscopy (real-time) (in NSTX-U 5 Year Plan) | Upgraded 3D coils (NCC) (in NSTX-U 5 Year Plan)
Research in today’s presentation is part of NSTX-U’s evolving capabilities for disruption prediction/avoidance
  +New Disruption Event Characterization and Forecasting code, initial results

## Slide 4: Joint NSTX / DIII-D experiments and analysis gives unified kinetic RWM physics understanding for disruption avoidance
RWM Dynamics
  RWM rotation and mode growth observed
  No strong NTM activity
  Some weak bursting MHD in DIII-D plasma
    Alters RWM phase
  No bursting MHD in NSTX plasma
DIII-D (bN = 3.5)
NSTX (bN = 4.4)
DBpn=1(G)
fBpn=1(deg)
(arb)
Frequency (kHz)
t (s)
t (s)
amplitude
phase
Da
toroidal magnetics
rotation
growth
rotation
growth
amplitude
phase
Da
toroidal magnetics
S. Sabbagh et al., APS Invited talk 2014

## Slide 5: Evolution of plasma rotation profile leads to linear kinetic RWM instability as disruption is approached
DIII-D (minor disruption)
NSTX (major disruption)
MISK
unstable
stable
increasing time
gtwall
MISK
unstable
stable
increasing time
gtwall
Kinetic RWM stabilization occurs from broad resonances between plasma rotation and particle precession drift, bounce/circulating and collision frequencies
S. Sabbagh et al., APS Invited talk 2014

## Slide 6: Bounce resonance stabilization dominates for DIII-D vs. precession drift resonance for NSTX at similar, high rotation
|δWK| for trapped resonant ions vs. scaled experimental rotation (MISK)
DIII-D experimental rotation profile
NSTX experimental rotation profile
133103 @ 3.330 s
stable plasma
133776 @ 0.861 s
stable plasma
precession
resonance
bounce / circulating
resonance
precession
resonance
bounce / circulating
resonance
DIII-D
NSTX
- J. Berkery et al., PRL 104, 035003 (2010)
- S. Sabbagh, et al., NF 50, 025020 (2010)
- J. Berkery et al., PRL 106, 075004 (2011)
- S. Sabbagh et al., NF 53, 104007 (2013)
- J. Berkery et al., PoP 21, 056112 (2014)
- J. Berkery et al., PoP 21, 052505 (2014)
- J. Berkery et al., NF 55, 123007 (2015)
Some NSTX / MISK analysis references

## Slide 7: State space rotation controller designed for NSTX-U using non-resonant NTV and NBI to maintain stable profiles
Momentum force balance – wf decomposed into Bessel function states
NTV torque:
(non-linear)
yN
NBI, -NTV torque density (N/m2)
0.0
0.5
1.0
1.5
0.0
0.2
0.4
0.6
0.8
1.0
NBI and NTV torque profiles for NSTX-U
Momentum Actuators
New NBI
(broaden rotation)
3D Field Coil
(shape wf profile)
-NTV
Torque
NBI
Torque
(NSTX)

## Slide 8: State space rotation controller designed for NSTX-U using non-resonant NTV and NBI to maintain stable profiles
Momentum force balance – wf decomposed into Bessel function states
NTV torque:
(non-linear)
yN
NBI, -NTV torque density (N/m2)
0.0
0.5
1.0
1.5
0.0
0.2
0.4
0.6
0.8
1.0
NBI and NTV torque profiles for NSTX-U
Momentum Actuators
New NBI
(broaden rotation)
3D Field Coil
(shape wf profile)
NBI
Torque
(NSTX)
-NTV
Torque
NBI Torque
(NSTX-U)

## Slide 9: State space rotation controller designed for NSTX-U can evolve plasma rotation profile toward global mode stability
MISK
unstable
stable
increasing time
gtwall
I. Goumiri (Princeton student), S.A. Sabbagh (Columbia U.), C. Rowley (P.U.), D.A. Gates, S.P. Gerhardt (PPPL)
Recall: NSTX (major disruption)
Plasma rotation (kHz)
0
15
20
10
5
yN
0.0
0.2
0.4
0.6
0.8
1.0
NSTX-U (6 NBI sources and n = 3 NTV)
Steady-state reached in ~ 3tm
Marginally stable profile
Broader stable
profile
NBI, -NTV torque density (N/m2)
0.0
0.5
1.0
1.5
2.0
NBI
NTV

## Slide 10: With planned NCC coil upgrade, rotation controller can reach desired rotation profile faster, with greater fidelity
NSTX-U wf control with
  6 NBI sources
  Greater core NTV from planned NCC upgrade
Better performance
  Faster to target t ~ 0.5tm
  Matches target wf better
Marginally stable profile
Broader stable
profile
NBI
NTV
Plasma rotation (kHz)
0
15
20
10
5
NBI, -NTV torque density (N/m2)
0.0
0.5
1.0
1.5
2.0
0.0
0.2
0.4
0.6
0.8
1.0
yN
Planned NCC upgrade
Also, calculations show that NCC can allow RWM control up to ideal MHD wall limit

## Slide 11
Disruption Event Characterization And Forecasting Code (DECAF) yielding initial results (pressure peaking example)
PRP warnings
PRP
VDE
IPR
SCL
Detected at: 0.4194s
0.4380s
0.4522s
0.4732s
NSTX
142270
Disruption
10 physical events presently defined in code with quantitative warning points
  Builds on characterization work of de Vries
  Builds on warning algorithm of Gerhardt
  New code written (in Python) to be easily expandable, portable to other tokamaks
Example: Pressure peaking (PRP) disruption event chain identified by code
  (PRP) Pressure peaking warnings identified first
  (VDE) VDE condition subsequently found 19 ms after last PRP warning
  (IPR) Plasma current request not met
  (SCL) Shape control warning issued
Event chain
P.C. de Vries et al., Nucl. Fusion 51 (2011) 053018
S.P. Gerhardt et al., Nucl. Fusion 53 (2013) 063021

## Slide 12: Initial DECAF results detect RWM events when applied to dedicated 44 shot NSTX disruption database
Several events were detected for all shots
  DIS: Disruption occurred
  RWM: RWM event warning
  VDE: VDE warning (42 shots)
  IPR: Plasma current request not met
  LOQ: Low edge q warning
Very simple RWM event criteria
  RWM BPn=1 lower sensor amplitude used
  Simple criterion + no threshold optimization yet  “false positive” rate is high; adjust criteria to reduce it
Code already sees common disruption event chains
  (event)VDESCLIPR occurs in 52% of the shots
RWM event warning timing
(simple criterion, not optimized)
Within 100 ms of DIS
(64%)
Before 100 ms of DIS
(36%)
VDE
SCL
IPR
Common event chain
(event)
Also see poster by M. Parsons PP12.00118 (Wed 2 pm) for related work on supervised machine learning for disruption prediction

## Slide 13: In addition to active mode control, the NSTX-U RWM state space controller will be used for real-time disruption warning
RWM state space controller used for RWM control in NSTX - long pulse plasmas reached high stability parameters bN = 6.4, bN /li = 13
S. Sabbagh et al., Nucl. Fusion 53 (2013) 104007
RWM Sensor Differences (G)
dBp180
100
200
0
-100
t (s)
0.56
0.58
0.60
0.62
RWM
Measurement
Controller
(observer)
The controller “observer” produces a physics model-based calculation of the expected sensor measurements – a real-time synthetic diagnostic
If the real-time synthetic diagnostic poorly matches the measured sensor data, a real-time disruption warning signal can be triggered
  Technique will be assessed using the DECAF code
RWM sensors

## Slide 14: Global MHD mode stabilization understanding and control will synergize in NSTX-U for disruption avoidance
Physics Understanding
  Unification of DIII-D / NSTX experiments and analysis gives improved RWM understanding for disruption avoidance
  Complementarity found: at similar high rotation, kinetic RWM stabilization physics is dominated by bounce orbit resonance in DIII-D, and by ion precession drift resonance in NSTX
  Disruption Event Characterization and Forecasting code initial results identify RWM events and disruption event chains
Stability Control
  Rotation profile control has potential to steer away from unstable profiles
  Model-based active RWM state-space controller can also be used as synthetic diagnostic for disruption warning
  Further improvements to rotation profile control, active mode control possible with planned NCC 3D coil upgrade

## Slide 15
Supporting slides follow

## Slide 16: Active RWM control design study for proposed NSTX-U 3D coil upgrade (NCC coils) shows superior capability up to ideal wall limit
NCC 2x12 with favorable sensors, optimal gain
NCC 2x6 odd parity, with favorable sensors
Full NCC coil set allows control close to ideal wall limit
  NCC 2x6 odd parity coils: active control to bN/bNno-wall = 1.58
  NCC 2x12 coils, optimal sensors: active control to bN/bNno-wall = 1.67
NCC (plasma facing side)