## Slide 1: Results of using the NSTX-U plasma control system for scenario development
58th APS-DPP , Results of using the NSTX-U Plasma Control System for scenario development, M.D. Boyer, 11/01/16 1
M.D. Boyer1, D.J. Battaglia1, D.A. Gates1, S. Gerhardt1,
J. Menard1, D. Mueller1, C.E. Myers1,
J. Ferron2, S. Sabbagh3, F. Scotti4
1PPPL, 2General Atomics, 3Columbia University, 4LLNL
58th Annual Meeting of the APS Division of Plasma Physics Oct 31 – Nov 4, 2016, San Jose, California

## Slide 2: Advanced control will be required for achieving many of the research goals of NSTX-U
High-beta operation and non- inductive scenarios
  Maximizing elongation
  Shaping and profile control
Heat flux handling
  X-point, strike point control
  Snowflake control
Disruption detection/mitigation
  Real-time plasma monitoring
  Event-handling
This talk will cover:
Vertical control
Shape control
Plasma shutdown handler
Near-term plans

## Slide 3: Increased aspect ratio of NSTX-U makes vertical control more challenging
Added sensors and noise rejection to improve estimation of vertical position/velocity
Sensor weights determined by least squares fit to IpZp
of free boundary equilibria
Filtering removes noise, power supply ripple, and spurious signal due to MHD events
Mueller
NP10.00003

## Slide 4: Scenarios similar to NSTX were achieved at higher aspect ratio using new vertical position/velocity estimator
NSTX-U (10 run weeks) NSTX (10 years)

## Slide 5: Scenarios similar to NSTX were achieved at higher aspect ratio using new vertical position/velocity estimator
NSTX-U (10 run weeks) NSTX (10 years)
Vertical control tuned at very high li

## Slide 6: Scenarios similar to NSTX were achieved at higher aspect ratio using new vertical position/velocity estimator
Settled into an L-mode scenario used for many commissioning activities
NSTX-U (10 run weeks) NSTX (10 years)
Vertical control tuned at very high li
L-mode flattop

## Slide 7: Scenarios similar to NSTX were achieved at higher aspect ratio using new vertical position/velocity estimator
Settled into an L-mode scenario used for many commissioning activities
H-mode scenarios enabled access to lower li, higher kappa
L-mode flattop
NSTX-U (10 run weeks) NSTX (10 years)
H-mode flattop
Vertical control tuned
at very high li

## Slide 8: Scenarios similar to NSTX were achieved at higher aspect ratio using new vertical position/velocity estimator
Vertical control tuned at very high li
Settled into an L-mode scenario used for many commissioning activities
Vertical stability limit
not reached in the H-modes
room to grow.
H-mode scenarios enabled access to lower li, higher kappa
NSTX-U (10 run weeks) NSTX (10 years)
L-mode flattop
H-mode flattop

## Slide 9: Scenarios similar to NSTX were achieved at higher aspect ratio using new vertical position/velocity estimator
Vertical control tuned at very high li
Settled into an L-mode scenario used for many commissioning activities
Vertical stability limit
not reached in the H-modes
room to grow.
H-mode scenarios enabled access to lower li, higher kappa
NSTX-U (10 run weeks) NSTX (10 years)
L-mode flattop
H-mode flattop
Future goal

## Slide 10: rtEFIT/ISOFLUX updated to enable precise, reproducible control of shape, x-points, drsep, and strikepoints
Real-time EFIT upgraded to more closely match offline magnetics-only EFIT:
  Enable more precise x-point, snowflake control
  65x65 grid size
  Vessel current fitting
  Enabled by use of multiple cores to meet calculation time requirements
 Only single core used previously
X-point and strikepoint control with PF1A and PF2
– Used multi-input-multi-output control structure to account for actuator coupling
 Improves transient response
t=0.399s t=0.498s t=0.697s t=0.799s
10
PF2U PF1AU
PF1AL
PF2L

## Slide 11: rtEFIT/ISOFLUX updated to enable precise, reproducible control of shape, x-points, drsep, and strikepoints
t=0.399s t=0.498s t=0.697s t=0.799s
PF2U PF1AU
PF1AL
PF2L
0.3
0.4
0.7
0.8
0.9
0.7
1.1
1
0.9
0.8
Good tracking of step requests in strikepoint radial location
– Fast response, little overshoot, no oscillations
203879
0.5 0.6
Time [s]
Outer strikepoint R [m]
Lower Strike point
Upper Strike point
Target

## Slide 12: rtEFIT/ISOFLUX updated to enable precise, reproducible control of shape, x-points, drsep, and strikepoints
Strikepoint tracking results confirmed by peak of CII emission
t=0.399s t=0.498s t=0.697s t=0.799s
PF2U PF1AU
PF1AL
PF2L
[F. Scotti]

## Slide 13: A method for inner gap control (a challenge for ST’s) has also been tested
1.2
1.01
1.015
1.02
1.025
1.03
0.4 0.6 0.8 1
Time [s]
Upper outer gap R target [m]
0.4
1
1.2
0.6
0.62
0.64
0.66
0.68
0.7
1.035 0.72
0.6 0.8
Time [s]
X−point R target [m]
0.4
1
1.2
0
0.02
0.04
0.06
0.08
0.6 0.8
Time [s]
Inner gap [m]
204737 (control off)
204742 (control on)
Target
No way to independently control the inner gap
  No shaping coils on inboard side, available coils already assigned…
Approach:
  Automatically adjust other shaping parameters based on operator provided weight matrix to achieve desired inner gap
Inner gap
204737 (control off)
204742 (control on)
Upper outer gap R target
 | X-point R target | 
 |  | 204737 (control off) 204742 (control on)

## Slide 14: State-machine-based automated ramp-down now used routinely to limit forces and avoid disruptions
Plasma control system detects loss of control
  OH near max current
  Vertical oscillations exceed threshold
  ABS (Ip - Ip request ) too
large
– Locked mode detected
Feedback control
switches to new “states” that attempt to gently end the discharge
P
I [kA]
IP Request
(including asynchronous transition to rampdown)
ZP(dZP/dt) threshold
t=0.705
m
“State” |  |  |  |  |  | 
Nor | al |  |  |  |  | 
Time [s]
ZP(dZP/dt) [m2/s]
Gerhardt NP10.00005

## Slide 15: State-machine-based automated ramp-down now used routinely to limit forces and avoid disruptions
P
I [kA]
IP Request
(including asynchronous transition to rampdown)
ZP(dZP/dt) threshold
Plasma control system detects loss of control
  OH near max current
  Vertical oscillations exceed threshold
  ABS (Ip - Ip request ) too
large
– Locked mode detected
Feedback control
switches to new “states” that attempt
t=0.705 t=0.793
“State” |  |  |  |  |  | 
 | Fast IP R | ampdo | wn |  |  | 
Nor | al |  |  |  |  | 
ZP(dZP/dt) [m2/s]
m
to gently end the discharge
Gerhardt NP10.00005
Time [s]
15

## Slide 16: State-machine-based automated ramp-down now used routinely to limit forces and avoid disruptions
P
I [kA]
IP Request
(including asynchronous transition to rampdown)
ZP(dZP/dt) threshold
“State” |  |  |  |  |  | 
 | Fast IP R | ampdo | wn |  |  | 
Nor | al |  |  |  |  | 
Plasma control system detects loss of control
  OH near max current
  Vertical oscillations exceed threshold
  ABS (Ip - Ip request ) too
large
– Locked mode detected
Feedback control switches to new
t=0.705 t=0.793
t=0.849
ZP(dZP/dt) [m2/s]
“states” that attempt to gently end the discharge
Gerhardt NP10.00005
m
Time [s]

## Slide 17: State-machine-based automated ramp-down now used routinely to limit forces and avoid disruptions
P
I [kA]
IP Request
(including asynchronous transition to rampdown)
ZP(dZP/dt) [m2/s]
ZP(dZP/dt) threshold
Plasma control system detects loss of control
  OH near max current
  Vertical oscillations exceed threshold
  ABS (Ip - Ip request ) too
large
– Locked mode detected
Feedback control switches to new
t=0.705 t=0.793
t=0.849
t=0.897
“State” | Ins | ufficien | t IP |  |  | 
 | Fast IP R | ampdo | wn |  |  | 
Nor | al |  |  |  |  | 
“states” that attempt to gently end the discharge
Gerhardt NP10.00005
m
Time [s]

## Slide 18: New plasma control capabilities enabled rapid development of high-performance plasmas on NSTX-U
Early scenario development enabled by improvements in vertical control, and shape control
  Commissioned tools to facilitate experiments (strikepoint/inner gap control)
New event handler for reducing stress on machine and facilitating disruption detection/avoidance/mitigation studies
Poised to support future scientific goals with new capabilities:
  Snowflake divertor control for studying heat flux management
 Algorithm tested in hardware-in-the-loop simulations
18
– Stored energy and li control, rotation and current profile control for high-
beta and non-inductive scenario development
 Approaches tested in TRANSP simulations, PCS algorithms being implemented