## Slide 1: Disruption Event Characterization and Forecasting in NSTX-U
58th Annual Meeting of the APS Division of Plasma Physics, San Jose, California
11/1/16
V1.6
S.A. Sabbagh1, J.W. Berkery1, J.M. Bialek1, Y.S. Park1, R.E. Bell2, M.D. Boyer2, S.P. Gerhardt2, C. Myers2 , J.D. Riquezes3
1Department of Applied Physics, Columbia University, New York, NY, 2Princeton Plasma Physics Laboratory, Princeton, NJ, 3University of Michigan, Ann Arbor, MI
*This work supported by the US DOE contracts DE-AC02-09CH11466 and DE-FG02-99ER54524

## Slide 2: Disruption event chain characterization capability started for NSTX-U as next step in disruption avoidance plan
Approach to disruption prevention
  Identify disruption event elements and chains
  Predict events in disruption chains
  Cue disruption avoidance systems to break event chains
    Attack events at several places with active control
  Synergizes and builds upon both physics understanding, control successes of NSTX
t
Disruption prediction/avoidance framework
(from DOE Report on Transients in Tokamak Plasmas (2015))

## Slide 3
Disruption Event Characterization And Forecasting Code (DECAF) yielding initial results
PRP event
PRP
VDE
IPR
SCL
Detected at: 0.4194s
0.4380s
0.4522s
0.4732s
NSTX
142270
Disruption
10 physical events presently defined in code with quantitative warning points
  Builds on characterization work of de Vries
  Builds on warning algorithm of Gerhardt
  New code written (in Python) to be easily expandable, portable to other tokamaks (reads NSTX, NSTX-U, DIII-D data)
Example: Pressure peaking (PRP) disruption event chain identified by code
  (PRP) Pressure peaking warnings identified first
  (VDE) VDE condition subsequently found 19 ms after last PRP warning
  (IPR) Plasma current request not met
  (SCL) Shape control warning issued
Event chain
P.C. de Vries et al., Nucl. Fusion 51 (2011) 053018
S.P. Gerhardt et al., Nucl. Fusion 53 (2013) 063021

## Slide 4: DECAF results detect disruption chain events when applied to dedicated 44 shot NSTX RWM disruption database
Several events detected for all shots
  RWM: Resistive wall mode
  SCL: Loss of shape control
  IPR: Plasma current request not met
  DIS: Disruption occurred
  LOQ: Low edge q warning
  VDE: VDE warning (40 shots)
Other Events
  PRP: Pressure peaking warning
  LON: Low density warning
  GWL: Greenwald limit
  LTM: Locked tearing mode
Many occur after RWM

## Slide 5: DECAF analysis is finding common disruption event chains
Event chains with RWM and VDE (52.3%)
  Related chains
    RWM  VDE  SCL  IPR  DIS
    RWM  SCL  VDE  IPR  DIS
    VDE  RWM  SCL  IPR  DIS
    VDE  RWM  IPR  DIS  SCL
    RWM  SCL  VDE  GWL  IPR  DIS
Disruption event chains w/o VDE (11.4%)
New insights being gained
  Chains starting with GWL are found that show rotation and bN rollover before RWM (6.8%)
    GWL  VDE  RWM  SCL  IPR  DIS
    GWL  SCL  RWM  IPR  DIS
Disruption event chains with RWM (44 shot database)
Event chains with RWM and VDE
(52.3%)
No
VDE
(11.4%)
Other
(29.5%)
GWL start
(6.8%)
NSTX

## Slide 6: DECAF analysis yields time relation of chain events when applied to NSTX RWM disruption database
VDE
Most RWM events near major disruption
  61% of RWM occur within 20 tw of disruption time (tw = 5 ms)
  Earlier RWM events NOT false positives – cause large decreases in bN with recovery (minor disruptions)

## Slide 7: Global mode stability forecasting: DECAF initial reduced kinetic MHD model tests well on unstable RWM database
gtw contours vs. ν and wE
gtw
Increasing time
ideal
ideal + kinetic
unstable
stable
Norm. growth rate vs. time
gtw
139514
disruption
predicted instability
Predicted instability statistics
Chart: 
Stable
(16%)
Instability within 100 ms of minor
disruption
(33%)
Instability < 320 ms
before disruption
(44%)
(7%) False
positives
84% predicted unstable (unoptimized)
7% false positives
See J. Berkery invited talk YI2.00005 (Fri 11:30 AM)
Reduced model guided by full kinetic RWM stability model

## Slide 8: Essential new step for DECAF analysis of general tokamak data: Identification of rotating MHD (e.g. NTMs)
See JP10.00057 J. Riquezes (Tue PM)
Magnetic spectrogram of rotating MHD
138854
Mode frequency vs. time (zoomed in)
lock
Mode frequency
bifurcation
DECAF FFT analysis determines mode frequency, bifurcation, and mode locking
Initial mode locking prediction model developed
frequency (kHz)

## Slide 9: DECAF rotating MHD analysis identifies the state of the modes found
Magnetic signal / analysis (mode locking / unlocking)
1 = mode rotating
-1 = mode locked
0 = No mode
DECAF mode status
204202
mode lock
Frequency vs. time
t (s)
n = 1 mode
frequency (kHz)
4
0
8
12
16
t (s)
0.68
0.70
0.72
0.74
0.76
0.78
B (G)
20
10
0
-10
-20
-30
0
-2
-1
1
2
0.66
0.70
0.74
0.78
NSTX-U

## Slide 10: DECAF replicates the triggers found in new real-time plasma shutdown capability of NSTX-U
Important capability of DECAF: compare analysis using offline vs. real-time data
Plasma Shutdown Handler conditions are analogous to DECAF events
  Control system loss of vertical control  DECAF
DECAF comparison: VDE event
  Matches Plasma Control System when r/t signal is used (1 criterion)
  VDE event 13 ms earlier using offline EFIT signals (3 criteria: Z0, dZ0/dt, Z0 x dZ0/dt)
VDE
(for shutdown handler: see NP10.00005 S. Gerhardt (Wed AM)
PCS state
Z0 (m)
Ip (MA)

## Slide 11: Disruption event characterization, forecasting, and control are synergizing in NSTX-U for disruption avoidance
Physics Understanding
  Disruption Event Characterization and Forecasting code (DECAF) development continues: defining / forecasting disruption event chains
  Recent DECAF development includes initial kinetic RWM forecasting, and initial identification of rotating MHD modes, bifurcation, and locking
Stability Control
  An arsenal of control tools will be available on NSTX-U for disruption avoidance (e.g. rotation, q profile control; RWM state-space controller)

## Slide 12: Supporting Slides Follow

## Slide 13: Disruption avoidance is a critical need for future tokamaks; NSTX-U is focusing stability research on this
The present “grand challenge” in tokamak stability research
  Can be done! (JET: < 4% disruptions w/C wall, < 10% w/ITER-like wall)
    ITER disruption rate: < 1 - 2% (energy load, halo current); << 1% (runaways)
Strategic plan: utilize/expand stability/control research success
  Synergize and build upon past MHD stability/control success (don’t just repeat!)
  Utilize this knowledge / evolve into disruption prediction and avoidance research
FESAC 2015 DOE Transient Events report: Disruption Predicition, Avoidance, Mitigation a Tier 1 (highest priority) initiative
Research at NSTX-U producing focused approach on disruption prediction and avoidance with quantitative measures of progress
s

## Slide 14: Global mode stability forecasting: build from success of drift kinetic theory modification to MHD as a model
Kinetic modification to ideal MHD
Stability depends on
  Trapped / circulating ions, electrons
  Collisionality; Energetic particles
  Integrated wf profile matters!!! : broad rotation resonances in dWK
ion gyro-orbit
and trajectory
(Fig. adapted from R. Pitts et al., Physics World (Mar 2006))
Trapped particle orbit precession drift
Trapped particle
orbit
Trapped orbit 2D
projections
plasma integral over particle energy
collisionality
wf profile (enters in wE)
precession drift
bounce
Just some references:
B. Hu, R. Betti, et al., PoP 12 (2005) 057301
J. Berkery et al., PRL 104 (2010) 035003
S. Sabbagh, et al., NF 50 (2010) 025020
J. Berkery et al., PRL 106 (2011) 075004
J. Berkery et al., NF 55 (2015) 123007