## Slide 1
Gas Puff Imaging Diagnostic on NSTX-U
S.J. Zweben1, F. Scotti2, D.P. Stotler1,
A. Diallo1, N. Mandell1, J.L. Terry3, W. Han3
PPPL, Princeton NJ USA
LLNL, Livermore CA USA
MIT, Cambridge MA USA
Abstract NP10-00027
Wednesday morning, Nov. 2, 2016
This work was supported by USDOE Contracts #DE-AC02-09CH11466, DE-SC0014264, and DE-AC52-07NA27344.

## Slide 2
Abstract
The first results and plans for the gas puff imaging (GPI) diagnostic on NSTX-U will be described. The GPI optical efficiency has been improved by about x10 using a new fiber bundle and interference filter, and the new optics has a zoom lens which can potentially resolve turbulence below the ion-gyroradius scale. Experiments are planned to study high-k edge turbulence, correlations of edge turbulence with the SOL heat flux width, and the trigger mechanism of the L-H transition. A second fast camera is planned to view the GPI gas cloud from across the machine, which can potentially measure the field line pitch by simultaneously viewing individual field-aligned blob filaments in the radial vs. poloidal (GPI) and toroidal vs. poloidal (second camera) directions. An incoming collaboration from MIT will bring a 9x10 pixel APD-based detector array from Alcator C-Mod to NSTX-U, initially for faster and more sensitive imaging of the existing GPI gas puff. New results and further diagnostic plans will be described.

## Slide 3
Gas Puff Imaging (GPI) Diagnostic on NSTX
• D2 gas puffed from GPI manifold on outer wall above midplane
• Da light emission from gas puff viewed from along local B field
• Fluctuations in Da light emission interpreted as edge turbulence
GPI gas
puffer
GPI optical
viewport
Da emission
from puff
RF limiter
B field

## Slide 4
Typical GPI Images from NSTX (2010 data)
separatrix
RF antenna
shadow
GPI gas
injector
L-mode
H-mode
poloidal
80 pixels
30 cm
radial
64 pixels
24 cm
• Exposure time/frame = 2.1 µsec/frame @ 400,000 frames/sec

## Slide 5
GPI Optics Improvements for NSTX-U
These upgrades were implemented for the 2016 run:
• New Schott coherent fiber bundle, 8x10 mm and 9 ft. long
(improves signal x4 due to browning of prior bundle)
• New Da interference filter with wider bandwidth 9 nm FWHM
(~80% transmission vs. prior ~35%)
• New optical zoom lenses to improve GPI spatial resolution
(manual zoom from ~0.5 cm to ~0.1 cm at gas cloud)
=> ~10x larger GPI signal should allow reduced GPI gas puff
rate and better space and/or time resolution

## Slide 6
Zoom Lens for Improved Spatial Resolution
Front lens changed from
25 mm to 8-48 mm zoom
Camera lens changed from
25 mm to 8-48 mm zoom
2010
front
end
lens
2016
front
end
lens

## Slide 7
Limitation due to B Field Angle Alignment
• Maximum GPI optical zoom has ~ 1 mm spatial resolution
• Could resolve structure kpol ri ~ 1 at edge (Ti=100 eV, B=1 T)
• But misalignment of GPI view with B can “smear” resolution
smearing due to parallel length of
GPI cloud: Δsmear ~ LII,cloud tan θB
e.g. for θ ~ 1º, LII,cloud ~ 15 cm,
Δsmear ~ 0.3 cm
Typical misalignment
angles to local B field
θB ~ 0º perfect alignment (no smearing)
θB ~ 8º large misalignment (2.0 cm smearing)
θB ~ 2.7º slight misalignment (0.7 cm smearing)
.
Arrows are misalignment
angles to the local B field
.
24x30 cm
GPI field
of view
139501
0.515 sec

## Slide 8
Present GPI Configuration for 2016 Run
• Started with same GPI view as NSTX but with improved optics
• No gas puff available in 2016 run due to engineering delays
• Used Da filter to view background edge light at 100 kHz
• Zoom lens had vigneting in 24x30 cm view (as expected)
good data on edge turbulence in background Da light for
  whole duration of ~ 100 shots (but with no GPI puff)
good data on radial Da profile for edge neutral density
  measurement (for comparison with ENDD)

## Slide 9
Present GPI Results from 2016 Run
• Edge turbulence in background Da looked about as expected
large fluctuation levels at ~5 cm scale length in L-mode
quiet band of Da emission during H-mode periods
• But difficult to analyze due to lack of GPI spatial localization
L-mode
L-mode
L-mode
H-mode

## Slide 10
Planned and Possible GPI Upgrades
Planned
• APD array from C-Mod to improve signal/noise and bandwidth
• Second Phantom 710 camera to view GPI cloud from the side
• Helium line ratio measurement of edge Te and ne profiles
Possible
• Additional GPI view(s) for measuring 3-D filament structure
• Better collimated gas manifold for higher spatial resolution
• Remote control of GPI pan/zoom for small-scale structure

## Slide 11
Incoming GPI Collaboration from MIT

## Slide 12
Configuration of MIT APD Array for GPI

## Slide 13
Planned Side View of GPI Gas Puff Cloud
• Compare cloud shape with DEGAS 2
• Correlate filaments with GPI images
• Find local B field line angle => q(r)
assuming filaments aligned with B
• Add another gas puffer in field of
view to check B-field alignment
Edge filaments
in GPI cloud
Using the Phantom 710 camera previously used for GPI at C-Mod
GPI optical
viewport
B

## Slide 14
Planned Helium Line Ratio Measurement
• The GPI view can be used to measure neutral helium line ratios
to determine radial profiles of Te and ne in edge (proposed
by RFX-mod/Padova and Wisconsin)
• Initial evaluation of expected helium line signals looks good for measurements at > 1 kHz (Burgos et al, Phys. Plasmas 2016)
• These profiles will be useful for the interpretation of GPI signals,
and increasing frequency range up to ~100 kHz may be possible with large helium gas puffs (Agostini et al, RSI 2015)
• Main issues are possible perturbation effect of helium gas puff,
and self-absorption of helium lines in a large gas puff

## Slide 15
Possible Additional GPI Views
divertor plate surface
X-point region
inner wall
4) ~ 2 m along B from GPI
5) ~ 5 m along B from (4)
1
2
3
4
5
• Needed to evaluate parallel structure/dynamics of turbulence
• Each new view will need a new gas puffer a new fast camera

## Slide 16
Possible Improvement to Gas Manifold
• Present GPI gas manifold has holes 1 mm diam. x 1 mm deep,
which should emit gas with a wide ~ cosine dependence
• TEXTOR GPI manifold has holes 0.5 mm diam. x 15 mm deep,
which emits gas with ~20º FWHM angular dependence
• New manifold could significantly improve spatial resolution of
GPI, due to shorted parallel length along cloud (see p. 7)
TEXTOR manifold (measured)
NSTX manifold (estimated)
(Shesterikov et al, RSI 2013)

## Slide 17
Remote Control of GPI Zoom and Pan
• Present GPI zoom must be adjusted by hand in test cell, and the front-end optics removed to adjust the tilt angle (pan)
• This makes alignment with local B field for measuring small-
scale turbulence structure very difficult (can try to adjust
plasma to match pre-set zoom and pan)
• Zoom lenses and front-end mirror could be remotely controlled
between shots for more efficient measurements
• Main issues are exposure of stepper motors to magnetic fields
(air motors ?), and accuracy/reproducibility of the settings

## Slide 18
Planned GPI Experiments on NSTX-U
18
=> these can be done with existing GPI hardware:
• Search for small-scale edge turbulence structure at kpolri ~ 1
(w/Ren, Guttenfelder)
• Correlation of edge turbulence with heat flux SOL width and
XGC-1 results (w/ Gray, Chang)
• Continue study of L-H transition (w/Stoltfus-Dueck)
• Continue correlation of GPI with divertor plate turbulence
(w/Soukhanovskii)

## Slide 19
• Measure turbulence up to ~ 1 MHz with APDs
• Measure turbulence far inside separatrix with APDs
• Measure edge q(r) from GPI + side view filaments
• Compare GPI gas cloud side view with DEGAS 2
• Measure edge Te and ne profiles with helium line ratios
also:
- Continue study of blobs, GAMs, zonal flows
  - Search for RF-SOL interaction dynamics
  Search for effects of application of 3-D fields
  Study effects of divertor geometry and detachment
  Study coherent edge modes (QCM, EHO, KBM, etc)
Planned GPI Studies on NSTX-U
=> these require upgraded GPI hardware:

## Slide 20
Please ask Filippo Scotti (next poster) for further information,
or sign up for a copy of this poster: