## Slide 1: Generation of Non-Inductive H-Mode Plasmas with 30 MHz Fast Wave Heating in NSTX-U*
G. Taylor1, N. Bertelli1, S. P. Gerhardt1, J. C. Hosea1, D. Mueller1, R. J. Perkins1, F. M. Poli1, R. Raman2, J. R. Wilson1
1Princeton Plasma Physics Laboratory, Princeton, NJ 08543, USA
2University of Washington, Seattle, WA 98195, USA
Paper NP10.00035
APS-DPP Meeting
San Jose, California
November 2, 2016
* This work is supported by USDOE Contract No. DE-AC02-09CH11466

## Slide 2
Introduction

## Slide 3: Developing fully non-inductive (NI) plasmas is a NSTX-U 10-year research goal
In a Fusion Nuclear Science Facility based on a spherical tokamak the plasma current (Ip) needs to be initiated, ramped-up and sustained with little or no central solenoid field
30 MHz fast wave (FW) heating can play a critical role in NSTX-U supporting non-inductive (NI) Ip ramp-up to 300 kA:
  FW heating effectively heats low density plasmas with Ip ≤ 300 kA, whereas neutral beam injection (NBI) requires Ip ≥ 300 kA to ensure fast ion confinement and to maintain shine through below 50%
Experiments on NSTX-U aim to couple ~ 3 MW of FW power into Ip ~ 300 kA plasmas, achieving NI current fraction, fNI ≥ I
This poster presents the first results from time-dependent transport simulations of these FW-heated Ip ~ 300 kA plasmas

## Slide 4
NSTX-U facility includes a 6 MW, 30 MHz FW heating system previously used on NSTX
30 MHz FW System
1st NBI
2nd NBI
NSTX-U

## Slide 5: NSTX-U performance will far exceed NSTX with regard to maximum Ip, BT and I2t*
NSTX 30 MHz FW heating was operated in the high harmonic FW (HHFW) regime, with RF damping on up to 11wci at BT(0) = 0.55 T
NSTX-U 30 MHz FW heating will operate in the Medium Harmonic FW (MHFW) regime, with RF damping on up to 5wci at BT(0) = 1 T
* J. E. Menard et al., Nucl. Fusion 52 (2012) 083015
Parameter | NSTX (Max.) | FY2016 NSTX-U Operations Achieved | FY2017 NSTX-U Repair PF | FY2018 NSTX-U Operations | NSTX-U Ultimate Goal
IP (MA) | 1.2 | ~1.1 | - | 2.0 | 2.0
BT (T) | 0.55 | ~ 0.65 | - | 1.0 | 1.0
Allowed TF I2t (MA2s) | 7.3 | 80 | - | 160 | 160

## Slide 6
Development of NI Plasmas Heated by 30 MHz FW Power

## Slide 7: Experiments in NSTX-U will develop NI start-up, ramp-up and plasma sustainment separately
NBI and Bootstrap current sustainment
IP Target [kA]
Time
30 MHz FW heating
NBI and FW heating &
Bootstrap current ramp-up
CHI, 28 GHz EC/EBW and/or plasma gun startup
~ 150
~ 300
~ 750
NSTX-U NI Plasma Strategy
H-mode

## Slide 8
Time-dependent modeling of NSTX-U NI Ip ramp-up predict that NBI is not suitable for Ip ≤ 300 kA
TRANSP modeling of NI plasma started with NBI predicts very high shine-through during the first 100 ms when Ip ≤ 300 kA
Simulations suggest that an additional source of current is needed in the first 200 ms of a NI plasma*
FW power can effectively heat plasma at low density
FW heating can be through both the electron and ion channels, depending on the antenna phasing**
Plan to use ~3 MW of 30 MHz FW power to ramp Ip to 300 kA
** N. Bertelli et al., AIP Conf. Proc. 1580 (2014) 310
* F. M. Poli et al., Nuclear Fusion 55 (2015) 123011

## Slide 9: To support development of FW-heated Ip ramp-up in NSTX-U first demonstrate fully NI Ip ~ 300 kA discharges
Couple 30 MHz FW heating as early as possible into the Ip flattop
Ramp FW power as fast as possible to maximum FW power, preferably in < 50 ms to generate early H-mode transition
Use k// = - 8 m-1 current drive phasing
NI current drive via both direct FW current drive and bootstrap current generated through FW heating
First experiment was run in NSTX during 2010 campaign:
  Achieved fNI ~ 0.7 in an Ip = 300 kA H-mode plasma sustained for several 100 ms using only Prf ~ 1.4 MW (next slide)
Extend scenario to higher Prf at higher BT(0) in NSTX-U to achieve sustained Ip = 300 kA H-mode plasma with fNI ≥ 1

## Slide 10
FW heating of an Ip = 300 kA plasma in NSTX resulted in rapid increase of Te(0) and fNI > 70% H-mode*
Notably the Bootstrap current contribution was greater than that from direct RF current drive
50% fluctuations in bootstrap current during H-mode phase due to fluctuations in pressure profile
* G. Taylor et al., Phys. Plasmas 19 (2012) 042501
  1.4 MW of 30 MHz, k// = 8 m-1 HHFW power rapidly increased Te(0) from 250 eV to 2 keV and triggered an H-mode transition (NSTX shot 138506)

## Slide 11
nf = -21
nf = -12
nf = -21
nf = -12
NSTX BT(0) = 0.55 T NSTX-U BT(0) = 1 T
* N. Bertelli et al., Nuclear Fusion 54 (2014) 083004
Modeling predicts low 30 MHz power losses over a wider range of SOL densities at higher BT(0) in NSTX-U
AORSA modeling predicts RF power losses to SOL increase substantially above the FW cutoff density, consistent with experimental trends*
SOL power losses versus SOL density in front of antenna. Vertical lines represent values of density for which the FW cutoff starts to “open” in front of the antenna

## Slide 12
TRANSP Modeling of Ip = 300 kA Plasmas Heated by 30 MHz FW Power

## Slide 13
TRANSP time-dependent transport simulation being used to model FW heated NI NSTX-U plasmas
Simulations ramped ne(0) to 1.15x1013 m-3, between 0 and 100 ms
ne(0) is similar to NSTX shot 138506, but didn’t attempt to reproduce the density profile of that shot
An H-mode transition was imposed at 100 ms by transitioning to a more flat density profile

## Slide 14
MultiMode MMM7.1* transport model used for ions and electrons:
  MMM7.1 gave the best fit to experimental electron temperature profile for NBI-heated Ip = 300 kA NSTX plasmas, compared to Coppi-Tang or current diffusive ballooning mode model (CDBM)**
Ip flat top started at 100 ms, FW power turned on at 100 ms and ramped to full power in 40 ms
  FW heating and current drive calculated with TORIC full wave spectral code+
  Used k// = 8 m-1 current drive antenna phasing
Simulations for BT(0) = 0.5, 0.75 and 1.0 T and Prf = 2, 3 and 4 MW
TRANSP simulated FW heating of an Ip = 300 kA plasma with BT(0) between 0.5 and 1 T and Prf up to 4 MW
* T. Rafiq et al., Phys. Plasmas 20 (2013) 032506
** F. M. Poli et al., Nucl. Fus. 55 (2015) 123011
+ M. Brambilla, Plasma Phys. Control. Fusion 44 (2002) 2423
Ip = 300 kA NBI-heated NSTX plasma

## Slide 15
Simulation for BT(0) = 0.5 T NSTX-U plasma predicts
fNI ≥ 1 is only achievable with Prf ~ 4 MW
At 400 ms:
RF current drive = 130 kA
Bootstrap current = 60 kA
Increasing Prf to 4 MW yields a NI current of 280 kA

## Slide 16
Simulation for BT(0) = 0.75 T NSTX-U plasma predicts
fNI ≥ 1 probably achievable with Prf ~ 3 MW
At 400 ms:
RF current drive = 205 kA
Bootstrap current = 70 kA
Increasing Prf to 4 MW yields a NI current of 400 kA

## Slide 17
Simulation for BT(0) = 1.0 T NSTX-U plasma predicts
fNI ≥ 1 is achievable with Prf ~ 3 MW
At 400 ms:
RF current drive = 220 kA
Bootstrap current = 80 kA
Increasing Prf to 4 MW yields a NI current of 410 kA

## Slide 18
For the same Prf, fNI improved significantly when BT(0) was increased from 0.5 to 0.75 T
Much smaller improvement in fNI when BT(0) was increased from 0.75 T to 1 T, compared to fNI increase when BT(0) was increased froim 0.5 to 0.75T
When Prf was increased from 2 to 4 MW, the relative improvement in fNI became smaller when BT(0) was increased from 0.75 T to 1 T

## Slide 19
Simulations using MMM7.1 transport model show significant disagreement with NSTX shot 138506
Simulation of an Ip = 300 kA plasma using MMM7.1 transport model with similar BT(0) and Prf to NSTX shot 138506 predicts much lower Te(0) and central plasma pressure than was obtained in experiment
Simulation using MMM7.1 transport model also predicts much lower FW current drive and bootstrap current than attained in shot 138506

## Slide 20
Simulation with 5 times lower electron diffusivity gives better match to Te(0) in NSTX shot 138506
Simulation with 5 times lower electron diffusivity better matches Te(0) and central pressure on NSTX shot 138506, but poorer match at r/a ~ 0.5
Appears core transport in the FW-heated Ip = 300 kA discharge is much lower than in the NBI-heated Ip = 300 kA discharge

## Slide 21
Simulation with BT(0) = 0.5 T, Prf = 3 MW and 5 times lower electron diffusivity predicts fNI ~ 1
At 400 ms:
RF current drive = 160 kA
Bootstrap current = 105 kA

## Slide 22: Summary
TRANSP simulations, using MMM7.1 transport model, were run for FW-heated Ip = 300 kA NSTX-U plasmas with BT(0) = 0.5, 0.75 and 1.0 T and Prf = 2, 3 and 4 MW
For the same Prf, fNI improved significantly when BT(0) was increased from 0.5 to 0.75 T
fNI=1 should be achievable with Prf ~ 3 MW in BT(0) =1 plasma and possibly in BT(0) = 0.75 T plasma
Simulation using the MMM7.1 model under conditions similar to FW-heated NSTX shot 138506 predicts much lower Te(0) than was achieved experimentally:
  Suggests core transport lower in FW-heated plasma than in NBI-heated plasma, where MMM7.1 model predictions agree better with experiment
  Decreasing ce by 5x gave better agreement between predicted and measured Te(0) in 138506  possible that fNI ~ 1 is achievable in a BT(0) = 0.5 T NSTX-U plasma with Prf ~ 3 MW

## Slide 23: Future Work
Need transport model that gives better agreement to Te(R) profile obtained in NSTX shot 138506 in order to project performance of FW heating and current drive in NSTX-U
Simulations will be run with a density profile that better matches NSTX shot 138506
Study the effect of the timing and ramp rate of Prf on fNI