## Slide 1: Characterization and Forecasting of Unstable Resistive Wall Modes in NSTX and NSTX-U
Jack Berkery, Columbia University
S.A. Sabbagh1, Y.S. Park1, R.E. Bell2, S.P. Gerhardt2, C.E. Meyers2
1Columbia University, 2Princeton Plasma Physics Laboratory
58th Annual Meeting of the APS Division of Plasma Physics
San Jose, CA, October 31 – November 4, 2016

## Slide 2: Outline
Disruption Event Characterization and Forecasting
  New DECAF code developed and used to analyze NSTX disruptions
Characterization
  Example: Resistive wall modes (RWM)
  Analysis of a database of RWM unstable discharges in NSTX
Forecasting
  Modification of ideal stability by kinetic effects explains experimental instability
  Reduced kinetic model implemented in DECAF, successfully used on database
Can real-time reduced model be used in NSTX-U to avoid disruptions?

## Slide 3: Disruption event chain characterization capability started for NSTX-U as next step in disruption avoidance plan
Approach to disruption prevention
  Identify disruption event chains and elements
  Predict events in disruption chains
  Cues disruption avoidance systems to break event chains
    Attack events at several places with active control
  Builds upon both physics and control successes of NSTX
t
[DOE report on Transient events (2015)]

## Slide 4: Disruption Event Characterization And Forecasting (DECAF) code is structured to ease parallel development
Physical event modules
  Present grouping follows work of deVries [P.C. de Vries et al., Nucl. Fusion 51, 053018 (2011)]
  – BUT, easily appended or altered
Warning algorithm
  Present approach follows [S.P. Gerhardt et al., Nucl. Fusion 53, 063021 (2013)]
  More flexible: arbitrary number of tests, thresholds, and user-defined levels and warning points
Main data structure
Code control workbooks
Density Limits
Confinement
Technical issues
Tokamak dynamics
Power/current handling
Mode stability
Physical event modules
Output processing
Kinetic RWM analysis will be used in DECAF as a reduced stability model

## Slide 5: Outline
Disruption Event Characterization and Forecasting
  New DECAF code developed and used to analyze NSTX disruptions
Characterization
  Example: Resistive wall modes (RWM)
  Analysis of a database of RWM unstable discharges in NSTX
Forecasting
  Modification of ideal stability by kinetic effects explains experimental instability
  Reduced kinetic model implemented in DECAF, successfully used on database
Can real-time reduced model be used in NSTX-U to avoid disruptions?

## Slide 6: An unstable RWM is a plasma-induced exponential growth of magnetic field line kinking that can cause disruptions
Bp
[S. Sabbagh et al., Nucl. Fusion 46, 635 (2006)]
βNno-wall
βNwith-wall
unstable
stable
0
Ideal Kink
Mode
Resistive Wall Mode
~τw-1

Copper plate
unstable RWM
137722
140102
NSTX

## Slide 7: An unstable RWM is a plasma-induced exponential growth of magnetic field line kinking that can cause disruptions
Bp
[S. Sabbagh et al., Nucl. Fusion 46, 635 (2006)]
βNno-wall
βNwith-wall
unstable
stable
0
Ideal Kink
Mode
Resistive Wall Mode
~τw-1

Copper plate
unstable RWM
137722
140102
NSTX

## Slide 8: Initial DECAF results detects disruption chain events when applied to dedicated 44 shot NSTX RWM disruption database
RWM BPn=1 threshold 30G (δB/B0 ~ 0.67%)
~60% within 14 τw of disruption time (τw = 5 ms)
unstable RWM
137722
140102
NSTX
RWM events in DECAF
Disruption

## Slide 9: Initial DECAF results detects disruption chain events when applied to dedicated 44 shot NSTX RWM disruption database
  RWM: RWM event warning
  VSC: Vertical stability control
  IPR: Plasma current request not met
  LOQ: Low edge q warning
RWM BPn=1 threshold 30G (δB/B0 ~ 0.67%)
~60% within 14 τw of disruption time (τw = 5 ms)
unstable RWM
137722
140102
NSTX
RWM events in DECAF
Disruption

## Slide 10: Initial DECAF results detects disruption chain events when applied to dedicated 44 shot NSTX RWM disruption database
RWM BPn=1 threshold 30G (δB/B0 ~ 0.67%)
~60% within 14 τw of disruption time (τw = 5 ms)
unstable RWM
137722
140102
NSTX
Disruption
  Minor disruptions cause large decreases in βN and stored energy with subsequent recovery
Earlier RWM events not false positives!

## Slide 11: Outline
Disruption Event Characterization and Forecasting
  New DECAF code developed and used to analyze NSTX disruptions
Characterization
  Example: Resistive wall modes (RWM)
  Analysis of a database of RWM unstable discharges in NSTX
Forecasting
  Modification of ideal stability by kinetic effects explains experimental instability
  Reduced kinetic model implemented in DECAF, successfully used on database
Can real-time reduced model be used in NSTX-U to avoid disruptions?

## Slide 12: A full description of RWM stability includes both fluid and “kinetic effects”: taking into account complex particle motion
Precession Drift
~Plasma Rotation
[R. Pitts et al., Physics World, March 2006]
MISK code
Solves for RWM growth rate
is solved by using from the drift kinetic equation
[J. Berkery et al., Phys. Rev. Lett. 104, 035003 (2010)]

## Slide 13: MISK calculations validated against unstable experimental plasmas; reproduce approach towards marginal stability
NSTX
MISK Calculations
[J. Berkery et al., Nucl. Fusion 55, 123007 (2015)]
unstable
stable
MISK Calculations
NSTX
βN
Bp

## Slide 14: Goal is to forecast mode growth rate in real-time using parameterized reduced models for δW terms
no-wall limit
no-wall limit
with-wall limit
with-wall limit
fluid RWM growth rate
stabilized by kinetic effects
β limits
δW
growth
rate
(γτw)
Fluid Terms
Modeled estimates for NSTX no-wall limit
NSTX 138556
Internal inductance
Pressure peaking
Aspect ratio
Composite no-wall limit model
RWM dispersion relation

## Slide 15: Physics understanding from previous RWM research used to construct a reduced kinetic model
RWM dispersion relation
Kinetic Effects
Bounce resonances
Precession resonance
<ν> = 1 kHz
Gaussian functions are used for resonances
  Positions in <ωE> determined by ωD and ωb
  Height (a), width (b), and position (c) dependent on ν/ωD or ν/ωb
  Coefficients selected to reflect NSTX experience
real
imaginary

## Slide 16: DECAF contains modeled kinetic quantities for generation of stability maps
Normalized growth rate vs. time
unstable
region
Cβ
Fluid
Fluid + Kinetic
unstable
stable
Stability diagram shows trajectory of a discharge towards unstable regions
Cβ = (βN – βNno-wall)/
(βNwith-wall – βNno-wall)

## Slide 17: DECAF reduced kinetic model results initially tested on a database of NSTX discharges with unstable RWMs
84% of shots are predicted unstable
44% predicted unstable < 320 ms before disruption
33% predicted unstable within 100 ms of a minor disruption
Predicted instability statistics (45 shots)
Normalized growth rate vs. time
unstable
stable
Chart: 
Stable
(16%)
Instability within 100 ms of minor
disruption
(33%)
Instability < 320 ms
before disruption
(44%)
(7%) False
positives
Tradeoff: missed vs. early warnings

## Slide 18: Reduced kinetic model distinguishes between stable and unstable NSTX discharges
Unstable cases
Stable cases
If <ωE> ~ 0 warnings are eliminated, 10/13, or 77%, of stable cases are stable in the model
Model is successful in first incarnation - development continues to improve forecasting performance

## Slide 19: Outline
Disruption Event Characterization and Forecasting
  New DECAF code developed and used to analyze NSTX disruptions
Characterization
  Example: Resistive wall modes (RWM)
  Analysis of a database of RWM unstable discharges in NSTX
Forecasting
  Modification of ideal stability by kinetic effects explains experimental instability
  Reduced kinetic model implemented in DECAF, successfully used on database
Can real-time reduced model be used in NSTX-U to avoid disruptions?

## Slide 20: Next step: Can this reduced model be used in real-time to steer clear of RWM instability regions?
[M. Podesta and R.E. Bell, submitted to Rev. Sci. Inst. (2016)]
(and poster, this conference)
Real-time velocity data now available on NSTX-U
[I.R. Goumiri et al., Nucl. Fusion 56, 036023 (2016)]
(and invited talk, this conference)
Steer plasma back into stable region
State space rotation control designed for NSTX-U
  New 6-source NBI provides broader profile, more flexibility
204202

## Slide 21: Next step: Can this reduced model be integrated into a larger disruption avoidance and mitigation scheme?
IP
IP Request
(including transition to rampdown)
  ZP(dZP/dt)
  ZP(dZP/dt) threshold
Plasma control system detects loss of control
  Ex: vertical oscillations exceeding a threshold
  Switches to new states that gently end the discharge
New MGI will study variation of poloidal injection location
  MGI valves 1 and 2 fully functional on NSTX-U
[R. Raman et al., IEEE Trans. on Plasma Sci., (2016)]
(D. Boyer talk, and S. Gerhardt poster, this conference)

## Slide 22: NSTX-U had scientifically productive first year, is poised to perform disruption avoidance experiments
1 2 3 4
Achieved H-mode on 8th day of 10 weeks of operation
Surpassed magnetic field and pulse-duration of NSTX
NSTX-U scenario achieved with H98 ≥ 1, βN ≥ no-wall limit
  Matches best NSTX performance at Ip = 0.9MA
Identified and corrected dominant error fields
Implemented techniques for controlled plasma shut down, commissioned new tools for mitigation
Aim to resume plasma operations end of 2017 / early 2018

## Slide 23: Summary
DECAF code developed for disruption characterization and forecasting
Kinetic theory modifies ideal stability, includes rotation, collisionality
  MISK code calculations can explain experimental RWM stability
  Full MISK code calculations of δWK can not be performed in real time, but physics insight used to create a reduced model
Reduced kinetic model for disruption avoidance is implemented, ready to be tested in NSTX-U
  Success rate is surprisingly high given its initial state and relative simplicity
  Will enable unstable growing RWM to be anticipated, rather than reacted to

## Slide 24: Backup

## Slide 25: Physics understanding from previous research used to construct a reduced kinetic model
MISK2 Calculations
Benchmarked8, Comp. to Expts3,4,6,7,9
Reduced Kinetic Model
References
[1] B. Hu et al., Phys. Rev. Lett. 93, 105002 (2004)
[2] B. Hu et al., Phys. Plasmas 12, 057301 (2005)
[3] J. Berkery et al., Phys. Rev. Lett. 104, 035003 (2010)
[4] J. Berkery et al., Phys. Plasmas 17, 082504 (2010)
[5] J. Berkery et al., Phys. Rev. Lett. 106, 075004 (2011)
[6] H. Reimerdes et al., Phys. Rev. Lett. 106, 215002 (2011)
[7] J. Berkery et al., Phys. Plasmas 21, 056112 (2014)
[8] J. Berkery et al., Phys. Plasmas 21, 052505 (2014)
[9] S. Sabbagh APS invited (2014)
[10] J. Berkery et al., Nucl. Fusion 55, 123007 (2015)
… more
Goal is to forecast γ in real-time using parameterized reduced models for δW terms
Need δWK as a function of the most important, real-time measurable quantities
Rotation3,
Collisionality5
Kinetic Effects1
Fluid Terms10

## Slide 26: Several threshold tests are currently included in DECAF

## Slide 27: The DECAF code is being used to characterize disruption event chains on NSTX, including RWMs
Disruption event chain
  Resistive wall mode (RWM)
  Vertical stability control (VSC)
  Wall proximity control (WPC)
  Low density (LON)
  Plasma current not meeting request (IPR)
  Low q (LOQ)
  Excessive pressure peaking (PRP)
  Disruption
Also, flags:
  Flattop start (FTS)
  Flattop end (FTE)
  Etc…

## Slide 28: More detailed example of DECAF threshold testing: Vertical Stability Control
Warning algorithm
  Present approach follows [S.P. Gerhardt et al., Nucl. Fusion 53, 063021 (2013)]
  More flexible: arbitrary number of tests, thresholds, and user-defined levels and warning points
Vertical stability tests
  Axis position
  Axis velocity
  Excessive Z*dZ/dt
NSTX 140132

## Slide 29: The unstable region of the stability diagram is determined by the fluid δW terms; Kinetic effects can stabilize the RWM
Stability diagram in kinetic stability space
The unstable region, inside the circle, moves when β changes
Size and position of the circle determined by fluid δW terms
Moderate levels of kinetic effects stabilize the RWM at certain beta values
Large kinetic effects – robustly stable

## Slide 30: Kinetic theory consistent with RWM destabilization at intermediate plasma rotation and collisionality affects the strength of resonances
Destabilization appears between:
  precession resonance at low ωφ
  bounce resonance at high ωφ
Stabilizing resonant kinetic effects enhanced at low ν
(marginal stability)
ν/νexp (marginal stability)
instability
(NSTX
experiment)
ωφ/ωφexp (marginal stability)
MISK calculations of γτw contours vs. ν and ωφ
unstable
Precession drift resonance stabilization

## Slide 31: Initial DECAF analysis already finding common disruption event chains, giving new insight
Identifying common chains of events can provide insight on how to cue avoidance systems
  6 (out of theoretically 42) two-event combinations following RWM accounted for 70% of the cases in the database
VSC
WPC
IPR
WPC
PRP
VSC
Other
RWM
PRP
PRP
WPC
VSC
IPR
WPC
15.9%
13.6%
11.4%
11.4%
9.1%
9.1%
29.5%
Several events detected for all shots
  RWM: RWM event warning
  WPC: Wall proximity control
  IPR: Plasma current request not met
  LOQ: Low edge q warning
  Others:
    PRP: Pressure peaking warning (34/44)
    VSC: Vertical stability control (31/44)

## Slide 32: A scalar critical plasma rotation model can not explain RWM stability; it depends on the ωφ profile
unstable RWM
137722
140102
NSTX
Early theories with scalar “critical rotation” for stability could not explain experiments
New theory: consider kinetic effects
Plasma rotation
unstable
slowed by n=3 braking
[B. Hu et al., Phys. Rev. Lett. 93, 105002 (2004)]
Ideal Stability
Kinetic Effects