## Slide 1: Abstract
The Disruption Event Characterization and Forecasting (DECAF) code, being developed to meet the challenging goal of high reliability disruption prediction in tokamaks, automates data analysis to determine chains of events that lead to disruptions and to forecast their evolution. The relative timing of magnetohydrodynamic modes and other events including plasma vertical displacement, loss of boundary control, proximity to density limits, reduction of safety factor, and mismatch of the measured and desired plasma current are considered. NSTX/-U databases are examined with analysis expanding to DIII-D, KSTAR, and TCV. Characterization of tearing modes has determined mode bifurcation frequency and locking points. In an NSTX database exhibiting unstable resistive wall modes (RWM), the RWM event and loss of boundary control event were found in 100%, and the vertical displacement event in over 90% of cases. A reduced kinetic RWM stability physics model [1] is evaluated to determine the proximity of discharges to marginal stability. The model shows high success as a disruption predictor (greater than 85%) with relatively low false positive rate.
[1] J.W. Berkery, et al., Phys. Plasmas 24 (2017) 506103
*Supported by US DOE Contracts DE-FG02-99ER54524, DE-AC02-09CH11466, and DE-SC0016614.

## Slide 2: Disruption event chain characterization capability started as next step in disruption avoidance plan
Approach to disruption prevention
  Identify disruption event chains and elements
  Predict events in disruption chains
  Cues disruption avoidance systems to break event chains
    Attack events at several places with active control
  Builds upon both physics and control successes of NSTX
t
Disruption prediction/avoidance framework
[DOE report on Transient events (2015)]

## Slide 3: Disruption Event Characterization And Forecasting (DECAF) code is structured to ease parallel development
Main data structure
Code control workbooks
Density Limits
Confinement
Technical issues
Tokamak dynamics
Power/current handling
Mode stability
Physical event modules
Output processing
Kinetic RWM analysis used as a reduced stability model in DECAF
Physical event modules
  Present grouping follows work of deVries [P.C. de Vries et al., Nucl. Fusion 51, 053018 (2011)]
  – BUT, easily appended or altered
Warning algorithms
  Present approach follows [S.P. Gerhardt et al., Nucl. Fusion 53, 063021 (2013)]
  More flexible: arbitrary number of tests, thresholds, and user-defined levels and warning points

## Slide 4: Examples of some threshold tests currently included in DECAF
Update

## Slide 5: DECAF uses threshold tests and more sophisticated models to declare events and event chains
Example DECAF analysis on single NSTX discharge
  Ex: RWM BPn=1 threshold 30G (δB/B0 ~ 0.67%)
NSTX
Disruption Events and Chain

## Slide 6: Tests can be combined with “warning points”
NSTX
Example DECAF analysis on single NSTX discharge
  Ex: VSC uses Z, dZ/dt, and ZdZ/dt

## Slide 7: Initial DECAF results detects disruption chain events when applied to dedicated 45 shot NSTX RWM disruption database
unstable RWM
137722
140102
NSTX
  RWM: RWM event warning
  VSC: Vertical stability control
  IPR: Plasma current request not met
  LOQ: Low edge q warning
RWM BPn=1 threshold 30G (δB/B0 ~ 0.67%)
~58% within 20 τw of disruption time (τw = 5 ms)
RWM events in DECAF
Disruption

## Slide 8: Initial DECAF analysis finding common disruption event chains, giving new insight
Identifying common chains of events can provide insight into how to cue avoidance systems
  5 (out of theoretically 56) two-event combinations followed 77% of RWM cases (that occurred within 20τw of DIS)
Earlier RWM events not false positives
  cause large decreases in βN and stored energy with subsequent recovery (minor disruptions)
VSC
VSC
WPC
PRP
IPR
Other
RWM
PRP
WPC
VSC
VSC
WPC
30.8%
19.2%
11.5%
7.7%
7.7%
23.1%

## Slide 9: DECAF now incorporates a reduced kinetic MHD stability model for global MHD
Precession Drift
~ Plasma Rotation
Rotational resonance effect
[J. Berkery et al., Phys. Rev. Lett. 104, 035003 (2010)]
MISK code
Solves for RWM growth rate
is solved by using from the drift kinetic equation
[R. Pitts et al., Physics World, March 2006
D. Pace et al., Physics Today 68, 34 (2015)]

## Slide 10: MISK calculations validated against unstable experimental plasmas; reproduce approach towards marginal stability
MISK calculations including kinetic effects have been tested against many marginally stable NSTX experimental cases
MISK also validated in dedicated DIII-D experiment, analogous to NSTX expts
[J. Berkery et al., Nucl. Fusion 55, 123007 (2015)]
unstable
stable
NSTX
NSTX

## Slide 11: MISK kinetic stability analysis of KSTAR indicates large stabilizing effect of energetic particles
MISK calculations find the equilibrium is stable to resistive wall modes (consistent with experiment)
  Close to marginal stability with variation of the experimental rotation profile and without considering energetic particles
  Energetic particles contribute large stabilizing effect (due to large EP fraction)
Chart: Re(δWK)
 | -0.0141 | -0.013434 | -0.013074 | -0.012659 | -0.012268 | -0.012544 | -0.013329 | -0.01405 | -0.015871 | -0.015236 | -0.016387 | -0.015918 | -0.01532 | -0.019047 | -0.022566 | -0.026623 | -0.027417 | -0.027686 | -0.027285 | -0.028443
 | 11.975
 | 0 | 16325
 | -0.0029827 | -0.0033845 | -0.0036843 | -0.0038398 | -0.0040455 | -0.0043458 | -0.0047816 | -0.0048825 | -0.0058051 | -0.0041741 | -0.0044284 | -0.0027139 | -0.00081225 | -0.0020292 | -0.0027491 | -0.0035003 | -0.0040161 | -0.0041345 | -0.0042823 | -0.0046271
Chart: Scaled Rotation Profile (ωφ/ωφexp)
| 9.9999999999999006E-2 | 0.19999999999999901 | 0.29999999999999899 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9 | 2
 | -0.85352 | -0.84134 | -0.83529 | -0.82949 | -0.82549 | -0.83307 | -0.84757 | -0.86263 | -0.883 | -0.86522 | -0.8838 | -0.87386 | -0.85846 | -0.8884 | -0.90939 | -0.92763 | -0.93467 | -0.93789 | -0.93623 | -0.93906
 | -0.30806 | -0.46425 | -0.5813 | -0.66605 | -0.74316 | -0.82319 | -0.81414 | -0.90549 | -0.93726 | -0.61356 | -0.97573 | -0.59576 | -0.083202 | -0.20678 | -0.28979 | -0.38473 | -0.47232 | -0.50185 | -0.51646 | -0.58855
stable
unstable
Unstable region
Without EPs
With EPs
Without
EPs
With EPs
KSTAR
16325
@11.975s

## Slide 12: Goal is to forecast mode growth rate in real-time using parameterized reduced models for δW terms
no-wall limit
no-wall limit
with-wall limit
with-wall limit
fluid RWM growth rate
stabilized by kinetic effects
β limits
δW
growth
rate
(γτw)
[B. Hu et al., Phys. Rev. Lett. 93, 105002 (2004)]
Growth rate
Kinetic effects
Fluid terms
RWM dispersion relation
Bounce resonances
Precession resonance
<ν> = 1 kHz
Gaussian functions are used for resonances
  Coefficients selected to reflect NSTX experience
  NSTX 138556

## Slide 13: Physics understanding from previous research using full model, used to construct a reduced kinetic model
References
Goal is to forecast γ in real-time using parameterized reduced models for δW terms
Need δWK as a function of the most important, real-time measurable quantities
[J.W. Berkery et al., Nucl. Fusion 55, 123007 (2015)]
Kinetic effects1:
Fluid terms10
Rotation3
Collisionality5
Reduced Kinetic Model
[1] B. Hu et al., Phys. Rev. Lett. 93, 105002 (2004)
[2] B. Hu et al., Phys. Plasmas 12, 057301 (2005)
[3] J. Berkery et al., Phys. Rev. Lett. 104, 035003 (2010)
[4] J. Berkery et al., Phys. Plasmas 17, 082504 (2010)
[5] J. Berkery et al., Phys. Rev. Lett. 106, 075004 (2011)
[6] H. Reimerdes et al., Phys. Rev. Lett. 106, 215002 (2011)
[7] J. Berkery et al., Phys. Plasmas 21, 056112 (2014)
[8] J. Berkery et al., Phys. Plasmas 21, 052505 (2014)
[9] S. Sabbagh APS invited (2014)
[10] J. Berkery et al., Nucl. Fusion 55, 123007 (2015)
… more
+ Energetic
Particles4
MISK2 Calculations
  Benchmarked8
  Compared to Experiments3,4,6,7,9

## Slide 14: DECAF contains modeled kinetic quantities for generation of stability maps
Normalized growth rate vs. time
Stability diagram shows trajectory of a discharge towards unstable regions
Cβ = (βN – βNno-wall)/
(βNwith-wall – βNno-wall)
Fluid
Fluid + Kinetic
unstable
stable
unstable
region
Cβ
  NSTX 139514
[J. Berkery et al., Physics of Plasmas 24, 056103 (2017)]

## Slide 15
84% of shots are predicted unstable
44% predicted unstable < 320 ms (approx. 60τw) before current quench
33% predicted unstable within 100 ms of a minor disruption
Predicted instability statistics (45 shots)
Normalized growth rate vs. time
Chart: 
Stable
(16%)
Instability within 100 ms of minor
disruption
(33%)
Instability < 320 ms
before disruption
(44%)
unstable
stable
(7%) False
positives
DECAF reduced kinetic model results initially tested on a database of NSTX discharges with unstable RWMs
[J. Berkery et al., Physics of Plasmas 24, 056103 (2017)]

## Slide 16: Reduced kinetic model distinguishes between stable and unstable NSTX discharges
If <ωE> ~ 0 warnings are eliminated, 10/13, or 77%, of stable cases are stable in the model
Model is successful in first incarnation - development continues to improve forecasting performance
Unstable cases
Stable cases
[J. Berkery et al., Physics of Plasmas 24, 056103 (2017)]

## Slide 17: Essential new step for DECAF analysis of general tokamak data: Identification of rotating MHD (e.g. NTMs)
Initial goals
  Create portable code to identify existence of rotating MHD modes
  Track characteristics that lead to disruption
    e.g. rotation bifurcation, mode lock
Approach
  Apply FFT analysis to determine mode frequency, bandwidth evolution
  Determine bifurcation and mode locking
Magnetic spectrogram of rotating MHD in NSTX
n = 1 mode frequency vs. time
(initial code)
ω0 ~ 9 kHz
bifurcation ~ 4 kHz

## Slide 18: Fast Fourier transforms used to find mode peak frequency within a time interval
Reveals potential issues handling multiple frequency peaks
Now adding processing of toroidal array / n number discrimination
Odd-n
Even-n
FFTs
Signals

## Slide 19
      Many shots with rotating MHD (e.g. NTMs) examined for NSTX and NSTX-U – two illustrated here
Magnetic spectrogram of rotating MHD mode locking termination
NSTX 138854
NSTX-U 204202
NSTX “stable periods” – enhanced by high elongation (κ ~ 2.7), lithium wall conditioning
NSTX-U: rotating MHD at lower κ ~ 2.3 , no Li wall conditioning

## Slide 20: The characterization algorithm shows that the expected bifurcation and locking events can be found
Algorithm written looks for a “quasi-steady state” period, a potential bifurcation, and possible mode locking
NSTX-U shot 204202
odd-n peak frequencies
lock
NSTX shot 138854
odd-n peak frequencies
lock
Mode frequency
bifurcates

## Slide 21: DECAF rotating MHD analysis identifies the state of the modes found (n = 1)
Magnetic signal / analysis (mode locking / unlocking)
204202
mode lock
Frequency vs. time
n = 1 mode
frequency (kHz)
4
0
8
12
16
t (s)
0.68
0.70
0.72
0.74
0.76
0.78
B (G)
20
10
0
-10
-20
-30
1 = mode rotating
-1 = mode locked
0 = No mode
DECAF mode status
t (s)
0
-2
-1
1
2
0.66
0.70
0.74
0.78
NSTX-U

## Slide 22: DECAF rotating MHD analysis identifies the state of the modes found (n = 2)
Magnetic signal / analysis (mode present, not locked)
Frequency vs. time
DECAF mode status
1 = Mode present
-1 = Mode locked
0 = No mode
204202
frequency (kHz)
10
0
20
30
1
0
2
-1
-2
0.66
0.70
0.74
0.78
t (s)
B (G)
30
-30
-20
-10
20
10
0
t (s)
0.68
0.70
0.72
0.74
0.76
0.78
NSTX-U
0.68
0.70
0.72
0.74
0.76
0.78
0.66
Signal
n = 2 mode

## Slide 23: DECAF now being tested on TCV tokamak data, including detection of MHD
TCV advantages:
  Excellent real time measurement and control capabilities
  Capability to detect modes (also in real time)
Measured Ip
Requested Ip
Measured zaxis
Requested zaxis
Measured <ne>
Greenwald <ne>
DECAF events implemented:
IPR
(Ip not meeting request)
MHD (presence of an MHD mode)
[C. Galperti et al., IEEE TNS 64, 1446 (2017)]
GWL (Greenwald density limit)
VSC
(Vertical stability control)

## Slide 24: New tool for MHD stability analysis, resistive DCON, used on KSTAR for the first time
New resistive DCON code used to calculate the q=2 Δ’ for a KSTAR case with sudden appearance of n=1 mode
  Positive Δ’ would indicate classical instability at q=2
Calculation shows a near marginal Δ’ around time of mode onset
  Requires further analysis
Resistive DCON capability could be used for future DECAF mode onset warning
?
Resistive DCON: [A. H. Glasser et al., Physics of Plasmas 23, 112506 (2016)]
Resistive DCON

## Slide 25: Summary and next steps
The Disruption Event Characterization and Forecasting code (DECAF)
  Focuses on quantitative characterization, based on physics models, of the chains of events which most often lead to disruption of plasmas
  The goal is to provide forecasts which integrate with a disruption avoidance system and are ultimately utilized in real-time during a device's operation
Reduced kinetic model for disruption avoidance is implemented
  Success rate is surprisingly high for the initial analysis
Rotating MHD is common, causes disruptions; Identification essential
  Characterization algorithm utilizes FFT, finds expected bifurcation and locking
Next steps to the development and usage of DECAF include:
  Continued improvement of accuracy of event determination
  Significant expansion of events and event chains
  Expansion of the dataset to multiple devices (including DIII-D, TCV, KSTAR)
*This work supported by the US DOE contracts DE-AC02-09CH11466,
DE-FG02-99ER54524,
and DE-SC0016614

## Slide 26: Related talk/posters
Observation of the Generalized Neoclassical Toroidal Viscosity Offset Rotation Profile in KSTAR – S.A. Sabbagh, 10:54am Wednesday
Automated Identification of MHD Mode Bifurcation and Locking in Tokamaks – J.D. Riquezes
Kinetic equilibrium reconstruction of KSTAR plasmas including internal pitch angle profile measurement – Y. Jiang
Transport and stability analyses supporting disruption prediction in high beta KSTAR plasmas – J.H. Ahn
MHD stability analysis and global mode identification preparing for high beta operation in KSTAR – Y.S. Park
Thursday afternoon posters

## Slide 27: Sign up for a copy

## Slide 28: Disruption Event Characterization and Forecasting in Tokamaks
Jack Berkery
Columbia University
S.A. Sabbagh1, Y.S. Park1, J.H. Ahn1, Y. Jiang1, J.D. Riquezes1, S.P. Gerhardt2, C.E. Meyers2
1Columbia University, 2Princeton Plasma Physics Laboratory
59th Annual Meeting of the APS Division of Plasma Physics
Milwaukee, Wisconsin, October 23-27, 2017
*This work supported by the US DOE contracts DE-AC02-09CH11466 and DE-FG02-99ER54524

## Slide 29: Another TCV slide?