## Slide 1: Energy Transport via Compressional Alfven Eigenmodes Coupling to Kinetic Alfven Waves
Z.- H. Deng,1 NA Crocker,1, Y Ren2
1UCLA, 2PPPL
59th Annual Meeting of the APS Division of Plasma Physics
Milwaukee, Wisconsin
October 23 - 27, 2017
*Supported by US DOE Contracts DE­SC0011810 & DE­AC02­09CH11466
Notes: The topic of my research is focused on the energy transport by the interaction between CAEs and KAWs

## Slide 2: Energy confinement is important in fusion
Confinement is the challenge
  Tokamaks are hot (150 million degrees)
    Need magnetic confinement
  Heat/Energy is escaping
Loss mechanisms are an area of intense investigation
Tokamaks often are heated by beams which excite coherent waves contributing to loss of energy

## Slide 3: NSTX investigates fusion physics
Spherical Tokamak
D+ plasmas
Temperatures ~ 1 KeV
B ~ 0.35 - 0.55 T
Current ~ 1 Mamp
Density ~

## Slide 4: Compressional Alfven Eigenmodes(CAEs) could play a significant role in plasma energy confinement
Beams excite long wavelength, high frequency Alfven Eigenmodes (AE) including Compressional AE (CAE) in NSTX
Anomalous temperature profile flattening observed to correlated with high frequency activity in CAEs in the core of National Spherical Torus eXperiment (NSTX) plasma
Theory suggest CAEs could contribute to the heat loss
  Multiple mechanisms have been proposed
  One candidate is CAE-KAW coupling
    This theory still requires experimental validation
Stutman, PRL 2009
Notes: Mystery – Why does the temperature not go up in the center, but does in the mid radius.
From stuntman’s paper, more mode activity occurs at higher Beam power. Wonder if CAE

## Slide 5: CAE-KAW coupling may explain anomalous flattening
CAE takes energy from core localized beam ions.
CAE couple to kinetic Alfven waves (KAW) at resonance location
  CAE dispersion relationship:
  Resonance location is where KAW excitation
  Energy dissipated during KAW excitation
  KAW energy absorbed during propagation
KAW are short wavelength (in contrast to CAE)
Theory applies for Global Alfven Eigenmodes as well [Kolesnichenko, PRL 2010]
Notes: Idea is that we don’t rea`lly know if thye are CAE or GAE, so focus on CAE coupling, when GAE can do same thing. GAE seem to be at lower frequency
Ignore fast ions
Not implausible that K_perpRhoS ~ 1-6~

## Slide 6: Magnetic diagnostic sensitive to CAEs
measured from conducting loop at edge
Faraday’s law
Toroidal mode number via 10 toroidally distributed coils
f
B-dot coil locations
NSTX cross-section
Top Down view of NSTX
Notes: Diagnostic that may be sensitive to CAE and KAWs
Make point about k roughly in the
W_scatter = W_fluc + W_probe, W_fluc << W_scat,
Point out K_fluc*Rho_S ~ 1

## Slide 7: Magnetic diagnostic sensitive to CAEs
Multiple peaks observed in magnetic spectrum at
Identified as CAE because at large fraction of
Notes: Quote f_{ci} at magnetic axis

## Slide 8: High K-Scattering diagnostic potentially detects KAWs from CAE-KAW coupling
280 GHz millimeter wave probe beam scatters into 5 receivers
Each channel is sensitive to a different K
Bragg Scattering
is density fluctuation of KAW or turbulence
beams refracted that changes over time, it has been raytraced, and K’s for different channels are determined.
Notes: Diagnostic that may be sensitive to CAE and KAWs
Make point about k roughly in the
W_scatter = W_fluc + W_probe, W_fluc << W_scat,
Point out K_fluc*Rho_S ~ 1
Electric field is about +280 MHz, but we subtracted input

## Slide 9: High K-Scattering diagnostic potentially detects KAWs from CAE-KAW coupling
  Two contributions to scattered electric field: Turbulence and KAW
    - frequency of turbulence,
    - CAE frequency; large wavelength fluctuations (amplitude ) modulate E-field scattered from turbulence.
    R – relative scattering power
Notes: Put reference. From basic scattering theory

## Slide 10: Scattering diagnostic probes KAW wavelengths
T
Channel 1:
Channel 2:
Channel 3:
Channel 4:
Channel 5:

T = 0.4483 sec
Notes: Oval the mode.
Different K for different channels
GO through Yan ren’s math and give paraemters to justify
B = ?
Rho for plasma = ?
Temperature = ?
Density = ?

## Slide 11: High K combined with magnetics allows detection of CAE-KAW coupling
Both diagnostic show peaks at similar frequency in CAE range  CAE-KAW coupling?
Expect coupling to produce KAW coherent with CAE must be verified with analysis
Verify peak in high k spectrum results from scattering.
Verify if detected k consistent with KAW theory.
  Some Channels see peaks, other’s don’t.

## Slide 12: Establishing coherence of high k spectrum peak with magnetic peak is a multistep process
Isolates mode oscillation from each signal.
  Determine f(t) for peak  filter signals to isolate mode
Using SVD, isolate global mode oscillation (from mag)
Calculate coherence of global signal with mode oscillation in scattering signal
  Test statistical significance for each high-k channel.

## Slide 13: Filtering: Determine times and frequencies with image feature analysis
Track time evolution of mode by choosing a time, frequency range, and a frequency bandwidth.
Identified f(t) can be used to create filter to isolate mode.
Feature analysis finds mode in spectrum.

## Slide 14: Filtering: Construct time dependent bandpass filter from times and frequencies
Fit an analytic (polynomial) f(t) to (t,f) from image analysis
Integrate f(t) to get Φ(t)
is used to Dopplershift to DC
Low pass filter used to isolate mode.
Un-Dopplershift with
Notes: Cannot isolated mode over a long period of time
Simple bandpass filter (freq) would

## Slide 15: SVD:Singular value decomposition gives better “global mode” δb
global mode observed by 10 bdot coils (HN array)
“filter” signals with SVD ⇒ global mode w/reduced noise
  SVD factors space & time dependence of signal matrix:
Steps before SVD …
  bandpass filter coil signals to isolate mode
  make signals complex ⇒ spatial phase (e.g. nϕj) factors out automatically:
    =
SVD
bdot coil signals
“global mode”
“noise”
Notes: SVD uses 10 signals and finds common mode, subtract the common mode, and subtract from 10 channels to get noise.

## Slide 16: SVD: finds global mode from eigenvector of signal correlation matrix
SVD solves factoring problem
  by minimizing
  ⇒ spatial coefficients () of global mode from eigenvector of correlation matrix with largest eigenvalue:

## Slide 17: Scattering Verification: Scattering produces an asymmetric spectrum
Peaks at CAE frequency observed for 2 reasons.
  Sidebands of scattering from low frequency turbulence
  Scattering from KAW
Notes:  from KAW
= 0.1
CAE is 1e6 Hz
〖R𝑒〗^(𝑖(𝜔_𝑐𝑎𝑒 𝑡))  from KAW

## Slide 18: Scattering Verification: Scattering produces an asymmetric spectrum
Asymmetry strength across different channels is determined by dividing power at positive mode frequency by power by negative mode frequency
Channel
1
2
3
4
5

## Slide 19: Coherence: Is scattering peak is coherent with magnetic peak as expected?
Outgoing KAW from mode conversion should be coherent with incoming CAE
  average over time
Coherence is evaluated with filtered magnetic and scattering spectral peaks
Resulting coherence is evaluated for statistical significance
  Monte Carlo Simulation using identically filtered random signals

## Slide 20: Comparison of high k channels shows peak at CAE frequency has well defined k
Expect to see KAW predominantly in only one channel
Channel sensitive to peak should correspond to k from theory
Possible to have asymmetry from turbulence with low coherence

## Slide 21: CAEs observed in shot 139395, analyzed for evidence of KAW coupling
several modes identified
  10KHz bandwidth for filtering
t = 0.4483
0.448 | 1.07e6 | 0.046
0.481 | 1.06e6 | 0.035
0.487 | 1.04e6 | 0.132
0.498 | 9.11e5 | 0.047
0.448 | 1.07e6 | 0.046
0.481 | 1.06e6 | 0.035
0.487 | 1.04e6 | 0.132
0.498 | 9.11e5 | 0.047
Notes: 〖R𝑒〗^(𝑖(𝜔_𝑐𝑎𝑒 𝑡))  from KAW

## Slide 22: Asymmetry varies with scattered k, as expected
Channel one typically demonstrate a high asymmetry at times where mode is present.
t = 0.482 sec
Coherence =
Channel
1
2
3
4
5
0.448 1.07e6 | 6.2
0.481 1.06e6 | 3.8
0.487 1.04e5 | 6.3
0.493 9.11e5 | 4.1
0.448 1.07e6 | 6.2
0.481 1.06e6 | 3.8
0.487 1.04e5 | 6.3
0.493 9.11e5 | 4.1
Notes: Suggest higher k c
Peak should show up by modulation
Mode jagged because mode is jaggeded
Draw a line, formula (<p_+(t)>) P_+(t) = power @ +- peak

## Slide 23: Asymmetry observed in high k channels for multiple modes
Channel
1
2
3
4
5

## Slide 24: Coherence found between magnetics and scattering found for following modes

## Slide 25: Observation consistent with CAE-KAW coupling
Peaks at same frequency in magnetic and scattering signal are coherent
Comparison of scattering signals at different k demonstrate well defined k for peaks at CAE freq
Peaks at lower k spectra demonstrate high asymmetry, in contrast with high k spectra
Coherence + Asymmetry strongly implies scattering from KAW

## Slide 26: Future work
Compare scattering measurement with expectation from KAW dispersion relationship
  Predict which channels see KAWs as profiles evolve
  Assess absorption to determine if significant power can reach measurement location
Evaluate potential contamination of scattering signal by refraction of probe beam.
  Beam tracing

## Slide 27: Request Electronic Copy