## Slide 1
S.A. Sabbagh1, J.W. Berkery1, Y.S. Park1, J.H. Ahn1, Y. Jiang1, J.D. Riquezes1, R.E. Bell2, M.D. Boyer2, A.H. Glasser3, J. Hollocombe4, J. Kim5, A. Kirk4, J. Ko5, W. Ko5, L. Kogan4, B. LeBlanc2, J.H. Lee5, Y.K. Oh5, F. Poli2, S.D. Scott2, A. Thornton4, L. Terzolo5, S.W. Yoon5, S.J. Wang5, Z.R. Wang2
V2.7
1Department of Applied Physics, Columbia University, New York, NY
2Princeton Plasma Physics Laboratory, Princeton, NJ
3Fusion Theory and Computation, Inc., Kingston, WA
4Culham Centre for Fusion Energy, UKAEA, Abingdon, UK
5National Fusion Research Institute, Daejeon, Republic of Korea
Disruption Event Characterization and Forecasting (DECAF) in Tokamaks
60th APS Division of Plasma Physics Meeting
6 November 2018
Portland, OR

## Slide 2: A broadened disruption prediction and avoidance approach is progressing for ITER and future tokamaks
Motivation: Disruption prediction/avoidance is a critical need
  Why? A disruption stops plasma operation, might cause device damage
  A highest priority DOE FES (Tier 1) initiative - present “grand challenge” in tokamak stability research:
    Can be done! (JET tokamak: < 4% disruptions with carbon wall)
    ITER disruption allowance: < 1 - 2% (energy + E&M loads); << 1% (runaways)
Talk Outline
  Disruption predictor requirement metrics
  Disruption Event Characterization and Forecasting (DECAF) approach
  Physical models in DECAF, continued progress toward early prediction
  Initial multiple-device, large database analysis
  Present evolution of disruption forecasting performance

## Slide 3: DECAF is a logical, physics-based paradigm that meets all disruption predictor requirement metrics
Disruption predictor must
  Predict SPECIFIC pre-disruptive phenomena  link to control
  Provide CONTINUOUS variable quantifying proximity (& can GENERATE triggers)
  Provide SUFFICIENT LEAD TIME for mitigation or avoidance
  Be EXTRAPOLABLE to new device (e.g. ITER) prior to operation
  Be REAL-TIME calculable
D. Humphreys, et al., PoP 22 (2015) 021806
DECAF in disruption prediction / avoidance framework
DECAF

## Slide 4: DECAF determines disruption triggers and automatically generates event chains
t (s)
NSTX 140132
Events (in this chain)
  resistive wall mode
  vertical instability
  wall proximity control
  low density warning
  not meeting Ip request
  low q warning
  disruption (current quench)
Global MHD mode trigger
Warning time: 30 ms
  Absolute: Just sufficient time for disruption mitigation in ITER
  Normalized: ~ 6 RWM growth times in NSTX – far longer time (~ s) in ITER

## Slide 5: Reduced kinetic MHD model in DECAF provides early forecast of instability boundary to global MHD modes
Full physics model (years of effort) reduced
  Stability contours CHANGE for each time point
  Allows real-time stability and mode growth rate prediction
ideal
Ideal + kinetic
unstable
stable
Norm. growth rate vs. time
gtw
139514
disruption
predicted instability
J.W. Berkery, S.A. Sabbagh, R. Bell, et al., Phys. Plasmas 24 (2017) 056103
Disruption forecasting
Global kinetic MHD mode growth
gtw
Increasing time
Collisionality (kHz)
Rotation
Predicted instability statistics
84% of shots are predicted unstable (stringent evaluation)
44% predicted unstable < 320 ms (approx. 60tw) before current quench
33% predicted unstable within 100ms of a minor disruption
NSTX

## Slide 6: Recently a density limit model has been examined in DECAF based on power balance in an island
Power density balance:
D. Gates et al., Phys. Rev. Lett. 108 165004 (2012)
Local island power balance limit
  Power balance in island between Ohmic heating and radiated power loss
  If radiated power at the island exceeds the input power (Ploss > Pinput), island grows
NSTX
134020

## Slide 7: DECAF density limit analysis started: global, local density limits examined, correlation of MHD onset near limits
Disruptivity vs. density
DIS
Magnetic spectrogram
(toroidal array)
Greenwald limit
  Near 0.9 when mode starts (range 0.75 – 1.05)
Rad. island power balance
  Near 1.0 when mode starts (range 0.60 – 1.50)  next step: reduce range
GWL
IPB
GWL
GWL
IPB
See CP11.00095: J.W. Berkery
0.9
NSTX

## Slide 8: More powerful automated MHD event objects have been developed for DECAF
More capable MHD event objects required for analysis of wider tokamak databases
DECAF MHD events now include
  Mode number (n) discrimination
  Full history of mode evolution, including bifurcation and locking
  Many disruption warning criteria
DECAF automated MHD events
MHD-n1
MHD-n3
MHD-n2
Magnetic spectrogram
(toroidal array)
GWL
IPB
0.9
NSTX
See CP11.00110: J.D. Riquezes

## Slide 9: New DECAF MHD events utilize history of 15 criteria to define time evolving disruption warning level
MHD-n1
MHD-n3
MHD-n2
DECAF automated MHD objects
LTM-n1
LTM-n2
BIF-n1
BIF-n2
DECAF “heat map” (for MHD)
“quasi-steady
state (O)”
Very low f mode 
f below bifurcation 
 High amplitude 
Decreasing plasma rotation 
 Core plasma rotation < 6 kHz 
Locked mode > 25G 
Key notables of MHD warning
  “Safe”/“unsafe” MHD periods found
  Early, slow warning level evolution
    Locked mode amplitude important, but warning comes in very late
  Mode frequency below bifurcation, decreasing plasma rotation key
DECAF MHD warning level
Safe

## Slide 10: Progress on DECAF now moving to processing of multi-machine databases
Analysis
  Kinetic equilibrium / stability analysis on KSTAR; planned for MAST
DECAF database started
  Requires storage of DECAF analysis
Device / Capability | KSTAR | MAST | NSTX | DIII-D | TCV
Full database access (type) | Yes (MDSplus) | Yes (UDA) | Yes (MDSplus) | Yes (MDSplus) | Yes (MDSplus)
Database analysis | continuing | continuing | continuing |  | started
Equilibrium analysis | Kinetic + MSE | scheduled | Kinetic + MSE | available | 
Stability | Ideal, Resistive Kinetic MHD | scheduled | Ideal, kinetic MHD (resistive) | Ideal, kinetic MHD | 
shot*seconds (for kinetic analysis) | 1,886 (2016+2017) | 2,667 (est) (M5 - M9 runs) | 2,000 / year (est) |  | 
Aim to add ASDEX-U next, then JET and C-Mod databases

## Slide 11: Tearing mode stability examined in KSTAR plasmas varied bN , q95 (supports future DECAF models)
Higher q95 plasma (tearing stable)
*Resistive DCON
16325
16295
Classical tearing stability index, D′, computed at q = 2 surface using outer layer solutions
At higher q95, D′ is mostly positive predicting unstable classical tearing mode
  Indicates neoclassical effects, additional physics are needed to produce stability
Time evolution of ideal MHD stability also computed with DCON to support DECAF
*A.H. Glasser PoP (2016)
Experimentally
Unstable 2/1
Experimentally
2/1 stable
See CP11.00100: Y.S. Park
High bN plasma (tearing unstable)
*Resistive DCON
See CP11.00099: Y. Jiang
bN ~ 2
bN > 3
See POSTER version of talk (next session) for more

## Slide 12: Initial DECAF analysis of large databases further supports result that disruptivity doesn’t increase with βN
DECAF analysis of event alone
  Similar to a “standard” disruptivity analysis
  Analyzed at 10 ms intervals (> million tests)
Analysis during steady plasma current
  MAST: 8,902 plasmas analyzed
  NSTX: 10,432 plasmas analyzed
  KSTAR: 1,309 plasmas analyzed
DIS
MAST
NSTX
KSTAR
(internal inductance)
Plasma normalized beta
(~ plasma energy content)

## Slide 13: DECAF provides early disruption warning and understanding of disruption event chain beyond disruptivity plots
NSTX
Example: What are the most important regions to study on this plot?

## Slide 14: DECAF provides early disruption warning and understanding of disruption event chain beyond disruptivity plots
NSTX
Example: What are the most important regions to study on this plot?
  Studies usually focus on the high disruption probability regions
  What causes the disruptions? (low bN, mid-li ???)
  Problem plasma conditions can change significantly between first problem detected and when disruption happens
DIS
DIS

## Slide 15: DECAF provides early disruption warning and understanding of disruption event chain beyond disruptivity plots
NSTX
DIS
DIS
Answer: the circles mark the key region to study!
  DECAF shows the plasmas suffer several “events” that are started in this region, and end up far from that region when they disrupt (at the crosses )
Example: What are the most important regions to study on this plot?
  Studies usually focus on the high event probability regions
  What causes the disruptions? (low bN, mid-li ???)
  Problem plasma conditions can change significantly between first problem detected and when disruption happens

## Slide 16: Example: DECAF shows plasma parameters of VDE event can occur far from those of DIS event
Largest portion of detected VDE events appear at (li,k) with very small portion of DIS events detected
NSTX
Plasma elongation
(internal inductance)

## Slide 17: DECAF provides an early disruption forecast - on transport timescales – giving potential for disruption avoidance
DECAF event chain reveals physics
  Rotating MHD slows, bifurcates, and locks
126962
Disruption forecast level
DECAF MHD events
MHD-n1
PRP
DIS
IPR
WPC
VDE
(0.490s)
BIF-n1
LTM-n1
(+.068s)
(+.073s)
(+.073s)
(+.077s)
(+.080s)
(+.005s)
(+.045s)
DECAF event chain
  Then, plasma has an H-L back-transition (pressure peaking warning PRP) before DIS
  Early warning gives the potential for disruption avoidance by plasma profile control
NSTX
Safe
n
1
2
3
DIS

## Slide 18: DECAF event analysis of large databases of different devices shows physical distinctions
Databases
  MAST: 8,789 shots (3,360 shots*seconds)
  NSTX: 10,094 shots (6,400 shot*seconds)
Loss of vertical stability control occurs closer in time to disruption in MAST compared to NSTX
  May be due to presence of copper stabilizing plates in NSTX
Understanding aids in DECAF extrapolation to new devices
Chart: Histogram of event
| 0.1 | 9.5000000000000001E-2 | 0.09 | 8.5000000000000006E-2 | 0.08 | 7.4999999999999997E-2 | 7.0000000000000007E-2 | 6.5000000000000002E-2 | 0.06 | 5.5E-2 | 0.05 | 4.4999999999999998E-2 | 0.04 | 3.5000000000000003E-2 | 0.03 | 2.5000000000000001E-2 | 0.02 | 1.4999999999999999E-2 | 0.01 | 4.9999999999999897E-3 | 0 | -4.9999999999999099E-3 | -9.99999999999991E-3 | -1.4999999999999901E-2 | -1.99999999999999E-2 | -2.4999999999999901E-2 | -2.9999999999999898E-2 | -3.4999999999999899E-2 | -3.9999999999999897E-2 | -4.4999999999999998E-2 | -0.05 | -5.5E-2 | -0.06 | -6.5000000000000002E-2 | -7.0000000000000007E-2 | -7.4999999999999997E-2 | -0.08 | -8.5000000000000006E-2 | -0.09 | -9.5000000000000001E-2 | -0.1
 | 8 | 4 | 14 | 9 | 17 | 14 | 14 | 10 | 11 | 12 | 16 | 25 | 19 | 37 | 44 | 48 | 86 | 230 | 385 | 748 | 86 | 28 | 18 | 11 | 9 | 11 | 5 | 3 | 0 | 2 | 1 | 3 | 1 | 2 | 5 | 4 | 2 | 2 | 0 | 0
MAST
DIS
VDE
Chart: Time before disruption (s)
| 0.1 | 9.5000000000000001E-2 | 0.09 | 8.5000000000000006E-2 | 0.08 | 7.4999999999999997E-2 | 7.0000000000000007E-2 | 6.5000000000000002E-2 | 0.06 | 5.5E-2 | 0.05 | 4.4999999999999998E-2 | 0.04 | 3.5000000000000003E-2 | 0.03 | 2.5000000000000001E-2 | 0.02 | 1.4999999999999999E-2 | 0.01 | 4.9999999999999897E-3 | 0 | -4.9999999999999099E-3 | -9.99999999999991E-3 | -1.4999999999999901E-2 | -1.99999999999999E-2 | -2.4999999999999901E-2 | -2.9999999999999898E-2 | -3.4999999999999899E-2 | -3.9999999999999897E-2 | -4.4999999999999998E-2 | -0.05 | -5.5E-2 | -0.06 | -6.5000000000000002E-2 | -7.0000000000000007E-2 | -7.4999999999999997E-2 | -0.08 | -8.5000000000000006E-2 | -0.09 | -9.5000000000000001E-2 | -0.1
 | 32 | 26 | 37 | 42 | 43 | 57 | 50 | 86 | 102 | 144 | 159 | 270 | 374 | 439 | 683 | 805 | 619 | 321 | 321 | 582 | 360 | 136 | 61 | 58 | 27 | 42 | 28 | 10 | 7 | 10 | 8 | 2 | 1 | 3 | 2 | 1 | 2 | 5 | 5 | 3 | 38
DIS
NSTX

## Slide 19: Limited event chain analysis of large databases evolves initial performance of disruption prediction
First test on large, general database
Analysis with only 5 DECAF events tested for 10,094 discharges with disruptions (NSTX)
  Events used: VDE, GWL, LOQ, IPR, DIS
Performance (Model 3)
  91.2% true positives (warning occurs)
  8.7% false negatives (no warning)
    Somewhat high number of false negatives expected: only 5 DECAF events are used in this large database analysis
In 5,909 shots, vertical instability was part of the disruption chain
DECAF Disruption Forecasting Performance Evolution
greater realism
ITER need
~10 events, ~102 shots*s
(initial event validation)
~10 events, ~102 shots*s
(earlier forecasting)
5 events
~104 shots*s
(general database)
VDE

## Slide 20: Rapidly-expanding DECAF code provides a new paradigm for disruption prediction research
Multi-faceted, integrated approach to disruption prediction and avoidance that meets disruption predictor requirement metrics
  Physics-based approach yields key understanding of evolution toward disruptions needed for confident extrapolation of forecasting
  Physics-based DECAF events can guide disruption avoidance by control
  Full multi-machine databases used (full databases needed!)
  Open to all methods of data analysis (physics, machine learning, etc.)
DECAF is now producing early warning disruption forecasts
  On transport timescales: potential disruption avoidance by profile control
Next steps
  Expand number of DECAF events evaluated in large database analysis
  Continue / expand disruption prediction performance analysis ( ITER)
  Implement DECAF disruption prediction models in real-time ( KSTAR)
We are hiring post-doctoral researchers!  Email: sabbagh@pppl.gov

## Slide 21: Supporting Slides Follow

## Slide 22: Global MHD modes can also be “slow” and allow early warnings for disruptions, potentially allowing avoidance
123856
DECAF rotating MHD warning level
IPR
DIS
PRP
VDE
RWM
LOQ
(0.629s)
(+.010s)
(+.012s)
(+.058s)
(+.101s)
(+.101s)
(+.107s)
MHD-n1
LTM-n1
WPC
(+.106s)
(+.101s)
DECAF event chain
Global MHD (RWM) can also be “slow”
  Rotating MHD warning level decreases after 0.46s  DANGEROUS for RWM onset!
  H – L back transition (PRP) drags out time to disruption (> 100 ms – transport timescale)
NSTX
DECAF MHD events
n
1
2
3
Safe

## Slide 23: DECAF code based on initial successful research/results is now advancing to a new level
DECAF brief highlights of prior results
  First automated event chain analysis (followed deVries’ manual work)
  Excellent performance on smaller, targeted databases (NSTX)
    Ex.: DIS, WPC, IPR, LOQ, RWM events found 100%, VDE event 91%
    Computed events accurately represented experiment (~ 10 events)
    Physics model forecasted global MHD disruptions with ~ 85% reliability
  Disruption chains often repeated, e.g.:
Recent progress
  Density limit model based on radiating island power balance being tested
  New MHD events in DECAF allow forecasting on transport timescales
  Linear resistive MHD analysis as first step to theory-based forecasting
  Analysis of disruption chains from general databases
  Multi-machine database analysis and disruption prediction with small number of verified events
RWM
DIS
VDE
WPC
IPR
J.W. Berkery, S.A. Sabbagh, R. Bell, et al., Phys. Plasmas 24 (2017) 056103

## Slide 24
DCON stability calculation shows high bN equilibria are subject to n = 1 ideal instability
Equilibria at lower bN ~ 2 is consistently stable to n = 1 ideal modes in DCON
Unlike the lower bN case, DCON calculates unstable n = 1 mode with no-wall (bN > bN no-wall) at the achieved high bN > 3
The small deviations in the reconstructed profiles in the high bN phase is responsible for reduced equilibrium convergence and the scatter in dW
DCON computed ideal MHD n = 1 dW with no-wall
DCON dW
KSTAR 16295
bN > 3
A.H. Glasser, Phys. Plasmas 23 (2016) 072505
KSTAR 16325
DCON dW
bN ~ 2
See CP11.00100: Y.S. Park
See CP11.00099: Y. Jiang

## Slide 25: Higher q95 plasma has greater ideal n = 1 no-wall stability computed in DCON
Unlike higher bN plasma, equilibria is mostly stable to n = 1 ideal modes in DCON
  Note generally smooth evolution of stability criterion – reached with improved kinetic equilibria
The q-profile at higher BT evolves higher qmin above 1
  Sawteeth disappear
Reconstructed lower q shear at higher values of q does not lead to n = 1 instability in DCON
High q95 equilibria
DCON
KSTAR 16325
High q95 equilibria
qmin (w/ MSE)
}
See CP11.00100: Y.S. Park
See CP11.00099: Y. Jiang

## Slide 26: A broad non-inductive current fraction profile leads to low shear at low q in high plasma
t=1.482s
t=3.484s
t=4.084s
106
Current profile components
TRANSP
(67% non-inductive)
16295 t=1.75s
Magnetic spectrogram
0.0 0.2 0.4 0.6 0.8 1.0
yN
0.0 0.2 0.4 0.6 0.8 1.0
yN
0.0 0.2 0.4 0.6 0.8 1.0
yN
8
6
4
2
0
q
q
q
Kinetic + MSE reconstructed q profile evolution
Evolves to low shear at low q
Weak n = 2 mode
βN>3
10
6
4
2
0
8
12
10
8
6
4
2
0

## Slide 27: Kinetic EFIT reconstructed again shows evolution to low-sheared q-profiles but now at high q
16325 t=2.05s
t=4.979s
t=10.491s
t=1.906s
0.0 0.2 0.4 0.6 0.8 1.0
yN
0.0 0.2 0.4 0.6 0.8 1.0
yN
0.0 0.2 0.4 0.6 0.8 1.0
yN
15
10
5
0
20
5
0
10
15
Kinetic + MSE reconstructed q profile evolution
106
Current profile components
TRANSP
(71% non-inductive)
Magnetic spectrogram
Low shear forms again, but at high q
q
q
q
15
10
5
0
20
Tearing modes absent

## Slide 28: New DECAF MHD events are now being tested on KSTAR to define evolving disruption warning level
DECAF automated MHD objects
DECAF “heat map” (for MHD)
Mode locking at reduced plasma rotation
Key notables of MHD warning
  “Safe”/“unsafe” MHD periods
  Early disruption warning (300 ms)  on transport timescale
MHD warning level
Safe
KSTAR
16299
MHD-n1
MHD-n2
Very low frequency mode 
Plasma rotation profile
and dynamics
High amplitude mode 
}
Decreasing bN 
condition
time (s)
frequency (kHz)
warning level
n
1
2
3
See CP11.00110: J.D. Riquezes

## Slide 29: Kinetic reconstructions focused first on KSTAR plasmas with high-non-inductive fraction; NICF exceeds 75%
18492
16498
18476
16325
16295
TRANSP analysis of experimental plasmas
Non-inductive fraction
  Beam-driven
  Bootstrap
Non-inductive fraction is key for stable high beta steady state operation
Volume average electron density (m-3)
See CP11.00102: J.H. Ahn

## Slide 30: Predictive TRANSP analysis shows KSTAR design target ~5 can be approached with ~100%
<TRANSP>
bN = 3.4
fNI = 96%
PNBI = 6.5 MW
Up to 75% NICF already reached in similar plasmas
NBI  6.5 MW (4 sources)
By altering and values, , up to KSTAR design target 5 can be achieved with 100% NICF
n=1 no-wall limit
n=1 with-wall limit
/=6
/=5
=1.5T
Predicted
=2.0T
=1.7T
Interpretive
“Predict-first” analysis used to design high-β , 100% non-inductive current fraction (NICF) experiments for present KSTAR run campaign
See CP11.00102: J.H. Ahn

## Slide 31: New 2nd NBI system is installed in KSTAR aims to be available for 2018 run campaign
90°
Geometry of 2nd NBI system is included in TRANSP model
  2018 : upward-slanted source
  2019+ : all 3 sources available
  1.5MW/source

## Slide 32: Predictive transport capability (TRANSP) allows “predict-first” projections for upcoming runs
6.5 MW NBI (2018)
96%
TRANSP 16325 | 2016 actual | 2018 NBI | 2019 NBI
NIC fract. (%) | 71% | 96% | 130%
bN | 2.7 | 3.4 | 4.4
li | 0.9 | 0.91 | 0.95
Ti(0) (keV) | 4.5 | 5.5 | 7.2
Te(0) (keV) | 4.6 | 3.3 | 3.3
ne(0) (1020m-3) | 5.2 | 5.6 | 5.5
fGreenwald | 0.5 | 0.5 | 0.5
H98y2 | 1.25 | 1.25 | 1.25
16325 projection
Project from existing KSTAR plasmas
  Set fraction of Greenwald density and confinement factor ITER H98y2
    Neoclassical ion transport, electron transport set to match H98y2
  KSTAR 1st and 2nd NBI systems are modeled (incl. aiming angles); power levels set realistically based on MSE needs, etc.

## Slide 33: Transport analysis projections allow for variations of plasma parameters to meet targets
TRANSP 16295 (BT; Ip) | 2016 actual (1.2T) | 2018 NBI (1.2T) | 2018 NBI | 2019 NBI
NIC fract. (%) | 67% | 105% | 95% | 126%
bN | 3.5 | 5.4 | 3.5 | 4.4
li | 0.9 | 0.83 | 0.95 | 0.84
Ti(0) (keV) | 3.6 | 4.8 | 5.4 | 7.3
Te(0) (keV) | 2.3 | 2.8 | 3.2 | 3.3
ne(0) (1019m-3) | 6.0 | 4.8 | 5.6 | 5.6
fGreenwald | 0.6 | 0.5 | 0.5 | 0.5
H98y2 | 1.25 | 1.25 | 1.25 | 1.25
105%
6.5 MW NBI (2018)
16295
95%
BT = 2T, Ip = 0.5 MA
6.5 MW NBI (2018)
(2T, 0.5 MA)
BT=1.2T, Ip=0.44 MA

## Slide 34: Initial analysis of large databases further supports published result that disruptivity doesn’t increase with plasma β
DECAF analysis of event
  Similar to a “standard” disruptivity analysis
  Shots analyzed at 10 ms intervals
Analysis during Ip flat-top
  MAST: 8902 plasmas analyzed
  NSTX: 10,432 plasmas analyzed
  KSTAR: 1309 plasmas analyzed
MAST
NSTX
KSTAR
DIS