## Slide 1: Validation of Ion and Electron Scale Gyrokinetic Simulations in NSTX and Comparisons with a High-k Scattering Synthetic Diagnostic
60th Annual Meeting of the APS Division of Plasma Physics
Portland, Oregon, Nov 5-9, 2018
J. Ruiz Ruiz1
W. Guttenfelder2, A. E. White1, N. Howard1, N. F. Loureiro1, J. Candy3, Y. Ren2, D. R. Smith4, C. Holland5 1. MIT 2. PPPL 3. General Atomics 4. U Wisconsin 5. UCSD
Work supported by DOE contracts DE-AC02-09CH11466 and DE-AC02-05CH11231

## Slide 2: Extensive validation effort underway to study electron thermal transport in NSTX H-mode plasma
NBI heated H-mode with controlled current ramp-down; two steady discharge phases, little MHD activity
Local increase in equilibrium density gradient |n| modifies ETG drive from strong to weak, consistent with changes in measured high-k turbulence [Ruiz Ruiz PoP 2015]
In this work: Compare experimental heat fluxes and measured high-k turbulence are to validate extensive set of nonlinear ion-scale and electron-scale gyrokinetic simulations
Scatt. Region
r/a~0.7
  Strong ETG Drive
  Weak ETG Drive
0.1
0.2
0.3
0.4
0.5
0.6
t [s]
  Strong ETG Drive Time
  Weak ETG Drive Time
Ip [MA]
Notes: Slide with shear and q in r!

## Slide 3: Compare experimental Qe to all simulations; measured high-k turbulence only to e- scale simulations
Electron heat flux (Qe) comparisons with TRANSP are done via sensitivity scans of GYRO simulations within exp. uncertainties
High-k turbulence comparisons will deploy a new synthetic diagnostic to e- scale simulations that best match to Qeexp
Can e-scale simulations reproduce the high- frequency & wavenumber spectra?
  Strong ETG drive
  Weak ETG drive
EXP
  Strong ETG
  Weak ETG
EXP
Notes: Cannot apply synthetic diagnostic to ion scale simulations (would need multiscale sim)
Slide with shear and q in r!

## Slide 4
GYRO code is used to perform ion-scale and electron-scale nonlinear gyrokinetic simulations
  Ion scale simulation resolves low-k turbulence kθρs ⪝ 1
  Electron scale simulation resolves ETG-scale turbulence 1 < kθρs ⪝ 60
  Experimental profiles used as input
  Local simulations performed at scattering location (r/a~0.7, R~135 cm).
  3 kinetic species, D, C, e (Zeff~1.85-1.95)
  Electromagnetic: A||+B||, βe~ 0.3 %.
  Collisions (ei ~ 1 cs/a).
  ExB shear (E~0.13-0.16 cs/a) + parallel flow shear (p ~ 1-1.2 cs/a)
  Fixed boundary conditions (buffer widths)
Electron Scale
Ion scale
kθ𝝆s
0.1
1
10
high-k diagnostic
Notes: Mention necessity of hybrid scale for accurate deployment of syn diagnostic

## Slide 5: Local ion and electron-scale simulations under-predict experimental Qe with experimental gradients as input
e- scale sim
ion scale sim
scan
e- scale sim
Pe [MW]
EXP
EXP
ion scale sim
  Strong ETG drive time
  Weak ETG drive time
Pe [MW] = Qe [MW/m2] * Area
Notes: Qi close to neoclassical levels
Will name Pe & Qe interchangeably, in this presentation always use Pe [MW]
Power-heat flux interchangeably

## Slide 6
Sensitivity Scans for Heat Flux Comparisons
Notes: Both ion and electron scale simulations

## Slide 7
Strong ETG drive condition: electron scale simulations can match Qeexp within experimental uncertainty
a/Ln scaled 1-𝜎
a/Ln scaled 1-𝜎
Sensitivity scans carried out to maximize turbulent drive within error bars
Notes: ETG highly unstable
Sensitivity scans for highest drives
Simulations are converged in box size, dr-resolution and -resolution
Only show alne_scaled
ETG highly unstable
Sensitivity scans for highest drives
Simulations are converged in box size, dr-resolution and 𝑘_𝜃-resolution
Only show alne_scaled

## Slide 8
Sensitivity scans carried out to maximize turbulent drive within error bars
Ion scale simulation
Scans (a/LT, a/Ln)
Suppressed by ExB shear (Qesim ~ 0)
a/Ln scaled 1-𝜎
a/Ln scaled 1-𝜎
Strong ETG drive condition: electron scale simulations can match Qeexp within experimental uncertainty
Notes: ETG highly unstable
Sensitivity scans for highest drives
Simulations are converged in box size, dr-resolution and -resolution
Only show alne_scaled
ETG highly unstable
Sensitivity scans for highest drives
Simulations are converged in box size, dr-resolution and 𝑘_𝜃-resolution
Only show alne_scaled

## Slide 9
a/Ln scaled 1-𝜎
a/Ln scaled 1-𝜎
Sensitivity scans carried out to maximize turbulent drive within error bars
Ion scale simulation
Scans (a/LT, a/Ln)
Suppressed by ExB shear (Qesim ~ 0)
Electron scale simulation
Scans (a/LT, a/Ln)
Can match Qeexp
Strong ETG drive condition: electron scale simulations can match Qeexp within experimental uncertainty
Notes: ETG highly unstable
Sensitivity scans for highest drives
Simulations are converged in box size, dr-resolution and -resolution
Only show alne_scaled
ETG highly unstable
Sensitivity scans for highest drives
Simulations are converged in box size, dr-resolution and 𝑘_𝜃-resolution
Only show alne_scaled

## Slide 10
a/Ln scaled 1-𝜎
a/Ln scaled 1-𝜎
Sensitivity scans carried out to maximize turbulent drive within error bars
Ion scale simulation
Scans (a/LT, a/Ln)
Suppressed by ExB shear (Qesim ~ 0)
Electron scale simulation
Scans (a/LT, a/Ln)
Can match Qeexp
Electron scale simulation
Scan (a/LT, a/Ln, q, s)
Can match Qeexp
Strong ETG drive condition: electron scale simulations can match Qeexp within experimental uncertainty
Notes: ETG highly unstable
Sensitivity scans for highest drives
Uncertainties in eq reconstruction --> scans in q, s can further enhance Qe --> build on confidence that ETG is responsible for Qe
Simulations are converged in box size, dr-resolution and -resolution
ETG highly unstable
Sensitivity scans for highest drives
Simulations are converged in box size, dr-resolution and 𝑘_𝜃-resolution
Only show alne_scaled

## Slide 11
Sensitivity scans carried out to maximize turbulent drive within error bars
Ion scale simulation
Scans (a/LT, a/Ln)
Suppressed by ExB shear (Qesim ~ 0)
Electron scale simulation
Scans (a/LT, a/Ln)
Can match Qeexp
Electron scale simulation
Scan (a/LT, a/Ln, q, s)
Can match Qeexp
a/Ln scaled 1-𝜎
a/Ln scaled 1-𝜎
Ion heat flux Qi close to neoclassical levels
Strong ETG drive condition: electron scale simulations can match Qeexp within experimental uncertainty
Notes: Simulations are converged in box size, dr-resolution and -resolution
Qi close to neoclassical levels within exp uncertainty
ETG highly unstable
Sensitivity scans for highest drives
Simulations are converged in box size, dr-resolution and 𝑘_𝜃-resolution
Only show alne_scaled

## Slide 12
a/Ln scaled 1-𝜎
a/Ln scaled 1-𝜎
Strong ETG drive condition: electron scale simulations can match Qeexp within experimental uncertainty
Sensitivity scans carried out to maximize turbulent drive within error bars
Ion scale simulation
Scans (a/LT, a/Ln)
Suppressed by ExB shear (Qesim ~ 0)
Electron scale simulation
Scans (a/LT, a/Ln)
Can match Qeexp
Electron scale simulation
Scan (a/LT, a/Ln, q, s)
Can match Qeexp
Ion heat flux Qi close to neoclassical levels
Conclusions from strong ETG drive:
ETG alone can explain Qeexp
Ion scale turbulence suppressed
Notes: Simulations are converged in box size, dr-resolution and -resolution
Qi close to neoclassical levels within exp uncertainty
ETG highly unstable
Sensitivity scans for highest drives
Simulations are converged in box size, dr-resolution and 𝑘_𝜃-resolution
Only show alne_scaled

## Slide 13
Weak ETG drive condition: sensitivity scans for ion scale simulations bracket Qeexp within error bars
Ion scale sim (TEM)
Scans in a/LT, (a/Ln scaled 1-𝜎)
Extremely stiff: Qesim  10 X Qeexp !!
a/Ln scaled 1-𝜎
EXP
Notes: Ion scale in- ‘Dimits shift
Both ion and e- scale turbulence near NL threshold

## Slide 14
a/Ln scaled 1-𝜎
ZOOM
Ion scale sim (TEM)
Scans in a/LT, (a/Ln scaled 1-𝜎)
Extremely stiff: Qesim  10 X Qeexp !!
Weak ETG drive condition: sensitivity scans for ion scale simulations bracket Qeexp within error bars
Notes: Ion scale in- ‘Dimits shift
Both ion and e- scale turbulence near NL threshold

## Slide 15
a/Ln scaled 1-𝜎
ZOOM
Ion scale sim (TEM)
Scans in a/LT, (a/Ln scaled 1-𝜎)
Extremely stiff: Qesim  10 X Qeexp !!
Electron scale sim (ETG)
Scans in a/LT, (a/Ln scaled 1-𝜎)
Less stiff, under-predicts Qeexp
Ion heat flux Qi close to neoclassical levels
Weak ETG drive condition: sensitivity scans for ion scale simulations bracket Qeexp within error bars
Notes: Ion scale in- ‘Dimits shift
Both ion and e- scale turbulence near NL threshold

## Slide 16
a/Ln scaled 1-𝜎
ZOOM
Ion heat flux Qi close to neoclassical levels
Weak ETG drive condition: sensitivity scans for ion scale simulations bracket Qeexp within error bars
Ion scale sim (TEM)
Scans in a/LT, (a/Ln scaled 1-𝜎)
Extremely stiff: Qesim  10 X Qeexp !!
Electron scale sim (ETG)
Scans in a/LT, (a/Ln scaled 1-𝜎)
Less stiff, under-predicts Qeexp
Conclusion at weak ETG Drive:
Ion-scale simulation can bracket Qeexp
Electron scale turb. active, cannot match Qeexp
Notes: Ion scale in- ‘Dimits shift
Both ion and e- scale turbulence near NL threshold

## Slide 17
High-k Turbulence Comparisons

## Slide 18
Deploy synthetic diagnostic to highest Qe e- scale simulations
a/Ln scaled 1-𝜎
Strong ETG Drive
Weak ETG Drive
Notes: Pink simulation dot at Strong ETG
Blue simulation dot at Weak ETG Drive

## Slide 19
Highest Qe e- scale simulations match k-spectrum shape and fluctuation level ratio
GYRO
GYRO
exp
exp
e- scale sims
Strong ETG Drive (matched Qeexp)
Reproduces shape of -spectrum
Weak ETG Drive (Qesim/Qeexp ~ 65%)
-spectra can be matched within error bars
Notes: – e- scale sim does not correctly resolve enough modes in synthetic signal, need to resolve more k’s to quantitatively reproduce turbulent f-spectrum
Hybrid scale sim at high ETG Drive has lower fluctuation power – cannot match k-spectrum
k-resolution in e- scale simulation is too coarse for quantitative comparisons of -spectra
– e- scale sim does not correctly resolve enough modes in synthetic signal, need to resolve more k’s to quantitatively reproduce turbulent f-spectrum
Hybrid scale sim at high ETG Drive has lower fluctuation power – cannot match k-spectrum
k-resolution in e- scale simulation is too coarse for quantitative comparisons of 𝑓-spectra

## Slide 20
Strong ETG Drive (matched Qeexp)
Reproduces shape of -spectrum
Weak ETG Drive (Qesim/Qeexp ~ 65%)
-spectra can be matched within error bars
-spectra: k-resolution in e- scale simulation too coarse for quantitative comparisons  need big-box e- scale simulations
Can match fluctuation level ratio S(Strong ETG Drive)/S(weak ETG Drive)
Highest Qe e- scale simulations match k-spectrum shape and fluctuation level ratio
GYRO
GYRO
exp
exp
e- scale sims
Notes: – e- scale sim does not correctly resolve enough modes in synthetic signal, need to resolve more k’s to quantitatively reproduce turbulent f-spectrum
Big-box e- scale sim at high ETG Drive has lower fluctuation power – cannot match k-spectrum
Big-box e- scale simulations recover much better prediction of frequency spectra than e- scale simulations, not so much k-spectra
k-resolution in e- scale simulation is too coarse for quantitative comparisons of -spectra
– e- scale sim does not correctly resolve enough modes in synthetic signal, need to resolve more k’s to quantitatively reproduce turbulent f-spectrum
Hybrid scale sim at high ETG Drive has lower fluctuation power – cannot match k-spectrum
k-resolution in e- scale simulation is too coarse for quantitative comparisons of 𝑓-spectra

## Slide 21
-spectra: k-resolution in e- scale simulation too coarse for quantitative comparisons  need big-box e- scale simulations
Strong ETG Drive (matched Qeexp)
Reproduces shape of -spectrum
Weak ETG Drive (Qesim/Qeexp ~ 65%)
-spectra can be matched within error bars
Can match fluctuation level ratio S(Strong ETG Drive)/S(weak ETG Drive)
Highest Qe e- scale simulations match k-spectrum shape and fluctuation level ratio
GYRO
GYRO
exp
exp
e- scale sims
Conclusion from synthetic comparisons:
Match shape of -spectrum and fluctuation level ratio between strong and weak ETG drive, consistent with Qe agreement
Notes: – e- scale sim does not correctly resolve enough modes in synthetic signal, need to resolve more k’s to quantitatively reproduce turbulent f-spectrum
Hybrid scale sim at high ETG Drive has lower fluctuation power – cannot match k-spectrum
k-resolution in e- scale simulation is too coarse for quantitative comparisons of -spectra
– e- scale sim does not correctly resolve enough modes in synthetic signal, need to resolve more k’s to quantitatively reproduce turbulent f-spectrum
Hybrid scale sim at high ETG Drive has lower fluctuation power – cannot match k-spectrum
k-resolution in e- scale simulation is too coarse for quantitative comparisons of 𝑓-spectra

## Slide 22: Conclusions and Next Steps
Next Steps
Multi-scale simulation of NSTX H-mode + quant. comparisons with syn. diagnostic
Deploy synthetic diagnostic for additional NSTX discharges
Projections of new high-k diagnostic for NSTX-U
Strong ETG Drive
Ion-scale turbulence is suppressed
e- scale can match Qeexp, consistent with agreement in high-k wavenumber spectrum
Weak ETG Drive
Ion scale sim can bracket Qeexp , extremely stiff transport
Electron scale is active, under-predicts Qeexp
Ion scale turbulence (TEM) might be responsible for most Qeexp, cross-scale interactions likely important (ETG active)
e- scale turbulence (ETG) is likely responsible for Qeexp
Notes: Carried extensive validation effort for ion and electron scale GK sims in NSTX H mode plasma

## Slide 23: Additional Material

## Slide 24
Input Parameters into Nonlinear Gyrokinetic Simulations Presented
 | t=398 | t = 565
r/a | 0.71 | 0.68
a [m] | 0.6012 | 0.596
ne [10^19 m-3] | 4.27 | 3.43
Te[keV] | 0.39 | 0.401
a/Lne | 1.005 | 4.06
a/LTe | 3.36 | 4.51
βeunit | 0.0027 | 0.003
a/LnD | 1.497 | 4.08
a/LTi | 2.96 | 3.09
Ti/Te | 1.13 | 1.39
nD/ne | 0.785030 | 0.80371
nc/ne | 0.035828 | 0.032715
a/LnC | -0.87 | 4.08
a/LTC | 2.96 | 3.09
Zeff | 1.95 | 1.84
nuei (a/cs) | 1.38 | 1.03
q | 3.79 | 3.07
s | 1.8 | 2.346
R0/a | 1.52 | 1.59
SHIFT =dR0/dr | -0.3 | -0.355
KAPPA = κ | 2.11 | 1.979
sk=rdln(κ)/dr | 0.15 | 0.19
DELTA = δ | 0.25 | 0.168
sδ=rd(δ)/dr | 0.32 | 0.32
M | 0.2965 | 0.407
γE | 0.126 | 0.1646
γp | 1.036 | 1.1558
ρ* | 0.003 | 0.0035
λD/a | 0.000037 | 0.0000426
cs/a (105 s-1) | 4.4 | 2.35
Qe (gB) | 3.82 | 0.0436
Qi (gB) | 0.018 | 0.0003
Bt_loc [T] | -0.35 | -0.35
cs [m/s] | 2.105 | 2.105
𝛀i [1/s] | 3.5*107 | 3.5*107

## Slide 25
Hybrid Scale Simulation Necessary to Correctly Resolve High-k Scattering Wavenumber
e- scale
hybrid scale
ch 1
ch 2
ch 3
ch 1
ch 2
ch 3
Hybrid scale is NOT multiscale simulation:
, but does not fully resolve ion scales
Only run for e- time scales (Tsim ~ 30a/cs)
Measurement-k from channels 1-3 of high-k scattering system in NSTX mapped to GYRO wavenumber grid

## Slide 26
Synthetic f-spectrum at High ETG Drive, Ch1
e- scale
hyb scale

## Slide 27
Numerical Resolution Details of GYRO Simulations Needed for Synthetic Diagnostic of High- Scattering
Extensive Box size scans show Hybrid Scale Simulation is trade off:
  Computational cost ~ 0.5 M CPU h
  Correctly resolving experimental k
Electron Scale Simulation:
  Only e- scale turbulence
Electron Scale
  Lr x Ly = 20-14 x 21-16 ρs (L/a~0.08)
  nr x n = 512-450 x 140-220
  Lr x Ly = 4 x 6 ρs (L/a ~0.02)
  nr x n = 192 x 42
Hybrid Scale
Notes: Do not talk about full box

## Slide 28
Experimental f-spectrum for ch1, 2, 3
High ETG Drive condition for ch3 has little doppler shift from f=0 (lowest k  low k.v) contamination of signal by f=0 noise peak

## Slide 29
Total Thermal Transport Budget at Low ETG
Qeexp ~ 1 MW - Can be matched by ion scale GK sim within 1(+Te,-ne)
Qiexp ~ 0.23 MW - Qi << Qe - Qisim(ion scale) ~ 10X Qiexp within 1(+Te,-ne) (similar to Qe)  Can be matched by ion scale GK sim - Neoclassical Qi still TBD.
Experiment sits near nonlinear threshold of both ion and electron scale turbulence.
Ionscale turbulence displays much higher stiffness than e- scale

## Slide 30
GYRO simulations using exp. inputs (∇T, ∇n) under-predict fluctuation power at low ETG drive
High ETG Drive (Qesim/Qeexp ~ 20%):
GYRO cannot match spectrum at lowest-k (unclean diagnostic signal)
Low ETG Drive (Qesim ~ 0)
Underprediction in fluct. power consistent with under-prediction in Qe for experimental (∇T, ∇n) inputs in GYRO (hyb. scale shown)
Hybrid-scale sims better match shape of -spectrum (dominated by Dop shift, not shown)
Detected fluctuation power is scaled by constant (diagnostic not absolutely calibrated)
GYRO
GYRO
exp
exp
Hybrid scale sims
Notes: Bpth for e- and hybrid scale simulations underpredict fluct power
– e- scale sim does not correctly resolve enough modes in synthetic signal
High ETG Drive lowest k signal contaminated by f=0 peak

## Slide 31: Mapping (krρs,kθρs)GYRO  (kR, kZ)exp
Preamble 3 Wavenumber mapping under simplifying assumptions
Assumptions
  ζ=0, dζ/dr=0 (squareness + radial derivative)
  Z0=0, dZ0/dr=0 (elevation + radial derivative)
  UD symmetric (up-down asymmetry of flux surface)
  theta=0 (outboard mid-plane)
In the following slides, develop mapping when assumptions are not satisfied, invert
(R(r,θ),Z(r,θ))=(Rexp, Zexp) (rexp,θexp) .