## Slide 1: High harmonic fast wave propagation in the scrape-off layer (SOL) of NSTX/NSTX-U Effect of Wall Boundary on Power Losses in the SOL
Eun-Hwa Kim N. Bertelli, M. Ono, E. Valeo, J. Hosea, and R. Perkins
PPPL
S. Shiraiwa and J. Wright PSFC, MIT
2018 APS-DPP / TP11.00095

## Slide 2: NSTX studies showed significant amounts of HHFW power missing from core
The Interaction between the RF antennas and the scrape of layer (SOL) plasma is of crucial importance in determining the overall performance of RF in a tokamak
  All frequencies: LH, IC, HHFW, etc …
In NSTX
  Strong interactions between HHFW and SOL plasm [Hosea et. al POP 2008, Phillips et al., 2009, Perkins et. al. PRL 2012]
  Core Heating Effieicny (𝜂) enhanced in stronger magnetic field
    B𝜙 = 0.45T (n𝜙 = -12) : 𝜂 ~ 44%  Power loss (Ploss) ~ 56%
    B𝜙 = 0.55T (n𝜙 = -12) : 𝜂 ~ 65%  Power loss (Ploss) ~ 35%
  Larger power losses occur for high density in front of the antenna

## Slide 3: Density where FW cutoff is open is critical
[Hosea et al, POP 2008]
Nant ≤ Nec (Nant : density in front of antenna)
FW cannot propagate in the SOL
Higher heating
less power losses
Nant >> Nec
FW propagate in the SOL
Lower heating
higher power losses
n𝜙 = -21
n𝜙 = -12
n𝜙 = -12
n𝜙 = -21
Nant
(X 1018 m-3)
Density
In front of
Antenna
NSTX HHFW
B𝜙 = 0.55T
Critical Density (Nec) (or Onset Density)
: where FW cutoff in front of the antenna is open

## Slide 4: Previous simulations suggest SOL wave excitation can lead to significant SOL power losses
[Bertelli et al., NF 2014]
nφ = -21
FW cutoff
Strong |E|
Strong Pabs
Wave evanescent
Weaker Pabs
nφ = -12
nφ = -12
Fraction of SOL power losses (Pabs)
WSOL (core) : Power loss in the SOL (core)
Density in front of antenna
Nant [1018 m-3]
Nant ≤ Nec : closed FW cutoff
Nant > Nec : open FW cutoff

## Slide 5: Previous simulations adopted idealized boundary for simplicity
Scrape-off Layer
Rectangle
Vacuum vessel
Wide SOL !
[Bertelli et al 2014]

## Slide 6
FW2D Model Description

## Slide 7: 2D Full-wave model (FW2D) has been developed to investigate SOL physics in realistic boundaries
Wave equations : frequency domain
dielectric tensor in cold plasma
External source
m : Azimuthal (toroidal) wave number
output
Successfully examined waves at planetary magnetospheres
Kim et al., GRL 2015; Kim and Johnson, GRL 2016; Kim et al., EPJ 2017
Wave solution using finite element method and unstructured triangle mesh
Easily adopted to various geometries (e.g., dipole, tokamak…)
Easily adopt various boundaries (e.g., rectangle, vacuum vessel…)
Fast!

## Slide 8: FW2D code provide rapid cold plasma wave field computation
To simulate wave absorption, collisional frequency (𝜈 ) can be implemented in the momentum equation, then
Wave in the plasma core : change with
Wave in the SOL : not affected by
Possible to estimate the SOL power losses by adopting an arbitrary collisions in the plasma core
 15.35 0.5 % (almost identical)
for

## Slide 9: FW2D and AORSA simulations show excellent agreement in SOL field structure
FW2D  COLD approximation
 FAST computation
AORSA  Plasma kinetic effect  slow computation
Wave transmission and reflection coefficients at the LCFS are not the same  Two wave solutions cannot be exactly same
The wave structure shows very good agreement between FW2D and AORSA
 FW2D code can be used to
(efficiently) examine waves in the
cold SOL

## Slide 10
HHFW in various boundaries
: Effects of SOL size variation

## Slide 11: HHFW standing mode in the SOL becomes weaker as SOL size is reduced
Adopted vessel boundaries
Artificial – rectangle, hexagon
Realistic – vacuum vessel
Weaker standing mode

## Slide 12: SOL Power losses in the SOL size decreases as SOL size is reduced
Big Rect.
Consistent with Bertelli et al. 2014
Pabs tends to be steepened near the critical density where the FW cutoff is open
SIZE
DENSITY
Density with maximum Pabs increases as SOL size increases
Hexagon
Pabs gradually increases

## Slide 13
HHFW in vacuum vessel boundary

## Slide 14: HHFW are examined by adopting a realistic vacuum vessel boundary
Vacuum vessel
Rectangle
nφ = -21
Last Closed Flux Surface
Fast wave cutoff layer
Kim et al. (2018b) in preparation
  Narrow FW SOL cavity (among LCFS, FW cutoff layer and outer boundary)
  Weaker wave power
  Large FW SOL cavity
  FW standing mode
  Large Pabs
Nant ≤ Nec
Nant > Nec

## Slide 15: HHFW gradually propagate into the SOL as Nant increases
nφ = -12
  Nant ~ Nec
  Waves are localized near the antenna even though the FW cutoff layer is open
Last Closed Flux Surface
Fast wave cutoff layer
  Nant > Nec
  Standing mode structure appears

## Slide 16: Power losses increases linearly with collision in SOL
Lower than one in a hexagonal boundary (SOL in this boundary is smaller)
Collision
SOL could be collisional losses but also represent other loss mechanisms such as convective losses to walls

## Slide 17: Power losses decreases as the SOL size is reduced
SIZE
Adopt three magnetic equilibria of NSTX
: different location of the plasma core
Pabs gradient
decreases
as SOL size
decreases

## Slide 18
HHFW in various magnetic field strength plasma

## Slide 19: Power losses decreases as BT increases
Power losses increases as B0 increases  Consistent with experiments [e.g., Hosea et al 2008]
(for lower Pabs) increases as BT increases
 HHFW can propagate to the plasma core in wide range of density in front of antenna for strong magnetic field case
B0
NSTX-U
nφ = -12
nφ = -21

## Slide 20: Power losses decreases as BT increases
nφ = -12
nφ = -21
Normalized Density (Nant/Nec)
Normalized Density (Nant/Nec)
Lower Pabs occurs
Nant/Nec < 1.25
Nant/Nec < 2
Lower Pabs
Lower Pabs

## Slide 21: Summary
Reduce
SOL collisional power losses in the vacuum vessel
Lower Density in front Antenna
Narrower
Distance between LCFS and antenna
Stronger
Magnetic field strength
Consistent with Experiments
[e.g., Hosea et al., 2008; Phillips et al., 2009]
Minimum SOL collisional losses occur (all magnetic field strength)  near the critical density where FW cutoff is open
Minimum SOL collisional losses occur (strongly magnetized plamsa)  with wide range of the density in front of antenna

## Slide 22
Fast wave in LADP
LH wave
launcher
Fast wave in
Alcartor C-Mod
Future Work
We will examine the HHFW in the NSTX/NSTX-U using recently developed Petra-M code and compare the results from FW2D
(e.g., BP11.00082 : Shiraiwa et al., Development of Petra-M Framework: toward OS integrated FEM analysis)