## Slide 1
First analysis of the updated ITPA global H-mode confinement database
S.M. Kaye1, G. Verdoolaege2,3, C. Angioni4, O.J.W.F. Kardaun4, M. Maslov5, M. Romanelli5, F. Ryter4, K. Thomsen4,
the ASDEX Upgrade Team*, the EUROfusion MST1 Team† and JET Contributors‡
1Princeton Plasma Physics Laboratory, Princeton, NJ, USA
2Department of Applied Physics, Ghent University, Ghent, Belgium
3Laboratory for Plasma Physics, Royal Military Academy, Brussels, Belgium
4Max Planck Institute for Plasma Physics, Garching, Germany 5UKAEA, Culham Science Centre, Abingdon, UK
* See the author list of “A. Kallenbach et al. Nuclear Fusion 57 (2017) 102015”
† See the author list of “H. Meyer et al., Nucl. Fusion 57 (2017), 102014”
‡ See the author list of “X. Litaudon et al., Nucl. Fusion 57 (2017), 102001”
* Work supported by US DOE Contract No. DE-AC02-09CH11466
Global energy confinement scaling
  Extrapolate plasma performance to new machines (e.g. ITER)
  Reference for confinement in present experiments
  Boundary condition for numerical models
  Guidance for development of theoretical models
  Global H-Mode Confinement Database (°1989):
  Presently under ITPA umbrella
  DB4v5: data from 19 tokamaks [1, 2]
  Version 3 (DB3, subset DB2v8) for IPB98(y,2) (1998) [3]
}
+ C-Mod = ‘High-Z’ subset
(metal WALMAT, LIMMAT, DIVMAT)
Histograms for the main scaling variables in STD5, with low-Z (carbon wall components) vs. high-Z (fully metal-wall devices).
Number of data points per tokamak in DB5, the standard set before the latest update (STD3), the current standard set (STD5) and two ITER-relevant subsets (ST5-SEL1 and STD-SEL2).
Summary statistics for the main scaling variables in STD5 (values in DB2v8 in parentheses).
Pairwise correlation coefficients between the main scaling variables in STD5 (values in DB2v8 in parentheses). Correlations above are highlighted (it is noted that the correlation table provides only a simplified picture of predictor inter-dependencies).
Regression methods
  Complications arising in the analysis:
  Heterogeneous data from multiple devices and diagnostics
  Heterogeneous measurement uncertainties,
  log-transformation [13, 14]
  Within-device vs. between-device variability
  Model uncertainty
  Uncertainty in predictor and response variables
  (, , , , , …) [13 – 16]
  Predictor variable interdependencies (medium to strong collinearity)
Deterministic model component: regression function
Stochastic model component
Motivation and goals
  Add data closer to ITER conditions and expand parameter range
  Add data from devices with fully metallic walls
  Improve reactor-relevant database coverage w.r.t. IPB98(y,2) (high , low , high )
(high ne, low q95, high β)
Database update: DB5
  Addition of data from fully metallic devices (2017):
    627 time slices from JET-ILW (ITER-like wall) H-modes [6, 7]
    825 from ASDEX Upgrade (AUG) full W wall [8]
  Improved fast-particle loss estimates (AUG)
  DB5v7: 13913 points from 19 devices
    STD5 (H-mode selection criteria [9]): 7294 points
    STD5-SEL1 (, , , ): 5956 points
    STD5-SEL2 (, , , ): 1674 points
  200+ variables, added , , torque (JET, AUG)
ne,sep, ne,SOL, torque (JET, AUG)
(q95>2.8, 1.3<κ<2.2, ε<0.5, Zeff<5: 5956 points)
Zeff<3): 1674 points)
(2.8<q95<3.5, 1.6<κ<2.0, 0.28<ε<0.385
(τE,th, Pl,th, ρ*, ν*, β, …) [13-16]
Parameter estimation techniques
ITER parameters used: Ip=15 MA, BT=5.3 T, ne=10.3e19 m-3, R=6.2 m, ε=a/R=0.32, κ=1.7, δ=0.33, Meff=2.5, Pheat=87 MW
‘H18’
Device | DB5 | STD3 | STD5 | STD5-SEL1 | STD5-SEL2
ASDEX |  |  |  |  | 
AUG-C |  |  |  |  | 
AUG-W |  |  |  |  | 69
C-Mod |  |  |  |  | 
COMPASS |  |  |  |  | 
DIII-D |  |  |  |  | 
JET-C |  |  |  |  | 
JET-ILW |  |  |  |  | 
JFT-2M |  |  |  |  | 
JT60-U |  |  |  |  | 
MAST |  |  |  |  | 
NSTX |  |  |  |  | 
PBXM |  |  |  |  | 
PDX |  |  |  |  | 
START |  |  |  |  | 
T10 |  |  |  |  | 
TCV |  |  |  |  | 
TdeV |  |  |  |  | 
TEXTOR |  |  |  |  | 
TFTR |  |  |  |  | 
TUMAN3M |  |  |  |  | 
Total |  |  |  |  | 
Variables |  | ln BT | ln ne |  |  |  |  |  | ln
ln Ip |  | − | − | − | − | − | − | − | −
 | () |  | − | − | − | − | − | − | −
 | () | ( |  | − | − | − | − | − | −
 | () | () | () |  | − | − | − | − | −
 | () | () | () | () |  | − | − | − | −
 | ( | () | () | () | () |  | − | − | −
 | ( | () | () | () | () | () |  | − | −
 | () | () | () | () | () | () | () |  | −
Meff | () | () | () | () | () | () | () | () | 
Statistic | τE,th (s) | IP (MA) | BT (T) | ne (1019 m-3) | PL,th (MW) | (m) |  |  |  | Meff
Min. | () | () | () | () | () | () | () | () | () | ()
Max. | () | () | () | () | () | () | () | () | () | ()
Mean | () | () | () | () | () | () | () | () | () | ()
Median | () | () | () | () | () | () | () | () | () | ()
Stand. dev. | () | () | () | () | () | () | () | () | () | ()